## Slide 1: BSS Channel Width Configuration
Date: 2020-04-29
Authors:
Name | Affiliations | Address | Phone | email
Young Hoon Kwon Liwen Chu Manish Kumar Hongyuan Zhang Yan Zhang Rui Cao Sudhir Srinivasa Hui-Ling Lou | NXP |  |  | 

## Slide 2: Recap:
We have reached the following consensus
  Do you support to define EHT operation element with the following fields to indicate 320/160+160 MHz BSS bandwidth?
    Channel Width field
    CCFS field
Rationale behind this consensus is to reuse currently defined mechanism in VHT/HE Operation element as much as possible.
  In VHT Operation element
    Channel Width subfield indicates the BSS bandwidth
      0: 20/40 MHz
      1: 80/160/80+80 MHz
    CCFS0
      For 20/40/80MHz BSS BW, indicates the channel center frequency index (CCFI) for the channel.
      For 160MHz BSS BW, indicates the CCFI of the 80MHz channel segment that contains the primary channel.
      For 80+80MHz BSS BW, indicates the CCFI for the primary 80 MHz channel.
    CCFS1
      For 20/40/80MHz BSS BW, is set to 0.
      For 160MHz BSS BW, indicates the CCFI of the 160MHz channel.
      For 80+80MHz BSS BW, indicates the CCFI of the secondary 80MHz channel.

## Slide 3: Backgrounds
[1] also proposed a mechanism to indicate 320/160+160MHz BSS bandwidth using Channel Width subfield and EHT CCFS subfield in EHT Operation element:
    160 MHz (|CCFS0-CCFS1/CCFS2|=8), Channel Width =1/3 (VHT op/HE op), EHT Channel Width = 0
    80+80 MHz (|CCFS0-CCFS1/CCFS2|>16), Channel Width =1/3 (VHT op/HE op), EHT Channel Width = 0
    320 MHz (|CCFS1/CCFS2- EHT CCFS|=16), Channel Width =1/3 (VHT op/HE op), EHT Channel Width = 1
    160+160 MHz (|CCFS1/CCFS2- EHT CCFS|>32), Channel Width =1/3 (VHT op/HE op), EHT Channel Width = 1
However, we think there are several cases that this mechanism does not fully cover, especially when BSS channel includes puncturing.
Primary 80 MHz
Secondary 80 MHz
CCFS0
CCFS1/CCFS2
Secondary 160 MHz
EHT CCFS
Primary 80 MHz
Secondary 80 MHz
CCFS0
CCFS1/CCFS2
Secondary 160 MHz
EHT CCFS

## Slide 4: Observations
When a BSS bandwidth for EHT STAs is greater than 160/80+80MHz, we cannot assume that BSS bandwidth for VHT STAs is 160/80+80MHz.
  Especially when the BSS includes punctured channels.
Information on BSS bandwidth for VHT/HE STAs may not be useful for identifying BSS bandwidth for EHT STAs.
  We better have separate channel bandwidth indication for EHT STAs instead of just indicating 320/160+160MHz or not.
CCFS1/2 may not be useful in some scenarios as these are set to 0 if the BSS bandwidth for VHT/HE STAs is less than 160MHz.
  We better not rely on CCFS1/CCFS2 in identifying the channel bandwidth for EHT STAs.

## Slide 5: Observations
In 5GHz and 6GHz bands, channel center frequency index is constructed in a nested structure:
  For a channel with bandwidth of X, there is only one channel with bandwidth of 2X that includes the channel with bandwidth of X.
    Therefore, if a channel index of primary 20MHz is given, there’s one primary 40MHz that corresponds to the primary 20MHz channel.
    Similarly, if a channel index of primary 40MHz is given, there’s one primary 80MHz that corresponds to the primary 40MHz channel.
  Therefore, if a channel number of a primary channel is given, the CCFI of primary 80MHz channel can be easily obtained (by calculation or by table-lookup).
    E.g., for 6GHz band, if the channel number of P20 is X, the CCFI of 80MHz channel (Y80) and 160MHz channel (Y160) that includes X can be obtained as
      Y80 = floor(X/16)*16 + 7
      Y160 = floor(X/32)*32 + 15
 | 20MHz | 1 | 5 | 9 | 13 | 17 | 21 | 25 | 29 | 33 | 37 | 41 | 45 | 49 | 53 | 57 | 61 | 65 | 69 | 73 | 77 | 81 | 85 | 89 | 93
 | 40 MHz | 3 |  | 11 |  | 19 |  | 27 |  | 35 |  | 43 |  | 51 |  | 59 |  | 67 |  | 75 |  | 83 |  | 91 | 
 | 80 MHz | 7 |  |  |  | 23 |  |  |  | 39 |  |  |  | 55 |  |  |  | 71 |  |  |  | 87 |  |  | 
 | 160 MHz | 15 |  |  |  |  |  |  |  | 47 |  |  |  |  |  |  |  | 79 |  |  |  |  |  |  | 

## Slide 6: Proposals
As we already agreed to have Channel Width and CCFS subfields, let’s try to find out solutions under this assumption.
Channel Width subfield
  This subfield indicates BSS bandwidth for EHT STAs that is not tied to BSS bandwidth for VHT/HE STAs.
    0: 20MHz
    1: 40MHz
    2: 80MHz
    3: 160/80+80MHz
    4: 320/160+160MHz

## Slide 7: Proposals
CCFS subfield
  As CCFS1/2 may not be useful in some scenarios, we cannot directly extend current CCFS1/2 definition to EHT_CCFS.
Option 1: Defines 2 CCFSs in EHT Operation element: EHT_CCFS0/1
  EHT_CCFS0 is an extension of CCFS0 in VHT/HE.
    For 20/40/80MHz BSS BW, indicates the CCFI of the channel.
    For 160MHz BSS BW, indicates the CCFI of the 80MHz channel segment that contains the primary channel.
    For 80+80MHz BSS BW, indicates the CCFI for the primary 80 MHz channel.
    For 320MHz BSS BW, indicates the CCFI of the 160MHz channel segment that contains the primary channel.
    For 160+160MHz BSS BW, indicates the CCFI for the primary 160MHz channel.
  EHT_CCFS1 is an extension of CCFS1/2 in VHT/HE
    For 20/40/80MHz BSS BW, is set to 0.
    For 160/320MHz BSS BW, indicates the CCFI of the channel.
    For 80+80MHz BSS BW, indicates the CCFI of the secondary 80MHz channel.
    For 160+160MHz BSS BW, indicates the CCFI of the secondary 160MHz channel.

## Slide 8: Proposals
For an EHT STA, bandwidth can be indicated as
  Channel Width = 0/1/2: 20/40/80MHz (Location from CCFS0)
  Channel Width =3:
    160MHz: EHT_CCFS1>0 & |EHT_CCFS1-EHT_CCFS0| = 8.
    80+80MHz: EHT_CCFS1>0 & |EHT_CCFS1-EHT_CCFS0| > 16.
  Channel Width = 4:
    320MHz: EHT_CCFS1>0 & |EHT_CCFS1-EHT_CCFS0| = 16.
    160+160MHz: EHT_CCFS1>0 & |EHT_CCFS1-EHT_CCFS0| > 32.
As this is a direct extension of VHT mechanism, it is a simple and clean solution.
  However, it requires additional indication overhead.

## Slide 9: Proposals
Option 2: Define 1 CCFS in EHT Operation element:
  EHT_CCFS indicates:
    Set to 0 if Channel Width is 20/40MHz.
    The CCFI of the channel if Channel Width is 80MHz.
    The CCFI of secondary 80MHz if Channel Width is 160/80+80MHz.
    The CCFI of secondary 160MHz if Channel Width is 320/160+160MHz.
  From the channel number of P20, EHT STA can calculate:
    CCFI of primary 80MHz that includes the P20.
      Let’s say the calculated CCFI is denoted as CCFS_P80.
    CCFI of primary 160MHz that includes the P20.
      Let’s say the calculated CCFI is denoted as CCFS_P160.

## Slide 10: Proposals
For an EHT STA, bandwidth can be indicated as
  Channel Width = 0/1: 20/40MHz
    20MHz or 40MHz from HT/HE op.
  Channel Width = 2: 80MHz (CCFI = EHT_CCFS)
  Channel Width = 3: Calculate CCFS_P80
    160MHz: |CCFS_P80-EHT_CCFS| = 16. (CCFI = (CCFS80+EHT_CCFS)/2)
    80+80MHz: |CCFS_P80-EHT_CCFS| > 16.
  Channel Width = 4: Calculate CCFS_P160
    320MHz: |CCFS_P160-EHT_CCFS| = 32. (CCFI = (CCFS160+EHT_CCFS)/2)
    160+160MHz: |CCFS_P160-EHT_CCFS| > 32.
One EHT_CCFS is enough.
  But, STA needs one more step of calculating CCFS_P80/160.

## Slide 11: Proposals
Operation example for Option 2
  BSS bandwidth for VHT/HE STAs is 80MHz.
  BSS bandwidth for EHT STA is 320MHz.
    Based on P20, calculate CCFS_P160 (CCFS_P160 = CCFI of 160C (= 15)).
    EHT_CCFS indicates the channel center frequency of 160D (=47).
  As |CCFS_P160 – EHT_CCFS| = 32, the BSS bandwidth is identified to be 320MHz.
  And, the channel center frequency index of the 320MHz channel is (CCFS160+EHT_CCFS)/2 = 31.
For VHT/HE STAs: 80 BSS (80F)
For EHT STAs: 320MHz BSS (320B)
80E (7)
80F (23)
80G (39)
80H (55)
160C (15)
160D (47)
CCFS0
EHT CCFS
CCFS_P160
320B (31)

## Slide 12: Summary
Setting of Channel Width & EHT CCFS subfields are discussed.
  Channel Width subfield indicates BSS bandwidth for EHT STAs that is not tied to BSS bandwidth for VHT/HE STAs.
  EHT_CCFS
    Option 1
      Two EHT_CCFS subfields
      Simple extension of VHT CCFS0/1
    Option 2
      Single EHT_CCFS subfield
      EHT STA needs to calculate primary 80/160 from P20.

## Slide 13: Reference
[1] IEEE 802.11-20/0384r1, 320 MHz BSS Configuration, Intel.

## Slide 14: SP
Do you support in TGbe SFD that
  There are two CCFS subfields (EHT_CCFS0/EHT_CCFS1) in EHT Operation element.
EHT BSS channel width | EHT_CCFS0 subfield | EHT_CCFS1 subfield
20/40/80 MHz | CCFI of the EHT BSS channel width | 0
160 MHz | CCFI of the primary 80 MHz | CCFI of the EHT BSS channel width
80+80MHz | CCFI of the primary 80 MHz | CCFI of the secondary 80 MHz
320 MHz | CCFI of the primary 160 MHz | CCFI of the EHT BSS channel width
160+160 MHz | CCFI of the primary 160 MHz | CCFI of the secondary 160 MHz

## Slide 15: Appendix: Example case 1
If the supported BSS BW is
  80MHz for VHT/HE STAs: 80F
  320MHz for EHT STAs: 320B
    80E to be punctured 240MHz (Assuming no separate 240/80+160/160+80MHz indication)
In VHT/HE Operation element
  Channel Width is set to 0/2 (VHT/HE).
  CCFS0 is set to CCFI of 80E and CCFS1/2 is set to 0.
For EHT Operation element
  Channel Width is set to 1 (320/160+160MHz).
  EHT_CCFS is set to CCFI of 320B.
Then, |CCFS1 – EHT_CCFS| is meaningless as CCFS1 = 0.
80A
80B
80C
80D
80E
80F
80G
80H
160A
160B
160C
160D
320A
80 MHz
160 MHz
320 MHz
CCFS0
EHT_CCFS
320B

## Slide 16: Appendix: Example case 2
If the supported BSS BW is
  80+80MHz for VHT/HE STAs: 80D (P80) + 80G (S80)
  160+160MHz for EHT STAs: 160B (P160) + 160D (S160)
    80C to be punctured  80+160MHz
In VHT/HE Operation element
  Channel Width is set to 1/3 (VHT/HE).
  CCFS0 is set to CCFI of 80D and CCFS1/2 is set to CCFI of 80G.
For EHT Operation element
  Channel Width is set to 1 (320/160+160MHz).
  EHT_CCFS is set to CCFI of 160D.
Then, |CCFS1/2 – EHT_CCFS| = 8 < 32.
  The result deviates from the proposed equation.
80A
80B
80C
80D
80E
80F
80G
80H
160A
160C
160D
320A
320B
80 MHz
160 MHz
320 MHz
CCFS0
CCFS1/2
EHT_CCFS
160B

## Slide 17: Appendix: Example case 3
If the supported BSS BW is
  80+80MHz for VHT/HE STAs: 80E (P80) + 80G (S80)
  320MHz for EHT STAs: 320B
    80F to be punctured  80+160MHz
In VHT/HE Operation element
  Channel Width is set to 1/3 (VHT/HE).
  CCFS0 is set to CCFI of 80E and CCFS1/2 is set to CCFI of 80G.
For EHT Operation element
  Channel Width is set to 1 (320/160+160MHz).
  EHT_CCFS is set to CCFI of 320B.
Then, |CCFS1/2 – EHT_CCFS| = 8 (≠ 16).
  So, the result deviates from the proposed equation.
  Also the outcome is the same with Case 2.  Cannot tell if it is 320 or 160+160MHz.
80A
80B
80C
80D
80E
80F
80G
80H
160A
160B
160C
160D
320A
80 MHz
160 MHz
320 MHz
CCFS0
CCFS1/2
EHT_CCFS
320B