## Slide 1: Single STA Trigger
Date: 2020-04-28
Authors:
Name | Affiliations | Address | Phone | email
Young Hoon Kwon Liwen Chu Manish Kumar Hongyuan Zhang Yan Zhang Rui Cao Sudhir Srinivasa Hui-Ling Lou | NXP |  |  | 

## Slide 2: Background:
For a transmission to a non-AP non-STR MLD on multiple links, an AP MLD would like to align the transmission end time on the multiple links.
At the same time, the AP MLD would like to solicit immediate response frame to be carried on PPDUs occupying the same packet duration during the AP MLD’s TXOPs on multiple links.
DATA1
BA1
DATA3
BA3
DATA2
BA2
DATA4
BA4
Link 1
Link 2

## Slide 3: Background
Baseline rules for rate selection for control response frame:
  If a CTS or Ack frame is carried in a non-HT PPDU, the primary rate is defined to be the highest rate in the BSSBasicRateSet parameter that is less than or equal to the rate (or non-HT reference rate) of the previous frame.
  If no rate in the BSSBasicRateSet parameter meets these conditions, the primary rate is defined to be the highest mandatory rate of the attached PHY that is less than or equal to the rate (or non-HT reference rate) of the previous frame.
  The STA may select an alternate rate according to the rules in 10.6.6.5.4.
  The STA shall transmit the non-HT PPDU CTS or Ack frame at either the primary rate or the alternate rate, if one exists.
  Similar rule is applied to BA frame transmission.

## Slide 4: Issues
There are several cases that the length of PPDU carrying immediate response frame can be different on different links:
  Different primary rate on different links
  Different acknowledgement frame on different links
    Ack frame on link1 and BA on link2
  Different bitmap size on different links
    BA with 64 bitmap on link1 and BA with 1024 bitmap on link2
We need a mechanism to align the packet duration for the control response frames on different links even under above operation cases.
Several previous contributions mentioned using a (modified version of) Trigger frame to determine the packet duration of the control response frame for this purpose.

## Slide 5: Trigger information
If a Trigger frame is used for this purpose:
  Aligning symbol boundary between HE TB PPDUs from different STAs are not needed.
    TXOP holder does not need to dictate details of the PPDU carrying the control response frame from a single STA.
  UL Power control from different STAs are not needed.
  For short control response frame transmission, no reason to use STBC, Doppler, spatial reuse, etc.
  As a single STA will occupy full bandwidth, no reason to indicate RU allocation.
  As the solicited frame is a control response frame, CS shall not be required unless the size of the responding PPDU is over a limit.

## Slide 6: Trigger information
PPDU format for control response frame:
  In case of baseline Trigger frame, HE TB PPDU shall be used for the acknowledgement frame.
  However, in case of single STA trigger, there’s no gain of using HE TB PPDU:
    No protection from legacy STAs
      Especially for initial frame exchange of a TXOP that the HE TB PPDU is the first frame transmitted by a TXOP responder.
    If higher data rate and/or wide bandwidth transmission is preferred, VHT/HE SU PPDU gives better protection to legacy VHT/HE STAs.
  Allowing an acknowledgement frame transmission in SU PPDU format is beneficial.
    RU Allocation information is not needed.
    As only one STA is triggered for this use case, TXOP holder doesn’t need to dictate which PPDU format to use as long as the control response frame satisfy the required PPDU length condition.

## Slide 7: Trigger information
Then, mandatory information needed for this purpose is
  Indication not to use HE TB PPDU
  PPDU duration
Also, the Trigger information should be included in a PPDU that initiates a TXOP.
  When an AP MLD obtains a TXOP on link1 and initiates data transmission (DATA1) with/without a Trigger frame.
  However, when the AP MLD’s backoff reaches 0 and initiates data transmission (DATA2) on link2, trigger information needs to be included in the PPDU carrying DATA2.
  As DATA2 initiates the TXOP, it should be carried on a PPDU with non-HT (duplicate) PPDU format.
DATA1 + (Tr)
BA1
DATA3 + Tr
BA3
DATA2 + Tr
BA2
DATA4 + Tr
BA4
Link 1
Link 2
RTS
CTS

## Slide 8: Single STA Trigger format
Trigger frame
  We may define a new variant of a Trigger frame to indicate that SU type PPDU is solicited.
    Or, we can reuse/repurpose some bits in Common/User Info field of Basic Trigger frame.
  However, except UL length subfield, all other subfields may need to set to reserved as these information are not required.
    Use of over 30 Octets to carry 12-bit UL length information looks over-kill.
  If a target STA fails to receive the Trigger frame correctly either on one link or on both links, it is needed to define the target STA’s behavior further.
  Also, as A-MPDU is not carried in a non-HT (duplicate) PPDU, use of a separate Trigger frame may not be a good solution for TXOP initiating frame transmission.
Trigger information in A-Control field
  we may define a new Control ID to indicate that SU type PPDU is solicited.
    Or, we may reuse current TRS Control variant A-Control subfield (with some modification).
  This has lower overhead compared to separate Trigger frame, and can be added in non-HT (duplicate) PPDU.
Both are fine, but we prefer Trigger information carried in A-Control field.

## Slide 9: Single STA Trigger
If solicited packet duration is shorter than baseline frame transmission time:
  E.g., when BA1 and CTS are transmitted simultaneously.
  Use of higher data rate than allowed may be used.
  Use of PPDU format other than non-HT (duplicate) format may be used.
    For better legacy protection, we can limit this usage case only when the TXOP is protected from the TXOP responder side.
DATA1 + Tr
BA1
DATA2 + Tr
BA2
RTS
CTS
Link 1
Link 2
RTS
CTS
BUSY
…
…
DATA2 + Tr
BA2

## Slide 10: Summary
Need of single STA trigger frame is discussed:
  Triggering a SU PPDU with indicated PPDU length.
Use of A-Control field looks more suitable.
  Less overhead and more flexible usage
Single STA trigger can also be used to solicit an acknowledgement frame with higher rate and/or specific PPDU format even in single link operation.
  To reduce BA overhead especially for a BA with large bitmap size

## Slide 11: SP
Do you support in R1 of TGbe that
  A non-AP STA can include an indication in a PPDU that solicits an AP to transmit a control response frame in an SU PPDU whose duration is indicated by the indication in a new A-ctrl subfield. The new A-ctrl subfield will be specifically designed to include that duration for the control response.
  The SU PPDU can be carried in at least HE/EHT PPDU to meet the indicated duration.