## Slide 1: Aggregated PPDU for Large BW
Date: 2020-05-02
Authors:

## Slide 2: Introduction
EHT allows up to 320MHz BSS operation.
Many EHT client STAs will operate in 20/80/160MHz.
Many HE STAs with operating BW of 20/80/160MHz will exist at the time of EHT APs coming to market.
How to get the most Tput out of large BW BSS?
  SST Mechanism for STAs parking on secondary channels
  Aggregated PPDU

## Slide 3: Aggregated PPDU (A-PPDU)
Aggregated PPDU consists of multiple sub-PPDUs.
  Each sub-PPDU occupies non-overlapping frequency segments.
  The sub-PPDUs are orthogonal in frequency domain symbol-by-symbol.
  Each sub-PPDU can have the same or different PPDU format.
  Similar to Coordinated OFDMA format using small-BW PPDU.
Both downlink and uplink are applicable.
Sub-PPDU-3
Sub-PPDU-2
Sub-PPDU-1
Aggregated PPDU
160MHz
80MHz
80MHz

## Slide 4: Sub-PPDU Format
Sub-PPDU can be EHT or HE PPDU.
EHT-HE aggregation
  Most useful case
  Achieve good throughput gain with traffic from mixed STAs.
  Better support of secondary channel parking of EHT STAs.
EHT-EHT aggregation
  Similarly to EHT OFDMA, with limitation of resource allocation.
  May save some EHT-SIG overhead.
HE-HE aggregation
  Achieves double/quadruple throughput with similar overhead.
  May not work well in punctured channels.
  HE 80MHz operating STA parking on secondary 80MHz does NOT have good support for punctured channels.

## Slide 5: Enabler for A-PPDU
Mechanism for STAs parked on secondary channels, e.g.
  SST protocol enhancement.
  PHY signaling for Puncture Information for each segment.
Preamble alignment across sub-PPDUs.
  EHT and HE are well aligned up to U-SIG/HE-SIGA.
  Alignment of EHT-SIG and HE-SIGB.
    Padding scheme to allow the same number symbols.
    HE-SIGB allows SU/MUMIMO transmission in uncompressed mode.
    EHT-SIG should also consider allowing SU/MUMIMO transmission in uncompressed mode.
  Same format of EHT-LTF and/or HE-LTF, or same as Data.
Data portion alignment
  The same tone spacing across sub-PPDUs: EHT and HE
  The same GI setting.

## Slide 6: Summary
A-PPDU is beneficial for BSS with large BW.
  When most client STAs having operating BW <= 160MHz.
  Boost BSS throughput for both DL/UL.
  Flexible scheduler for traffic from mixed generation of STAs.
With small design consideration in EHT preamble, A-PPDU can be easily supported.
A-PPDU is almost transparent to both EHT and HE receiver.

## Slide 7: SP
Do you agree to define aggregated PPDU for EHT?
  Aggregated PPDU consists of multiple sub-PPDUs.
    The sub-PPDU format combination limits to EHT and HE.
    Other combinations are TBD
    For the sub-PPDU using HE format, the PPDU BW TBD.
  A-PPDU will be R2 feature.
Y
N
A