## Slide 1: Phase Rotation Proposal Follow-up
Date: 2020-05-06
Authors:
Name | Affiliation | Address | Phone | Email
Eunsung Park | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | esung.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Introduction
In [1]-[3], we discussed how to design a phase rotation sequence in a wide bandwidth
Especially in [3], we proposed phase rotation designed by repeating 11ax 80MHz phase rotation and applying an additional coefficient to each 80MHz segment
  Additional coefficients were optimized in consideration of the preamble punctured patterns approved in 11be
However, we found that this approach cannot achieve an enough reduction in PAPR of the L-SIG part
In this contribution, we further investigate PAPR focusing on L-SIG even in narrow bandwidths as well as wide bandwidths
  In Appendix, we also show PAPRs for the other preamble parts
In addition, we propose an alternative phase rotation sequence which can further improve the PAPR in each bandwidth

## Slide 3: PAPR Investigation
We compare CDF of PAPR between L-SIG and the data part in 40/80/160/240/320 MHz
  To plot the CDF, we use all possible contents of L-SIG and 500 data parts which are randomly generated and are modulated by BPSK or QPSK
We also apply various phase rotation sequences to the L-SIG part
  For 40/80/160 MHz
    Option 1: conventional 11ax phase rotation
    Option 2: alternative phase rotation
    w/o phase rotation: phase rotation is not applied to the L-SIG part
  For 240/320 MHz
    Option 1: repeating conventional 11ax phase rotation
    Option 2: repeating conventional 11ax phase rotation and applying an additional coefficient to each 80MHz segment
    Option 3: alternative phase rotation
    w/o phase rotation: phase rotation is not applied to the L-SIG part

## Slide 4: PAPR Investigation
For the bandwidth ≥ 80MHz, CDF includes PAPRs for all approved punctured patterns as well as the non-punctured one
  For 40MHz, we only consider the non-punctured case
For the bandwidth ≥ 160MHz, two CDF figures are presented to take account of both contiguous and non-contiguous modes
  Figure 1: PAPR for the whole bandwidth considering the contiguous mode
    E.g., for 320MHz, PAPR only for whole 320MHz (IFFT is applied to 320MHz)
  Figure 2: PAPRs for two possible non-contiguous portions as well as the whole bandwidth considering the contiguous mode
    E.g., for 320MHz, PAPRs for each 160MHz (IFFT is applied to each 160MHz) as well as whole 320MHz (IFFT is applied to 320MHz)
  For the bandwidth < 160MHz, we only present Figure 1
In Appendix, PAPR results for the other preamble parts such as L-STF, L-LTF, U-SIG and EHT-SIG are also shown according to phase rotation

## Slide 5: PAPR Investigation - 40MHz
For 40MHz, there is no agreed preamble punctured pattern, and thus, the following figure only contains PAPR for the non-punctured one
Option 1: [1 j]
Option 2: [1 -1]
Option 1, i.e., the conventional phase rotation causes too much higher PAPR in the L-SIG part and seems even worse than the case without phase rotation
Option 2 can improve the PAPR although it has a higher PAPR than the data part
As can be seen in Appendix, option 2 has a slightly better PAPR in most of the preamble parts

## Slide 6: PAPR Investigation - 80MHz
The following figure contains PAPR for the agreed punctured patterns as well as the non-punctured one
Option 1: [1 -1 -1 -1]
Option 2: [1 -1 -1 1]
The case without phase rotation has a quite high PAPR in the L-SIG part
The trend of the others is similar to 40MHz

## Slide 7: PAPR Investigation - 160MHz
The following figures contain PAPR for the agreed punctured patterns as well as the non-punctured one
  Option 1: [1 -1 -1 -1 1 -1 -1 -1]
  Option 2: [1 1 1 -1 1 -1 -1 1]
Figure 1: PAPRs only for whole 160MHz
Figure 2: PAPRs for whole 160MHz and each 80MHz as well
Figure 1
Figure 2

## Slide 8: PAPR Investigation - 240MHz
The following figures contain PAPR for the agreed punctured patterns as well as the non-punctured one
  Option 1: [1 -1 -1 -1 1 -1 -1 -1 1 -1 -1 -1]
  Option 2: [1 -1 -1 -1 -1 1 1 1 -1 1 1 1]
  Option 3: [1 1 -1 1 -1 1 -1 -1 -1 -1 1 1]
Figure 1: PAPRs only for whole 240MHz
Figure 2: PAPRs for whole 240MHz and each 80MHz and 160MHz as well
Figure 1
Figure 2

## Slide 9: PAPR Investigation - 320MHz
The following figures contain PAPR for the agreed punctured patterns as well as the non-punctured one
  Option 1: [1 -1 -1 -1 1 -1 -1 -1 1 -1 -1 -1 1 -1 -1 -1]
  Option 2: [1 -1 -1 -1 1 -1 -1 -1 -1 1 1 1 -1 1 1 1]
  Option 3: [1 -1 j j 1 1 j -j j -j -1 -1 -j -j 1 -1]
Figure 1: PAPRs only for whole 320MHz
Figure 2: PAPRs for whole 320MHz and each 160MHz as well
Figure 1
Figure 2

## Slide 10: Conclusion
We have investigated PAPR for the preamble parts by applying various phase rotation sequences
  For reference, PAPR for the data part has been also examined
We have verified that
  11ax phase rotation in 40/80/160 MHz causes a bit high PAPR especially in L-SIG
  Reusing 11ax 80MHz phase rotation in 240/320 MHz seems less effective to reduce PAPR
  In all bandwidths, the alternative phase rotation can further improve PAPR for most of the preamble parts although it may be hard to make the PAPR especially for L-SIG better than the data part
    L-SIG or U-SIG Type 1 shown in Appendix seems to have the worst PAPR among the preamble parts
    The alternative phase rotation always outperforms the other options in these two parts, i.e., it has the minimum worst PAPR

## Slide 11: Straw Poll #1
Do you agree to add the following text to the TGbe SFD?
  Phase rotation is applied to legacy preamble, RL-SIG, U-SIG and EHT-SIG in EHT PPDU
Y/N/A: //

## Slide 12: Straw Poll #2
Do you agree to define a new phase rotation sequence which is different from the 11ax one for 40/80/160/80+80 MHz PPDU?
  It is not intended for SFD
Y/N/A: //

## Slide 13: Straw Poll #3
Do you agree to add the following text to the TGbe SFD?
  11be reuses the phase rotation sequence defined in 11ax for 20/40/80/160/80+80 MHz PPDU
Y/N/A: //

## Slide 14: Straw Poll #4
Do you agree to add the following text to the TGbe SFD?
  11be supports the following phase rotation sequence for 40MHz PPDU
    [1 -1]
Y/N/A: //

## Slide 15: Straw Poll #5
Do you agree to add the following text to the TGbe SFD?
  11be supports the following phase rotation sequence for 80MHz PPDU
    [1 -1 -1 1]
Y/N/A: //

## Slide 16: Straw Poll #6
Do you agree to add the following text to the TGbe SFD?
  11be supports the following phase rotation sequence for 160/80+80 MHz PPDU
    [1 1 1 -1 1 -1 -1 1]
Y/N/A: //

## Slide 17: Straw Poll #7
Do you agree to add the following text to the TGbe SFD?
  11be supports the following phase rotation sequence for 240/160+80 MHz PPDU
    [1 1 -1 1 -1 1 -1 -1 -1 -1 1 1]
Y/N/A: //

## Slide 18: Straw Poll #8
Do you agree to add the following text to the TGbe SFD?
  11be supports the following phase rotation sequence for 320/160+160 MHz PPDU
    [1 -1 j j 1 1 j -j j -j -1 -1 -j -j 1 -1]
Y/N/A: //

## Slide 19: References
[1] IEEE 802.11-19/1493r1 Phase Rotation for 320MHz
[2] IEEE 802.11-19/1890r2 Phase Rotation Follow-up
[3] IEEE 802.11-20/0406r1 Phase Rotation Proposal

## Slide 20: Appendix

## Slide 21: Assumptions
Appendix presents PAPR results for L-STF, L-LTF, U-SIG and EHT-SIG in all bandwidths
We consider two types of U-SIG
  Type 1: It is duplicated in every 20MHz in all bandwidths
  Type 2: It is duplicated in every 20MHz within 80MHz while each 80MHz has different U-SIG contents
  We plot CDF by randomly generating 500 U-SIG fields which are modulated by BPSK
We consider two types of EHT-SIG
  Type 1: It has [1 2 1 2 …] structure for all bandwidths, i.e., we consider only two content channels whatever the bandwidth is
  Type 2: It has [1 2 1 2] structure within 80MHz while each 80MHz has different EHT-SIG contents
  We plot CDF by randomly generating 500 EHT-SIG fields which are modulated by BPSK or QPSK

## Slide 22: 40MHz
L-STF
U-SIG
EHT-SIG
L-LTF

## Slide 23: 80MHz
L-STF
U-SIG
EHT-SIG
L-LTF

## Slide 24: 160MHz – Figure 1 (1/2)
L-STF
U-SIG Type 1
U-SIG Type 2
L-LTF

## Slide 25: 160MHz – Figure 1 (2/2)
EHT-SIG Type 1
EHT-SIG Type 2

## Slide 26: 160MHz – Figure 2 (1/2)
L-STF
L-LTF
U-SIG Type 1
U-SIG Type 2

## Slide 27: 160MHz – Figure 2 (2/2)
EHT-SIG Type 1
EHT-SIG Type 2

## Slide 28: 240MHz – Figure 1 (1/2)
L-STF
L-LTF
U-SIG Type 1
U-SIG Type 2

## Slide 29: 240MHz – Figure 1 (2/2)
EHT-SIG Type 1
EHT-SIG Type 2

## Slide 30: 240MHz – Figure 2 (1/2)
L-STF
L-LTF
U-SIG Type 1
U-SIG Type 2

## Slide 31: 240MHz – Figure 2 (2/2)
EHT-SIG Type 1
EHT-SIG Type 2

## Slide 32: 320MHz – Figure 1 (1/2)
L-STF
L-LTF
U-SIG Type 1
U-SIG Type 2

## Slide 33: 320MHz – Figure 1 (1/2)
EHT-SIG Type 1
EHT-SIG Type 2

## Slide 34: 320MHz – Figure 2 (1/2)
L-STF
L-LTF
U-SIG Type 1
U-SIG Type 2

## Slide 35: 320MHz – Figure 2 (2/2)
EHT-SIG Type 1
EHT-SIG Type 2