## Slide 1: Overhead Comparisons of EHT-SIG
Date: 2020-05-07
Authors:

## Slide 2: Introduction
In this contribution, we calculate the number of bits for EHT-SIG when 11ax SIG-B-style design or self-contained design is considered to compare the overhead of both methods according to the bandwidths and number of users.

## Slide 3: Overhead of EHT-SIG with 11ax SIG-B-style Design
Common field for each EHT-SIG content channel
  For BW 80MHz, common field for each EHT-SIG content channel has 31 bits (2*10 bits+1 bit+4 bits+6 bits as follows).
  Note: If we consider that the content channels per each 80MHz may carry the information of its 80MHz (based on passed motions and SPs in TGbe), the number of RU Allocation subfields can be set to 2 (N=2) for BW>=80MHz.
Subfield | Number of subfields | Number of bits per subfield | Description
RU Allocation | N | 10 | RU Allocation table of 10 bits is required to indicate multi-RU assignment and MU-MIMO STAs (up to 16).
Center 26-tone RU | 0 or 1 | 1 | 
CRC | 1 | 4 | 
Tail | 1 | 6 | 

## Slide 4: Overhead of EHT-SIG with 11ax SIG-B-style Design (Cont’d)
User field: 22 bits (as follows) + per user effective 5 bits for CRC + tail = 27 bits per user
  For Non-MU-MIMO allocation
  For MU-MIMO allocation
Subfield | Number of bits
STA-ID | 11
NSTS | 4 (due to 16SS in EHT)
Beamformed | 1
Subfield | Number of bits
MCS | 4
DCM | 1
Coding | 1
Subfield | Number of bits
STA-ID | 11
Spatial Configuration | 5 (due to 16SS in EHT)
Subfield | Number of bits
MCS | 4
Reserved | 1
Coding | 1

## Slide 5: Overhead of EHT-SIG with Self-contained Design
User field: 44 bits per user
  Note: One CRC and tail per one User field
    If there are 2 User fields in one User Block field, one CRC + tail for 2 User fields may be weak comparing to User field in 11ax SIG-B-style design.
    But, this can be changed so that the overall performance is similar.
Subfield | Number of bits per subfield | Description
AID12 | 12 | 
RU Allocation | 10 | RU Allocation table of 10 bits is required to indicate multi-RU assignment.
Coding | 1 | 
MCS | 4 | 
DCM | 1 | 
SS Allocation | 6 | 4 bits for starting spatial stream, 2 bits for number of spatial streams (up to 4 SS for MU-MIMO)
CRC | 4 | 
Tail | 6 | 

## Slide 6: Evaluation Assumptions for Overhead Comparisons
Perfect load balancing is assumed.
  There exists at least one user in 20MHz.
Two options for content channel are considered.
  Option 1: Duplicating EHT-SIG information per 40MHz, with different information in each 20MHz within the 40MHz (11ax-style)
  Option 2: Based on passed motions and SPs, the following structure is considered.
    EHT-SIG can be variant on each 80MHz segment.
    The content channels per each 80MHz may carry the information of its 80MHz.
    [1 2 1 2] structure for each 80MHz segment is considered.

## Slide 7: Results of Overhead Comparisons – BW 80MHz
Option 1
Option 2
Both options have the same overheads as they have the same structures of the content channel when BW=80MHz.
For both options, the overhead of 11ax SIG-B-style design is smaller than that of self-contained design.

## Slide 8: Results of Overhead Comparisons – BW 160MHz
Option 1
Option 2
For both options, the overhead of 11ax SIG-B-style design is smaller than that of self-contained design.

## Slide 9: Results of Overhead Comparisons – BW 240MHz
Option 1
Option 2
For both options, the overhead of 11ax SIG-B-style design is smaller than that of self-contained design.

## Slide 10: Results of Overhead Comparisons – BW 320MHz
Option 1
Option 2
For both options, the overhead of 11ax SIG-B-style design is smaller than that of self-contained design.

## Slide 11: Summary
In this contribution, we compared the overhead of 11ax SIG-B-style and self-contained designs
We confirmed that the overhead of 11ax SIG-B-style design is always smaller than that of self-contained design for any structure for content channel and bandwidth.