## Slide 1: Evaluation of signaling overhead for EHT-SIG
Date: 2020-05-xx
Authors:
Name | Affiliation | Address | Phone | Email
Dongguk Lim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | dongguk.lim@lge.com
Eunsung Park |  |  |  | Ensung.park@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
May 2020

## Slide 2: Introduction
For the signaling of RU allocation, two options for configuration of EHT-SIG have been suggested in previous meeting.
  Option 1 : based on the RU allocation subfield (i.e., similar to 11ax HE-SIGB) [1,2,3]
  Option 2 : based on the self-contained user field [4]
In this contribution, we investigated the signaling overhead according to each option.

## Slide 3: U-SIG content
Based on the 11be SFD, in the OFDMA transmission, the U-SIG can be composed as below.
  The details for bits of each content and some fields need to further discuss.
Index | contents | bits | Index | contents | bits
1 | PHY version identifier | 3 | 9 | Spatial reuse | 4
2 | UL/DL flag | 1 | 10 | EHT-SIG MCS (including DCM) | 3
3 | TXOP | 7 | 11 | Number of EHT-SIG Symbols/ Number of users for MU-MIMO | 5
4 | BSS Color | 6 | 12 | LDPC Extra Symbol Segment | 1
5 | BW | 4 | 13 | Pre-FEC Padding Factor | 2
6 | PPDU type | 2 | 14 | PE Disambiguity | 1
7 | Compression mode | 1 | 15 | CRC | 4
8 | GI+EHT-LTF Size | 2 | 16 | Tail | 6

## Slide 4: EHT-SIG content (1/2)
Option1 : Based on the RU allocation field.
  EHT-SIG consists of common field and user-specific field as defined in 11be SFD
  We assume that the common fields include the overflowed information from U-SIG.
    For example, as shown in below table, 7 bits are considered as the information overflowed from U-SIG.
  For example, the common field and the user-specific field can be composed as follows.
    Total bits for the common field : 10 x N + 19 bits
    Total bits for the User specific field : 32 bits
Index | contents | bits
1 | Doppler* | 1
2 | Number of HE-LTF Symbols And Midamble Periodicity* | 5
3 | STBC* | 1
4 | RU allocation | 10 x N
5 | center 26 RU | 2
6 | CRC | 4
7 | tail | 6
Index | contents | bits
1 | STA-ID | 11
2 | NSTS | 4
3 | beamfored | 1
4 | MCS | 4
5 | DCM | 1
6 | Coding | 1
7 | CRC | 4
8 | Tail | 6
The Common field
The User-specific field
* : information overflowed from U-SIG, N : 1/2/4/8 per 20 and 40/80/160/320MHz, respectively.

## Slide 5: EHT-SIG content (2/2)
Option 2 : Based on the self-contained user field.
  We assume that the information overflowed from U-SIG are included in self-contained user field.
  For example, the self-contained user field can be configured as below.
    The total number of bits : 49 bits
Index | contents | bits
1 | STA-ID | 12
2 | RU allocation | 9
3 | Doppler* | 1
4 | Number of HE-LTF Symbols And Midamble Periodicity* | 5
5 | STBC* | 1
6 | NSTS | 4
7 | beamfored | 1
8 | MCS | 4
9 | DCM | 1
10 | Coding | 1
11 | CRC | 4
12 | tail | 6
* : information overflowed from U-SIG

## Slide 6: Assumption
We consider the following assumptions
  BW : 80MHz/160MHz/320MHz
  # of EHT-SIG content channel : 2
  The size of Allocation information
    Opt.1 : 10bits, Opt.2 : 9bits
  # of user in user block : 2 (i.e., equal to configuration of 11ax user block)
  MCS : MCS0/MCS1/MCS3
  Perfect load balancing
Configuration of EHT-SIG content channel
  We considered the following structure as the configuration of EHT-SIG content channel
1
2
1
2
1
2
1
2
1
2
1
2
1
2
1
2
320MHz
40MHz

## Slide 7: Overhead comparison – 80 and 160MHz
For both bandwidth, the overhead of option 1 (i.e., based on RU allocation subfield) is smaller than option 2.
  In 80MHz, regardless of MCS level, opt.1 has a small overhead.
  In 160MHz, except for the case that a few users exist, generally, opt.1 has a small overhead.
Chart: # of EHT-SIG symbol in 80MHz
| 4 | 8 | 12 | 16 | 20 | 24 | 28 | 32 | 36 | 40 | 44 | 48 | 52 | 56 | 60
opt.1, MCS0 | 4 | 6 | 8 | 10 | 12 | 14 | 17 | 19 | 21 | 23 | 25 | 27 | 29 | 31 | 33
Opt.2, MCS0 | 4 | 7 | 10 | 13 | 16 | 19 | 22 | 25 | 29 | 32 | 35 | 38 | 41 | 44 | 47
Opt.1, MCS1 | 2 | 3 | 4 | 5 | 6 | 7 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
Opt.2, MCS1 | 2 | 4 | 5 | 7 | 8 | 10 | 11 | 13 | 15 | 16 | 18 | 19 | 21 | 22 | 24
Opt.1, MCS3 | 1 | 2 | 2 | 3 | 3 | 4 | 5 | 5 | 6 | 6 | 7 | 7 | 8 | 8 | 9
Opt.2, MCS3 | 1 | 2 | 3 | 4 | 4 | 5 | 6 | 7 | 8 | 8 | 9 | 10 | 11 | 11 | 12
Chart: # of EHT-SIG symbol in 160MHz
| 4 | 8 | 12 | 16 | 20 | 24 | 28 | 32 | 36 | 40 | 44 | 48 | 52 | 56 | 60
Opt.1, MCS0 | 5 | 7 | 9 | 11 | 13 | 15 | 17 | 19 | 21 | 24 | 26 | 28 | 30 | 32 | 34
Opt.2, MCS0 | 4 | 7 | 10 | 13 | 16 | 19 | 22 | 25 | 29 | 32 | 35 | 38 | 41 | 44 | 47
Opt.1, MCS1 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
Opt.2, MCS1 | 2 | 4 | 5 | 7 | 8 | 10 | 11 | 13 | 15 | 16 | 18 | 19 | 21 | 22 | 24
Opt.1, MCS3 | 2 | 2 | 3 | 3 | 4 | 4 | 5 | 5 | 6 | 6 | 7 | 7 | 8 | 8 | 9
Opt.2, MCS3 | 1 | 2 | 3 | 4 | 4 | 5 | 6 | 7 | 8 | 8 | 9 | 10 | 11 | 11 | 12

## Slide 8: Overhead comparison – 320MHz
In wideband width, generally, option 1 has a small overhead, despite a large number of RU allocation bits, except when there are few users.
When fewer users exist, opt.1 has a slight high overhead than opt.2. However, this difference is very small and if we consider the high MCS level, the overhead of both option are the same.
Chart: # of EHT-SIG symbol in 320MHz
| 4 | 8 | 12 | 16 | 20 | 24 | 28 | 32 | 36 | 40 | 44 | 48 | 52 | 56 | 60
Opt.1, MCS0 | 6 | 8 | 11 | 13 | 15 | 17 | 19 | 21 | 23 | 25 | 27 | 29 | 31 | 33 | 35
Opt.2, MCS0 | 4 | 7 | 10 | 13 | 16 | 19 | 22 | 25 | 29 | 32 | 35 | 38 | 41 | 44 | 47
Opt.1, MCS1 | 3 | 4 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18
Opt.2, MCS1 | 2 | 4 | 5 | 7 | 8 | 10 | 11 | 13 | 15 | 16 | 18 | 19 | 21 | 22 | 24
Opt.1, MCS3 | 2 | 2 | 3 | 4 | 4 | 5 | 5 | 6 | 6 | 7 | 7 | 8 | 8 | 9 | 9
Opt.2, MCS3 | 1 | 2 | 3 | 4 | 4 | 5 | 6 | 7 | 8 | 8 | 9 | 10 | 11 | 11 | 12

## Slide 9: Consideration for MU-MIMO
For MU-MIMO, we can consider the following two cases.
  Case 1 - Full bandwidth MU-MIMO
  Case 2 - MU-MIMO in OFDMA
If compressed mode (i.e., Full bandwidth MU-MIMO) is used, since the common field including RU allocation subfield can be omitted in the EHT-SIG field, the overhead of opt.1 can be more reduced.
And, opt.2 can also reduce the overhead by excluding RU allocation information from the user field, but it causes the problem that results in change of sizes of the user field.
So, for opt.2, two sizes of user field should be defined in 11be and it can increase the complexity.
In case 2, since opt.2 should include a RU information per user field whereas opt.1 has same RU allocation field regardless of MU-MIMO, the overhead of opt.2 is larger than opt.1

## Slide 10: Summary
We evaluated the overhead of signaling for EHT-SIG according to each option.
  Opt.1 - based on the RU allocation subfield
  Opt.2 - based on the self-contained user field
We have confirmed the results that the overhead of opt.1 is smaller than that of opt.2 considering BW, MCS.
  Opt.1 can also use a fixed size of the user field, whether or not using compression mode..

## Slide 11: Straw poll #1
Do you agree that N RU allocation subfields are present in an EHT-SIG content channel? ?
  Where, N is the number of RU allocation subfield in common field of EHT-SIG content channel.
  N = 1 if a 20MHz or 40MHz EHT PPDU sent to multiple users is used.
  N = 2 per 80MHz segment if a equal to or larger than 80MHz EHT PPDU sent to multiple users is used.
  The compressed modes are TBD.
  Y/N/A

## Slide 12: Reference
[1] 11-20/0370r0, “RU Allocation Subfield Design for Multi-RU Support”
[2] 11-20/0400r0, “Multi-RU Combination and Signaling”
[3] 11-20/652r0, “Signaling of RU allocation in 11be”
[4] 11-20/575r0. “Self Contained Signaling for E-SIG”