## Slide 1: Non-AP MLD Initiated Aggregation: Truncation of Back-off Count
Date: 2020-07-13
Authors:
Name | Affiliation | Address | Phone | Email
Insun Jang | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | insun.jang@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Taewon Song |  |  |  | taewon.song@lge.com
Namyeong Kim |  |  |  | namyeong.kim@lge.com

## Slide 2: Introduction
Many contributions [1]-[8] have addressed how to transmit UL PPDUs on multiple links simultaneously for non-STR non-AP MLD
In this contribution, we elaborate one of methods for non-STR non-AP MLD
  When gaining a channel access on a link, it performs UL aggregation including the other link(s)

## Slide 3: UL Aggregation of Non-STR Non-AP MLD
Basically, UL aggregation means aligning starting times and ending times of PPDUs that are sent simultaneously on multiple links
Several Scenarios
  No Aggregation: It may provide opportunities of power saving [9]
  When gaining a channel access (focus)
  After gaining a channel access, i.e., during TXOP (focus)

## Slide 4: Observations
When an STA obtains a channel access, what can happen on the other link(s)?
  BUSY (e.g., NAV): Cannot transmit any PPDUs
  AIFS Sensing: Can transmit a PPDU depending on CCA time
  Decrement backoff counter (BC) (like Link 1): Can transmit a PPDU by truncating BC
    This case would be Not BUSY and Not AIFS Sensing

## Slide 5: If AIFS Sensing is Being Performed
STA may be able to transmit a PPDU depending on
  What is sensing duration
  At Which point during AIFS
In baseline, STA can decrement BC
  Following AIFSN[AC] × aSlotTime – aRxTx of idle medium after SIFS after the last busy medium, which needs to be modified by considering the above factors
Even though we can transmit a PPDU in some cases, it would complicate EDCA rules for supporting non-STR
  We prefer not to transmit a PPDU when AIFS sensing

## Slide 6: Proposal: Aggregation
Motivated by Previous Observations
When an STA of a non-STR non-AP MLD gains a channel access and then transmits a PPDU, another STA of the MLD can transmit a PPDU simultaneously if its medium is IDLE and it is not performing AIFS sensing after BUSY
  Medium sensing duration is the interval of TBD (e.g., PIFS, aSlotTime) immediately preceding the start of the TXOP
  Starting and Ending times of the PPDUs are aligned with TBD margin

## Slide 7: Discussion on Fairness
When we truncate a current BC on a link, several factors impact on the fairness on legacy/single-link STAs
  Basically, ignoring the Remaining BC would be unfair
  See the table considering the first round and the second round of back-off
 | Existing EDCA |  | Truncation of BC | 
When TX | 1st | 2nd | 1st | 2nd
Remaining BC (RBC) | BC always shall be 0 per AC |  | BC can be more than 0 (called RBC_1) | BC can be also more than 0 (i.e., repetitive truncation)
Access Category (AC) |  |  | - | RBC_1 may be used for a different AC with higher priority
 |  |  | E.g., AC = BE | E.g., AC = VO
Failure | 2*CW |  | Due to truncation, More collisions may happen | 

## Slide 8: Additional Proposal: BC/AC Control
When a new BC is picked in the next round
  The BC is added by the previously remaining BC
  EDCA parameters of previously used AC are used only when an AC in the next round has higher priority than the previously used AC

## Slide 9: Proposal: Nonrecurrent Aggregation
Even though we add BCs, aggregation may be repetitive on a link
  It may make the method useless
Therefore, we propose nonrecurrent aggregation, i.e., in the next round, the newly picked BC shall become 0 to transmit any PPDU

## Slide 10: Failure case
In Failure case, the same rule can be applied while maintaining rules for contention window (CW)
  However, the collisions may happen due to the truncation of BC
  Therefore, if we want to impose more penalty, more increased parameters may be considered (e.g., 4*CW, 2*remaining BC)
Example

## Slide 11: Summary
We elaborated how to transmit UL PPDUs on multiple links simultaneously for non-STR non-AP MLD as one of several methods that have been proposed
Specifically, When an STA of a non-STR non-AP MLD gains a channel access and then transmits a PPDU, another STA of the MLD can transmit a PPDU simultaneously if its medium is IDLE and it is not performing AIFS sensing after BUSY
    Medium sensing duration is the interval of TBD (e.g., PIFS, aSlotTime) immediately preceding the start of the TXOP
    Starting and Ending times of the PPDUs are aligned with TBD margin
    For the next back-off procedure of the another STA,
      Remaining back-off counter (BC) is added to newly picked BC
      EDCA parameters of previously used AC are used only when the next AC has higher priority than the previously used AC
      The newly picked BC shall become 0 to transmit any PPDU
    NOTE: This operation is possible if regulation allows the operation

## Slide 12: SP #1
Do you agree that 11be shall define mechanism(s) for enabling a non-AP MLD with constraints to transmit PPDUs simultaneously on multiple links by aligning starting times and ending times of the PPDUs?
  NOTE: The differences between starting or ending times have the value of more than 0
Y/N/A

## Slide 13: SP #2
Do you agree that 11be shall define the following operation for non-STR
  When an STA of a non-STR non-AP MLD gains a channel access and then transmits a PPDU, another STA of the MLD may transmit a PPDU simultaneously if its medium is IDLE and it is not performing AIFS sensing after BUSY
    Medium sensing duration is the interval of TBD (e.g., PIFS, aSlotTime) immediately preceding the start of the TXOP
    Starting and Ending times of the PPDUs are aligned with TBD margin
    For the next back-off procedure of the another STA,
      Remaining back-off counter (BC) is added to newly picked BC
      EDCA parameters of previously used AC are used only when the next AC has higher priority than the previously used AC
      The newly picked BC shall become 0 to transmit any PPDU
    NOTE: This operation is possible if regulation allows the operation
Y/N/A

## Slide 14: Back-up: UL Aggregation (Non-STR) [2]
Basically, UL aggregation means aligning start/end of UL PPDUs that are sent simultaneously on multiple links
  The initiator of transmission is non-STR non-AP MLD
Non-AP Initiated Aggregation (e.g., Truncation of BC [1]-[5], [8])
AP-assisted Aggregation [2], [6], [7]
  Example: Request and Response for Aggregation [1]

## Slide 15: References
[1] 802.11-19/1144r6 Channel Access for Multi-link Operation
[2] 802.11-20/0414r4 Method for Handling Constrained MLD
[3] 802.11-20/0026r7 MLO: Sync PPDUs
[4] 802.11-20/0275r2 MLO: Need for sync PPDUs
[5] 802.11-20/0487r5 Multiple Link Operation Follow Up
[6] 802.11-20/0081r3 MLO-Synch-Transmission
[7] 802.11-20/0291r1 MLO a-synchronize and synchronize operation discussions
[8] 802.11-20/0577r0 RTS and CTS Procedure in Synchronous Multi-link Operation
[9] 802.11-20/0037r1 Power Saving Considering Non-AP without STR Capability