## Slide 1: Multi-link Element format
Date: 2020-05-11
Authors:
Name | Company | Address | Phone | Email
Rojan Chitrakar | Panasonic Corporation | 202 Bedok South Avenue 1, #02-11 Singapore 469332 |  | rojan.chitrakar@sg.panasonic.com
Lei Huang |  |  |  | 
Yanyi Ding |  |  |  | 
Yoshio Urabe |  |  |  | 

## Slide 2
Introduction
Many variants of Multi-link elements have been proposed in .11be. Defining multiple elements will cause the Element ID Extension space to run out faster. As of REVmd_D3.3, only 162 IDs are available.

## Slide 3
Multi-link elements - 1
Multi-link element for Discovery & Multi-link Setup [1]
Multiple Link Attribute (MLA) element for ML Discovery [6], [7]
 | Element ID | Length | Element ID Extension | Common Control | MLD Address | MLD SSID | Authentication Algorithm | … | Optional Sub-elements
Octets: | 1 | 1 | 1 | x | 0 or 6 | 0 or 32 | 0 or 2 | … | variable
Common/MLD Capabilities
Set of elements organized as a profile for every other STA of the MLD
Strcuture of Multiple Link Attribute element
MLD Addr Present
MLD SSID Present
Auth Algo Present

## Slide 4
Multi-link elements - 2
Multi-link IE for BSS Parameter update [5]
Element ID | Length | Element ID Extension | Link ID | Optional Subelements
1 octet | 1 octet | 1 octet | 1 octet | variable
<Multi-link IE>
Multi-link TIM element [2], [3], [4]
  Element to indicate more information about buffered BUs:
A set of LMB:
Size = 15 (5x3)
1
0
0
0
1
1
0
1
0
0
0
1
1
1
0
Link Indication:
TID bitmap:
Size = 40 (5x8) bits
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
TID Indication:
ML-TIM element
+
Link Recommendation element

## Slide 5
Multi-link elements: Others?
New elements may be needed for other Multi-link operations, e.g. TID-to-link mapping, per-link Medium State Information [9], MLD request element in Probe Request frame [8] etc.
It may be possible to design a unified format for some usage e.g. Multi-link Discovery and Multi-link Setup, but a common design that cater to all use cases may be more complicated and may lead to unnecessary overhead.

## Slide 6
Proposal: A common Multi-link element
A common Multi-link element to carry the information for various Multi-link operations, with a Type field to differentiate the various formats:
Type field Values | 
Value | Meaning
0 | Multi-link Discovery
1 | Multi-link Setup
2 | Multi-link BSS Parameter update
3 | TID-to-link Mapping
4 | Multi-link TIM
5 ~ 15 | Reserved
Type field Values | 
Value | Meaning
0 | Capabilities
1 | Operation Parameters
2 | BSS Parameter update
3 | TID-to-link Mapping
4 | Link/TID Indication/Recommendation
5 ~ 15 | Reserved
Option 1: Based on Usage:
Option 2: Based on content:

## Slide 7: Reference
[1] 20/28r1 - Indication of Multi-link Information (Insun Jang)
[2] 20/66r3 - Multi-Link TIM (Young Hoon Kwon)
[3] 20/84r1 - Multi-link TIM – follow up (Minyoung Park)
[4] 19/1955r2 - MLO: Efficient Paging (Abhishek Patil)
[5] 20/337r1 - Multi-link BSS Parameter Update (Yongho Seok)
[6] 20/356r3 - MLO: Discovery and beacon-bloating (Abhishek Patil)
[7] 20/357r0 - Container for advertising ML Information (Abhishek Patil)
[8] 20/389r3 - Multi-Link Discovery – part 1 (Laurent Cariou)
[9] 20/82r2- Synchronous Transmitter Medium State Information (Matthew Fischer)

## Slide 8
Straw Poll 1
Do you support that:
  A common element is defined to carry the information for various Multi-link operations, the element carrying a Type field to differentiate the various formats of the element.
  Y/N/A
  Note: This is not for SFD.

## Slide 9
Straw Poll 2
Which option do you prefer for the Type field:
  Option 1: Based on usage of the element
  Option 2: Based on contents of the element
  Opt1/Opt2/Others/Abstain
  Note: This is not for SFD.