## Slide 1: MU-MIMO Simplifications for EHT
Date: 2020-05-21
Authors:
Name | Affiliations | Address | Phone | Email
Sameer Vermani | Qualcomm |  |  | 
Alice Chen |  |  |  | 
Bin Tian |  |  |  | 
Youhan Kim |  |  |  | 
Ahmed ElSherif |  |  |  | 
Notes: September 2012

## Slide 2: Introduction
Almost full flexibility of MU-MIMO was allowed in 11ax
  Any RU above RU106 is allowed to have MU-MIMO
  Only subset of the allowed modes are useful in practice
For EHT
  Already passed SP that for MU-MIMO in EHT, RU242 is the minimum RU size
  We propose to have further simplifications to the case where MU-MIMO is done on part of the PPDU BW
    We call these transmissions as “Hybrid transmissions”
Benefits
  Reduce modes and testing burden
  Simplified RU allocation signaling
    May allow for compressed modes to include some of the canonical hybrid transmission modes

## Slide 3: Simplifications to Hybrid Transmissions
Minimum PPDU BW for hybrid transmissions: 80MHz
Propose the following as minimum RU sizes for MU-MIMO for different PPDU BWs
  80MHz PPDU: Min RU size for MU-MIMO is RU242
  160MHz PPDU: Min RU size for MU-MIMO is RU242
  >160MHz PPDU: Min RU size for MU-MIMO is RU484
Above implies that
  A maximum of 8 MU-MIMO RUs in PPDU BWs of 160MHz and 320MHz
  A maximum of 4 MU-MIMO RUs in a PPDU BW of 80MHz
    Would still allow for 32 MU-MIMO users to be served if we allow for 8 users per MU-MIMO RU

## Slide 4: Summary
Proposed simplifications to the allowed MU-MIMO modes for EHT
  Reduce the cases when MU-MIMO is allowed on part of the PPDU BW
    Reduces the testing burden and simplifies the RU allocation table

## Slide 5: Strawpoll 1
Do you agree that for EHT PPDUs where MU-MIMO is happening on part of the PPDU BW 80MHz is the minimum PPDU BW ?
  The limitation is also applicable to the case where the PPDU has multiple MU-MIMO RUs which collectively span the entire PPDU BW
  Y
  N
  A

## Slide 6: Strawpoll 2
Do you agree that for PPDU BWs of 80MHz and 160MHz, the min RU size for MU-MIMO is RU242?
  Y
  N
  A

## Slide 7: Strawpoll 3
Do you agree that for PPDU BW greater than 160MHz, the min RU size for MU-MIMO is RU484?
  Y
  N
  A