## Slide 1: Signaling of RU allocation follow-up
Date: 2020-06-09
Authors:
Name | Affiliation | Address | Phone | Email
Dongguk Lim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | dongguk.lim@lge.com
Eunsung Park |  |  |  | Ensung.park@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
June 2020

## Slide 2: Introduction
In the previous PHY ad-hoc conference call, the following Multiple RU combinations were agreed in OFDMA transmission.
  The 484 tones + 2x996 tones and 484 tones + 3x996 tones are supported in 240MHz and 320MHz, respectively.
For the indication of the newly added MRU aggregations in OFDMA transmission, we modified the RU allocation table.

## Slide 3: The required entries
The number of entry for new added MRU aggregation.
  Also, MU-MIMO is considered on the RUs.
  484 tone +2x 996 tone in 240MHz
    Since 6 cases are considered, so, totally 6x8 entries are required for indication.
  484 tone + 3x 996 tone in 320MHz
    8 cases are considered, and totally 8x8 entries are required.
In the 798r1, since reserved bits on the RU allocation field which consists of 8bits are about 80bits, it can not contain all entry for newly added above MRU aggregation.
So, to accommodate these indications, the RU allocation subfield is expanded to 9 bits.
  The same design way described in r1 is applied to the extended RU allocation subfield.

## Slide 4: RU allocation subfields (1/2)
MSB (1bit) | 8bit information | #1 | #2 | #3 | #4 | #5 | #6 | #7 | #8 | #9 | Number of entries
B8 | (B7 B6 B5 B4 B3 B2 B1 B0) |  |  |  |  |  |  |  |  |  | 
0 | 00000000 | 26 | 26 | 26 | 26 | 26 | 26 | 26 | 26 | 26 | 1
0 | 00000001 | 26 | 26 | 26 | 26 | 26 | 26 | 26 | 52 |  | 1
0 | 00000010 | 26 | 26 | 26 | 26 | 26 | 52 |  | 26 | 26 | 1
0 | 00000011 | 26 | 26 | 26 | 26 | 26 | 52 |  | 52 |  | 1
0 | 00000100 | 26 | 26 | 52 |  | 26 | 26 | 26 | 26 | 26 | 1
0 | 00000101 | 26 | 26 | 52 |  | 26 | 26 | 26 | 52 |  | 1
0 | 00000110 | 26 | 26 | 52 |  | 26 | 52 |  | 26 | 26 | 1
0 | 00000111 | 26 | 26 | 52 |  | 26 | 52 |  | 52 |  | 1
0 | 00001000 | 52 |  | 26 | 26 | 26 | 26 | 26 | 26 | 26 | 1
0 | 00001001 | 52 |  | 26 | 26 | 26 | 26 | 26 | 52 |  | 1
0 | 00001010 | 52 |  | 26 | 26 | 26 | 52 |  | 26 | 26 | 1
0 | 00001011 | 52 |  | 26 | 26 | 26 | 52 |  | 52 |  | 1
0 | 00001100 | 52 |  | 52 |  | 26 | 26 | 26 | 26 | 26 | 1
0 | 00001101 | 52 |  | 52 |  | 26 | 26 | 26 | 52 |  | 1
0 | 00001110 | 52 |  | 52 |  | 26 | 52 |  | 26 | 26 | 1
0 | 00001111 | 52 |  | 52 |  | 26 | 52 |  | 52 |  | 1
0 | 00010000 | 52 |  | 52 |  | - | 106 |  |  |  | 1
0 | 00010001 | 106 |  |  |  | - | 52 |  | 52 |  | 1
0 | 00010010 | 26 | 26 | 26 | 26 | 26 | 106 |  |  |  | 1
0 | 00010011 | 26 | 26 | 52 |  | 26 | 106 |  |  |  | 1
0 | 00010100 | 52 |  | 26 | 26 | 26 | 106 |  |  |  | 1
0 | 00010101 | 52 |  | 52 |  | 26 | 106 |  |  |  | 1
0 | 00010110 | 106 |  |  |  | 26 | 26 | 26 | 26 | 26 | 1
0 | 00010111 | 106 |  |  |  | 26 | 26 | 26 | 52 |  | 1
0 | 00011000 | 106 |  |  |  | 26 | 52 |  | 26 | 26 | 1
0 | 00011001 | 106 |  |  |  | 26 | 52 |  | 52 |  | 1
0 | 00011010 | 106 |  |  |  | - | 106 |  |  |  | 1
0 | 00011011 | 52 |  | 52 |  | - | 52 |  | 52 |  | 1
0 | 00011100 | 106 |  |  |  | 26 | 106 |  |  |  | 1
0 | 00011101 | 242-tone RU empty (with zero users) |  |  |  |  |  |  |  |  | 1
0 | 00011110 | 484-tone RU; contributes zero User fields to the User Specific field in the same HE-SIG-B content channel as this RU Allocation subfield |  |  |  |  |  |  |  |  | 1
0 | 00011111 | 996-tone RU; contributes zero User fields to the User Specific field in the same HE-SIG-B content channel as this RU Allocation subfield |  |  |  |  |  |  |  |  | 1
0 | 00100000 | 2x996-tone RU; contributes zero User fields to the User Specific field in the same HE-SIG-B content channel as this RU Allocation subfield |  |  |  |  |  |  |  |  | 1
0 | 00100001 | 3x996-tone RU*; contributes zero User fields to the User Specific field in the same HE-SIG-B content channel as this RU Allocation subfield |  |  |  |  |  |  |  |  | 1
0 | 0010001x0 | Reserved |  |  |  |  |  |  |  |  | 2
0 | 001001x1x0 | Reserved |  |  |  |  |  |  |  |  | 4
0 | 00101y2y1y0 | 242 |  |  |  |  |  |  |  |  | 8
0 | 00110y2y1y0 | 484 |  |  |  |  |  |  |  |  | 8
0 | 00111y2y1y0 | 996 |  |  |  |  |  |  |  |  | 8
0 | 01000y2y1y0 | 2x996 |  |  |  |  |  |  |  |  | 8
0 | 01001y2y1y0 | 3x996* |  |  |  |  |  |  |  |  | 8
0 | 0101y3y2y1y0 | Reserved |  |  |  |  |  |  |  |  | 16
0 | 011y4y3y2y1y0 | Reserved |  |  |  |  |  |  |  |  | 32
0 | 1y6y5y4y3y2y1y0 | Reserved |  |  |  |  |  |  |  |  | 128
*: 3x996 : it might not be required depending on the decision of channelization for 240MHz

## Slide 5: RU allocation subfields (2/2)
MSB (1bit) | 8bit information | #1 | #2 | #3 | #4 | #5 | #6 | #7 | #8 | #9 | Number of entries
B8 | (B7 B6 B5 B4 B3 B2 B1 B0) |  |  |  |  |  |  |  |  |  | 
1 | 00000000 | 26 | 26+52 |  |  | 26 | 26 | 26 | 26 | 26 | 1
1 | 00000001 | 26 | 26+52 |  |  | 26 | 26 | 26 | 52 |  | 1
1 | 00000010 | 26 | 26+52 |  |  | 26 | 52 |  | 26 | 26 | 1
1 | 00000011 | 26 | 26+52 |  |  | 26 | 52 |  | 52 |  | 1
1 | 00000100 | 26 | 26 | 26 | 26 | 26 | 52+26 |  |  | 26 | 1
1 | 00000101 | 26 | 26 | 52 |  | 26 | 52+26 |  |  | 26 | 1
1 | 00000110 | 52 |  | 26 | 26 | 26 | 52+26 |  |  | 26 | 1
1 | 00000111 | 52 |  | 52 |  | 26 | 52+26 |  |  | 26 | 1
1 | 00001000 | 26 | 26+52 |  |  | 26 | 52+26 |  |  | 26 | 1
1 | 00001001 | 26 | 26+52 |  |  | 26 | 106 |  |  |  | 1
1 | 00001010 | 106 |  |  |  | 26 | 52+26 |  |  | 26 | 1
1 | 00001011 | 26 | 26 | 26 | 26 | 26+106 |  |  |  |  | 1
1 | 00001100 | 26 | 26 | 52 |  | 26+106 |  |  |  |  | 1
1 | 00001101 | 52 |  | 26 | 26 | 26+106 |  |  |  |  | 1
1 | 00001110 | 52 |  | 52 |  | 26+106 |  |  |  |  | 1
1 | 00001111 | 106 |  |  |  | 106+26 |  |  |  |  | 1
1 | 00010000 | 106+26 |  |  |  |  | 26 | 26 | 26 | 26 | 1
1 | 00010001 | 106+26 |  |  |  |  | 26 | 26 | 52 |  | 1
1 | 00010010 | 106+26 |  |  |  |  | 52 |  | 26 | 26 | 1
1 | 00010011 | 106+26 |  |  |  |  | 52 |  | 52 |  | 1
1 | 00010100 | 106+26 |  |  |  |  | 106 |  |  |  | 1
1 | 00010101 | 106+26 |  |  |  |  | 52+26 |  |  | 26 | 1
1 | 00010110 | 26 | 26+52 |  |  | 26+106 |  |  |  |  | 1
1 | 00010111 | Reserved |  |  |  |  |  |  |  |  | 1
1 | 00011 y2y1y0 | 242+484 |  |  |  |  |  |  |  |  | 8
1 | 00100 y2y1y0 | 484(1)+996(2) |  |  |  |  |  |  |  |  | 8
1 | 00101 y2y1y0 | 484(2)+996(2) |  |  |  |  |  |  |  |  | 8
1 | 00110 y2y1y0 | 996(1)+484(4) |  |  |  |  |  |  |  |  | 8
1 | 00111 y2y1y0 | 996(1)+484(3) |  |  |  |  |  |  |  |  | 8
1 | 01000 y2y1y0 | 484(1)+996(2)+996(3) |  |  |  |  |  |  |  |  | 8
1 | 01001 y2y1y0 | 484(2)+996(2)+996(3) |  |  |  |  |  |  |  |  | 8
1 | 01010 y2y1y0 | 996(1)+484(3)+996(3) |  |  |  |  |  |  |  |  | 8
1 | 01011 y2y1y0 | 996(1)+484(4)+996(3) |  |  |  |  |  |  |  |  | 8
1 | 01100 y2y1y0 | 996(1)+996(2)+484(5) |  |  |  |  |  |  |  |  | 8
1 | 01101 y2y1y0 | 996(1)+996(2)+484(6) |  |  |  |  |  |  |  |  | 8
1 | 01110 y2y1y0 | 996(1)+996(2)+996(3) |  |  |  |  |  |  |  |  | 8
1 | 01111 y2y1y0 | 996(1)+996(2)+996(4) |  |  |  |  |  |  |  |  | 8
1 | 10000 y2y1y0 | 996(1)+996(3)+996(4) |  |  |  |  |  |  |  |  | 8
1 | 10001 y2y1y0 | 996(2)+996(3)+996(4) |  |  |  |  |  |  |  |  | 8
1 | 10010 y2y1y0 | 484(1)+996(2)+996(3)+996(4) |  |  |  |  |  |  |  |  | 8
1 | 10011 y2y1y0 | 484(2)+996(2)+996(3)+996(4) |  |  |  |  |  |  |  |  | 8
1 | 10100 y2y1y0 | 996(1)+484(3)+996(3)+996(4) |  |  |  |  |  |  |  |  | 8
1 | 10101 y2y1y0 | 996(1)+484(4)+996(3)+996(4) |  |  |  |  |  |  |  |  | 8
1 | 10110 y2y1y0 | 996(1)+996(2)+484(5)+996(4) |  |  |  |  |  |  |  |  | 8
1 | 10111 y2y1y0 | 996(1)+996(2)+484(6)+996(4) |  |  |  |  |  |  |  |  | 8
1 | 11000 y2y1y0 | 996(1)+996(2)+996(3)+484(7) |  |  |  |  |  |  |  |  | 8
1 | 11001 y2y1y0 | 996(1)+996(2)+996(3)+484(8) |  |  |  |  |  |  |  |  | 8
1 | 1101 y3y2y1y0 | Reserved |  |  |  |  |  |  |  |  | 16
1 | 1110 y3y2y1y0 | Reserved |  |  |  |  |  |  |  |  | 16
1 | 1111 y3y2y1y0 | Reserved |  |  |  |  |  |  |  |  | 16
Entries for newly added large MRU aggregation (including the MU-MIMO )

## Slide 6: SP#1
Do you agree that if a Common field is present in a 320 MHz or 160+160 MHz PPDU sent to multiple users, a 4×996 tone RU is not permitted.
  none are defined in RU allocation subfield for 4x996 tone RU.

## Slide 7: Straw poll #2
Do you agree that the RU allocation subfield includes entries to indicate the ‘Zero user field’ for RUs larger than 242 tone RU?
  The size of RU for the zero user field is TBD.

## Slide 8: Straw poll #3
Do you agree with applying the following to the 11be SFD?
  the RUs equal to or larger than 996-tone RU are referred to by two consecutive RU Allocation subfields per EHT-SIG content channel.
  For the RUs equal to or larger than 996-tone RU, first RU allocation subfield in each EHT-SIG content channel indicates the number of User fields signaled in the corresponding content channel, while the second RU Allocation subfield in the same EHT-SIG content channel indicates the zero additional User fields in the User Specific field.

## Slide 9: Straw poll #4
Do you agree that the RU allocation subfield of EHT-SIG field consists of 9bits?
  Detail for construction of RU allocation subfield is TBD.
  Y/N/A

## Slide 10: Appendix

## Slide 11: Backup slides – 789r1
Through the previous PHY ad-hoc CC, we have reached the following agreements.
  “Do you agree that the minimum RU size for EHT to support MU-MIMO shall be 242-tone RU?” [1]
    Results : 31Y/6N/13A
  “Do you agree that the max number of users that can be spatially multiplexed in EHT for DL transmissions is 8 per RU/MRU?”[2]
    Applicable to all transmission modes in 11be
    Results : 45Y/1N/6A .
In this contribution, we update the RU allocation subfield by considering the agreed above two Straw polls.

## Slide 12: Modification of entries (1/2)
Since we have agreed that the minimum size of RU to support the MU-MIMO in EHT is RU 242-tone, we just need the one entry in the RU allocation subfield for indication when the size of allocated RU is smaller than 242.
  For example, when the RU 106 and the RU 26+ RU 106 are used, since the number of user for those allocated RU is one, just one entry included in the RU allocation subfield is used per each case, respectively.
And, it is hard to reuse the same RU allocation subfield defined in 11ax for single RU allocation in EHT transmission because EHT does not support the MU-MIMO on RU 106.
  Based on the RU allocation subfield of 11ax, we can obtain the 148 bits more as the reserved bits if MU-MIMO is not applied on RU 106.

## Slide 13: Modification of entries (2/2)
Since the number of users for MU-MIMO is defined as 8 equal to the value for 11ax, if MU-MIMO is used in EHT transmission, the equal number of entries to that of 11ax are used in RU allocation subfield.
  Thus, to support the MU-MIMO in EHT transmission, we need the 8 entries in the RU allocation subfield.
Therefore, by taking into account all consideration as described above and the number of multiple RU aggregation[3], we can make the RU allocation subfield using 8 bits.
  Here, we also take into account the 3x996 case for both SRU and MRU.

## Slide 14: RU allocation subfield (1/4)
The RU allocation subfield consist of 8bits
As described in [4], the first 1 bit (i.e., MSB 1bit) is used to indicate whether the RU allocation is for M-RU aggregation or not.
The details for RU allocation for single RU/MRU aggregation are indicated by using the remaining 7 bits.
So, the RU allocation subfield can be composed as follow.
  RU allocation subfield = [X1 7bits] ( total 8 bits)
    Here, X1 is used to indicate whether RU allocation includes the allocation for MRU or not.

## Slide 15: RU allocation subfield (2/4)
Single RU allocation in RU allocation subfield
MSB 1bit | 7bit information | #1 | #2 | #3 | #4 | #5 | #6 | #7 | #8 | #9 | Number of entries
B7 | ( B6 B5 B4 B3 B2 B1 B0) |  |  |  |  |  |  |  |  |  | 
0 | 0000000 | 26 | 26 | 26 | 26 | 26 | 26 | 26 | 26 | 26 | 1
0 | 0000001 | 26 | 26 | 26 | 26 | 26 | 26 | 26 | 52 |  | 1
0 | 0000010 | 26 | 26 | 26 | 26 | 26 | 52 |  | 26 | 26 | 1
0 | 0000011 | 26 | 26 | 26 | 26 | 26 | 52 |  | 52 |  | 1
0 | 0000100 | 26 | 26 | 52 |  | 26 | 26 | 26 | 26 | 26 | 1
0 | 0000101 | 26 | 26 | 52 |  | 26 | 26 | 26 | 52 |  | 1
0 | 0000110 | 26 | 26 | 52 |  | 26 | 52 |  | 26 | 26 | 1
0 | 0000111 | 26 | 26 | 52 |  | 26 | 52 |  | 52 |  | 1
0 | 0001000 | 52 |  | 26 | 26 | 26 | 26 | 26 | 26 | 26 | 1
0 | 0001001 | 52 |  | 26 | 26 | 26 | 26 | 26 | 52 |  | 1
0 | 0001010 | 52 |  | 26 | 26 | 26 | 52 |  | 26 | 26 | 1
0 | 0001011 | 52 |  | 26 | 26 | 26 | 52 |  | 52 |  | 1
0 | 0001100 | 52 |  | 52 |  | 26 | 26 | 26 | 26 | 26 | 1
0 | 0001101 | 52 |  | 52 |  | 26 | 26 | 26 | 52 |  | 1
0 | 0001110 | 52 |  | 52 |  | 26 | 52 |  | 26 | 26 | 1
0 | 0001111 | 52 |  | 52 |  | 26 | 52 |  | 52 |  | 1
0 | 0010000 | 52 |  | 52 |  | - | 106 |  |  |  | 1
0 | 0010001 | 106 |  |  |  | - | 52 |  | 52 |  | 1
0 | 0010010 | 26 | 26 | 26 | 26 | 26 | 106 |  |  |  | 1
0 | 0010011 | 26 | 26 | 52 |  | 26 | 106 |  |  |  | 1
0 | 0010100 | 52 |  | 26 | 26 | 26 | 106 |  |  |  | 1
0 | 0010101 | 52 |  | 52 |  | 26 | 106 |  |  |  | 1
0 | 0010110 | 106 |  |  |  | 26 | 26 | 26 | 26 | 26 | 1
0 | 0010111 | 106 |  |  |  | 26 | 26 | 26 | 52 |  | 1
0 | 0011000 | 106 |  |  |  | 26 | 52 |  | 26 | 26 | 1
0 | 0011001 | 106 |  |  |  | 26 | 52 |  | 52 |  | 1
0 | 0011010 | 106 |  |  |  | - | 106 |  |  |  | 1
0 | 0011011 | 52 |  | 52 |  | - | 52 |  | 52 |  | 1
0 | 0011100 | 106 |  |  |  | 26 | 106 |  |  |  | 1
0 | 0011101 | 242-tone RU empty (with zero users) |  |  |  |  |  |  |  |  | 1
0 | 0011110 | 484-tone RU; contributes zero User fields to the User Specific field in the same HE-SIG-B content channel as this RU Allocation subfield |  |  |  |  |  |  |  |  | 1
0 | 0011111 | 996-tone RU; contributes zero User fields to the User Specific field in the same HE-SIG-B content channel as this RU Allocation subfield |  |  |  |  |  |  |  |  | 1
0 | 0100000 | 2x996-tone RU; contributes zero User fields to the User Specific field in the same HE-SIG-B content channel as this RU Allocation subfield |  |  |  |  |  |  |  |  | 1
0 | 0100001 | 3x996-tone RU*; contributes zero User fields to the User Specific field in the same HE-SIG-B content channel as this RU Allocation subfield |  |  |  |  |  |  |  |  | 1
0 | 010001x1 | reserved |  |  |  |  |  |  |  |  | 2
0 | 01001x1x2 | reserved |  |  |  |  |  |  |  |  | 4
0 | 0101y1y2y3 | 242 |  |  |  |  |  |  |  |  | 8
0 | 0110y1y2y3 | 484 |  |  |  |  |  |  |  |  | 8
0 | 0111y1y2y3 | 996 |  |  |  |  |  |  |  |  | 8
0 | 1000y1y2y3 | 2x996 |  |  |  |  |  |  |  |  | 8
0 | 1001y1y2y3 | 3x996* |  |  |  |  |  |  |  |  | 8
0 | 101x1x2x3x4 | reserved |  |  |  |  |  |  |  |  | 16
0 | 11x1x2x3x4x5 | reserved |  |  |  |  |  |  |  |  | 32
New entry for load balancing of MU-MIMO
*: 3x996 : it might not be required depending on the decision of channelization for 240MHz

## Slide 16: RU allocation subfield (3/4)
Multiple RU allocation in RU allocation subfield
MSB 1bit | 7bit information | #1 | #2 | #3 | #4 | #5 | #6 | #7 | #8 | #9 | Number of entries
B7 | ( B6 B5 B4 B3 B2 B1 B0) |  |  |  |  |  |  |  |  |  | 
1 | 0000000 | 26 | 26+52 |  |  | 26 | 26 | 26 | 26 | 26 | 1
1 | 0000001 | 26 | 26+52 |  |  | 26 | 26 | 26 | 52 |  | 1
1 | 0000010 | 26 | 26+52 |  |  | 26 | 52 |  | 26 | 26 | 1
1 | 0000011 | 26 | 26+52 |  |  | 26 | 52 |  | 52 |  | 1
1 | 0000100 | 26 | 26 | 26 | 26 | 26 | 52+26 |  |  | 26 | 1
1 | 0000101 | 26 | 26 | 52 |  | 26 | 52+26 |  |  | 26 | 1
1 | 0000110 | 52 |  | 26 | 26 | 26 | 52+26 |  |  | 26 | 1
1 | 0000111 | 52 |  | 52 |  | 26 | 52+26 |  |  | 26 | 1
1 | 0001000 | 26 | 26+52 |  |  | 26 | 52+26 |  |  | 26 | 1
1 | 0001001 | 26 | 26+52 |  |  | 26 | 106 |  |  |  | 1
1 | 0001010 | 106 |  |  |  | 26 | 52+26 |  |  | 26 | 1
1 | 0001011 | 26 | 26 | 26 | 26 | 26+106 |  |  |  |  | 1
1 | 0001100 | 26 | 26 | 52 |  | 26+106 |  |  |  |  | 1
1 | 0001101 | 52 |  | 26 | 26 | 26+106 |  |  |  |  | 1
1 | 0001110 | 52 |  | 52 |  | 26+106 |  |  |  |  | 1
1 | 0001111 | 106+26 |  |  |  |  | 106 |  |  |  | 1
1 | 0010000 | 106 |  |  |  | 106+26 |  |  |  |  | 1
1 | 0010001 | 106+26 |  |  |  |  | 26 | 26 | 26 | 26 | 1
1 | 0010010 | 106+26 |  |  |  |  | 26 | 26 | 52 |  | 1
1 | 0010011 | 106+26 |  |  |  |  | 52 |  | 26 | 26 | 1
1 | 0010100 | 106+26 |  |  |  |  | 52 |  | 52 |  | 1
1 | 0010101 | 106+26 |  |  |  |  | 52+26 |  |  | 26 | 1
1 | 0010110 | 26 | 26+52 |  |  | 26+106 |  |  |  |  | 1
1 | 0010111 | Reserved |  |  |  |  |  |  |  |  | 1
1 | 0011y1y2y3 | 242(1)+484(2), second 242 is not allocated in 80MHz |  |  |  |  |  |  |  |  | 8
1 | 0100y1y2y3 | 242(2)+484(2) , first 242 is not allocated in 80MHz |  |  |  |  |  |  |  |  | 8
1 | 0101y1y2y3 | 484(1)+242(4), third 242 is not allocated in 80MHz |  |  |  |  |  |  |  |  | 8
1 | 0110y1y2y3 | 484(1)+242(3), forth 242 is not allocated in 80MHz |  |  |  |  |  |  |  |  | 8
1 | 0111y1y2y3 | 484(1)+996(2), second 484 is not allocated in 160MHz |  |  |  |  |  |  |  |  | 8
1 | 1000y1y2y3 | 484(2)+996(2) , first 484 is not allocated in 160MHz |  |  |  |  |  |  |  |  | 8
1 | 1001y1y2y3 | 996(1)+484(4), third 484 is not allocated in 160MHz |  |  |  |  |  |  |  |  | 8
1 | 1010y1y2y3 | 996(1)+484(3), forth 484 is not allocated in 160MHz |  |  |  |  |  |  |  |  | 8
1 | 1011y1y2y3 | 996(1)+996(3)+996(4), second 996 is not allocated in 320MHz |  |  |  |  |  |  |  |  | 8
1 | 1100y1y2y3 | 996(1)+996(2)+996(4), third 996 is not allocated in 320MHz |  |  |  |  |  |  |  |  | 8
1 | 1101y1y2y3 | Reserved |  |  |  |  |  |  |  |  | 8
1 | 1110y1y2y3 | Reserved |  |  |  |  |  |  |  |  | 8
1 | 1111y1y2y3 | Reserved |  |  |  |  |  |  |  |  | 8
Entries for large MRU and MU-MIMO
Entries for small MRU

## Slide 17: RU allocation subfield (4/4)
As defined in 11be SFD, the decision that some RU aggregation is whether supported or not in OFDMA transmission has not been yet determined.
  For the OFDMA transmission in 320/160+160 MHz, 3×996+484 RU combinations is TBD.
  For the OFDMA transmission in contiguous 240 MHz, 2×996+484 RU combinations is TBD
And, we may either the other RU aggregation cases that have been supported in non-OFDMA transmission or new RU combination for OFDMA transmission.
Therefore, to support the above RU aggregation cases efficiently by using the RU allocation subfield, the RU allocation subfield can be composed of 9 bits.

## Slide 18: Summary
In this contribution, the RU allocation subfield was constructed by reflecting the following agreed straw polls.
  The minimum size of RU to support the MU-MIMO is RU 242-tone.
  The max number of users for MU-MIMO per RU/MRU is 8.
The RU allocation subfield can consist of 8 or 9bits.
  The MSB 1bit of RU allocation subfield is used to indicate whether MRU allocation is included or not.
  If we consider the more cases for RU aggregation, to support the whole cases efficiently, the RU allocation subfield can be composed of the 9 bits.

## Slide 19: Straw poll #1
Do you agreed that the RU allocation subfield includes all cases of large size of RU aggregation for OFDMA transmission defined in 11be SFD?
  For 80MHz
    484 + 242 – 4 cases
  For 160MHz
    484 + 996 – 4 cases
  For 320MHz
    3x996 – 4 cases
  Other cases are TBD.
  Y/N/A

## Slide 20: Reference
[1] 11-20/0609r3, Further discussion on RU allocation subfield in EHT-SIG (Ross Jian Yu, Huawei)
[2] 11-20/0767r0 , Number of Users in MU-MIMO ( Ron Porat, Broadcom)
[3] 11-20/403r0 , Signaling of Multiple RU aggregation in OFDMA ( Dongguk Lim, LGE)
[4] 11-20/652r0, Signaling of RU allocation in 11be (Dongguk Lim, LGE)

## Slide 21: Combination of small-size RUs (1/2)
Based on the passed motions in [1], we can consider the following allocation for combinations of small-size RUs.
  We assume the followings
    Bandwidth : 20MHz
    Number of allocated combination in BW : up to 2
    An Allocation subfield is configure per 20MHz.
    Multiple User transmission (i.e., OFDMA), but, MU-MIMO is not considered.
  Allocation for RU26+RU52,
Index | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
1 | 26 | 26 | 52 |  | 26 | 26 | 26 | 26 | 26
2 | 26 | 26 | 52 |  | 26 | 26 | 26 | 52 | 
3 | 26 | 26 | 52 |  | 26 | 52 |  | 26 | 26
4 | 26 | 26 | 52 |  | 26 | 52 |  | 52 | 
5 | 26 | 26 | 52 |  | 26 | 106 |  |  | 
6 | 26 | 26 | 26 | 26 | 26 | 52 |  | 26 | 26
7 | 26 | 26 | 52 |  | 26 | 52 |  | 26 | 26
8 | 52 |  | 26 | 26 | 26 | 52 |  | 26 | 26
9 | 52 |  | 52 |  | 26 | 52 |  | 26 | 26
10 | 106 |  |  |  | 26 | 52 |  | 26 | 26
11 | 26 | 26 | 52 |  | 26 | 52 |  | 26 | 26

## Slide 22: Combination of small-size RUs (2/2)
  Allocation for RU26+RU106
  We can also consider the allocation of two combinations configured with different small-size RUs.
    For example, RU26+RU52 and RU26+RU106 can be considered.
index | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
1 | 26 | 26 | 26 | 26 | 26 | 106 |  |  | 
2 | 26 | 26 | 52 |  | 26 | 106 |  |  | 
3 | 52 |  | 26 | 26 | 26 | 106 |  |  | 
4 | 52 |  | 52 |  | 26 | 106 |  |  | 
5 | 106 |  |  |  | 26 | 106 |  |  | 
6 | 106 |  |  |  | 26 | 26 | 26 | 26 | 26
7 | 106 |  |  |  | 26 | 26 | 26 | 52 | 
8 | 106 |  |  |  | 26 | 52 |  | 26 | 26
9 | 106 |  |  |  | 26 | 52 |  | 52 | 
10 | 106 |  |  |  | 26 | 106 |  |  | 
index | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
1 | 106 |  |  |  | 26 | 52 |  | 26 | 26
2 | 26 | 26 | 52 |  | 26 | 106 |  |  | 

## Slide 23: Combination of Large-size RUs
We can also consider the following allocation for Combination of Large-size RUs based on 11be SFD[1].
  We assume that the multiple user transmission(i.e. OFDMA) but MU-MIMO is not considered.
  In 80MHz
  In 160MHz
  For the 240MHz and 320MHz, the above combinations for 160MHz can be used in the continuous 160MHz within this bandwidth.
    Exception: 3×996 is supported.
index | 1 | 2 | 3 | 4
1 | 242 | 242 | 484 | 
2 | 242 | 242 | 484 | 
3 | 484 |  | 242 | 242
4 | 484 |  | 242 | 242
index | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
1 | 484 |  | 484 |  | 996 |  |  | 
2 | 484 |  | 484 |  | 996 |  |  | 
3 | 996 |  |  |  | 484 |  | 484 | 
4 | 996 |  |  |  | 484 |  | 484 |