## Slide 1: Dynamic Link Sets for MLDs
Date: 2020-05-15
Authors:
Name | Affiliations | Address | Phone | Email
Pooya Monajemi | Cisco |  |  | pmonajem@cisco.com
Brian Hart |  |  |  | brianh@cisco.com
Malcolm Smith |  |  |  | mmsmith@cisco.com
Khashayar Mirfakhraei |  |  |  | kmirfakh@cisco.com
Eldad Perahia | HPE |  |  | eldad.perahia@hpe.com
Gaurav Patwardhan |  |  |  | gaurav.patwardhan@hpe.com
Notes: September 2012

## Slide 2: Motivation
11be Introduces the concept of Multi-Link Devices
Enablement/disablement
  A link is defined enabled if there is at least one TIDs mapped to that link
  By default all TIDs are mapped to all links
Static Set of Links
  AP is expected to advertise about all links using MLA IEs in Beacons/Probe Responses/etc
  At association/setup, the AP MLD can grant a set of links to a non-AP STA MLD by sending a list of MLA IEs in the Association Response frame
  Once the setup is complete, no further modifications are currently envisioned to the set of links
Shortcomings
  In this contribution we discuss a few cases where a static set of links will face limitations
  Capability to dynamically add or remove links from an MLD setup is needed

## Slide 3: Case 1 : Dynamic Radio Role Changes
AP Radio Role Switching
  Many multi-radio APs can dynamically switch a radio’s mode of operation
  Radios may be dynamically turned on/off in order to manage interference levels/coverage
  Commonly used in 2.4GHz :
    In a deployment where AP placement is based on 5GHz coverage, the 2.4 GHz band is “over deployed”. Hence excess 2.4GHz APs may be turned off or switched in role
    The operation is dynamic, based on various factors
Various outcomes of the role switch:
  Operating band of a radio may be switched
    Radio starts to operate in a new band
    Radio reset will erase state information
    Might use different BSSIDs
  Radio may be turned into a “monitor-only” role for measurement purposes
    Requirement : Permanent removal of the link
  Or turned back into client-serving mode in 2.4GHz when needed
    Requirement : Addition of a new link

## Slide 4: Case 2 : Reachability Disparities
Link qualities between two MLDs may vary
  If the STA and AP can communicate in one link, there is no guarantee that they will also be able to communicate in the other links
  Pathloss differences
    Path loss in 2.4 GHz generally smaller than in 5/6 GHz bands
  Transmit power differences
    Limited by regulation, hardware, or configuration
    Not necessarily reciprocal
  Antenna directionality differences
    Different antenna sets may be assigned to each link
    Impossible to predict/estimate
Directional disparity
  We may have poor connection in either direction (UL/DL), as a result of TX power differences.
  Current solution proposed by TGbe addresses only the DL direction (STA-initiated power save)
Timing
  The problem might occur at association time, or post-association in a mobility scenario

## Slide 5: Status Quo
What we have today :
TID to Link Mapping
  TID to link mapping is a short-term solution
  No way to add a new link
  No way to permanently remove a link
  “Negotiated”, i.e. the receiver may reject
Power Save
  STA-initiated. Does not solve any problems at AP side.
  Short-term solution
  No way to add a new link
  No way to permanently remove a link
Reassociation
  Default method according to [2]
  Very disruptive: Buffered frames/BA sessions/… cleared

## Slide 6: Requirements
What is needed :
Notification that a new link is available
Notification that an existing link is about to be shutdown permanently
Remapping of TIDs after updates to existing set of links (?)
Minimal impact on connectivity :
  Maintain BA sessions
  TWT setups on current links
  …

## Slide 7: Conclusions
We described the need for maintaining a dynamic set of links in MLD setups
  Links may need to be added or removed
  We should not require a new MLD setup in order to change the link set

## Slide 8: SP1
Do you agree to define mechanisms to add links to, and remove links from, an MLD setup without disruption in traffic, initiated by any one of AP or non-AP STA?
Note: This SP is not meant for spec text.

## Slide 9: SP2
Do you agree that
  11be shall define mechanisms to add links to, and remove links from, an MLD setup without requiring a reassociation, initiated by any one of AP or non-AP STA.

## Slide 10: SP3
Do you agree that
  An AP MLD may announce the addition of a new link by adding a new MLA element in its Beacons/Probe Responses.
  A non-AP MLD may request the addition of a new link to an existing MLD setup
    Details of the request and response are TBD
  Any MLD entity may notify its counterpart that a link will be removed from the MLD setup.
    Note: Notification details are TBD.
    Note: Ultimately link’s information element from Beacon/Probe Reponses will be omitted

## Slide 11: References
[1] 11be SFD
[2] 11-20/0386r4 Multi-link Association Follow Up