## Slide 1: Triggered P2P transmissions follow up
Date: 2020-08-31
Authors:

## Slide 2
Authors:

## Slide 3: Abstract
Propose a simple/low-complexity Triggered P2P scheme to be used for 11be R1.

## Slide 4: Introduction
Direct Link transmission => A Direct Link Scheduled (“DLS”) STA communicates directly with another Direct Link Peer STA (“DLP”).
Benefits of Direct Link (“DiL”) transmission [1] :
  high throughput because lower number of transmissions
  low latency due to one hop communication.
Use-case of interest:
  Miracast streaming from laptop to monitor.
  VR applications
  Wireless file transfer from phone to printer.
Slide 4
AP
DiL-A
DLS STA
DLP STA
SIFS
Data
SIFS
Ack
TXOP

## Slide 5: Trigger based DiL sequence benefits
A DiL transmission sequence initiated by a TF transmission has following benefits for both the peer STA and AP .
  Increases the chances of P2P transmission as AP typically has higher chance of winning contention.
  Better medium management at AP as it can balance QoS requirements (e.g., low peak latency) within BSS by scheduling P2P STA and regular STA in same TXOP.
Submission 1117r1 (appendix) mentions some inefficiency of QTP to support Direct link:
  Legacy STA not prevented from channel access.
  AP is not aware of actual resource requests at STA during the QTP period. The initial configuration of schedules may be stale => medium inefficiency.

## Slide 6: Possible Topologies
ESS
Both STAs associated
to same AP.
Only one STA associated
to the Triggering AP.
: Non-AP STA
: AP
Case 1
Case 2
DLS
STA (laptop)
DLP
STA
(wireless monitor)
AP in the ceiling
of an office
DLS
STA (laptop)
DLP
STA
(wireless monitor)
AP in the ceiling
of an office
[Optional]
Another AP in the ESS
Notes: Case 3 is same as general Multi-AP.

## Slide 7: Principle
AP
STA1
STA2
SIFS
TXOP owned by the AP
TF for P2P
ACK 21
Allocated time
P2P PPDU
SU PPDU
(N x 20MHz)
SIFS
P2P traffic is triggered by the AP for a “Single-User style” PPDU :
  AP can share a part of the TXOP to the P2P traffic.
  P2P traffic uses a “P2P RU” = n x 20MHZ covering all the operating band for that period of time.
  The TF format can be similar to 11ax/11be Basic TF format except small changes to clarify the allocation is for P2P traffic.
  Peer STA may not be allowed to use EDCA after being triggered for some time (e.g., by extending MU-EDCA rules)

## Slide 8: Example in cascading sequence
AP
STA1
STA2
STA3
STA4
HE MU PPDU /TRS or TF
HE TB PPDU
HE TB PPDU
SIFS
SIFS
SIFS
SIFS
TXOP
MU cascading sequence
UL Length
TF for P2P
ACK 21
Allocated time
P2P PPDU
SU PPDU
(N x 20MHz)
Multi STA Block Ack
SIFS

## Slide 9: Summary
Discussed challenges with Triggered P2P operation.
Proposed a simple solution for R1

## Slide 10
Straw Poll #1
Do you support that 11be defines in R1, a procedure for an AP to share a part of the obtained TXOP for peer-to-peer (non-AP STA to non-AP STA) frame exchanges by signaling in a trigger frame, a TBD field specifying the allocated time for the peer to peer communication, and only one RU allocated to one non-AP STA associated to that AP.
Note :
  Format of trigger frame is TBD.
  Informing the AP of P2P traffic required resource, may be based on any existing mechanism (e.g. BSR on per packet level, TSPEC at stream level, or any TBD channel access/TWT/scheduling mechanism.)
  Peer STA may not be allowed to use EDCA for some time for P2P transmissions after being triggered (e.g., by extending MU-EDCA rules).
Results: Y/N/A

## Slide 11: Reference
[1]. 11-18-1481-01: Technology for EHT
[2] 11-20-0871-00-be-simplified-p2p-release1
[3]. 11-19-1117-00: Coordinated OFDMA Operation
[4]. 11-20-0095-02: Triggered P2P transmissions
[5]- 11-18-2009-06-0rta-rta-report-draft

## Slide 12: Backup slides

## Slide 13: FAQ
C: Is this a new P2P protocol like TDLS, WFA protocols etc. ?
R: No. The proposed mechanism only deals with AP granting explicit channel access to a peer STA using a Ctrl frame and hence is orthogonal to the P2P protocol (P2P discovery, session/schedule setup, security establishment etc.). The proposed scheme therefore complements existing P2P schemes.
C: How many and what type of frames can peer STA transmit during allocation ?
R: Any frame the peer STA is allowed to transmit to the other peer.
C: Why not use RDG ?
R: Using RDG to assist P2P requires implementations to build RDG support followed by any P2P extensions. This is more effort implementation-wise and equivalent effort spec-wise.
C: Is the peer STA assumed to be soft-AP ?
R: It can be soft-AP or just a non-AP STA. We intend to not bring up any soft-AP definition but rather just use the term currently used in spec for QTP : “peer-to-peer link”.
C: What is the performance gain ?
R: It is scenario dependent in the same way as TF versus EDCA for UL transmissions. If the network is not busy, the gains may not be high. If the network is busy, this is useful esp. for QoS Mgt as it can reduce contention among non-AP STAs.

## Slide 14: FAQ (contd.)
C: What else would you require ?
R: All that we need is captured in the notes:
  Capability signaling during association.
  Signaling presence of P2P traffic (using a new TID value between 8-15 in QoS Null frame) or using existing schemes such as TSPEC or similar.
  MU-EDCA type mechanism following triggered P2P to restrict EDCA by non-AP STA.
C: How do you know the peer STA is going to use the allocation ?
R: Peer STA can signal presence of P2P traffic (see Notes). AP can recover TXOP using baseline mechanism if peer STA does not transmit.
C: Are we defining new terms for peer STA pairs ?
R: No. The terms “DLP” and “DLS” used in this presentation are just for illustration purposes. In the spec, we can use any traditional terms for them (e.g., “STA that supports Triggered P2P”).
C: Why not restrict to TDLS use-cases ?
R: We don’t see any technical/spec reason to restrict the scope to TDLS. Note that the protocol only depends on one peer STA being associated to AP. Since the other STA need not be known at AP, there is no need to restrict.

## Slide 15: Triggered P2P Transmissions follow up
No Change in the direct link setup/teardown procedure.
Triggered P2P feature should be controlled by a capability (both at AP or STA level).
A non-AP STA can signal the need for P2P transmission thanks to Tspec or BSR (exact signaling is TBD).
P2P traffic is triggered by the AP for a “Single-User style” PPDU :
  AP can share a part of the TXOP to the P2P traffic
    The AP provides resource to the source P2P station that is associated with it.
    TF May be included in a cascading mechanism.
  P2P traffic uses a “P2P RU” = n x 20MHZ covering all the operating band for that period of time.
  Simple signaling (typically 1 bit) to signal “P2P RU”.
  P2P traffic uses its own preamble on its distinct channel :
    AP does not need to provide all trigger transmission parameters (e.g. MCS)
    No synchronization requirement (even for Ack part)
  PPDU format is TBD (e.g. SU or MU PPDU format can be envisaged)

## Slide 16: 1117r1: Direct Link issues with 11ax amendments
Direct link provides high “interferences” to the AP
  Direct link traffic carries large amount of data
    Large video transmission for VR, or video streaming.
  Direct link traffic often requires low latency thus frequently accesses the medium.
    Interactive applications (VR, visio conferences, etc.)
Direct link cannot be efficiently scheduled by an AP today
  AP cannot trigger the sending of direct link data, so fine scheduling is not possible.
    Direct link only relies on EDCA.
    Multi User OFDMA doesn’t support Direct link traffic.
  Quiet time period mechanism is not incentive enough
    Every station with direct link traffic will contend on the same period. Even if this period has been negotiated by a STA, the quiet time period is open for all direct link stations
    Other stations with uplink data may also contend during this period (Quiet time period is just intended to give a better priority of medium access for direct link traffic).
    No specific protection against legacy stations.

## Slide 17: Motivation
P2P communication can significantly reduce the load on the BSS and simultaneously the latency by a one-hop communication.
About 70% reduction in
latency/airtime possible in
the two floor home scenario
by using P2P communication among users in the same room.

## Slide 18: Example in cascading sequence 2/2
AP
STA1
STA2
STA3
STA4
HE MU PPDU / TRS or TF
ACK 21
HE MU PPDU /TRS or TF
HE TB PPDU
HE TB PPDU
Multi STA Block Ack
SIFS
SIFS
SIFS
SIFS
SIFS
TXOP
MU cascading sequence
Allocated Time
P2P PPDU
UL Length
SU PPDU
(N x 20MHz)