## Slide 1: MLO: Link Info in Mgmt. Frames
Name | Affiliation | Address | Phone | Email
Abhishek Patil | Qualcomm Inc. |  |  | appatil@qti.qualcomm.com
Duncan Ho | Qualcomm Inc. |  |  | 
George Cherian | Qualcomm Inc. |  |  | 
Alfred Asterjadhi | Qualcomm Inc. |  |  | 
Yanjun Sun | Qualcomm Inc. |  |  | 
Date: 2020-04-20

## Slide 2: Motivation
A non-AP MLD may monitor a single link [1, 2]
  It may do so to conserve power, or it may be a single radio device
How would an MLD provide link-specific information for link(s) where the non-AP MLD is not active?
MLO framework needs to provide a mechanism to address such cases.

## Slide 3: Solution
Carry link ID in an individually addressed Mgmt. frame
  The link ID indicates the link for which the contents of the mgmt. frame apply to.
Examples of link-specific info: timer resets, schedule updates, operational parameter changes
  A STA of an MLD may want to change parameter(s) or schedule for an individual TWT
  An AP of an AP MLD may want to reset the MU EDCA parameter for certain AC(s)
  A STA of a non-AP MLD may want to change its operating BW

## Slide 4: Example of TWT schedule update for a dozing link

## Slide 5: Some thoughts on signaling of Link ID
Requirements for carrying link identifier info:
  Should not require any changes to existing mgmt. frame format
  Fixed location to simplify parsing at the receiving side
Possible options for signaling link info:
  A-Control field
  Address 3 field of an individually addressed mgmt. frame

## Slide 6: Summary
This contribution motivates the need to identify the link for which the contents of an individually addressed mgmt. frame apply to
  The scheme is useful when providing link-specific information (such as schedule changes, resetting timers or updates to operational parameters) for a STA of an MLD that is in doze state

## Slide 7: SP #1
Do you support that 11be spec shall provide a mechanism to identify the link for which the contents of an individually addressed mgmt. frame apply to?
  NOTE – mechanism to identify the link is TBD
  Y:
  N:
  A:

## Slide 8: References
[1]: 11-19-1526 Multi-link Power-save (Abhishek Patil, Qualcomm)
[2]: 11-19-1542 Multi-link Broadcast Addressed Frame Reception (Po-Kai Huang, Intel)

## Slide 9: Resetting MU EDCA for a dozing link
MU-EDCA Reset sent on link2 identifies link1 as the intended link for which the reset applies