## Slide 1: EHT SIG Structure for Multi-user Support
Date: 2020-05-29
Authors:

## Slide 2: Multi-RU and MU-MIMO in EHT
Multi-RU [1]
  11be task group has approved that 11be shall allow more than one RUs to be assigned to a single STA.
  Many motions on multi-RU combination have been passed, including small RU combination and large RU combination.
Furthermore, during the TGbe PHY conference calls, the following SPs on MU-MIMO were passed.
  The minimum RU size for EHT to support MU-MIMO shall be 242-tone RU. [20/0609r3, Y/N/A: 31/6/13]
  The max number of users that can be spatially multiplexed in EHT for DL transmissions is 8 per RU/MRU. [20/0767r0, Y/N/A: 45/1/6]
There are concerns on overhead of RU Allocation subfield, especially for large bandwidth PPDU

## Slide 3: Discussion on EHT SIG Structure
The current SFD [1] defines EHT SIG as follows:
  The EHT-SIG (immediately after the U-SIG) in an EHT PPDU sent to multiple users shall have a common field and user-specific field(s).
    Special case compressed modes (e.g., full BW MU-MIMO) are TBD.
  An RU Allocation subfield is present in the Common field of the EHT-SIG field of an EHT PPDU sent to multiple users.
    Compressed modes are TBD.
    Contents of the RU Allocation subfield are TBD.
  For the PPDU transmitted to MU, the User field having TBD bits is contained in the user-specific field of EHT-SIG
    The User field indicates user information assigned to each RU similar to that used in HE MU PPDU.
    Detailed descriptions are TBD.

## Slide 4: Discussion on EHT SIG Structure (cont’d)
Furthermore, during the TGbe PHY conference calls, the following were passed.
  RU allocation subfield in the EHT-SIG field of an EHT-PPDU sent to multiple users includes the RU allocation for Multiple RUs as well as Single RU. [20/0652r0, Y/N/A: 38/0/10]
  An RU Allocation subfield that is present in the Common field of the EHT-SIG field of an EHT PPDU sent to multiple users (except EHT TB PPDU), indicates RU assignment, including the size of the RU(s) and their placement in the frequency domain, to be used in the EHT modulated fields of the PPDU in the frequency domain. [20/0609r3, Y/N/A: 37/0/8]
    Compressed modes are TBD.
From those aspects,
  EHT non-AP STA can share the same parsing logic in 11ax.
  Non-compressed and compressed modes need to be defined in EHT.
In this contribution, we propose non-compressed and compressed modes according to the supported features and discuss the details to support both of them.

## Slide 5: Logical Flow of Signaling in EHT SIG
  EHT non-AP STA can share the same parsing logic in 11ax as following.
The common field in EHT SIG has the information which is needed for recipients in common and the information in this field is shared between users within the same sub-band channel.
  RU allocation is common information to all or sub-set of recipients
    A map of RU assignment is indicated and decoded by a group of STAs.
    The number of STAs in that group can be informed, which also indicates the number of user fields.
The user-specific field in EHT SIG has the information for a specific user.
  User field indicates user information assigned to each RU or multi-RU similar to that used in HE MU PPDU.
Common | User specific
EHT-STF | EHT-LTF
80 MHz
Common | User specific
EHT-STF | EHT-LTF
80 MHz
EHT SIG
OFDMA Payload
STA 1 | STA 2 | STA 3 | STA 4
STA 1 | STA 2

## Slide 6: Non-Compressed and Compressed Modes Design
Non-OFDMA mode (compressed mode)
  Used for Full BW SU or Full BW MU-MIMO (incl. preamble punctured mode)
  RU allocation info in the common field can be omitted.
OFDMA mode (non-compressed mode 1)
  Used for OFDMA with RUs with size of < 242 tones.
  MU-MIMO is not considered.
  RU Allocation subfield in the common field may indicate the RU assignment information with granularity of 20MHz.
Large-size RU OFDMA mode (non-compressed mode 2)
  Used for OFDMA with RUs with size of >= 242 tones
  RU Allocation subfield is per 40MHz for 80MHz or 160MHz (minimum RU size of 242) and per 80MHz for 240MHz or 320MHz (minimum RU size of 484).
Non-OFDMA | OFDMA | 
 | RUs with size of < 242 tones (non MU-MIMO) | RUs with size of >= 242 tones (MU-MIMO and non MU-MIMO)
Non-OFDMA mode (compressed mode) | OFDMA mode (non-compressed mode 1) | Large-size RU OFDMA mode (non-compressed mode 2)

## Slide 7: OFDMA Mode in EHT
OFDMA mode is used to support OFDMA without MU-MIMO.
Considering the passed SP that the minimum RU size for EHT to support MU-MIMO shall be 242-tone RU, it is better that single user is allocated to the small-size RU or multi-RU of size < 242 tones in OFDMA mode.
  TBD to include RUs larger than or equal to 242 tones (SU-MIMO) in OFDMA mode
  Inclusion will enable flexible scheduling while all >=RU242 allocation modes are duplicated in other mode
It is preferred that RU Allocation subfield in the common field indicates the RU assignment information with granularity of 20MHz as in 11ax.
  Better to reuse 11ax RU Allocation subfield as much as possible if there is no strong motivation
    Reserved field to inform additional mode (MRU)
    Make some mode (MU-MIMO) to be reserved

## Slide 8: Other Modes in EHT
Non-OFDMA mode is used to support Full BW SU or Full BW MU-MIMO, which is similar to compressed mode in 11ax.
  RU Allocation subfield in the common field can be omitted.
Large-size RU OFDMA mode is used to support OFDMA with MU-MIMO.
  This mode is for larger than 80MHz.
  Considering the passed SP that the minimum RU size for EHT to support MU-MIMO shall be 242-tone RU, users can be multiplexed in the same large-size RU or multi-RU of size >= 242 tones in Large-size RU OFDMA mode.
  Many values in RU Allocation subfield in 11ax are not used to indicate the RU assignment information in large-size RU OFDMA mode.
  Therefore, new RU Allocation subfield for large-size RU OFDMA mode can be defined.

## Slide 9: Principles of RU Allocation Subfield Design
All of modes can share RU Allocation subfield.
  E.g., 10-bit RU Allocation subfield proposed in [2] can be used.
However, it may be better to use different RU Allocation subfield for each mode, in order to reduce the bit-width of RU Allocation subfield because OFDMA and large-size RU OFDMA modes require different RU mapping information.
  RU Allocation Subfield for OFDMA mode
    Small-size RU or multi-RU is assigned to a single STA.
    RU Allocation subfield with granularity of 20MHz as in 11ax.
  RU Allocation Subfield for large-size RU OFDMA
    Large-size RU or multi-RU is assigned to a single STA or multiple STAs.
    Define RU Allocation subfield based on min RU size where RU242 for 80/160MHz and RU484 for 240/320MHz and then we can share RU Allocation subfield.

## Slide 10: RU Allocation Subfield Design for OFDMA Mode in EHT
We introduce two options for signaling of RU assignment information for OFDMA mode.
  Option 1: Leverage the reserved values of RU Allocation subfield in 11ax to indicate the small-size multi-RU assignments
    E.g., 8-bit RU Allocation subfield in appendix
  Option 2: Redesign the RU Allocation subfield only for OFDMA mode to reduce the bit-width of RU Allocation subfield
    E.g., 6-bit RU Allocation subfield in appendix
For each option, the details of example of RU Allocation subfield table is included in Appendix.

## Slide 11: RU Allocation Subfield Design for Large-size RU OFDMA Mode in EHT
To support large-size RU OFDMA mode used for OFDMA with MU-MIMO, we can define another new RU Allocation subfield to indicate the RU assignment information only for large-size RU OFDMA.
It is preferred to define RU Allocation subfield based on min RU size where RU242 for 80/160MHz and RU484 for 240/320MHz.
Then, we can share RU Allocation subfield.

## Slide 12: RU Allocation Subfield Design for Large-size RU OFDMA Mode in EHT (Cont’d)
The following table shows an example of RU Allocation subfield table for large-size RU OFDMA in 80/160MHz PPDU.
  Minimum RU size of 242, granularity of 40MHz
  The structure of [1 2 1 2] for content channels is considered as in 11ax.
  Then, there can be only one RU Allocation subfield in the common field for 80MHz segment.
  The details of example of 8-bit RU Allocation subfield table for this is included in Appendix.
RUs associated with RU Allocation subfield for content channel
RU Allocation subfield (B8 B7 B6 B5 B4 B3 B2 B1 B0) | #1 | #2 | Number of entries
0-63 (00y2y1y0z2z1z0) | 242 | 242 | 64
64-127 (01y2y1y0z2z1z0) | 484 | 242 | 64
128-191 (10y2y1y0z2z1z0) | MRU of 484+996 | 242 | 64
192-199 (11000y2y1y0) | 242 | zero users | 8
200-207 (11001y2y1y0) | zero users | 242 | 8
208-215 (11010y2y1y0) | 484 | zero users | 8
216-223 (11011y2y1y0) | MRU of 242+484 |  | 8
224-231(11100y2y1y0) | MRU of 484+242 |  | 8
232-239 (11101y2y1y0) | 996 |  | 8
240-247 (11110y2y1y0) | MRU of 484+996 | zero users | 8
248 (11111000) | zero users | zero users | 1
249-255 | Reserved |  | 7
 | 80MHz | 
 | CC1 | CC2
242 | 1, 3 | 2, 4
484 | 1, 242RU3 | 2, 242RU2

## Slide 13: Examples of Proposed RU Allocation Subfield for Large-size RU OFDMA Mode
Examples
  BW 80 MHz OFDMA
  For simplicity, only one STA is assigned to each RU or multi-RU.
  The structure of [1 2 1 2] for content channels is considered as in 11ax.
Please see Appendix for more examples.
80MHz PPDU |  |  |  |  | Values of RU Allocation subfields | 
1 | 2 | 3 | 4 |  | CC1,RAU1 | CC2,RAU1
242 | 242 | 242 | 242 |  | 0 | 0
242 | empty | 242 | 242 |  | 0 | 200
484 |  | 242 | 242 |  | 64 | 200
242 | empty | 484 |  |  | 192 | 208
242 | 242 | 484 |  |  | 192 | 216
242 | empty | 484 |  |  | 216 | 248
484 |  | 242 | 242 |  | 224 | 200
484 |  | 242 | 242 |  | 200 | 224

## Slide 14: Summary
In this contribution, we proposed multiple modes according to the supported features as follows.
Also, we discussed RU Allocation subfield design to support both of them.
Non-OFDMA | OFDMA | 
 | RUs with size of < 242 tones (non MU-MIMO) | RUs with size of >= 242 tones (MU-MIMO and non MU-MIMO)
Non-OFDMA mode (compressed mode) | OFDMA mode (non-compressed mode 1) | Large-size RU OFDMA mode (non-compressed mode 2)

## Slide 15: Straw Poll #1
Do you support to define the following non-compressed and compressed modes in EHT?
  In OFDMA mode, whether RUs larger than or equal to 242 tones (only for SU-MIMO) in OFDMA mode is TBD.
Non-OFDMA | OFDMA | 
 | RUs with size of < 242 tones (non MU-MIMO) | RUs with size of >= 242 tones (MU-MIMO and non MU-MIMO)
Non-OFDMA mode (compressed mode) | OFDMA mode (non-compressed mode 1) | Large-size RU OFDMA mode (non-compressed mode 2)

## Slide 16: Straw Poll #2
Do you support to following details of EHT-SIG mode?
  In non-OFDMA mode, RU Allocation subfield is omitted, whether puncturing information is in common field of EHT-SIG or not is TBD.
  In OFDMA mode, each RU Allocation subfield in an EHT-SIG content channel corresponding to a 20 MHz frequency segment (same as 11ax).
  In large-size RU OFDMA mode, the number of RU Allocation subfield in an EHT-SIG contents channel is one for 80MHz and two for 160MHz and 320MHz.

## Slide 17: Reference
802.11-20/0566r21, Specification Framework for TGbe.
802.11-20/0373r3, RU Allocation Subfield Design for Multi-RU Support.

## Slide 18: APPENDIX

## Slide 19: Appendix - Example of 8-bit RU Allocation Subfield Table for Option 1 of OFDMA Mode
RU Allocation subfield ( B7 B6 B5 B4 B3 B2 B1 B0) | #1 | #2 | #3 | #4 | #5 | #6 | #7 | #8 | #9 | Number of entries
0 | 26 | 26 | 26 | 26 | 26 | 26 | 26 | 26 | 26 | 1
1 | 26 | 26 | 26 | 26 | 26 | 26 | 26 | 52 |  | 1
2 | 26 | 26 | 26 | 26 | 26 | 52 |  | 26 | 26 | 1
3 | 26 | 26 | 26 | 26 | 26 | 52 |  | 52 |  | 1
4 | 26 | 26 | 52 |  | 26 | 26 | 26 | 26 | 26 | 1
5 | 26 | 26 | 52 |  | 26 | 26 | 26 | 52 |  | 1
6 | 26 | 26 | 52 |  | 26 | 52 |  | 26 | 26 | 1
7 | 26 | 26 | 52 |  | 26 | 52 |  | 52 |  | 1
8 | 52 |  | 26 | 26 | 26 | 26 | 26 | 26 | 26 | 1
9 | 52 |  | 26 | 26 | 26 | 26 | 26 | 52 |  | 1
10 | 52 |  | 26 | 26 | 26 | 52 |  | 26 | 26 | 1
11 | 52 |  | 26 | 26 | 26 | 52 |  | 52 |  | 1
12 | 52 |  | 52 |  | 26 | 26 | 26 | 26 | 26 | 1
13 | 52 |  | 52 |  | 26 | 26 | 26 | 52 |  | 1
14 | 52 |  | 52 |  | 26 | 52 |  | 26 | 26 | 1
15 | 52 |  | 52 |  | 26 | 52 |  | 52 |  | 1
16-23 (00010y2y1y0) | 52 |  | 52 |  | _ | 106 |  |  |  | 8
24-31 (00011y2y1y0) | 106 |  |  |  | _ | 52 |  | 52 |  | 8
32-39(00100y2y1y0) | 26 | 26 | 26 | 26 | 26 | 106 |  |  |  | 8
40-47 (00101y2y1y0) | 26 | 26 | 52 |  | 26 | 106 |  |  |  | 8
48-55 (00110y2y1y0) | 52 |  | 26 | 26 | 26 | 106 |  |  |  | 8
56-63 (00111y2y1y0) | 52 |  | 52 |  | 26 | 106 |  |  |  | 8
64-71 (01000y2y1y0) | 106 |  |  |  | 26 | 26 | 26 | 26 | 26 | 8
72-79 (01001y2y1y0) | 106 |  |  |  | 26 | 26 | 26 | 52 |  | 8
80-87 (01010y2y1y0) | 106 |  |  |  | 26 | 52 |  | 26 | 26 | 8
88-95 (01011y2y1y0) | 106 |  |  |  | 26 | 52 |  | 52 |  | 8
96-111 (0110y1y0z1z0) | 106 |  |  |  | _ | 106 |  |  |  | 16
112 | 52 |  | 52 |  | _ | 52 |  | 52 |  | 1
113 | 242-tone RU empty (with zero users) |  |  |  |  |  |  |  |  | 1
114 | 484-tone RU; contributes zero User fields to the User Specific field in the same HE-SIG-B content channel as this RU Allocation subfield |  |  |  |  |  |  |  |  | 1
115 | 996-tone RU; contributes zero User fields to the User Specific field in the same HE-SIG-B content channel as this RU Allocation subfield |  |  |  |  |  |  |  |  | 1
116 | 26 | 26+52 multi-RU |  |  | 26 | 26 | 26 | 26 | 26 | 1
117 | 26 | 26+52 multi-RU |  |  | 26 | 26 | 26 | 52 |  | 1
118 | 26 | 26+52 multi-RU |  |  | 26 | 52 |  | 26 | 26 | 1
119 | 26 | 26+52 multi-RU |  |  | 26 | 52 |  | 52 |  | 1
120 | 26 | 26 | 26 | 26 | 26 | 52+26 multi-RU |  |  | 26 | 1
121 | 26 | 26 | 52 |  | 26 | 52+26 multi-RU |  |  | 26 | 1
122 | 52 |  | 26 | 26 | 26 | 52+26 multi-RU |  |  | 26 | 1
123 | 52 |  | 52 |  | 26 | 52+26 multi-RU |  |  | 26 | 1
124 | 26 | 26+52 multi-RU |  |  | 26 | 106 |  |  |  | 1
125 | 106 |  |  |  | 26 | 52+26 multi-RU |  |  | 26 | 1
126 | 106+26 multi-RU |  |  |  |  | 26 | 26 | 26 | 26 | 1
127 | 106+26 multi-RU |  |  |  |  | 26 | 26 | 52 |  | 1
128-191 (10y2y1y0z2z1z0) | 106 |  |  |  | 26 | 106 |  |  |  | 64
192-199 (11000y2y1y0) | 242 |  |  |  |  |  |  |  |  | 8
200-207 (11001y2y1y0) | 484 |  |  |  |  |  |  |  |  | 8
208-215 (11010y2y1y0) | 996 |  |  |  |  |  |  |  |  | 8
216 | 106+26 multi-RU |  |  |  |  | 52 |  | 26 | 26 | 1
217 | 106+26 multi-RU |  |  |  |  | 52 |  | 52 |  | 1
218 | 26 | 26 | 26 | 26 | 26+106 multi-RU |  |  |  |  | 1
219 | 26 | 26 | 52 |  | 26+106 multi-RU |  |  |  |  | 1
220 | 52 |  | 26 | 26 | 26+106 multi-RU |  |  |  |  | 1
221 | 52 |  | 52 |  | 26+106 multi-RU |  |  |  |  | 1
222 | 26 | 26+52 multi-RU |  |  | 26+106 multi-RU |  |  |  |  | 1
223 | 106+26 multi-RU |  |  |  |  | 52+26 multi-RU |  |  | 26 | 1
224 | 106+26 multi-RU |  |  |  |  | 106 |  |  |  | 1
225 | 106 |  |  |  | 26+106 multi-RU |  |  |  |  | 1
226 | 26 | 26+52 multi-RU |  |  | 26 | 52+26 multi-RU |  |  | 26 | 1
227-255 | Reserved |  |  |  |  |  |  |  |  | 29

## Slide 20: Appendix - Example of 6-bit RU Allocation Subfield Table for Option 2 of OFDMA Mode
RU Allocation subfield (B5 B4 B3 B2 B1 B0) | #1 | #2 | #3 | #4 | #5 | #6 | #7 | #8 | #9 | Number of entries
0 | 26 | 26 | 26 | 26 | 26 | 26 | 26 | 26 | 26 | 1
1 | 26 | 26 | 26 | 26 | 26 | 26 | 26 | 52 |  | 1
2 | 26 | 26 | 26 | 26 | 26 | 52 |  | 26 | 26 | 1
3 | 26 | 26 | 26 | 26 | 26 | 52 |  | 52 |  | 1
4 | 26 | 26 | 52 |  | 26 | 26 | 26 | 26 | 26 | 1
5 | 26 | 26 | 52 |  | 26 | 26 | 26 | 52 |  | 1
6 | 26 | 26 | 52 |  | 26 | 52 |  | 26 | 26 | 1
7 | 26 | 26 | 52 |  | 26 | 52 |  | 52 |  | 1
8 | 52 |  | 26 | 26 | 26 | 26 | 26 | 26 | 26 | 1
9 | 52 |  | 26 | 26 | 26 | 26 | 26 | 52 |  | 1
10 | 52 |  | 26 | 26 | 26 | 52 |  | 26 | 26 | 1
11 | 52 |  | 26 | 26 | 26 | 52 |  | 52 |  | 1
12 | 52 |  | 52 |  | 26 | 26 | 26 | 26 | 26 | 1
13 | 52 |  | 52 |  | 26 | 26 | 26 | 52 |  | 1
14 | 52 |  | 52 |  | 26 | 52 |  | 26 | 26 | 1
15 | 52 |  | 52 |  | 26 | 52 |  | 52 |  | 1
16 | 52 |  | 52 |  | _ | 106 |  |  |  | 1
17 | 106 |  |  |  | _ | 52 |  | 52 |  | 1
18 | 26 | 26 | 26 | 26 | 26 | 106 |  |  |  | 1
19 | 26 | 26 | 52 |  | 26 | 106 |  |  |  | 1
20 | 52 |  | 26 | 26 | 26 | 106 |  |  |  | 1
21 | 52 |  | 52 |  | 26 | 106 |  |  |  | 1
22 | 106 |  |  |  | 26 | 26 | 26 | 26 | 26 | 1
23 | 106 |  |  |  | 26 | 26 | 26 | 52 |  | 1
24 | 106 |  |  |  | 26 | 52 |  | 26 | 26 | 1
25 | 106 |  |  |  | 26 | 52 |  | 52 |  | 1
26 | 106 |  |  |  | _ | 106 |  |  |  | 1
27 | 52 |  | 52 |  | _ | 52 |  | 52 |  | 1
28 | 242-tone RU empty (with zero users) |  |  |  |  |  |  |  |  | 1
29 | 106 |  |  |  | 26 | 106 |  |  |  | 1
30 | 242 |  |  |  |  |  |  |  |  | 1
31 | 484 |  |  |  |  |  |  |  |  | 1
32 | 996 |  |  |  |  |  |  |  |  | 1
33 | 26 | 26+52 multi-RU |  |  | 26 | 26 | 26 | 26 | 26 | 1
34 | 26 | 26+52 multi-RU |  |  | 26 | 26 | 26 | 52 |  | 1
35 | 26 | 26+52 multi-RU |  |  | 26 | 52 |  | 26 | 26 | 1
36 | 26 | 26+52 multi-RU |  |  | 26 | 52 |  | 52 |  | 1
37 | 26 | 26 | 26 | 26 | 26 | 52+26 multi-RU |  |  | 26 | 1
38 | 26 | 26 | 52 |  | 26 | 52+26 multi-RU |  |  | 26 | 1
39 | 52 |  | 26 | 26 | 26 | 52+26 multi-RU |  |  | 26 | 1
40 | 52 |  | 52 |  | 26 | 52+26 multi-RU |  |  | 26 | 1
41 | 26 | 26+52 multi-RU |  |  | 26 | 106 |  |  |  | 1
42 | 106 |  |  |  | 26 | 52+26 multi-RU |  |  | 26 | 1
43 | 106+26 multi-RU |  |  |  |  | 26 | 26 | 26 | 26 | 1
44 | 106+26 multi-RU |  |  |  |  | 26 | 26 | 52 |  | 1
45 | 106+26 multi-RU |  |  |  |  | 52 |  | 26 | 26 | 1
46 | 106+26 multi-RU |  |  |  |  | 52 |  | 52 |  | 1
47 | 26 | 26 | 26 | 26 | 26+106 multi-RU |  |  |  |  | 1
48 | 26 | 26 | 52 |  | 26+106 multi-RU |  |  |  |  | 1
49 | 52 |  | 26 | 26 | 26+106 multi-RU |  |  |  |  | 1
50 | 52 |  | 52 |  | 26+106 multi-RU |  |  |  |  | 1
51 | 26 | 26+52 multi-RU |  |  | 26+106 multi-RU |  |  |  |  | 1
52 | 106+26 multi-RU |  |  |  |  | 52+26 multi-RU |  |  | 26 | 1
53 | 106+26 multi-RU |  |  |  |  | 106 |  |  |  | 1
54 | 106 |  |  |  | 26+106 multi-RU |  |  |  |  | 1
55 | 26 | 26+52 multi-RU |  |  | 26 | 52+26 multi-RU |  |  | 26 | 1
56-63 | Reserved |  |  |  |  |  |  |  |  | 8

## Slide 21: Appendix - Example of RU Allocation Subfield Table for Large-size RU OFDMA Mode in 80MHz/160MHz PPDU
RU Allocation subfield (B8 B7 B6 B5 B4 B3 B2 B1 B0) | #1 | #2 | Number of entries
0-63 (00y2y1y0z2z1z0) | 242 | 242 | 64
64-127 (01y2y1y0z2z1z0) | 484 | 242 | 64
128-191 (10y2y1y0z2z1z0) | MRU of 484+996 | 242 | 64
192-199 (11000y2y1y0) | 242 | zero users | 8
200-207 (11001y2y1y0) | zero users | 242 | 8
208-215 (11010y2y1y0) | 484 | zero users | 8
216-223 (11011y2y1y0) | MRU of 242+484 |  | 8
224-231(11100y2y1y0) | MRU of 484+242 |  | 8
232-239 (11101y2y1y0) | 996 |  | 8
240-247 (11110y2y1y0) | MRU of 484+996 | zero users | 8
248 (11111000) | zero users | zero users | 1
249-255 | Reserved |  | 7
Minimum RU size of 242, granularity of 40MHz
RUs associated with RU Allocation subfield for content channel
 | 80MHz | 
 | CC1 | CC2
242 | 1, 3 | 2, 4
484 | 1, 242RU3 | 2, 242RU2
 | 160MHz |  |  | 
 | CC1, RUA1 | CC2, RUA2 | CC1, RUA2 | CC2, RUA2
242 | 1, 3 | 2, 4 | 5, 7 | 6, 8
484 | 1, 242RU3 | 2, 242RU2 | 3, 242RU7 | 4, 242RU8
996 | 1 | 2 |  | 

## Slide 22: Appendix - Examples of Content Channels in 80MHz PPDU
Based on RU Allocation subfield table and for large-size RU OFDMA Mode in 80MHz PPDU
80MHz PPDU |  |  |  |  | Values of RU Allocation subfields |  | 
1 | 2 | 3 | 4 |  | CC1,RAU1 | CC2,RAU1 | 
242 | 242 | 242 | 242 |  | 0 | 0 | 
empty | 242 | 242 | 242 |  | 200 | 0 | 
242 | empty | 242 | 242 |  | 0 | 200 | 
242 | 242 | empty | 242 |  | 192 | 0 | 
242 | 242 | 242 | empty |  | 0 | 192 | 
484 |  | 484 |  |  | 208 | 208 | 
484 |  | 242 | 242 |  | 64 | 200 | 
484 |  | empty | 242 |  | 208 | 200 | 
484 |  | 242 | empty |  | 64 | 248 | 
242 | 242 | 484 |  |  | 192 | 64 | 
empty | 242 | 484 |  |  | 248 | 64 | 
242 | empty | 484 |  |  | 192 | 208 | 
242 | 242 | 484 |  |  | 192 | 216 | MRU
empty | 242 | 484 |  |  | 248 | 216 | 
242 | 242 | 484 |  |  | 216 | 192 | 
242 | empty | 484 |  |  | 216 | 248 | 
484 |  | 242 | 242 |  | 224 | 200 | 
484 |  | 242 | empty |  | 224 | 248 | 
484 |  | 242 | 242 |  | 200 | 224 | 
484 |  | empty | 242 |  | 248 | 224 | 

## Slide 23: Appendix - Examples of Content Channels in 160MHz PPDU
Based on RU Allocation subfield table for large-size RU OFDMA Mode in 80MHz/160MHz PPDU
160MHz PPDU |  |  |  |  |  |  |  |  | Values of RU Allocation subfields |  |  |  | 
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 |  | CC1, RUA1 | CC2, RUA1 | CC1, RUA2 | CC2, RUA2 | 
242 | 242 | 242 | 242 |  |  |  |  |  | 0 | 0 |  |  | 
empty | 242 | 242 | 242 |  |  |  |  |  | 200 | 0 |  |  | 
242 | empty | 242 | 242 |  |  |  |  |  | 0 | 200 |  |  | 
242 | 242 | empty | 242 |  |  |  |  |  | 192 | 0 |  |  | 
242 | 242 | 242 | empty |  |  |  |  |  | 0 | 192 |  |  | 
484 |  | 484 |  |  |  |  |  |  | 208 | 208 |  |  | 
484 |  | 242 | 242 |  |  |  |  |  | 64 | 200 |  |  | 
484 |  | empty | 242 |  |  |  |  |  | 208 | 200 |  |  | 
484 |  | 242 | empty |  |  |  |  |  | 64 | 248 |  |  | 
242 | 242 | 484 |  |  |  |  |  |  | 192 | 64 |  |  | 
empty | 242 | 484 |  |  |  |  |  |  | 248 | 64 |  |  | 
242 | empty | 484 |  |  |  |  |  |  | 192 | 208 |  |  | 
242 | 242 | 484 |  |  |  |  |  |  | 192 | 216 |  |  | MRU
empty | 242 | 484 |  |  |  |  |  |  | 248 | 216 |  |  | 
242 | 242 | 484 |  |  |  |  |  |  | 216 | 192 |  |  | 
242 | empty | 484 |  |  |  |  |  |  | 216 | 248 |  |  | 
484 |  | 242 | 242 |  |  |  |  |  | 224 | 200 |  |  | 
484 |  | 242 | empty |  |  |  |  |  | 224 | 248 |  |  | 
484 |  | 242 | 242 |  |  |  |  |  | 200 | 224 |  |  | 
484 |  | empty | 242 |  |  |  |  |  | 248 | 224 |  |  | 
996 |  |  |  |  |  |  |  |  | 232 | 248 |  |  | 
484 |  | 242 | 242 | 996 |  |  |  |  | 128 | 200 | 248 | 248 | MRU
484 |  | empty | 242 | 996 |  |  |  |  | 240 | 200 | 248 | 248 | 
484 |  | 242 | empty | 996 |  |  |  |  | 129 | 248 | 248 | 248 | 
484 |  | empty | empty | 996 |  |  |  |  | 240 | 248 | 248 | 248 | 
484 |  | 484 |  | 996 |  |  |  |  | 240 | 208 | 248 | 248 | 
242 | 242 | 484 |  | 996 |  |  |  |  | 192 | 128 | 248 | 248 | 
empty | 242 | 484 |  | 996 |  |  |  |  | 249 | 128 | 248 | 248 | 
242 | empty | 484 |  | 996 |  |  |  |  | 192 | 240 | 248 | 248 | 
empty | empty | 484 |  | 996 |  |  |  |  | 249 | 240 | 248 | 248 | 
484 |  | 484 |  | 996 |  |  |  |  | 208 | 240 | 248 | 248 | 
996 |  |  |  | 484 |  | 242 | 242 |  | 248 | 248 | 128 | 200 | 
996 |  |  |  | 484 |  | empty | 242 |  | 248 | 248 | 240 | 200 | 
996 |  |  |  | 484 |  | 242 | empty |  | 248 | 248 | 129 | 248 | 
996 |  |  |  | 484 |  | empty | empty |  | 248 | 248 | 240 | 248 | 
996 |  |  |  | 484 |  | 484 |  |  | 248 | 248 | 240 | 208 | 
996 |  |  |  | 242 | 242 | 484 |  |  | 248 | 248 | 192 | 128 | 
996 |  |  |  | empty | 242 | 484 |  |  | 248 | 248 | 249 | 128 | 
996 |  |  |  | 242 | empty | 484 |  |  | 248 | 248 | 192 | 240 | 
996 |  |  |  | empty | empty | 484 |  |  | 248 | 248 | 249 | 240 | 
996 |  |  |  | 484 |  | 484 |  |  | 248 | 248 | 208 | 240 | 

## Slide 24: Appendix - Example of RU Allocation Subfield Table for Large-size RU OFDMA Mode in 240MHz/320MHz PPDU
RU Allocation subfield (B8 B7 B6 B5 B4 B3 B2 B1 B0) | #1 | #2 | Number of entries
0-63 (00y2y1y0z2z1z0) | 484 | 484 | 64
64-127 (01y2y1y0z2z1z0) | 996 | 484 | 64
128-191 (10y2y1y0z2z1z0) | MRU of 3x996 | 484 | 64
192-199 (11000y2y1y0) | 484 | zero users | 8
200-207 (11001y2y1y0) | zero users | 484 | 8
208-215 (11010y2y1y0) | 996 | zero users | 8
216-223 (11011y2y1y0) | MRU of 484+996 |  | 8
224-231(11100y2y1y0) | MRU of 996+484 |  | 8
232-239 (11101y2y1y0) | 2x996 |  | 8
240-247 (11110y2y1y0) | MRU of 3x996 | zero users | 8
248 (11111000) | zero users | zero users | 1
249-255 | Reserved |  | 7
Minimum RU size of 484, granularity of 80MHz
RUs associated with RU Allocation subfield for content channel
 | 320MHz |  |  | 
 | CC1, RUA1 | CC2, RUA2 | CC1, RUA2 | CC2, RUA2
484 | 1, 3 | 2, 4 | 5, 7 | 6, 8
996 | 1, 484RU3 | 2, 484RU2 | 3, 484RU7 | 4, 484RU8
2x996 | 1 | 2 |  | 

## Slide 25: Appendix - Examples of Content Channels in 320MHz PPDU
Based on RU Allocation subfield table for large-size RU OFDMA Mode in 240MHz/320MHz PPDU
320MHz PPDU |  |  |  |  |  |  |  |  | Values of RU Allocation subfields |  |  |  | 
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 |  | CC1, RUA1 | CC2, RUA1 | CC1, RUA2 | CC2, RUA2 | 
484 | 484 | 484 | 484 |  |  |  |  |  | 0 | 0 |  |  | 
empty | 484 | 484 | 484 |  |  |  |  |  | 200 | 0 |  |  | 
484 | empty | 484 | 484 |  |  |  |  |  | 0 | 200 |  |  | 
484 | 484 | empty | 484 |  |  |  |  |  | 192 | 0 |  |  | 
484 | 484 | 484 | empty |  |  |  |  |  | 0 | 192 |  |  | 
996 |  | 996 |  |  |  |  |  |  | 208 | 208 |  |  | 
996 |  | 484 | 484 |  |  |  |  |  | 64 | 200 |  |  | 
996 |  | empty | 484 |  |  |  |  |  | 208 | 200 |  |  | 
996 |  | 484 | empty |  |  |  |  |  | 64 | 248 |  |  | 
484 | 484 | 996 |  |  |  |  |  |  | 192 | 64 |  |  | 
empty | 484 | 996 |  |  |  |  |  |  | 248 | 64 |  |  | 
484 | empty | 996 |  |  |  |  |  |  | 192 | 208 |  |  | 
448 | 484 | 996 |  |  |  |  |  |  | 192 | 216 |  |  | MRU
empty | 484 | 996 |  |  |  |  |  |  | 248 | 216 |  |  | 
484 | 484 | 996 |  |  |  |  |  |  | 216 | 192 |  |  | 
484 | empty | 996 |  |  |  |  |  |  | 216 | 248 |  |  | 
996 |  | 484 | 484 |  |  |  |  |  | 224 | 200 |  |  | 
996 |  | 484 | empty |  |  |  |  |  | 224 | 248 |  |  | 
996 |  | 484 | 484 |  |  |  |  |  | 200 | 224 |  |  | 
996 |  | empty | 484 |  |  |  |  |  | 248 | 224 |  |  | 
2x996 |  |  |  |  |  |  |  |  | 232 | 248 |  |  | 
996 |  | 484 | 484 | 2x996 |  |  |  |  | 128 | 200 | 248 | 248 | MRU
996 |  | empty | 484 | 2x996 |  |  |  |  | 240 | 200 | 248 | 248 | 
996 |  | 484 | empty | 2x996 |  |  |  |  | 129 | 248 | 248 | 248 | 
996 |  | empty | empty | 2x996 |  |  |  |  | 240 | 248 | 248 | 248 | 
996 |  | 996 |  | 2x996 |  |  |  |  | 240 | 208 | 248 | 248 | 
484 | 484 | 996 |  | 2x996 |  |  |  |  | 192 | 128 | 248 | 248 | 
empty | 484 | 996 |  | 2x996 |  |  |  |  | 249 | 128 | 248 | 248 | 
484 | empty | 996 |  | 2x996 |  |  |  |  | 192 | 240 | 248 | 248 | 
empty | empty | 996 |  | 2x996 |  |  |  |  | 249 | 240 | 248 | 248 | 
996 |  | 996 |  | 2x996 |  |  |  |  | 208 | 240 | 248 | 248 | 
2x996 |  |  |  | 996 |  | 484 | 484 |  | 248 | 248 | 128 | 200 | 
2x996 |  |  |  | 996 |  | empty | 484 |  | 248 | 248 | 240 | 200 | 
2x996 |  |  |  | 996 |  | 484 | empty |  | 248 | 248 | 129 | 248 | 
2x996 |  |  |  | 996 |  | empty | empty |  | 248 | 248 | 240 | 248 | 
2x996 |  |  |  | 996 |  | 996 |  |  | 248 | 248 | 240 | 208 | 
2x996 |  |  |  | 484 | 484 | 996 |  |  | 248 | 248 | 192 | 128 | 
2x996 |  |  |  | empty | 484 | 996 |  |  | 248 | 248 | 249 | 128 | 
2x996 |  |  |  | 484 | empty | 996 |  |  | 248 | 248 | 192 | 240 | 
2x996 |  |  |  | empty | empty | 996 |  |  | 248 | 248 | 249 | 240 | 
2x996 |  |  |  | 996 |  | 996 |  |  | 248 | 248 | 208 | 240 |