## Slide 1: Management of RU allocation field
Date: 2020-06-01
Authors:
Name | Affiliation | Address | Phone | Email
Dongguk Lim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | dongguk.lim@lge.com
Eunsung Park |  |  |  | Ensung.park@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
June 2020

## Slide 2: Introduction
Based on the 11be SFD, we have achieved the following agreements through the previous discussion.
  The RU allocation subfield includes the allocation for both Multiple RU aggregation and single RU.
  an EHT-SIG content channel contains the following # of RU allocation subfield according to BW, respectively.
    20MHz or 40MHz : N =1
    80MHz : N= 2
    Other BW : TBD
In this contribution, we investigate the number of RU allocation subfield for the efficient signaling and reduction of overhead when the MRU aggregation and BW>80MHz are considered.

## Slide 3: The EHT-SIG field
The agreement in 11be SFD
  The EHT-SIG in an EHT PPDU sent to multiple users shall have a common field and user-specific field(s).
    An RU Allocation subfield is present in the Common field of the EHT-SIG field
  The EHT-SIG field consists of the two EHT-SIG content channels in each 80MHz
    A EHT-SIG content channel is composed of a 20 MHz frequency segment.
    The content channels (i.e., CC1 and CC2) per each 80MHz may carry different information

## Slide 4: Consideration (1/2)
As introduced in [1], in the BW > 80MHz, STA which supports the SST operation can be parked on an 80MHz segment within BW.
And, since the STA parked on an 80MHz segment only looks at the 80MHz it is parked, it can get the information by decoding the U-SIG and EHT-SIG of the assigned 80MHz segment.
In addition, as described in [2], since the RU allocation subfield can include the assignment information for the large size of RU aggregation cross the 80MHz in BW> 80MHz, STA can know the information of allocated RU located on either allocated 80MHz and outside.
Therefore, the STA parked on an 80MHz segment can know the assignment information even if the assignment is outside because the EHT-SIG can contain the assignment outside of the 80MHz segment as well as the parked 80MHz segment.

## Slide 5: Consideration (2/2)
In 11be, since the BW can be expanded up to 320MHz, for the MU-MIMO+OFDMA, we can consider the size of RU lager than 996-tone.
  For example, 2x996, 3x996 as well as the large size of RU aggregations defined in 11be SFD can be considered for the MU-MIMO+OFDMA.
And the MU-MIMO STA’s information on allocated large size RU > 996-tone can be distributed on the two EHT-SIG content channels in an 80MHz segment for the load balancing for MU-MIMO.
  also, there is no STA to signal in the EHT-SIG of other 80MHz segment.
Therefore, to indicate this, we can consider the using the entry which indicates the zero STA allocated of RU allocation subfield field for the indication of zero STA similar to 11ax.
  For example,
    2x996 tone RU contributed zero STA
    3x996 tone RU contributed zero STA

## Slide 6: Signaling of RU allocation (1/2)
By taking into account both the RU allocation subfield in [2] and the considerations described in previous slides, we can consider the following indication of RU assignment information on the BW > 80MHz .
  By using the 2 consecutive RU allocation subfields in each EHT-SIG content channel on 80MHz, we can indicate the assignment of each STA parked on an 80MHz segment.
    In addition, the assignment information can include either allocated 80MHz segment and other 80MHz segments for supporting of large MRU aggregation in OFDMA.
  The large MRU indication on RU allocation subfield
    For example, RU allocation subfield includes the indication for 3x996 in 320MHz
    The indication for other MRU cases is described in appendix.
  By using this indicator, the STA can know the large MRU allocation information wherever the STA is located when BW > 80MHz.
*: 3x996 : it might not be required depending on the decision of channelization for 240MHz
Bit index | RU allocation | Entry
001001y2y1y0 | 3x996* | 8
· · · | · · · | · · ·
101110 y2y1y0 | 996(1)+996(2)+996(3) | 8
101111 y2y1y0 | 996(1)+996(2)+996(4) | 8
110000 y2y1y0 | 996(1)+996(3)+996(4) | 8
110001 y2y1y0 | 996(2)+996(3)+996(4) | 8

## Slide 7: Signaling of RU allocation (2/2)
Example on 160MHz
  The STAs parked on the 80MHz segment ch2 are allocated on the 484+ 996 RU for the MU-MIMO transmission.
    In the 80MHz segment ch1, the assignment of ch#5 ~8 does not need to be included in two EHT-SIG content channel because all related STA are located in other 80MHz.
      Even if these STA are located in 80MHz segment ch1, that can know the allocation of MRU aggregation crossed the other 80MHz by using the 2 consecutive RU allocation subfield.
The STAs (#10 ~ 17) can know the assigned information by using the 2 consecutive RU allocation subfields in each EHT-SIG content channel.
The second RU allocation subfield for ch#3 and ch#4 include the indication for zero STA, respectively.

## Slide 8: Overhead
In terms of overhead for the common field, we can reduce the number of RU allocation subfield which located in an EHT-SIG content channel.
  As shown in slide 7, for the OFDMA transmission in 160MHz, we can compose the common field with 2 consecutive RU allocation subfields per an EHT-SIG content channel.
  And, the number of RU allocation subfields can be fixed as 2 regardless of BW when BW >80MHz.
    Whereas we can assume the increased N according to BW like 11ax to support some STAs that can be parsed into the 80MHz segment that does not include the STA's allocated RU, this case does not look desirable.
  So, when we compare with 11ax’s way that increases the # of RU allocation subfields according to BW, it can reduce the overhead as ½ times and ¼ times in the 160MHz and 320MHz, respectively.

## Slide 9: Summary
Basically in the 11be transmission, the 80MHz segment operation was agreed.
  For this operation, the U-SIG and EHT-SIG that contain the different contents per 80MHz segment are applied to 11be.
For the efficient signaling for RU allocation in OFDMA transmission, the enhanced RU allocation subfield[2] can include the assignment information for MRU aggregation in BW> 80Mz.
we can consider the new composition of a common field in the EHT-SIG content channel by considering the above.
  A common field includes the only two RU allocation subfields in an EHT-SIG content channel even when BW .
  We can reduce the overhead of the common field because only 2 RU allocation fields are used.

## Slide 10: Straw poll #1
Do you agree that the number of User fields per RU contributed to the user specific field in the same EHT-SIG content channel is indicated by the RU Allocation subfields in 11be OFDMA transmission?
  Compressed mode is TBD
  Y/N/A

## Slide 11: Straw poll #2
Do you agree that the specific 80MHz segment on which a STA is parked includes the STA’s allocated RU.
  Y/N/A

## Slide 12: Straw poll #3
Which option do you prefer to define the number of RU allocation subfields in a common field in the EHT-SIG field when BW is larger than 80MHz (assuming STAs are parked on one of 80MHz segments)
  Option 1: same with 11ax’s
    N= 4 and 8 for 160MHz and 320MHz, respectively
  Option 2: fixed number for N
    N = 2 for 160MHz and 320MHz
  Abs
  It does not intend to the SFD.
  Opt.1/Opt.2/Abs

## Slide 13: Straw poll #4
Do you agree that the number of RU allocation subfields in a common field is defined as 2 when BW is larger than 80MHz (assuming STAs are parked on one of 80MHz segments)?
  Y/N/A

## Slide 14: Reference
[1] 11-20/380, U-SIG Structure and Preamble Processing, (Sameer, Qualcom)
[2] 11-20/798r1, Signaling of RU allocation follow-up, (Dongguk Lim, LGE)

## Slide 15: Appendix

## Slide 16: RU allocation subfield (1/2)
Single RU allocation in RU allocation subfield
MSB (1bit) | 8bit information | #1 | #2 | #3 | #4 | #5 | #6 | #7 | #8 | #9 | Number of entries
B8 | (B7 B6 B5 B4 B3 B2 B1 B0) |  |  |  |  |  |  |  |  |  | 
0 | 00000000 | 26 | 26 | 26 | 26 | 26 | 26 | 26 | 26 | 26 | 1
0 | 00000001 | 26 | 26 | 26 | 26 | 26 | 26 | 26 | 52 |  | 1
0 | 00000010 | 26 | 26 | 26 | 26 | 26 | 52 |  | 26 | 26 | 1
0 | 00000011 | 26 | 26 | 26 | 26 | 26 | 52 |  | 52 |  | 1
0 | 00000100 | 26 | 26 | 52 |  | 26 | 26 | 26 | 26 | 26 | 1
0 | 00000101 | 26 | 26 | 52 |  | 26 | 26 | 26 | 52 |  | 1
0 | 00000110 | 26 | 26 | 52 |  | 26 | 52 |  | 26 | 26 | 1
0 | 00000111 | 26 | 26 | 52 |  | 26 | 52 |  | 52 |  | 1
0 | 00001000 | 52 |  | 26 | 26 | 26 | 26 | 26 | 26 | 26 | 1
0 | 00001001 | 52 |  | 26 | 26 | 26 | 26 | 26 | 52 |  | 1
0 | 00001010 | 52 |  | 26 | 26 | 26 | 52 |  | 26 | 26 | 1
0 | 00001011 | 52 |  | 26 | 26 | 26 | 52 |  | 52 |  | 1
0 | 00001100 | 52 |  | 52 |  | 26 | 26 | 26 | 26 | 26 | 1
0 | 00001101 | 52 |  | 52 |  | 26 | 26 | 26 | 52 |  | 1
0 | 00001110 | 52 |  | 52 |  | 26 | 52 |  | 26 | 26 | 1
0 | 00001111 | 52 |  | 52 |  | 26 | 52 |  | 52 |  | 1
0 | 00010000 | 52 |  | 52 |  | - | 106 |  |  |  | 1
0 | 00010001 | 106 |  |  |  | - | 52 |  | 52 |  | 1
0 | 00010010 | 26 | 26 | 26 | 26 | 26 | 106 |  |  |  | 1
0 | 00010011 | 26 | 26 | 52 |  | 26 | 106 |  |  |  | 1
0 | 00010100 | 52 |  | 26 | 26 | 26 | 106 |  |  |  | 1
0 | 00010101 | 52 |  | 52 |  | 26 | 106 |  |  |  | 1
0 | 00010110 | 106 |  |  |  | 26 | 26 | 26 | 26 | 26 | 1
0 | 00010111 | 106 |  |  |  | 26 | 26 | 26 | 52 |  | 1
0 | 00011000 | 106 |  |  |  | 26 | 52 |  | 26 | 26 | 1
0 | 00011001 | 106 |  |  |  | 26 | 52 |  | 52 |  | 1
0 | 00011010 | 106 |  |  |  | - | 106 |  |  |  | 1
0 | 00011011 | 52 |  | 52 |  | - | 52 |  | 52 |  | 1
0 | 00011100 | 106 |  |  |  | 26 | 106 |  |  |  | 1
0 | 00011101 | 242-tone RU empty (with zero users) |  |  |  |  |  |  |  |  | 1
0 | 00011110 | 484-tone RU; contributes zero User fields to the User Specific field in the same HE-SIG-B content channel as this RU Allocation subfield |  |  |  |  |  |  |  |  | 1
0 | 00011111 | 996-tone RU; contributes zero User fields to the User Specific field in the same HE-SIG-B content channel as this RU Allocation subfield |  |  |  |  |  |  |  |  | 1
0 | 00100000 | 2x996-tone RU; contributes zero User fields to the User Specific field in the same HE-SIG-B content channel as this RU Allocation subfield |  |  |  |  |  |  |  |  | 1
0 | 00100001 | 3x996-tone RU; contributes zero User fields to the User Specific field in the same HE-SIG-B content channel as this RU Allocation subfield |  |  |  |  |  |  |  |  | 1
0 | 0010001x0 | Reserved |  |  |  |  |  |  |  |  | 2
0 | 001001x1x0 | Reserved |  |  |  |  |  |  |  |  | 4
0 | 00101y2y1y0 | 242 |  |  |  |  |  |  |  |  | 8
0 | 00110y2y1y0 | 484 |  |  |  |  |  |  |  |  | 8
0 | 00111y2y1y0 | 996 |  |  |  |  |  |  |  |  | 8
0 | 01000y2y1y0 | 2x996 |  |  |  |  |  |  |  |  | 8
0 | 01001y2y1y0 | 3x996 |  |  |  |  |  |  |  |  | 8
0 | 0101y3y2y1y0 | Reserved |  |  |  |  |  |  |  |  | 16
0 | 011y4y3y2y1y0 | Reserved |  |  |  |  |  |  |  |  | 32
0 | 1y6y5y4y3y2y1y0 | Reserved |  |  |  |  |  |  |  |  | 128

## Slide 17: RU allocation subfield (2/2)
Multiple RU allocation in RU allocation subfield
MSB (1bit) | 8bit information | #1 | #2 | #3 | #4 | #5 | #6 | #7 | #8 | #9 | Number of entries
B8 | (B7 B6 B5 B4 B3 B2 B1 B0) |  |  |  |  |  |  |  |  |  | 
1 | 00000000 | 26 | 26+52 |  |  | 26 | 26 | 26 | 26 | 26 | 1
1 | 00000001 | 26 | 26+52 |  |  | 26 | 26 | 26 | 52 |  | 1
1 | 00000010 | 26 | 26+52 |  |  | 26 | 52 |  | 26 | 26 | 1
1 | 00000011 | 26 | 26+52 |  |  | 26 | 52 |  | 52 |  | 1
1 | 00000100 | 26 | 26 | 26 | 26 | 26 | 52+26 |  |  | 26 | 1
1 | 00000101 | 26 | 26 | 52 |  | 26 | 52+26 |  |  | 26 | 1
1 | 00000110 | 52 |  | 26 | 26 | 26 | 52+26 |  |  | 26 | 1
1 | 00000111 | 52 |  | 52 |  | 26 | 52+26 |  |  | 26 | 1
1 | 00001000 | 26 | 26+52 |  |  | 26 | 52+26 |  |  | 26 | 1
1 | 00001001 | 26 | 26+52 |  |  | 26 | 106 |  |  |  | 1
1 | 00001010 | 106 |  |  |  | 26 | 52+26 |  |  | 26 | 1
1 | 00001011 | 26 | 26 | 26 | 26 | 26+106 |  |  |  |  | 1
1 | 00001100 | 26 | 26 | 52 |  | 26+106 |  |  |  |  | 1
1 | 00001101 | 52 |  | 26 | 26 | 26+106 |  |  |  |  | 1
1 | 00001110 | 52 |  | 52 |  | 26+106 |  |  |  |  | 1
1 | 00001111 | 106 |  |  |  | 106+26 |  |  |  |  | 1
1 | 00010000 | 106+26 |  |  |  |  | 26 | 26 | 26 | 26 | 1
1 | 00010001 | 106+26 |  |  |  |  | 26 | 26 | 52 |  | 1
1 | 00010010 | 106+26 |  |  |  |  | 52 |  | 26 | 26 | 1
1 | 00010011 | 106+26 |  |  |  |  | 52 |  | 52 |  | 1
1 | 00010100 | 106+26 |  |  |  |  | 106 |  |  |  | 1
1 | 00010101 | 106+26 |  |  |  |  | 52+26 |  |  | 26 | 1
1 | 00010110 | 26 | 26+52 |  |  | 26+106 |  |  |  |  | 1
1 | 00010111 | Reserved |  |  |  |  |  |  |  |  | 1
1 | 00011 y2y1y0 | 242+484 |  |  |  |  |  |  |  |  | 8
1 | 00100 y2y1y0 | 484(1)+996(2) |  |  |  |  |  |  |  |  | 8
1 | 00101 y2y1y0 | 484(2)+996(2) |  |  |  |  |  |  |  |  | 8
1 | 00110 y2y1y0 | 996(1)+484(4) |  |  |  |  |  |  |  |  | 8
1 | 00111 y2y1y0 | 996(1)+484(3) |  |  |  |  |  |  |  |  | 8
1 | 01000 y2y1y0 | 484(1)+996(2)+996(3) |  |  |  |  |  |  |  |  | 8
1 | 01001 y2y1y0 | 484(2)+996(2)+996(3) |  |  |  |  |  |  |  |  | 8
1 | 01010 y2y1y0 | 996(1)+484(3)+996(3) |  |  |  |  |  |  |  |  | 8
1 | 01011 y2y1y0 | 996(1)+484(4)+996(3) |  |  |  |  |  |  |  |  | 8
1 | 01100 y2y1y0 | 996(1)+996(2)+484(5) |  |  |  |  |  |  |  |  | 8
1 | 01101 y2y1y0 | 996(1)+996(2)+484(6) |  |  |  |  |  |  |  |  | 8
1 | 01110 y2y1y0 | 996(1)+996(2)+996(3) |  |  |  |  |  |  |  |  | 8
1 | 01111 y2y1y0 | 996(1)+996(2)+996(4) |  |  |  |  |  |  |  |  | 8
1 | 10000 y2y1y0 | 996(1)+996(3)+996(4) |  |  |  |  |  |  |  |  | 8
1 | 10001 y2y1y0 | 996(2)+996(3)+996(4) |  |  |  |  |  |  |  |  | 8
1 | 10010 y2y1y0 | 484(1)+996(2)+996(3)+996(4) |  |  |  |  |  |  |  |  | 8
1 | 10011 y2y1y0 | 484(2)+996(2)+996(3)+996(4) |  |  |  |  |  |  |  |  | 8
1 | 10100 y2y1y0 | 996(1)+484(3)+996(3)+996(4) |  |  |  |  |  |  |  |  | 8
1 | 10101 y2y1y0 | 996(1)+484(4)+996(3)+996(4) |  |  |  |  |  |  |  |  | 8
1 | 10110 y2y1y0 | 996(1)+996(2)+484(5)+996(4) |  |  |  |  |  |  |  |  | 8
1 | 10111 y2y1y0 | 996(1)+996(2)+484(6)+996(4) |  |  |  |  |  |  |  |  | 8
1 | 11000 y2y1y0 | 996(1)+996(2)+996(3)+484(7) |  |  |  |  |  |  |  |  | 8
1 | 11001 y2y1y0 | 996(1)+996(2)+996(3)+484(8) |  |  |  |  |  |  |  |  | 8
1 | 1101 y3y2y1y0 | Reserved |  |  |  |  |  |  |  |  | 16
1 | 1110 y3y2y1y0 | Reserved |  |  |  |  |  |  |  |  | 16
1 | 1111 y3y2y1y0 | Reserved |  |  |  |  |  |  |  |  | 16

## Slide 18: Combination of small-size RUs (1/2)
Based on the passed motions in [1], we can consider the following allocation for combinations of small-size RUs.
  We assume the followings
    Bandwidth : 20MHz
    Number of allocated combination in BW : up to 2
    An Allocation subfield is configure per 20MHz.
    Multiple User transmission (i.e., OFDMA), but, MU-MIMO is not considered.
  Allocation for RU26+RU52,
Index | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
1 | 26 | 26 | 52 |  | 26 | 26 | 26 | 26 | 26
2 | 26 | 26 | 52 |  | 26 | 26 | 26 | 52 | 
3 | 26 | 26 | 52 |  | 26 | 52 |  | 26 | 26
4 | 26 | 26 | 52 |  | 26 | 52 |  | 52 | 
5 | 26 | 26 | 52 |  | 26 | 106 |  |  | 
6 | 26 | 26 | 26 | 26 | 26 | 52 |  | 26 | 26
7 | 26 | 26 | 52 |  | 26 | 52 |  | 26 | 26
8 | 52 |  | 26 | 26 | 26 | 52 |  | 26 | 26
9 | 52 |  | 52 |  | 26 | 52 |  | 26 | 26
10 | 106 |  |  |  | 26 | 52 |  | 26 | 26
11 | 26 | 26 | 52 |  | 26 | 52 |  | 26 | 26

## Slide 19: Combination of small-size RUs (1/2)
  Allocation for RU26+RU106
  We can also consider the allocation of two combinations configured with different small-size RUs.
    For example, RU26+RU52 and RU26+RU106 can be considered.
index | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
1 | 26 | 26 | 26 | 26 | 26 | 106 |  |  | 
2 | 26 | 26 | 52 |  | 26 | 106 |  |  | 
3 | 52 |  | 26 | 26 | 26 | 106 |  |  | 
4 | 52 |  | 52 |  | 26 | 106 |  |  | 
5 | 106 |  |  |  | 26 | 106 |  |  | 
6 | 106 |  |  |  | 26 | 26 | 26 | 26 | 26
7 | 106 |  |  |  | 26 | 26 | 26 | 52 | 
8 | 106 |  |  |  | 26 | 52 |  | 26 | 26
9 | 106 |  |  |  | 26 | 52 |  | 52 | 
10 | 106 |  |  |  | 26 | 106 |  |  | 
index | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
1 | 106 |  |  |  | 26 | 52 |  | 26 | 26
2 | 26 | 26 | 52 |  | 26 | 106 |  |  | 

## Slide 20: Combination of Large-size RUs
We can also consider the following allocation for Combination of Large-size RUs based on 11be SFD[1].
  We assume that the multiple user transmission(i.e. OFDMA) but MU-MIMO is not considered.
  In 80MHz
  In 160MHz
  For the 240MHz and 320MHz, the above combinations for 160MHz can be used in the continuous 160MHz within this bandwidth.
    Exception: 3×996 is supported.
index | 1 | 2 | 3 | 4
1 | 242 | 242 | 484 | 
2 | 242 | 242 | 484 | 
3 | 484 |  | 242 | 242
4 | 484 |  | 242 | 242
index | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
1 | 484 |  | 484 |  | 996 |  |  | 
2 | 484 |  | 484 |  | 996 |  |  | 
3 | 996 |  |  |  | 484 |  | 484 | 
4 | 996 |  |  |  | 484 |  | 484 |