## Slide 1: A Channel Measurement Procedure for WLAN Sensing
Date: 2020-06-03
Authors:

## Slide 2: Abstract
This contribution addresses channel measurements for WLAN sensing.
We consider the particular case in which a STA (sensing initiator) obtains wireless channel measurements (for example, CFR) by receiving/transmitting PPDUs from/to a second STA (sensing responder).
  We do not consider monostatic cases in this contribution.
We propose a request-and-response procedure in which a sensing initiator solicits a sensing responder to make a transmission with certain characteristics that enable reliable WLAN sensing.
The proposed procedure can be built upon to define other procedures, such as those that include scheduling and multiple sensing responders.

## Slide 3: Outline
Abstract and outline
WLAN sensing implementation challenges
  Mechanisms for channel measurement
  Transmit configuration adaptations
WLAN sensing sounding
  Proposed procedure
  Transmit configuration
Other considerations
  Scalability
  Scheduling

## Slide 4: WLAN Sensing Implementation Challenges
Many of the technical challenges and standard gaps identified in presentations made to WNG, SENS TIG, and SENS SG are related to channel measurements.
Specifically, the IEEE 802.11 standard and current amendments under development do not define procedures necessary for WLAN Sensing applications to reliably and efficiently obtain channel measurements.
Example:
Certain WLAN sensing applications are implemented by tracking one or more wireless links over time and using algorithms (application-layer) to classify channel variations into events/activities.
Amplitude, static environment (no motion).
Amplitude, dynamic environment (motion).

## Slide 5: Mechanisms for Channel Measurement: Examples
There are different approaches a sensing initiator could use to obtain channel measurements, each with advantages and limitations.
Example 1: Sensing initiator could “opportunistically” obtain channel estimates by PPDUs sent by the sensing responder (management frames, for example).
  Difficult/not possible to guarantee periodicity.
  Overhead if transmissions must be triggered.
Example 2: Sensing initiator could send an NDP to the sensing responder and track the channel by using the feedback sent in return.
  Sensing initiator would use compressed beamforming feedback – may lead to performance loss.
  Feedback may take significant airtime, particularly as the number of streams and bandwidth increase.

## Slide 6: Transmit Configuration Adaptations
Channel variations observed by the sensing initiator could be a result of different occurrences, including:
  Actual motion in the environment (e.g., a person entered a room); or
  Changes in transmit settings of the sensing responder, such as
    Number of transmit antennas and/or antenna used
    Beamforming update
Changes in transmit settings may noticeably impact WLAN sensing performance.
Need for transmit configuration freeze/hold was discussed in previous presentations made to WNG/SENS TIG/SENS SG.
Example transmitter adaptation

## Slide 7: WLAN Sensing Procedures for Channel Measurement
To support different applications and architectures, the WLAN sensing amendment will likely define a (limited) number of channel measurement procedures. Such procedures, for example, could be
  Based on unsolicited or requested transmissions
  On-demand (e.g., request-and-response) or scheduled
In this contribution, we present a channel measurement procedure that consists of a request-and-response sounding exchange.
  Could be used as a building block for other procedures
  May not be applicable or “optimal” to all WLAN sensing architectures and applications

## Slide 8: WLAN Sensing Sounding: Procedure
The proposed procedure is illustrated below:
  Sensing initiator sends a frame to a peer station (sensing responder) requesting the transmission of an NDP with certain transmission characteristics (next slide).
  STA that receives the NDP request (sensing responder) sends an NDP announcement frame followed by an NDP to the sensing initiator.
Advantages: No feedback necessary. Sounding multiple dimensions.
Notes:
  Different from the beamforming NDP procedure, the NDP is sent by the ”beamformee.”
  Sensing initiator takes the role of sensing receiver. Sensing responder is the sensing transmitter.
  It may not be necessary to include an NDP announcement frame.

## Slide 9: WLAN Sensing Sounding: Transmit Configuration 1/2
To address the “transmit configuration adaptations” issue previously discussed, we define that NDP announcements and NDPs sent by a given sensing responder in response to different requests by the same sensing initiator shall be transmitted with the same set of transmit parameters, unless specified by the sensing initiator.
One option would be to define in the sensing NDP request frame a bit (for example, “TX configuration hold”) that
  When set to 1, indicates that the sensing responder shall use the same transmit parameters in the transmission of the NDP announcement and NDP than the immediately previous WLAN sensing sounding with the same sensing initiator.
  When set to 0, indicates that the sensing responder may use any set of transmit parameters when transmitting the NDP announcement and NDP.

## Slide 10: WLAN Sensing Sounding: Transmit Configuration 2/2
A second option would be to define a field in the sensing NDP request frame that specifies a particular transmit configuration set, out of a possible N transmit configurations (limited by the number in the frame), the sensing responder shall use in the transmission of the NDP announcement and NDP.
  The sensing responder shall use the same transmit parameters in the transmission of the NDP announcement and NDP to requests that have the same TX configuration set number.
  The transmit parameters used by the sensing responder for a given TX configuration set number is implementation dependent.
Other options could be defined.

## Slide 11: Other considerations: Scalability
Some WLAN sensing applications rely on the ability of a sensing initiator to measure multiple wireless links.
  Example: Home security, STAs in different rooms and floors.
Procedures could be defined that allow for a sensing initiator to request transmissions from multiple sensing responders simultaneously.
  Basic – possibly over simplistic – example:
Other approaches are possible, including those that make use of MU transmissions.
Sensing responders/
Sensing transmitters
Sensing initiator/
Sensing receiver

## Slide 12: Other considerations: Scheduling
WLAN sensing procedures/protocols that include scheduling will likely be defined.
  Certain WLAN sensing applications may have channel measurement periodicity requirements.
  Reduced overhead/improve scalability.
Procedure would likely include, depending on the WLAN sensing architecture and application, multiple phases, such as negotiation, polling, measurement, and reporting.
  Procedure proposed here could serve as a building block for measurement phase, for example.

## Slide 13: Conclusions
We proposed a request-and-response procedure in which a sensing initiator solicits a sensing responder to make a transmission with certain transmit characteristics that enable reliable WLAN sensing.
  Advantages: Transmit configuration freeze/hold, no loss due to feedback compression, and sounding of multiple antennas/streams.
More contributions on WLAN sensing channel measurements, such as those that include scheduling and MU transmission, are necessary.
  Proposed procedure may not be applicable or “optimal” to all WLAN sensing architectures and applications.
The proposed procedure can be built upon to define other procedures.

## Slide 14: References