## Slide 1: MLO BSS Information Transmission with and without Multiple BSSID
Date: 2020-06-01
Authors:
Name | Affiliations | Address | Phone | email
Liwen Chu Young Hoon Kwon Manish Kumar Hongyuan Zhang Yan Zhang Rui Cao Sudhir Srinivasa Hui-Ling Lou | NXP |  |  | 

## Slide 2: Recap: AP MLD with and without Multiple BSSID in Multiple Links
An AP MLD may support multiple BSSID feature in one link while not supporting multiple BSSID feature in another link.
ML element with Per Link Info elements is used to carry MLO information.
  ML element may not be carried in Beacon.
ML element may be carried in Multiple BSSID element.
Elements related to Multiple BSSID are not carried in Association Response frame.
AP MLD1
MAC with Addr11 (AP11)
MAC with Addr21 (AP21)
Common MAC
Link1
Link2
SAP of BSSID11 (addr11)
AP MLD2
MAC with Addr12 (AP12)
MAC with Addr22 (AP22)
Common MAC
Link1
Link2
SAP of BSSID12 (addr12)
AP MLD3
MAC with Addr13 (AP13)
MAC with Addr23 (AP23)
Common MAC
Link1
Link2
SAP of BSSID13 (addr13)
AP MLD4
MAC with Addr14 (AP14)
MAC with Addr24 (AP24)
Common MAC
Link1
Link2
SAP of BSSID14 (addr14)
APs with Addr11, 12, 13, 14 are not defined by a Multiple BSSID element.
APs with Addr21, 22, 23, 24 are defined by a Multiple BSSID element.

## Slide 3: Incomplete Information after Multi-Link Association
Every AP’s Beacon in the link without Multiple BSSID support carries the AP in another link that is affiliated with the same AP MLD as the Beacon transmitter.
  The AP in another link has non-transmitted BSSID.
Through the Probe Response in one link (e.g. link 1) without Multiple BSSID support, a STA MLD may not know the Multiple BSSID arrangement in another link:
  The Per Link Info for an AP in another link (e.g. link2) doesn’t include the Multiple BSSID element.
In the Association Response frame, the Multiple BSSID element and/or Multiple BSSID Configuration element are not carried.
AP MLD1
MAC with Addr11 (AP11)
MAC with Addr21 (AP21)
Common MAC
Link1
Link2
SAP of BSSID11 (addr11)
AP MLD2
MAC with Addr12 (AP12)
MAC with Addr22 (AP22)
Common MAC
Link1
Link2
SAP of BSSID12 (addr12)
AP MLD3
MAC with Addr13 (AP13)
MAC with Addr23 (AP23)
Common MAC
Link1
Link2
SAP of BSSID13 (addr13)
AP MLD4
MAC with Addr14 (AP14)
MAC with Addr24 (AP24)
Common MAC
Link1
Link2
SAP of BSSID14 (addr14)
APs with Addr11, 12, 13, 14 are not defined by a Multiple BSSID element.
APs with Addr21, 22, 23, 24 are defined by a Multiple BSSID element.
AP1x and AP2x are affiliated with one AP MLD.

## Slide 4: Incomplete Information after Multi-Link Association (Cont’d)
After association, the following features don’t work correctly:
  NAV maintenance.
    Some PPDUs from APs that are in same device with associated AP may be discarded.
  Rx Control Frame To MultiBSS doesn’t work correctly.
    The transmitted BSSID is not known.
AP MLD1
MAC with Addr11 (AP11)
MAC with Addr21 (AP21)
Common MAC
Link1
Link2
SAP of BSSID11 (addr11)
AP MLD2
MAC with Addr12 (AP12)
MAC with Addr22 (AP22)
Common MAC
Link1
Link2
SAP of BSSID12 (addr12)
AP MLD3
MAC with Addr13 (AP13)
MAC with Addr23 (AP23)
Common MAC
Link1
Link2
SAP of BSSID13 (addr13)
AP MLD4
MAC with Addr14 (AP14)
MAC with Addr24 (AP24)
Common MAC
Link1
Link2
SAP of BSSID14 (addr14)
APs with Addr11, 12, 13, 14 are not defined by a Multiple BSSID element.
APs with Addr21, 22, 23, 24 are defined by a Multiple BSSID element.
AP1x and AP2x are affiliated with one AP MLD.

## Slide 5: Methods to Acquire Full BSS Information (Cont’d)
The ML element in (Re)Association Response frame can carry the following information:
  the transmitted BSSID through Multiple BSSID Index,
  the MaxBSSID Indicator.
AP MLD1
MAC with Addr11 (AP11)
MAC with Addr21 (AP21)
Common MAC
Link1
Link2
SAP of BSSID11 (addr11)
AP MLD2
MAC with Addr12 (AP12)
MAC with Addr22 (AP22)
Common MAC
Link1
Link2
SAP of BSSID12 (addr12)
AP MLD3
MAC with Addr13 (AP13)
MAC with Addr23 (AP23)
Common MAC
Link1
Link2
SAP of BSSID13 (addr13)
AP MLD4
MAC with Addr14 (AP14)
MAC with Addr24 (AP24)
Common MAC
Link1
Link2
SAP of BSSID14 (addr14)
APs with Addr11, 12, 13, 14 are not defined by a Multiple BSSID element.
APs with Addr21, 22, 23, 24 are defined by a Multiple BSSID element.
AP1x and AP2x are affiliated with one AP MLD.

## Slide 6: Straw Poll
Do you support that the reported AP’s profile in the ML element in Association Response frame shall carry the following information if the reported AP is a non-transmitted BSSID: the non-transmitted BSSID index, the MaxBSSID Indicator?
  Signaling TBD