## Slide 1: AP MLD Beaconing and Discovery
Date: 2020-06-08
Authors:

## Slide 2: Motivation
The existing beaconing and discovery schemes need to be extended to allow:
  Fast discovery and multi-link setup between an AP MLD and a Non-AP MLD, while maintaining the support for legacy STAs to discover and associate to the AP MLD
  The multi-link maintenance (multiple associations maintenance) with AP MLD

## Slide 3: Background, AP discovery
Scanning STA likely starts scanning at the 2.4 GHz band
  Least number of 20 MHz channels
  APs operate in this band for legacy support
  Large transmission coverage enables APs discovery over large area
The scanning STA selects the 5 & 6 GHz scanned channels based on Out-of-Band Discovery, i.e. Reduced Neighbor Report (RNR)

## Slide 4: Example AP MLD and its beacon transmission

## Slide 5: Example of Beacon Content

## Slide 6: AP Discovery
STA needs to find an AP to be able to establish MLD setup with the AP MLD
  STA needs to discover at least one AP in AP MLD to initiate authentication and MLD Setup
The MLD link setup creates multiple links
  The MLD link setup signalling is transmitted over a single link

## Slide 7: Concern: AP MLD discovery over one link?
A Non-AP MLD may scan all links anyway to evaluate link quality
  To accelerate connection setup, the Non-AP MLD may start authentication and association on the first discovered link while evaluating other links
Once a Non-AP MLD discovers an AP MLD on one link, it may transmit a unicast ML Query management frame to the AP MLD to collect the co-located APs’ detailed capability and operation information

## Slide 8: Proposal: Address Hierarchy for AP MLD

## Slide 9: Proposal: Address Hierarchy for AP MLD
Beacon includes the address mask or linkID mask length (M), e.g. 0<M≤8
M=3

## Slide 10: Proposal: Address Hierarchy for AP MLD

## Slide 11: Reduced Neighbor Report
RNR includes all AP in other channels that belong to the same AP MLD.
AP in MLD AP field is set to 1 if the reported AP belongs to AP MLD.

## Slide 12: Parameters of other APs in AP MLD
Alternatives for other AP information in Beacon:
  A single Beacon carries a complete set of parameters of other APs in the same AP MLD
  A single Beacon carries a partial set of parameters of other APs in the same AP MLD
  A single Beacon carries basic info (e.g. RNR) and Check Beacon of other APs in the same AP MLD.
A Non-AP MLD may send additional query or scan other links to obtain detailed parameters of other APs.

## Slide 13: Proposal – Check Beacon
Check Beacon is one octet long field that is updated if a critical link specific AP parameter value changes

## Slide 14: Parameters of other APs in AP MLD

## Slide 15: Links maintenance

## Slide 16: Unavailable AP in AP MLD
The STA MLD needs to detect if an AP in another link becomes unavailable
  An AP in AP MLD may be unavailable, if the AP has sent Quiet element or Channel Switch Mode = 1
  Quiet element may indicate a duration, or repeating time when AP is not available
  Channel Switch indicates the new operating channel and the exact timing of the link switch
Associated non-AP MLDs would benefit to get details of the quiet time duration and/or the time when AP switches channel and the new channel of the AP

## Slide 17: Unavailable AP in AP MLD
A STA MLD have STAs in power save and it may receive Beacons only from a single AP
  STA must avoid transmissions to the unavailable AP
  The scanning STAs needs to avoid transmissions to unavailable AP
  The STA needs to detect if some AP is not available also through other links
The AP MLD should include Quiet element or Channel Switch element to signal the details of the AP in AP MLD that is not available
The AP should not include unavailable AP to Reduced Neighbor Report it transmits
  The legacy STAs do not actively scan the unavailable AP

## Slide 18: Secure MLD Query
MLD Query is used by EHT STAs to obtain securely the parameters of the APs in AP MLD
  MLD Query Response provides AP link/BSS specific operating parameters and BSS Load/AP performance parameters

## Slide 19: Secure MLD Query
Unprotected AP parameter queries (Probe Request, etc.) to query AP parameters in other link should be avoided
The requests have privacy concerns
  Probe Requests may reveal STA capabilities and STA may be tracked
The responses may not be secure
  Probe Responses are not encrypted, and they do not have integrity protection
  It is very simple attack to send broadcast Probe Response with wrong parameter values

## Slide 20: Challenges of Probe request and Response in MLD Query
Probe Response must contain parameters of the transmit BSS and non-transmit BSSs
  A lot of information of the APs in the same link are added to probe response
  Only single BSS information may be relevant for the associated STA MLD
Broadcast probe response could be misused in 20 TU unsolicited broadcast Probe Response signaling
  This signaling has large management frame overhead, if BC Probe Responses contain parameters of other APs in AP MLD

## Slide 21: Example of MLD Query use in fast MLD Setup
The STA needs to get service from the AP immediately
  No time to setup Pre-Association Secure Negotiation (PASN)
STA MLD may simultaneously scan other channels while it is doing MLD Setup
  Multiple STAs may allow simultaneous link specific operations
STA may query AP parameters in other links after the MLD Setup
  Query frames are transmitted as protected management frames (PMF)
  STA gets service from the associated AP

## Slide 22: Summary
Only small changes are needed to legacy discovery to support AP MLD discovery and link maintenance
Due to large number of transmitted Beacon frames, the beacon size should be minimized
  The MAC Address hierarchy enables BSSID fields to carry MLD MAC Address and LinkIDs
  The Check Beacon indicates whether STA should obtain the link specific AP parameters
  The Reduced Neighbor Report indicates other APs availability
Secure MLD Query is used to maintain the parameters of APs in AP MLD

## Slide 23: Straw Poll 1
802.11be shall define a request and response signaling that uses Protected Management Frame (PMF) frames to query AP link specific parameters or AP MLD parameters.
Note: The exact frame formats are TBD.

## Slide 24: Straw Poll 2
802.11be shall define address hierarchy for EHT AP MAC Addresses as shown in slide 9:
- LinkId is included in the Octet 4 of the AP link specific addresses
- The AP MLD MAC address can be punctured from the link specific MAC addresses

## Slide 25: Straw Poll 3
802.11be shall have means to provide information of an AP in AP MLD that is silencing its associated STAs by:
- Signaling the Quiet Element, Channel Switch Element and identifier of the silencing AP in Beacons of all APs in AP MLD
- If an AP in AP MLD is silencing all associated STAs, then other APs in the AP MLD do not include the AP in the Reduced Neighbor Report element they transmit