## Slide 1: MLD Discovery follow up
Date: 2020-05-26
Authors:
Name | Affiliations | Address | Phone | email
Young Hoon Kwon Liwen Chu Manish Kumar Hongyuan Zhang Yan Zhang Rui Cao Sudhir Srinivasa Hui-Ling Lou | NXP |  |  | 

## Slide 2: Recap:
Following consensus has been made on MLO discovery:
  Do you agree that all APs that are part of the same MLD as the reporting AP and that are collocated with the reporting AP shall be reported in the RNR element that is included in the beacons and the broadcast probe responses transmitted by the reporting AP?
    Note: an AP is not included if it is not discoverable
    Note: RNR provides basic information (operating class, channel, BSSID, short SSID, …)
  Do you agree to define a mechanism for a STA of a non-AP MLD to send a probe request frame to an AP belonging to an AP MLD, that enables to request a probe response from the AP that includes the complete set of capabilities, parameters and operation elements of other APs affiliated to the same MLD as the AP
    The complete information is defined as all elements that would be provided if the reported AP was transmitting that same frame (exceptions TBD)
    It’s TBD if the AP is mandated or not to respond with the requested information
  Do you agree to define a new Multi-Link element (MLE) to report/describe multiple STAs of an MLD with at least the following characteristics?
    MLD-level information may be included
    A STA profile subelement is included for each reported STA (if any) and is made of a variable number of elements describing this STA
In this contribution, we discuss further on details on RNR and ML elements in Beacon and Probe Request/Response frames.

## Slide 3: RNR element
RNR element shall be included in a Beacon frame from an EHT AP.
A STA profile of an ML element includes elements describing a reported AP.
  If the STA profile indicates complete information, all elements that would be included in the reported AP’s Beacon frame will be included (exceptions TBD).
  As RNR element shall be included in a Beacon frame, it may imply that RNR element will be included in each STA profile of the ML element.
However, RNR elements from co-located APs are most likely duplicated.
  If Beacon and/or Probe Response frame includes RNR element, it is not useful to include additional RNR element in each STA profile of ML elements that included in the Beacon and/or Probe Response frame.
  Similar reason, in 11ax RNR element is not included in the multiple BSSID element:
    An AP with dot11MultiBSSIDImplemented equal to true shall not include Reduced Neighbor Report element in the Nontransmitted BSSID Profile subelement of the Multiple BSSID element.
We propose:
  An AP shall not include a RNR element in a STA profile subelement of a Multi-Link (ML) element.

## Slide 4: ML/MBSSID elements
When a non-AP STA requests a complete information of co-located APs of a reporting AP, a Probe Response frame will include
  Multiple BSSID element
    Each Nontransmitted BSSID profile subelement in the Multiple BSSID element indicates complete information of corresponding AP on the same link.
  ML element
    Each STA profile subelement in the ML element indicates complete information of corresponding AP on other link.
It is still not clear how to include some reported AP in which element as there are quite many different configurations of co-located APs.

## Slide 5: ML/MBSSID elements
When a non-AP MLD sends a Probe Request to a reporting AP (AP11) requesting complete information of other APs, which APs to be included?
  All co-located APs with the reporting AP?
    (AP21/12/22/32/23/33)
  APs affiliated with the same AP MLD? (AP21)
  APs within the same BSSID set? (AP12)
  How about
    Co-located APs that are affiliated with different AP MLD? (AP12/22/32)
    Co-located APs that are within the different BSSID set? (AP32/33)
    APs within the same BSSID set of an AP that is affiliated with the same AP MLD? (AP22/23)
    APs that is affiliated with the same AP MLD with an AP within the same BSSID set? (AP22/32)
It would be helpful if the non-AP MLD can indicate which APs the reporting AP should include in the response frame.
  All APs, specific AP, within the same AP MLD, …
 | MLD1 | MLD2 | 
LInk1 | AP11(T) | AP12(N) | 
Link2 | AP21(N) | AP22(T) | AP23(N)
Link3 |  | AP32(T) | AP33(N)

## Slide 6: ML/MBSSID elements
Operation example
  STA sends a Probe Request to AP11 requesting complete information.
  Probe Response from AP11 will include:
    Elements of AP11
    ML element including
      STA profile for AP21 including
        Elements of AP21
        MBSSID element including (?)
          Nontransmitted BSSID profile for AP22 including
            Elements of AP22
            ML element including
              STA profile for AP12 including …
    MBSSID element including
      Nontransmitted BSSID profile for AP12 including
        Elements of AP12
        ML element including (?)
          STA profile for AP22 including
            Elements of AP22
            ML element including
              STA profile for AP12 including …
 | MLD1 | MLD2
Link1 | AP11(T) | AP12(N)
Link2 | AP21(T) | AP22(N)

## Slide 7: ML/MBSSID elements
To avoid duplicated indication:
  An ML element shall not be included in a STA profile of another ML element.
  When an AP that is affiliated with an AP MLD transmits a frame that includes a ML element, if an information of a reported AP in the ML element is to be duplicated in the frame, the AP does not include the information of the reported AP more than once in the frame.
    The STA profile of the reported AP may include an indication that information of the reported AP is included elsewhere in the frame.

## Slide 8: ML/MBSSID elements
Operation example with restriction
  STA sends a Probe Request to AP11 requesting complete information.
  Probe Response from AP11 will include:
    Elements of AP11
    ML element including
      STA profile for AP21 including
        Elements of AP21
        MBSSID element including
          Nontransmitted BSSID profile for AP22 including
            Elements of AP22
    MBSSID element including
      Nontransmitted BSSID profile for AP12 including
        Elements of AP12
        ML element including
          STA profile for AP22 including
            Indication that information of AP22 is included in other place.
 | MLD1 | MLD2
Link1 | AP11(T) | AP12(N)
Link2 | AP21(T) | AP22(N)

## Slide 9: Summary
Duplicated RNR/ML/MBSSID elements in a Probe Response frame are discussed.

## Slide 10: SP1
Do you agree to add the following to 11be SFD:
  An AP shall not include a RNR element in a STA profile subelement of a Multi-Link (ML) element.

## Slide 11: SP2
Do you agree to add the following to 11be SFD:
  An ML element shall not be included in a STA profile of another ML element.

## Slide 12: SP3
Do you agree to add the following to 11be SFD:
  When an AP that is affiliated with an AP MLD transmits a frame that includes a ML element, if an information of a reported AP in the ML element is to be duplicated in the frame, the AP does not include the information of the reported AP more than once in the frame.
    The STA profile of the reported AP may include an indication that information of the reported AP is included elsewhere in the frame.