## Slide 1: Discussion on WLAN sensing evaluation methodology
Date: 2020-06-23
Authors:
Name | Affiliation | Address | Phone | Email
Rui Du | Huawei Technologies Co. Ltd | F3, Huawei Base, Shenzhen, China |  | Ray.du@Huawei.com
Meihong Zhang |  |  |  | 
Chenchen Liu |  |  |  | 
Yingxiang Sun |  |  |  | 
Danny Kaipin Tan |  |  |  | 
Edward Au |  |  |  | 

## Slide 2: Outline
Abstract
The discussion of SENS draft amendment
Example1: Evaluation Methodology at sub 7 GHz
Example2: Evaluation Methodology at 60 GHz
Main contains of evaluation methodology
How about for SENS ?
Summary
References
Rui Du, et al. (Huawei)

## Slide 3: Abstract
Discussion on SENS’ draft amendment development process has started during the meeting on April 14[1].
Detail information about evaluation methodology documents from several task groups is provided in this presentation.
Some initial ideas about evaluation methodology for SENS is discussed in this slides.
Rui Du, et al. (Huawei)

## Slide 4: The discussion of SENS draft amendment
The potential documents that SENS SG (or the future TG) would consider[1].
Usage model
Channel model
Functional requirements
Evaluation methodology
Specification framework
Draft amendment
Coexistence Assurance

## Slide 5
Example1: Evaluation Methodology at sub 7 GHz
Rui Du, et al. (Huawei)
TG ac’s evaluation methodology and simulation scenarios [2]:
PHY performance:
PHY Channel model(reuse 802.11n),
Hardware impairments(reuse 802.11n),
Comparison criteria.
Traffic models: consider traffic model defined in 802.11n and including high quality videos for VHT and high speed file transfer.
Simulation scenarios: in-home entertainment application, enterprise network.
Comparison criteria:
(Link level) PER vs. SNR,
(System level) aggregated throughput, throughput of each flow, packet loss.
TG ax’s evaluation methodology and simulation scenarios [3]:
PHY performance
PHY Channel model(an outdoor channel model is added),
Hardware impairments,
Comparison criteria.
Traffic models: full buffer model is baseline, FTP model and mix of small and large packet should also be considered.
Simulation scenarios[4]: residential scenario, enterprise scenario, indoor small BSS, outdoor large BSS, outdoor large BSS+residential.
Comparison criteria:
(Link level) PER vs. SNR,
(System level) STA/BSS throughput, packet loss, latency, per STA energy per transmit bit, per STA energy per receive bit.

## Slide 6
Example2: Evaluation Methodology at 60 GHz
Rui Du, et al. (Huawei)
TG ad’s evaluation methodology and simulation scenarios [5]:
PHY performance
PHY Channel impulse response,
Hardware impairments,
Comparison criteria(PER vs. SNR).
System evaluation
Traffic models(high throughput traffic): uncompressed video, lightly compressed video, local file transfer, web browsing, hard disk file transfer.
Simulation scenarios: home living room, office conference room, enterprise cubicle.
Comparison criteria: goodput (aggregate and per flow), delay, packet loss rate.
TG ay’s evaluation methodology and simulation scenarios [6]:
PHY performance
PHY Channel impulse response,
Hardware impairments,
Comparison criteria(PER vs. SNR).
System evaluation:
Traffic models: lightly compressed video, backhaul traffic, local file transfer, productivity docking, web browsing, hard disk file transfer, gaming.
Simulation scenarios:
(PHY-layer SLS scenarios) outdoor open area deployment, street canyon, hotel lobby.
(MAC-layer SLS scenarios) dense indoor D2D deployment, enterprise cubicle, dense indoor BSS deployment, sparse outdoor BSS deployment.
3. Comparison criteria: goodput (aggregate and per flow), delay, packet loss rate.

## Slide 7: Main contents of evaluation methodology
All the examples above on indicate the evaluation methodology documents mainly contain,
Channel model to be adopted;
Hardware impairment;
Traffic model;
Simulation scenarios;
Comparison criteria for LLS and/or SLS;
…

## Slide 8
How about for SENS ?
Rui Du, et al. (Huawei)
A ‘new’ channel model may be needed for sensing simulation
A moving target should be included in the channel model for device free sensing.
Hardware impairment
Could be same with 802.11ax and 802.11ay.
Traffic model
No traffic model (similar with 11az).
Similar traffic model with 11ax and 11ay if communication performance also need to be considered.
Simulation scenarios
The use cases of SENS SG(or future TG) spans widely, which lead to a large number of simulation scenarios. Which scenarios should be adopted by the group?
Comparison criteria for LLS and/or SLS
Which performance characteristics should be adopted to evaluate the performance from different contributions?
Accuracy,
Latency,
…

## Slide 9: Summary
In this slides, the detail structure of evaluation methodology documents from other TGs both at sub 7 GHz and 60 GHz is analyzed.
Some initial ideas about the evaluation methodology for SENS are presented and discussed.
Rui Du, et al. (Huawei)

## Slide 10: References
[1] 11-20-0602-01-SENS-discussion-on-wlan-sensing-draft-amendment-development-process.pptx
[2] 11-09-0451-16-00ac-tgac-functional-requirements-and-evaluation-methodology.doc
[3] 11-14-0571-12-00ax-evaluation-methodology.docx
[4] 11-14-0980-16-00ax-simulation-scenarios.docx
[5] 11-09-0296-16-00ad-evaluation-methodology.doc
[6] 11-15-0866-04-00ay-11ay-evaluation-methodology.doc
Rui Du, et al. (Huawei)