## Slide 1: Multilink Traffic Stream (TS) Operation
Date: 2020-06-29
Authors:
Rev 1: Incl. Q&A on the July 15th confcall (P.14) and comparison between TS and SCS (P.15); SPs are amended as well;

## Slide 2: Single Link TS Operation Overview
Traffic Stream (TS) is established between SMEs by using ADDTS request and response frames
MSDUs within a TS should be delivered subject to the QoS parameter values provided to the MAC in a particular TSPEC.
  TSPEC is a result of negotiation, based on actual requirements from one or more applications as well as actual MAC and PHY capabilities
  MAC entities determine the TSPEC applicable for delivery of MSDUs belonging to a particular TS using the priority parameter provided with those MSDUs at the MAC SAP.
TSPEC is accountable to enable scheduling and admission control for MAC data services
  Admission control can be applied to both EDCA and HCCA;
Traffic Classification (TCLAS) is used to associate a Layer-2 traffic stream to a higher layer application, or a category of applications
TID (8-15) = TSID comes from the ‘priority’ parameter at the MAC-SAP along with an MSDU；

## Slide 3: .11 Amendments on TS Operation
Firstly introduced by 802.11e
In support of Fast BSS transition by 802.11r
In support of Service Provider Interface (SSPN) and Expedited Bandwidth Request (EBR) by 802.11u
U-APSD Coexistence by 802.11v
Higher layer stream ID and AP-initiated ADDTS by 802.11aa
DMG extensions by 802.11ad for SP allocation
In support of MU transmission by 802.11ax

## Slide 4: QoS Architecture
The priority parameter specifies the requested priority of the data unit transfer.
The drop eligible parameter provides guidance on whether this request can be discarded in preference to other requests when there are insufficient resources in a STA.
Priority parameter carried by TID
  priority(TID)=0-7, interpreted as UP
  priority(TID)=8-15, provided as TSID, UP can be found in TSPEC (TS info subfield)
TS management primitive
MAC data service
TSPEC element {
Element ID,
Length,
TS info,
Nominal MSDU size,
Max MSDU size,
Min service interval,
Max service interval,
Inactivity Interval,
Suspension interval,
Service start time,
Min data rate,
Mean data rate,
Peak data rate,
Burst size,
Delay bound,
Min PHY rate,
Surplus bandwidth allowance,
Medium time,
DMG attributes
}
TS info{
Traffic type,
TSID,
Direction,
Access policy,
Aggregation,
APSD,
User priority,
TS info ACK policy,
Schedule,
Reserved,
}

## Slide 5: MLD QoS Architecture
Regarding a single MAC-SAP
  A common description about the higher layer data streams, for both traffic characteristics and QoS requirements;
  One data stream associates with one TS setup, re-using ADDTS REQ/RES;
  MLD level admission control policy (for both EDCA and HCCA);
Regarding multiple links
  Per-link resource reservation (allocation/schedule);
  Per-link channel access mechanism;
  Follow TID-to-Link mapping principles;

## Slide 6: TSPEC is Neither Scalable Nor Flexible
TS setup is basically a procedure to exchange and negotiate TSPEC between MAC entities
Basic TSPEC element contains the set of parameters that define the characteristics and QoS expectations of a traffic flow, in the context of a particular STA.
  Basic TSPEC is optional when DMG TSPEC is present in ADDTS request and response
DMG TSPEC element contains the set of parameters needed to create or modify an airtime allocation.
Basic TSPEC
DMG TSPEC
Schedule (Allocation) info

## Slide 7: Basic TS Setup
STA initiated setup:
Basic ADDTS request/response
HC co-located with AP
Requested TSPEC
Admitted TSPEC (medium time & schedule)

## Slide 8: DMG TS Setup
STA initiated setup:
DMG ADDTS request/response
HC co-located with AP
Requested Allocation
Admitted Allocation
DMG
DMG

## Slide 9: Multi-link TS Setup (1)
Non-AP MLD is built with full protocol stack, thus can have more information about the higher layer
Non-AP MLD should coordinate with AP MLD for more efficient use of the resources, with regards to the traffic characteristics and QoS requirements
Similar to other layer management functions, it is preferred to have a single TS setup between MLDs among multiple links.
  ADDTS information exchange can be re-used on one selected link (maybe same as other management frame handshake)
  Schedule/Allocation are established on the one or more links
  Admission control policy should be implemented at MLD level
A flexible and scalable TSPEC variant for multilink shall be defined
  Separate the common specification for traffic characteristics, associated with MAC-SAP and per-link schedule/allocation based on individual link capabilities.
  Similar idea is also considered in [1]

## Slide 10: Multi-link TS Setup (2)
STA1
STA2
SME
Non-AP MLD
SME
AP MLD
STA1
STA2
ML ADDTS Req
w/ one TSPEC
{ML-TSPEC(STA1, STA2) }
{ML-TSPEC(STA1-Sch, STA2-Sch)}
ML ADDTS Res
ML ADDTS Req
w/ multiple TSPEC
{ML-TSPEC(STA1), ML-TSPEC(STA2)}
{ML-TSPEC(STA1-Sch), ML-TSPEC(STA2-Sch)}
ML ADDTS Res
Option 1
Option 2
Re-design TSPEC for multilink
Re-use TSPEC for multilink

## Slide 11: Considerations on Other ADDTS Action Fields
Action Fields | Attributes | Basic ADDTS request | Basic ADDTS response | Note | Suggested Revision for Multi-link
TSPEC | Mandatory | Y | Y | Interface between MAC and higher layer | Shall
TCLAS (+ processing) | Optional | Y | Y | Higher layer related | May not
Intra AC priority | Optional | Y | -- |  | 
Higher layer stream ID | Only in AP initiated TS setup | Y | Y |  | 
U-PID | Optional | Y | Y |  | 
U-APSD coexistence | Optional | Y | -- | Specific to APSD | May
EBR | Optional | Y | Y | Specific to emergency service | May
Multi-band | Optional | Y | Y | DMG extensions | No need
Multiple MAC sublayer | Optional | Y | Y |  | 
TS delay | Mandatory | -- | Y | Delay for another retry | No need
Schedule | Optionally present if SUCCESS | -- | Y | Specifies the schedule information, service start time, SI, etc. | Should

## Slide 12: 11be Passed Motions
802.11be defines multi-link operation to better utilize the frequency band to enable high throughput low latency data transmission
Directional TID-to-link mapping mechanism allows the transmission of a specific TID to be carried on multiple links
  By default, after the multi-link setup, all TIDs are mapped to all setup links.
  The multi-link setup may include the TID-to-link mapping negotiation.
A single BA agreement is established between MLDs for a TID to be transmitted over one or more links
  Setup BA agreement by using ADDBA request and response frames

## Slide 13: Summary
TS operation shall be able to utilize the multilink capabilities provided by 11be
A consistent framework for multilink management is required regarding TS operation
  A single TS is established between MLDs for a TSID to be transmitted over one or more links
  TS setup procedure shall be re-using ADDTS request and response frames
  Successfully established TS triggers BA agreement to be setup on the same links
T(S)ID-to-link mapping rules
  Following the same rules defined for TID-to-link mapping
  A TS can be setup on any available links subject to admission control policy
  TS setup may update the TID-to-link mapping
Admission control should take into account the total capabilities of all available links

## Slide 14: Q&A on July 15th Confcall
Q: Direction of the contribution is correct, to use what in current spec to support low latency, we have a similar high level contribution in the queue. On slide 10, TSPEC is to convey the QoS demand and traffic pattern. Why use individual information for STA 1 and 2? What is specific for STA 1 and 2?
A: The scheduling infor (blue boxed field on slide 6) is per link. For example the ‘medium time’ field in TSPEC. The AP grants medium (air) time for the specific STA in support of the common traffic stream.
Q: TSPEC should be applied to MLD level, for medium time, the STA side may not know about it, rather AP can have more information because it is aware of the whole network.
A: Correct. STA signals the resource need for its higher layer traffic and AP allocates per link resources for individual STA. So the TSPEC variant needs to convey multiple per-link schedule (resource) infor during setup.
Q: Question on SP2, when you say TID 8-15, do you mean to reserve TSPEC only for these TIDs, BTW 15 and 14 has been taken? Why do you call out these TIDs?
A: TID 8-15 is interpreted as TS ID in current spec, and each TS is associated with a TSPEC and TS setup. This SP proposes to keep the consistency.
Q: It depends on whether the TSPEC map to a specific TID, so does it matter to use a TID or not to support low latency?
A: The high layer data streams need to be identified by MAC together with their QoS requirements first so that the proper MAC mechanism can be configured and resources can be allocated.
Q: Are you saying for TID<8 don’t do TSPEC or you allow to do TSPEC. For TID 8-15, TSPEC is mandated.
A: For keeping consistency with current spec, TID>7 is used to identify data streams with higher QoS requirement. In such cases, TSPEC or its variants should be associated.
Q: TSPEC should be implemented at MLD level, not the station level. Maybe it can be simplified the use of TSPEC in this context.
A: As explained on slide 6, part of TSPEC information is about MLD, and the other part is about link specific information. Both should be included in the next revision of TSPEC. But TS should setup at the MLD level for sure. Trying to separate TS and TSPEC in this context.
Q: We have a similar contribution, sort of aligned at the high level. Also think the QoS should be negotiated at the MLD level. Also thinks TID 8-15 should be reused for low latency traffic. But TSPEC may not be the right mechanism, because of negative effect of HCCA. Maybe other signaling is better, like SCS is more suitable. Need to discuss more. Agree on SP1 and 2 if remove the TS part.
A: We consider TS setup as a way of QoS negotiation, not something tied up with HCCA. One example is that in 11ax, it is used to assist AP scheduling. Will look into SCS and do more investigation.
Q: The path on how to extend TS to MLD is useful, correct direction, but how we use that is not clear. Need to clarify how the mechanism to work in MLD. Suggestion to avoid TID used in 11ax, change to TID >7. There is another contribution passed SP to use specific TID for NS, not sure if ADDTS is required to send anything belong to that TID value. Need more discussion on how to include that idea or single its out.
A: Agree, need to think more about the channel access. Regarding the NS service, the passed SP doesn’t rule out the use of TS.
Q: Need to confirm that for SP1, if TID 8-15 is exclusively for MLD or can also used for MLD.
A: All TID shall be used. TID is precious for identifying data stream to PHY/MAC.

## Slide 15: TS vs. SCS
 | TS | SCS
MLME Primitive | Yes | Yes
Actions | Add, Delete, Reserve | Add, Remove, Change
Initiator | Non-AP, AP | Non-AP
w/ TCLAS (processing) | Yes | Yes
w/ TSPEC | Yes | No
QoS infor | Yes | No
w/ Intra-AC Priority | Yes | Yes
Multi-purpose | Yes | No
Efficiency | 1 setup for 1 TS | 1 setup for Multiple SCS
SCS is a restricted version of TS with elements partial from TS, but it points a way to enhance TS for 11be MLO.

## Slide 16: SP#1
Do you agree that a multi-link TS setup is required to transmit QoS Data frames with TID >7 for 11be MLD?
  Note: Detail procedure and frame format in the multi-link TS setup is TBD.

## Slide 17: SP#2
Do you agree that a single TS that is negotiated between two MLDs for a TID > 7 that may be transmitted over one or more links?

## Slide 18: SP#3
Do you agree to use the container ADDTS Request and Response, TSPEC or their variants to setup or update a TS for the 11be MLD?
  Note: Detail format of frames and information elements are TBD.

## Slide 19: SP#4
Do you support to define the admission control policy to be implemented at the MLD level?

## Slide 20: Reference
20-0418r1, Low latency service in 802.11be
20-0408r4, Prioritized EDCA Channel Access Over Latency Sensitive Links in MLO
20-0566r30, Compendium of straw polls and potential changes to the Specification Framework Document