## Slide 1: On 52+26 M-RU
Date: 2020-06-19
Authors:
Name | Affiliations | Address | Phone | email
Ron Porat | Broadcom |  |  | ron.porat@broadcom.com

## Slide 2: Discussion
M-RU for 52+26 is currently defined in the SFD (14 lines in the RU table)
Propose to add one more combination (one line in the RU table) involving 52+26.
Enterprise networks extensively use 20MHz, 40MHz and 80MHz (especially in 6GHz) in deployments and it is important for them to be able to send 4 equal users in 20MHz.
In 11ax this was done by using this combination [52 52 – 52 52] at a loss of 11% Tput. This particular combination was also used for testing and therefore preferably preserved in 11be.
However, it is important that 11be allows the following combination [52 (52+26) 52 52] to improve efficiency of OFDMA in that important use case.
This can easily be facilitated since STA is mandated to support a 52+26 M-RU
  AP can still choose to use the combination [52 52 – 52 52]

## Slide 3: Straw Poll
Do you support adding the following combination [52,52+26,52,52] to the RU table to be used in 20MHz, 40MHz and 80MHz PPDU?
  Editorial note - propose to replace colors in RU table by merging the cells of small M-RU and using the notation 78 and 132