## Slide 1: Partial Bandwidth Feedback for Multi-RU
Date: 2020-07-01
Authors:

## Slide 2: Introduction
802.11be shall supports that
  Wideband band and noncontiguous spectrum utilization
  Large size RU combination assigned to a single STA [1].
  Maximum 16 spatial stream
Feedback overhead is significantly increased, compared to 11ax [2]
In order to reduce feedback overhead, the partial BW feedback is adopted in 11ax as an optional feature
  Partial BW feedback
    By choosing [RU Start Index, RU End Index] to cover the allocated RU only, feedback overhead can be reduced compared with full BW feedback
In this slide, we show a modified signaling for partial BW feedback for multi-RU combination in 802.11be

## Slide 3: Recap: HE NDP Announcement Frame
AP signals the partial BW info subfield in NDPA
  AP signals RU Start Index (the first 26-tone RU) and RU End Index (the last 26-tone RU) for feedback
  STA feedbacks channel information (CSI) in the tones between RU Start Index and RU End Index
  STA Info subfield: 4 byte

## Slide 4: Update for EHT NDPA
Based on the HE NDPA, EHT NDPA can be designed by updating following subfields:
  Sounding Dialog Token
    1: HE, 2: EHT, 3: Reserved
  Disambiguation
    Disambiguation subfield is set to 1 to prevent a VHT STA from wrongly identifying its AID in the HE/EHT NDPA, which will be positioned in
    B(16*n+11) for n=1,2… (i.e., B(27), B(43), B(59),…)
  Nc
    3bit  4bit (for 16 spatial streams support)
  Partial BW Info subfield
    14bit  16bit (for 320MHz support)
    Applicable only for option #1 and option #2 in slide 6 and 7
  “Feedback Type and Ng” and “Codebook Size”
    TBD

## Slide 5: Partial BW feedback for Multi-RU: Motivation
If scheduling algorithm determines to allocates 484+2996 RU for STA #1 and 484 RU for STA #2 with 240MHz OFDMA in 11be.
  Wasteful to feedback entire 240MHz by STA #1
Proposal
  AP signals separate indications for each non-adjacent subband (i.e., set of contiguous RUs) on which it would like to request feedback
  No need to feedback the CSI on the 2nd 484 RU by STA #1
    Can reduce ~2,000 byte in CSI feedback (8x2, HE, SU, Fine codebook, Ng=4)
    Can be reduced further for larger inter-subband width and number of streams
 | Partial BW Info | 
 | RU Start Index | RU End Index
STA Info 1 | 0 | 111
STA Info 2 | 18 | 35
Feedback by STA #1
996
484
484
996
0 …
…
RU index
18 … 35
… 111
Feedback by STA #2

## Slide 6: Partial BW feedback for Multi-RU: Option #1
B0 |  | B27 |  |  |  | B43 | B47
AID11 (11) | Partial BW Info #1 (16) | Disambiguation (1) | Feedback Type And Ng (TBD) Codebook Size (TBD) Nc (4) | Partial BW Info #2 Present (1) | Reserved (TBD) | Disambiguation (1) | Reserved (TBD)
Duplicated STA Info subfield for one STA
  Each Partial BW Info subfield indicates [RU Start Index, RU End Index] corresponding to each the non-adjacent subband respectively.
  Following STA Info subfield is present if the Partial BW Info #2 Present subfield is equal to 1
  STA Info subfield: 6 byte or 12 byte
Frame Control | Duration | RA | TA | Sounding Dialog Token | STA Info 1 | …. | STA Info n | STA Info n | FCS
Octets: 2 | 2 | 6 | 6 | 1 | TBD |  | TBD | TBD | 4
B0 |  | B27 |  |  |  | B43 | B47
AID11 (11) | Partial BW Info #2 (16) | Disambiguation (1) | Feedback Type And Ng (TBD) Codebook Size (TBD) Nc (4) | Partial BW Info #2 Present (1) | Reserved (TBD) | Disambiguation (1) | Reserved (TBD)

## Slide 7: Partial BW feedback for Multi-RU: Option #2
Add one more “Partial BW info subfield” for the non-adjacent sub band.
  STA Info subfield: 8 byte
Frame Control | Duration | RA | TA | Sounding Dialog Token | STA Info 1 | …. | STA Info n | FCS
Octets: 2 | 2 | 6 | 6 | 1 | TBD |  | TBD | 4
B0 |  | B27 |  |  | B43 |  | B59 | B63
AID11 (11) | Partial BW Info #1 (16) | Disambiguation (1) | Nc (4) Feedback Type And Ng (TBD) Codebook Size (TBD) | Reserved (TBD) | Disambiguation (1) | Partial BW Info #2 (16) | Disambiguation (1) | Reserved (TBD)

## Slide 8: Partial BW feedback for Multi-RU: Option #3
Use the RU allocation map
  “RU allocation subfield” along with bandwidth information can identify the size and the location of the RU, for which the beamformer is requesting feedback
    In [3], proposed the 9-bit RU Allocation subfield for Trigger frame to indicate the multi-RU combinations in EHT.
  Provide a table mapping the allocated RU to subcarrier indices [S, E]
    [S, E] tones may lie outside the RU to avoid extrapolation
  STA Info subfield: 4 byte
B0 |  |  | B27 |  | B31
AID11 (11) | RU allocation subfield (9) | … | Disambiguation (1) | Nc (4) Feedback Type And Ng (TBD) Codebook Size (TBD) | Reserved (TBD)
Frame Control | Duration | RA | TA | Sounding Dialog Token | STA Info 1 | …. | STA Info n | FCS
Octets: 2 | 2 | 6 | 6 | 1 | TBD |  | TBD | 4

## Slide 9: Example of the Mapping Table for Option #3
A table for mapping allocated RU to subcarrier indices [S, E]
  The table can be made separately according to the grouping size (Ng)
  Detailed implementation of the table is TBD
[Arrangement of RU Index]

## Slide 10: Update for EHT MIMO Control Field
Based on the HE MIMO control field, EHT MIMO control field can be designed by updating following subfields:
  Nc, Nr
    3bit  4bit (for 16 spatial streams support)
  BW
    0: 20MHz, 1: 40MHz, 2: 80MHz, 3: 160MHz, 4: 320MHz
    2bit  3bit
  Partial BW Info subfield
    14bit  16bit (for 320MHz support)
    Applicable only for option #1 and option #2 in slide 11
  Disallowed Subchannel Bitmap
    0 or 8bit  0 or 16bit (for 320MHz support)
  Others
    TBD

## Slide 11: Update for MIMO Control Field
EHT MIMO Control field format
  For Option #1 and Option #2
    [2nd RU Start Index, 2nd RU End Index] are present if the 2nd RU Start-End Index Present is equal to 1
  For Option #3
    RU Allocation Subfield (9bit)
RU Start Index | RU End Index | Sounding Dialog Token Number | Disallowed Subchannel Bitmap Present | 2nd RU Start-End Index Present | Reserved | Disallowed Subchannel Bitmap | 2nd RU Start Index | 2nd RU End Index | Reserved
8 | 8 | 6 | 1 | 1 | 3 | 0 or 16 | 8 | 8 | TBD
RU Allocation Subfield | Sounding Dialog Token Number | Disallowed Subchannel Bitmap Present | Reserved | Disallowed Subchannel Bitmap | Reserved
9 | 6 | 1 | 3 | 0 or 16 | TBD
Nc | Nr | BW | Grouping | Codebook Information | Feedback Type | Remaining Feedback Segments | First Feedback Segment | …
4 | 4 | 3 | TBD | TBD | 2 | TBD | 1 | 

## Slide 12: Summary
In this slide, we proposed a modified signaling for the partial BW feedback to reduce feedback overhead in multi-RU combination
  Option #1
    Duplicated STA Info subfield for one STA
    STA Info subfield: 6 byte or 12 byte
  Option #2
    Add one more Partial BW info subfield for non-adjacent subband
    STA Info subfield: 8 byte
  Option #3
    Use the RU allocation subfield
    STA Info subfield: 4 byte

## Slide 13: SP #1
Do you agree to modify the EHT NDPA and EHT MIMO control field as following?
  EHT NDPA
    Sounding Dialog Token
      1: HE, 2: EHT, 3: Reserved
    Nc : 4bit
  EHT MIMO control field
    Nc : 4bit
    Nr : 4bit
    BW: 3bit
      0: 20MHz, 1: 40MHz, 2: 80MHz, 3: 160MHz, 4: 320MHz
    Disallowed Subchannel Bitmap: 0 or 16bit
  Y / N / Abstain

## Slide 14: SP #2
Do you support that the STA Info. Subfield in the NDPA frame will include separate partial BW feedback indications for each non-adjacent subband (i.e., set of contiguous RUs) in the multi-RU on which it would like to request feedback?
  Y / N / Abstain

## Slide 15: SP #3
For the separate indication of the partial BW feedback, which option do you support in NDP Announcement frame and MIMO Control Field?
  Option #1
    Duplicated STA Info subfield for one STA
    STA Info subfield: 6 byte or 12 byte
  Option #2
    Add one more Partial BW info subfield for non-adjacent subband
    STA Info subfield: 8 byte
  Option #3
    Use the RU allocation subfield
    STA Info subfield: 4 byte

## Slide 16: Reference
[1] 802.11-20/0566r23, Specification Framework for TGbe.
[2] 802.11-19/0828r4, Feedback Overhead Analysis for 16 Spatial Stream MIMO
[3] 802.11-20/0828r0, RU Allocation Subfield Design for EHT Trigger Frame

## Slide 17: Appendices

## Slide 18: Example of Option #1 and Option #2
If scheduling algorithm determines to allocates 484+2996 RU for STA #1 and 484 RU for STA #2 with 240MHz OFDMA in 11be
 | Partial BW Info #1 |  | Partial BW Info #2 | 
 | RU Start Index | RU End Index | RU Start Index | RU End Index
STA Info 1 | 0 | 17 | 36 | 111
STA Info 2 | 18 | 35 | - | -
996
484
484
996
0 … 17
36 …
RU index
18 … 35
… 111
Feedback by STA #1
Feedback by STA #1
Feedback by STA #2

## Slide 19: Example of Option #3
If scheduling algorithm determines to allocates 484+2996 RU for STA #1 and 484 RU for STA #2 with 240MHz OFDMA in 11be
  See [3] for the value of RU allocation subfield
 | RU allocation subfield [X8-X0]
STA Info 1 | 001010111
STA Info 2 | 001000001
996
484
484
996
0 … 17
36 …
RU index
18 … 35
… 111
Feedback by STA #1
Feedback by STA #1
Feedback by STA #2