## Slide 1: 240MHz transmission
Date: 06/29/20
Authors | Email
Xiaogang Chen | Xiaogang.c.chen@intel.com
Qinghua Li | 
Feng Jiang | 
Daniel Bravo | 
Thomas Kenney | 
Laurent Cariou | 

## Slide 2: Background
Definition of the 240MHz transmission is not clear in the SFD.
  Dedicated 240MHz PPDU or 320MHz PPDU with 80MHz punctured?
  Do we need to define 240MHz channel and BSS?
Alt.1: Reuse 320MHz PPDU, 320MHz channelization.
Alt.2: Define a dedicated 240MHz PPDU, 240MHz channelization.

## Slide 3: Considerations on 240MHz PPDU
Very likely there will be no 240MHz only STA.
  240MHz STA will reuse the 320MHz baseband processing or even RF;
  996*3 RU is already supported in 320MHz PPDU as a punctured mode;
    The 320MHz receiver should be able to handle the case that an OBSS is in the punctured 80MHz.
  240MHz PPDU, even defined, will use the same mask as 320MHz punctured 80MHz;
  240MHz PPDU, even defined, is becoming a virtual concept.
Define 240MHz PPDU means a new mode with many related sub-topic to discuss and product verifications. E.g.
  STF/LTF sequence, Tx/Rx requirements, and any BW related issues;
  But the checkbox is still 320MHz supported in the product.
No 240MHz PPDU will simplify the spec and product verification.

## Slide 4: Considerations on 240MHz PPDU Cont’d
Example: MRUs defined for 240MHz merge to 320MHz PPDU without add any new entry or remove any existing entries.
The MRU merging should be the only addendum of not defining 240MHz PPDU.
BW | RU | Mandatory in Non-OFDMA for:
240 MHz | 3×996, 2×996+484, 2×996 (any 2) | AP, STA
320 MHz | 4×996, 3×996+484, 3×996 (any 3) | AP, STA
BW | RU | Mandatory in OFDMA for:
240 MHz | 2×996+484 | Non-AP STA only
320 MHz | 3×996+484, 3×996 (any 3) | Non-AP STA only
BW | RU | Mandatory in Non-OFDMA for:
320 MHz | 4×996, 3×996+484, 3×996 (any 3), 2×996+484 (within contiguous 240MHz), 2×996 (within contiguous 240) | AP, STA
BW | RU | Mandatory in OFDMA for:
320 MHz | 3×996+484, 3×996 (any 3), 2×996+484 (within contiguous 240MHz) | Non-AP STA only

## Slide 5: Considerations on 240MHz channel
The channelization in [1], if agreed, will cover all the popular cases of 240MHz transmission.
  All the non-staggered 240MHz in LPI;
  All the 240MHz in AFC.
Any other unique benefit of defining 240MHz channel/BSS instead of use 320MHz BSS?
  More 240MHz channels than 320MHz channels for flexible deployment?
    Enterprise deployment prefer smaller BW, e.g. 20/40 instead of >80;
    Comparing with 320MHz channels, the number of 240MHz channels is also not sufficient for frequency reuse.

## Slide 6: Summary
Propose to not define 240MHz PPDU and 240MHz channel in 11be.
  Simplify the spec draft;
  Reduce modes of validation;
  A better balance between complexity and gain.

## Slide 7: SP
Do you agree that no 240MHz PPDU and no 240MHz channelization are defined in 11be.
  The 240Mhz transmission is defined as 320MHz PPDU with 80Mhz punctured.
    The punctured 80MHz is either the left 80MHz or the right 80MHz in the 320MHz PPDU;
  The MRUs, including both OFDMA and Non-OFDMA, allowed in 240MHz transmission are still allowed in 320MHz PPDU.

## Slide 8: Reference
11-20-0953-00 “320MHz channelization”.

## Slide 9: Backup - Mask
Black: 320MHz PPDU mask (scaling of 160MHz)
Red: 320MHz PPDU mask + puncture mask
Green: 240MHz PPDU mask (scaling of 160MHz)