## Slide 1: 240MHz transmission
Date: 06/29/20
Authors | Email
Xiaogang Chen | Xiaogang.c.chen@intel.com
Qinghua Li | 
Feng Jiang | 
Daniel Bravo | 
Thomas Kenney | 
Laurent Cariou | 

## Slide 2: Background
Definition of the 240MHz transmission is not clear in the SFD.
  Dedicated 240MHz PPDU or 320MHz PPDU with 80MHz punctured?
  Do we need to define 240MHz channel and BSS?
Alt.1: Reuse 320MHz PPDU, 320MHz channelization.
Alt.2: Define a dedicated 240MHz PPDU, 240MHz channelization.

## Slide 3: Considerations on 240MHz PPDU
Very likely there will be no 240MHz only STA.
  240MHz STA will reuse the 320MHz baseband processing or even RF;
  996*3 RU is already supported in 320MHz PPDU as a punctured mode;
    The 320MHz receiver should be able to handle the case that an OBSS is in the punctured 80MHz.
  240MHz PPDU, even defined, will use the same mask as 320MHz punctured 80MHz;
  240MHz PPDU, even defined, is becoming a virtual concept.
Define 240MHz PPDU means a new mode with many related sub-topic to discuss and product verifications. E.g.
  STF/LTF sequence, Tx/Rx requirements, and any BW related issues;
  But the checkbox is still 320MHz supported in the product.
No 240MHz PPDU will simplify the spec and product verification.

## Slide 4: Considerations on 240MHz PPDU Cont’d
Example: MRUs defined for 240MHz merge to 320MHz PPDU without add any new entry or remove any existing entries.
The MRU merging should be the only addendum of not defining 240MHz PPDU.
BW | RU | Mandatory in Non-OFDMA for:
240 MHz | 3×996, 2×996+484, 2×996 (any 2) | AP, STA
320 MHz | 4×996, 3×996+484, 3×996 (any 3) | AP, STA
BW | RU | Mandatory in OFDMA for:
240 MHz | 2×996+484 | Non-AP STA only
320 MHz | 3×996+484, 3×996 (any 3) | Non-AP STA only
BW | RU | Mandatory in Non-OFDMA for:
320 MHz | 4×996, 3×996+484, 3×996 (any 3), 2×996+484 (within contiguous 240MHz), 2×996 (within contiguous 240) | AP, STA
BW | RU | Mandatory in OFDMA for:
320 MHz | 3×996+484, 3×996 (any 3), 2×996+484 (within contiguous 240MHz) | Non-AP STA only

## Slide 5: Considerations on 240MHz channel
The channelization in [1], if agreed, will cover all the popular cases of 240MHz transmission.
  All the non-staggered 240MHz in LPI;
  All the 240MHz in AFC.
Any other unique benefit of defining 240MHz channel/BSS instead of use 320MHz BSS?
  More 240MHz channels than 320MHz channels for flexible deployment?
    Enterprise deployment prefer smaller BW, e.g. 20/40 instead of >80;
    Comparing with 320MHz channels, the number of 240MHz channels is also not sufficient for frequency reuse.

## Slide 6: R1 Updates (page 6~10)
MRU clarification for 320MHz PPDU (right click to open as excel)
  Merging MRU defined for 240MHz into 320MHz PPDU.
Considerations on spec impacts of 240MHz PPDU definition.

## Slide 7: MRU defined for 240MHz transmission
Which 240MHz transmission is valid in 320MHz?
  All valid 80MHz x 3?
    Any MRU defined will be valid for every 240/160+80MHz definition.
    Too many modes. We avoided this route in 320Mhz PPDU.
  Only the one cover P160?
    We should decouple primary channel with the MRU to simplify the discussion.
  Proposed to only allow 240-1 and 240-2

## Slide 8: 996+484
996+484 straddle 80-2 and 80-3
  Straddle P160 and S160 is disallowed in 320MHz PPDU but allowed in 240Mhz transmission;
  The group agree 240MHz transmission will be implemented with 320MHz Tx/Rx chain. Propose to use the rule defined for 320MHz PPDU.

## Slide 9: 996x2
996x2-1 and 996x2-2 shall not be allowed.
  Indicated as 160Mhz PPDU.
  996x2 only cover S160 is not valid.
  Also propose to disallow the two options below.

## Slide 10: Current status of 240MHz transmission
Agreed:
  No 240 channelization;
  240MHz transmission use 320MHz PPDU mask;
No precedence to define a xBW PPDU without xBW channel in WiFi.
Any modes/MRU supported in 240MHz transmission can be supported in 320MHz PPDU without defining 240MHz PPDU.
If we don’t define 240MHz PPDU we can save in the following subclause:
  EHT-SIG:
    EHT-SIG RU allocation subfield; Frequency mapping…
  Subcarrier and resource allocation
    RU index; Null tone index; 20MHz operating within larger BW…
  Math equations…
  STF sequence, LTF sequence…
  Pilot index…
  Segment parser…
  Non-HT dup..
  Tx/Rx reqirements…
  CCA.

## Slide 11: Summary
Propose to not define 240MHz PPDU and 240MHz channel in 11be.
  Simplify the spec draft;
  Reduce modes of validation;
  A better balance between complexity and gain.

## Slide 12: SP
Do you agree that no 240MHz channelization is defined in 11be?

## Slide 13: SP1
Do you agree that no 240MHz PPDU is defined in 11be.
  The 240Mhz transmission is defined as 320MHz PPDU with 80Mhz punctured.
    The punctured 80MHz is either the left 80MHz or the right 80MHz in the 320MHz PPDU

## Slide 14: SP2
Do you agree to define the MRUs listed in the excel in this page as all the MRUs supported in 320MHz PPDU?

## Slide 15: Reference
11-20-0953-00 “320MHz channelization”.

## Slide 16: Backup - Mask
Black: 320MHz PPDU mask (scaling of 160MHz)
Red: 320MHz PPDU mask + puncture mask
Green: 240MHz PPDU mask (scaling of 160MHz)

## Slide 17
240MHz PPDU:
EHT-SIG content channel: 6 RU allocation subfield / CC?
Don’t have SEM for 240MHz PPDU?
N_tone_field in the equation of OFDM symbol formation.
All the RU/Tone index related table/figures. E.g. null tone table, PPDU figure, tone index table.
CCA rule:
MAC:
  OM control need to define for 240MHz PPDU
484+242 RU in 80MHz channel is not signaled as 60MHz PPDU…