## Slide 1: 240MHz transmission
Date: 06/29/20
Authors | Email
Xiaogang Chen | Xiaogang.c.chen@intel.com
Qinghua Li | 
Feng Jiang | 
Daniel Bravo | 
Thomas Kenney | 
Laurent Cariou | 

## Slide 2: Background
Definition of the 240MHz transmission is not clear in the SFD.
  Dedicated 240MHz PPDU or 320MHz PPDU with 80MHz punctured?
  Do we need to define 240MHz channel and BSS?
Alt.1: Reuse 320MHz PPDU, 320MHz channelization.
Alt.2: Define a dedicated 240MHz PPDU, 240MHz channelization.

## Slide 3: Considerations on 240MHz PPDU
Very likely there will be no 240MHz only STA.
  240MHz STA will reuse the 320MHz baseband processing or even RF;
  996*3 RU is already supported in 320MHz PPDU as a punctured mode;
    The 320MHz receiver should be able to handle the case that an OBSS is in the punctured 80MHz.
  240MHz PPDU, even defined, will use the same mask as 320MHz punctured 80MHz;
  240MHz PPDU, even defined, is becoming a virtual concept.
Define 240MHz PPDU means a new mode with many related sub-topic to discuss and product verifications. E.g.
  STF/LTF sequence, Tx/Rx requirements, and any BW related issues;
  But the checkbox is still 320MHz supported in the product.
No 240MHz PPDU will simplify the spec and product verification.

## Slide 4: Considerations on 240MHz PPDU Cont’d
Example: MRUs defined for 240MHz merge to 320MHz PPDU without add any new entry or remove any existing entries.
The MRU merging should be the only addendum of not defining 240MHz PPDU.
BW | RU | Mandatory in Non-OFDMA for:
240 MHz | 3×996, 2×996+484, 2×996 (any 2) | AP, STA
320 MHz | 4×996, 3×996+484, 3×996 (any 3) | AP, STA
BW | RU | Mandatory in OFDMA for:
240 MHz | 2×996+484 | Non-AP STA only
320 MHz | 3×996+484, 3×996 (any 3) | Non-AP STA only
BW | RU | Mandatory in Non-OFDMA for:
320 MHz | 4×996, 3×996+484, 3×996 (any 3), 2×996+484 (within contiguous 240MHz), 2×996 (within contiguous 240) | AP, STA
BW | RU | Mandatory in OFDMA for:
320 MHz | 3×996+484, 3×996 (any 3), 2×996+484 (within contiguous 240MHz) | Non-AP STA only

## Slide 5: Considerations on 240MHz channel
The channelization in [1], if agreed, will cover all the popular cases of 240MHz transmission.
  All the non-staggered 240MHz in LPI;
  All the 240MHz in AFC.
Any other unique benefit of defining 240MHz channel/BSS instead of use 320MHz BSS?
  More 240MHz channels than 320MHz channels for flexible deployment?
    Enterprise deployment prefer smaller BW, e.g. 20/40 instead of >80;
    Comparing with 320MHz channels, the number of 240MHz channels is also not sufficient for frequency reuse.

## Slide 6: Background of R2 (R2 updates: P6~P13)
Concerns of not defining 240MHz PPDU:
  Signaling: some of the signaling design is based on the assumption that “240MHz transmission” is 240MHz PPDU.
  Number of modes: This contribution increases/decreases the modes we agreed in SFD …
    Different interpretation of 240MHz transmission.
      E.g. 240MHz transmission and the associated puncturing modes can be present in any 996x3 frequency resource (contiguous/non-contiguous) in 320MHz PPDU. Defining 240MHz PPDU or not doesn’t affect these modes.
      E.g. If defining 240MHz PPDU, there will be only one 240MHz transmission within 320MHz PPDU, which is the one covering the P160.
      E.g. some interpretation in the middle.
But…we need to move forward…
  Clean up the modes supported in SFD;
  Decide if 240MHz PPDU is defined.

## Slide 7: Thoughts on 240MHz transmission (1/2)
Agreed:
  No 240 channelization;
  240MHz transmission use 320MHz PPDU mask.
No precedence to define a xx BW PPDU without xx BW channel and xx BW mask in WiFi.
  There were 20/40/80/160MHz PPDU and 20/40/80/160MHz mask. But no 60MHz/100MHz PPDU…
Based on the passed SP, 240MHz is a virtual concept in 320MHz PPDU already.
  If defining 240MHz PPDU, it’s a duplicated transmission mode with 320MHz with 80MHz punctured.
Any modes/MRU supported in 240MHz transmission can be supported in 320MHz PPDU.

## Slide 8: Thoughts on 240MHz transmission (2/2)
A new PPDU BW means many changes in spec / product validation.
If we don’t define 240MHz PPDU we can save the efforts of spec drafting in the following subclause:
  EHT-SIG:
    EHT-SIG RU allocation subfield; Frequency mapping…
  Subcarrier and resource allocation
    RU index; Null tone index; 20MHz operating within larger BW…
  Math equations…
  STF sequence, LTF sequence…
  Pilot index…
  Segment parser…
  Non-HT dup..
  Tx/Rx reqirements…
  CCA.
Strongly prefer not defining 240MHz PPDU.

## Slide 9: Modes clean up
“Any modes/MRU supported in 240MHz transmission can be supported in 320MHz PPDU”.
MRU clarification for 320MHz PPDU (right click to open as excel)
  Merging MRU defined for 240MHz into 320MHz PPDU.

## Slide 10: MRU defined for 240MHz transmission
Which 240MHz transmission is valid in 320MHz?
  All valid 80MHz x 3?
    Any MRU defined will be valid for every 240/160+80MHz definition.
    Too many modes. We avoided this route in 320MHz PPDU.
  Only the one covers P160?
    Reduced ~75% of the modes comparing with the one above...
In 320Mhz PPDU, propose to only allow puncturing 240-1 and 240-2.
  Note that 240-1,2,3,4 are allowed as un-punctured (320MHz with 80MHz punctured)

## Slide 11: 996+484
SP passed to disallow 996+484 straddles two 160MHz channels.
996+484 straddle 80-2 and 80-3
  Straddle P160 and S160 is disallowed in 320MHz PPDU but allowed in 240Mhz transmission;
  The group agree 240MHz transmission will be implemented with 320MHz Tx/Rx chain. Propose to use the rule defined for 320MHz PPDU.

## Slide 12: 996x2
996x2-1 and 996x2-2 shall not be allowed.
  Indicated as 160Mhz PPDU.
  996x2 only cover S160 is not valid.
996x2-3
  SP passed to disallow 996+484 which straddle two 160MHz channels;
  996x2-3 is the un-punctured version of 996+484;
  Propose to disallow under the same spirit.
Also propose to disallow the two options 996x2-4,5.
  80MHz hole in the middle may be risky depends on the puncturing mask definition.

## Slide 13: Summary
Propose to not define 240MHz PPDU in 11be.
  Simplify the spec draft;
  Reduce modes of validation;
  A better balance between complexity and gain.

## Slide 14: SP1
Do you agree that no 240MHz PPDU is defined in 11be.
  The 240Mhz transmission is defined as 320MHz PPDU with 80Mhz punctured.
    The punctured 80MHz is either the left 80MHz or the right 80MHz in the 320MHz PPDU

## Slide 15: SP2a
In 320MHz PPDU, do you agree with the options defined below for MRU 996x4, 996x3, 996+484, and 484+242.

## Slide 16: SP2b
Do you agree that MRU 996x2 shall not straddle two 160MHz channels?
  Note: The three options below are now allowed for MRU 996x2.

## Slide 17: SP2d
Which table defines the options for MRU 996x2+484 in 320MHz BSS?
Tab.I: 12 options.
Tab.II: 24 options.
Tab.III: 6 options.

## Slide 18: SP2c
Do you agree that only the following options are supported for MRU 996x2+484 in 320MHz PPDU

## Slide 19: SP2
Do you agree to define the MRUs listed below as all the MRUs supported in 320MHz PPDU?

## Slide 20: Reference
11-20-0953-00 “320MHz channelization”.

## Slide 21: Backup - Mask
Black: 320MHz PPDU mask (scaling of 160MHz)
Red: 320MHz PPDU mask + puncture mask
Green: 240MHz PPDU mask (scaling of 160MHz)