## Slide 1: 6GHz LPI Range Extension
Date: 2020-07-31
Authors:
Name | Affiliations | Address | Phone | email
Ron Porat | Broadcom |  |  | ron.porat@broadcom.com

## Slide 2: Abstract
In the US, 1.2GHz is now approved for unlicensed use under low power indoor (LPI) rules.
This provides a huge boost (3x) to the spectrum available to 11be and 11ax devices although at a reduced power and PSD  5dBm/MHz for AP and -1dBm/MHz for STA.
Hence, we propose to define one lower rate SU mode to improve DL and UL range over the 11ax design
Revision r3 added SP based on discussion on the call

## Slide 3: Max LPI Power and 11ax Rates
Tx BW [MHz] | Max Power AP EIRP [dBm] | Lowest rate in 11ax [Mbps] 0.8uS GI with DCM
20 | 18 | 4.3
40 | 21 | 8.6
80 | 24 | 18
160 | 27 | 36
320 | 30 | -
Tx BW [MHz] | Max Power STA EIRP [dBm] | Lowest rate in 11ax [Mbps] 0.8uS GI with DCM
20 | 12 | 4.3
40 | 15 | 8.6
80 | 18 | 18
160 | 21 | 36
320 | 24 | -
It is desirable by AP and STA to use the maximum available BW in the BSS in order to maximize the transmission power
Dropping BW doesn’t provide better SNR  prefer to maintain BW while lowering rates

## Slide 4: Proposal
For SU80, SU160 and SU320 transmissions define a DUP mode of SU40, SU80 and SU160 limited to MCS0+DCM @Nss=1 to generate lower rates
  For SU20 and SU40 11ax rates are quite low already and we don’t see the need to define lower rates
  E.g., 160MHz rates –>
    160 MCS0 (72Mbps)
    160 MCS0+DCM (36Mbps)
    160 (80MHz MCS0+DCM) + DUP (18Mbps)
  Note – we assume MCS0+DCM will be defined in 11be , see also [1]
Beacons can already be sent in Non-HT DUP mode in 11ax @6GHz  80MHz-wide beacons provide range extension for STA that combine the four repetitions.

## Slide 5: Summary
Lower SU rate using DUP design is proposed for 11be for improved range of the new LPI spectrum.

## Slide 6: References
[1] 20/0986 DCM for range extension in 6GHz LPI

## Slide 7: SP #1
Do you agree to define a DUP mode for non-punctured 80MHz, 160MHz and 320MHz PPDUs transmitted to a single user, limited to {MCS0+DCM, Nss=1}?
  80 DUP = 40 duplicated
  160 DUP = 80 duplicated
  320 DUP = 160 duplicated
  PAPR reduction scheme is TBD
  For rel. 1

## Slide 8: SP #2
Do you agree that duplication in the mode defined in SP #1 is done only on the data tones of the payload portion and that EHT-STF/LTF are based on the total BW?
For 80MHz the 80MHz OFDMA LTF sequence is used
For 160/320MHz the non-OFDMA 160/320 LTF sequence is used
Pilots are the same as pilots for the non-DUP mode of the same BW and using
  OFDMA tone plan for 80MHz
  Non-OFDMA tone plan for 160/320MHz

## Slide 9: SP #3
Do you agree that the mode defined in SP #1 is limited to 6GHz?