## Slide 1
Multi-user Triggered P2P Transmission
Date: 2020-06-30
Authors:

## Slide 2: Introduction
The Triggered P2P transmission was proposed and discussed in [1], [2], [3]
Triggered P2P transmissions have benefits from throughput and latency perspectives
Triggered P2P is initiated by an AP for a “Single-User style” PPDU
In [1], P2P PPDU format is left as TBD
In some scenarios, P2P transmissions can be to/from multiusers.
In this contribution, MU P2P transmission is discussed.

## Slide 3: Recap: Trigger based DiL transmission [1]
Basic Operation
  AP shares a part of the TXOP to the P2P traffic
AP
STA1
STA2
SIFS
TXOP owned by the AP
TF for P2P
ACK 21
Allocated time
P2P PPDU
SU PPDU
(N x 20MHz)
SIFS

## Slide 4: Multiuser P2P Scenario
A device can communicate with multiple devices
  P2P users are highly likely to be located close to each other
  In some scenarios, a P2P user can communication with multiple P2P devices and vice versa
  If P2P users use optimal transmission parameters, communication efficiency can be improved
  In this scenario, Multi user P2P is beneficial over Single user P2P

## Slide 5: Multiuser Peer 2 Peer
MU consideration

## Slide 6: Multiuser Peer 2 Peer (Downlink)
Downlink (TDM)
  Low efficiency due to SIFS periods between transmissions

## Slide 7: Multiuser Peer 2 Peer (Downlink)
Downlink (OFDMA)
  Efficient transmission scheme for MU
  OFDMA operation is same as 802.11ax

## Slide 8: Multiuser Peer 2 Peer (Uplink)
Uplink
  In order for STA1 to control the transmission, TF from STA1 has to elicit MU P2P Transmissions
  OFDMA operation is same as 802.11ax

## Slide 9: Conclusion
In this presentation, Multiuer P2P was discussed
Allocated time by an AP can be used as a MU P2P opportunity
A STA triggered by an AP controls MU P2P transmission
For downlink MU P2P, TDM based transmission may be used
  TDM based MU P2P has overhead due to SIFSs
For MU P2P, OFDMA transmission controlled by the triggered STA my be used
  Same OFDMA procedure shall be used as 802.11ax
MU P2P can be considered as a useful feature for R2

## Slide 10: Reference
[1] 11-20/0813r3 Triggered P2P transmissions follow up
[2] 11-20-0871r0 Simplified P2P Release1
[3] 11-20-0095r2 Triggered P2P transmissions