## Slide 1
Multi-link RTS-CTS operations with non-STR non-AP MLD
Date: 2020-06-29
Authors:

## Slide 2: Introduction
The multi-link operation includes the operation of non-STR multi-link operation[1].
Several presentations considered RTS-CTS mechanism of multi-link with non-STR non-AP MLD [2], [3].
This presentation continues to discuss the issue.

## Slide 3: Recap: multi-link operation and channel access
Previous submissions proposed the PPDU end-time alignment operation when multi-link operation is performed with non-STR non-AP MLD [2], [3].

## Slide 4: RTS-CTS transmission issue in non-STR operation
RTS-CTS mechanism on the second link may not be allowed in non-STR multi-link operations.
There is no clear rule for RTS frame transmission on non-STR multi-link  performance degradation
[SFD] When a STA in a non-STR MLD receives an RTS addressed to itself, if the NAV of the STA indicates idle but another STA in the same MLD is either a TXOP holder or a TXOP responder, the STA may not respond with a CTS frame.

## Slide 5: Synchronized ML RTS-CTS procedure
Whenever possible, synchronized RTS transmission is a simple solution for non-STR AP MLD.
  There are proposals for a synchronized ML transmission.
However, if channel access procedure on the other(second) link is taking too much time after a successful channel access on one link, it would be beneficial to consider semi-synchronized ML transmission.

## Slide 6: Semi-synchronized ML RTS-CTS procedure for non-STR multi-link operation
There are several cases for a semi-synchronized ML RTS-CTS procedure
  Case1: Second link’s backoff success < First link’s CTS TX start time
  Case2: Second link’s backoff success < First link’s PPDU TX start time
  Case3: Second link’s backoff success > First link’s PPDU TX start time

## Slide 7: Semi-synchronized ML RTS-CTS procedure for non-STR multi-link operation
Case1: Second link’s backoff success < First link’s CTS TX start time
  Do not transmit RTS on the second link (link 2).
  During STA1’s CTS transmission, AP2 can transmit CTS-to-Self for NAV setting.
  Alternatively, AP2 can transmit a PPDU on the second link using a synchronized ML transmission.

## Slide 8: Semi-synchronized ML RTS-CTS procedure for non-STR multi-link operation
Case2: Second link’s backoff success < First link’s PPDU TX start time
  Do not transmit RTS on the second link (link 2).
  AP2 can transmit a PPDU on the second link using a synchronized ML transmission.
  AP2 should transmit non-HT PPDU for better protection because the second link is not protected by RTS-CTS.

## Slide 9: Semi-synchronized ML RTS-CTS procedure for non-STR multi-link operation
Case3: Second link’s backoff success > First link’s PPDU TX start time
  Do not transmit RTS on the second link (link 2).
  AP2 transmits a PPDU after the transmission start time of PPDU on link 1. (Semi-synchronized ML transmission)
  AP2 should transmit non-HT PPDU for better protection because the second link is not protected by RTS-CTS.

## Slide 10: Conclusion
RTS-CTS mechanism for Non-STR MLD was discussed.
In case of Non-STR MLD, when a channel access on one link of a non-STR link pair is successful, there are several cases for RTS-CTS ML transmission on the other link.
  Case1: Second link’s backoff success < First link’s CTS TX start time
  Case2: Second link’s backoff success < First link’s PPDU TX start time
  Case3: Second link’s backoff success > First link’s PPDU TX start time
For all cases considered in this presentation, in case of transmitting PPDUs to non-STR non-AP MLD, it is recommended not to transmit RTS frame on the second link when using a semi-synchronized ML transmission.

## Slide 11: Reference
[1] 11-19/1262r6 Specification Framework for TGbe
[2] 11-19/1405 Multi-Link Operation Channel Access Discussion, Sharan Naribole (Samsung)
[3] 11-19/1546 Legacy Performance Impact on Multi-link Operation, Yongho Seok (MediaTek)
[4] 11-19/1916 MLO-Asynch-Qsynch-Synch, Matthew Fischer (Broadcom Inc)
[5] 11-19/1917 Considerations for multi-link channel access without simultaneous TX/RX capability, Insun Jang (LG Electronics)
[6] 11-19/1541 Performance aspects of Multi-link operations with constraints, Dmitry Akhmetov (Intel)

## Slide 12: Straw Poll #1​
Do you agree to add the following to R1 of 11be SFD: ​
  For non-STR non-AP MLD, when an RTS/CTS mechanism is used on one link, the PPDU on the other link shall be transmitted without sending an RTS frame.

## Slide 13: Straw Poll #2​
Do you agree to add the following to R1 of 11be SFD: ​
  For non-STR non-AP MLD, when an RTS/CTS mechanism is used on one link, when the PPDU transmission should be protected on the other link, a CTS-to-Self frame should be transmitted before the PPDU transmission and/or the PPDU should use non-HT PPDU format.

## Slide 14: Straw Poll #3​
Do you agree to add the following to R1 of 11be SFD: ​
  For non-STR non-AP MLD, when an RTS/CTS mechanism is used on one link, the PPDU transmission on the other link shall be synchronized with or started after the PPDU transmission on one link.