## Slide 1: Spoofing Indication in EHT-SIG
Date: 2020-06-30
Authors:
Name | Affiliations | Address | Phone | email
Mengshi Hu | Huawei |  |  | humengshi@Huawei.com
Ross Yu | Huawei |  |  | ross.yujian@huawei.com
Ming Gan | Huawei |  |  | 

## Slide 2: EHT PPDU Format
EHT has adopted the following format of an EHT PPDU sent to multiple users [1].
  There shall be a 2 OFDM symbol long, jointly encoded U-SIG in the EHT preamble immediately after the RL-SIG.
  The EHT-SIG (immediately after the U-SIG) in an EHT PPDU sent to multiple users shall have a common field and user-specific field(s).
  Special case compressed modes (e.g., full BW MU-MIMO) are TBD.
  An RU Allocation subfield is present in the Common field of the EHT-SIG field of an EHT PPDU sent to multiple users.
  Compressed modes are TBD.
  Contents of the RU Allocation subfield are TBD.
L-STF | L-LTF | L-SIG | RL-SIG | U-SIG | EHT-SIG | EHT-STF | EHT-LTF | Data
Common field | User Specific field
RU Allocation subfield

## Slide 3: Per-80MHz Preamble Signaling
On the basis of the EHT PPDU format sent to multiple users, an efficient per-80MHz preamble structure is designed [2-4].
  Information in U-SIG is allowed to vary from one 80 MHz to the next in an EHT PPDU of bandwidth > 80MHz
  Within each 80MHz, U-SIG is still duplicated in every non-punctured 20MHz.
  EHT-SIG may carry different content in each 80MHz.
  A STA only needs to process up to one 80 MHz segment of the pre-EHT preamble (up-to and including EHT-SIG) to get all the assignment information for itself.
… | U-SIG2 | EHT-SIG2_2 | …
… | U-SIG2 | EHT-SIG2_1 | …
… | U-SIG2 | EHT-SIG2_2 | …
… | U-SIG2 | EHT-SIG2_1 | …
… | U-SIG1 | EHT-SIG1_2 | …
… | U-SIG1 | EHT-SIG1_1 | …
… | U-SIG1 | EHT-SIG1_2 | …
… | U-SIG1 | EHT-SIG1_1 | …
Primary 80MHz
Secondary 80MHz
In the per-80MHz preamble structure, a STA parked on the secondary 80MHz only needs to process its corresponding 80MHz segment of the pre-EHT preamble (up-to and including EHT-SIG) to get all the assignment information for itself.

## Slide 4: Number of RU Allocation Subfields
In [5], we have discussed the non-compressed OFDMA mode (11be baseline method, similar as 11ax):
  RU Allocation subfield in the common field indicates the RU assignment information with granularity of 20MHz
  N RU Allocation subfields in one CC, where N=1 for 20/40MHz, N=2 for 80MHz, N=4 for 160MHz, and N=8 for 320MHz – needed for non-SST scenarios
  The baseline method enables allocating the RU/MRU in other segments to a STA (cross-segment allocation).

## Slide 5: Spoofing Signaling in Per-80MHz
  On the basis of the above baseline configuration, here we propose a spoofing signaling to save the overhead of User Specific fields.
Here we classify the spoofing signaling into three types from the perspectives of different resource granularities.
  Spoofing signaling in small-RU granularity
  Spoofing signaling in large-RU granularity
  Spoofing signaling in segment granularity
  In the following, we give the details of the proposed methods.

## Slide 6
  Spoofing signaling in small-RU granularity indicates a spoofing design utilizing small RU.
  Small RU means the RU with size smaller than 242 tones.
  The main idea is to use a smaller number of small RUs to replace the practical assigned small RUs which are not allocated to the users parked on this segment.
  Example:
Spoofing Signaling in Small-RU Granularity
Need 9 user fields
Need 5 user fields
Need 8 user fields
Yellow block: Practical RUs allocated to STAs in segment 1
Orange block: Practical RUs allocated to STAs in segment 2
White block: Dummy RUs through spoofing signaling

## Slide 7
  Spoofing signaling in large-RU granularity indicates a spoofing design utilizing large RU.
  Large RU means the RU with the size larger than or equal to 242 tones.
  The main idea is to use RU Allocation subfield corresponding to the large RU and zero user field to replace the practical assigned RUs which are not allocated to the users parked on this segment.
  Example:
The user fields corresponding to 9 26-tone RUs can be saved in Segment 1
  Note that 484 (0) and 996 (0) can also be replaced by multiple 242 (0).
Spoofing Signaling in Large-RU Granularity
The user fields corresponding to these yellow blocks can be saved in Segment 2
Yellow block: Practical RUs allocated to STAs in segment 1
Orange block: Practical RUs allocated to STAs in segment 2
White block: Dummy RUs through spoofing signaling

## Slide 8
  Spoofing signaling in segment granularity indicates a spoofing design utilizing non-OFDMA signaling in a segment
  The segment granularity indicates the resources allocated to a segment can be regarded as a non-OFDMA mode [6].
  This spoofing signaling can be used when the resource allocated to one segment is non-OFDMA and can be indicated by preamble puncture information. Thus the RU Allocation subfield can also be saved.
  Example:
Spoofing Signaling in Segment Granularity
Yellow block: Practical RUs allocated to STAs in segment 1
Orange block: Practical RUs allocated to STAs in segment 2
White block: Dummy RUs through spoofing signaling
Grey block: Dummy punctured RU

## Slide 9
Granularity | Description | OVERHEAD SAVED
Small RU | The User fields related to the users parked on the other segments can be saved, but some other user fields may be needed to be aligned with an available allocation entry in RU Allocation subfield. | 1. Up to 6 user fields per 242-tone boundary* (It depends on the available allocation pattern in RU Allocation subfield)
Large RU | The User fields related to the users parked on the other segments can be saved. | 1. Up to 9 user fields per 242-tone boundary
Segment | The RU Allocation subfield can be saved. The User fields related to the users parked on the other segments can be saved | 1. The RU Allocation subfield can be saved 2. Up to 9 user fields per 242-tone boundary
Overhead Analysis of Spoofing Signaling
Note*: For example, 6 user fields can be saved by using [106 26 106] to replace [26 26 26 26 26 26 26 26 26]. The red color indicates the practical resource allocated to the user belonging to its corresponding segment
In average, one user field consumes 27 bits (22 info bits + 5 bits half of CRC and tail), around 4 bytes per user

## Slide 10
Summary
  To save the overhead of EHT-SIG, the RU Allocation subfield may not need to reflect the practical allocation of the whole bandwidth. Each segment only needs to focus on the allocation of its own users (the users parked on it).
  Three types of spoofing signaling in per-80MHz is given from the perspectives of different resource granularities.
  Spoofing signaling in small-RU granularity
  Spoofing signaling in large-RU granularity
  Spoofing signaling in segment granularity

## Slide 11
[1] IEEE 802.11-20/0566r34 Compendium of straw polls and potential changes to the Specification Framework Document
[2] IEEE 802.11-20/0439r0 Efficient EHT Preamble Design
[3] IEEE 802.11-20/0380r0 U-SIG Structure and Preamble Processing
[4] IEEE 802.11-20/0605r0 Further Discussions on Efficient EHT Preamble
[5] IEEE 802.11-20/0922r2 RU allocation subfield in EHT-SIG Follow up II
[6] IEEE 802.11-20/0783r1 EHT-SIG Compression Format
References

## Slide 12: Straw Poll #1
Do you agree that the RU Allocation subfields in different segments corresponding to a same 20MHz can be different?
  The RU Allocation subfields in each segment only need to reflect the practical allocation of the users parked on that segment
  The RU Allocation subfields may not need to reflect the practical allocation of the whole bandwidth