## Slide 1: MLD Spatial Multiplexing Considerations
Date: 2020-07-15
Authors:

## Slide 2: Multi-link Spatial Multiplexing Background
Ideal Operation at non-AP MLD
  2x2 spatial streams capability on each link with dedicated receive chains
However, operating on two links or more, the receive chains may be shared among a subset of the setup links
Receive chain sharing and switching between STAs of a non-AP MLD has been studied in a few TGbe contributions [1]-[5]
We discuss the capability indication to enable receive chain switching, conditional switching mode and sounding procedures

## Slide 3: ML SM Default Operation Basic Example
In this example, non-AP MLD listens in 1x1 mode on each link and switches to 2x2 on one link upon receiving RTS on that link
This mode is being referred to as “enhanced multi-link operation” mode in [3]
Link A
Link B
AP A
STA A
AP B
STA B
DATA (2x2)
DATA (2x2)
BA
…
RTS
CTS
RTS
…
BA
CTS
Starts switching to 2x2
on Link B
Cannot perform
Listen/TX/RX on Link A
Switch back to 1x1
on Link A and B
Switching
Delay
Starts switching to 2x2
on Link A
Switch back to 1x1
on Link A and B
Switching
Delay
AP MLD needs to know that the 2 receive chains are being shared between STA 1 and STA 2 of non-AP MLD

## Slide 4: ML Spatial Multiplexing Capability Indication
For the set of links, non-AP MLD indicates
  Maximum Spatial Streams on each link
  Flag to indicate if receive chain sharing among the links
    Alternatively, number of receive chains being shared
Preferred location is to include this information in the ML Element along with STR Capability signaling
Enhanced multi-link operation mode can be enabled/disabled for a set of links semi-statically as presented in [3][4]

## Slide 5: ML Spatial Multiplexing Capability Examples (1/2)
NK = maximum spatial streams on link K
NA = 2, NB = 2, Shared = “1” (Enhanced single link radio)
  Non-AP MLD switches to 2x2 mode on the link TXOP is initiated by AP
NA = 2, NB = 1, Shared = “1” (Asymmetric capability)
  Non-AP MLD switches to 2x2 on Link A
  On Link B, always uses 1x1 mode. RTS not required to initiate TXOP on Link B.
Link A
Link B
AP A
STA A
AP B
STA B
DATA (2x2)
DATA (2x2)
BA
…
RTS
CTS
RTS
…
BA
CTS
Link A
Link B
AP A
STA A
AP B
STA B
DATA (1x1)
DATA (2x2)
BA
RTS
…
BA
CTS
DATA (1x1)
BUSY
…
BA
BUSY

## Slide 6: ML Spatial Multiplexing Capability Examples (2/2)
NA = 2, NB = 2, Shared = “0” (No Sharing)
  In this case, no receive chain switching occurs between links.
  Both the links are accessible simultaneously depending on STR capability
  This corresponds to enhanced multi-link operation mode not applied on links A and B
NA = 2, NB = 2, NC =2 and Shared = “1” (More than two links sharing)
  In this example, three links are sharing the receive chains
  Non-AP MLD switches to 2x2 on the link on which RTS is received
  Other links are not accessible during that TXOP
Link A
Link B
AP A
STA A
AP B
STA B
BA
DATA (2x2)
BA
BUSY
DATA (2x2)

## Slide 7: ML Spatial Multiplexing NAV Sync Issue
Identical to non-STR MLD losing NAV sync on other links during TX on one link
Link A
Link B
AP A
STA A
AP B
STA B
DATA (2x2)
BA
CTS
RTS
Starts switching to 2x2
on Link B
Cannot perform
Listen/TX/RX on Link A
Switch back to 1x1
on Link A and B
Switching
Delay
Switching
Delay
Proposal
  Use same rules that will be defined for non-STR MLD NAV Sync issue
NAV out of sync

## Slide 8: Non-Immediate Switching Operation Motivation
Default mode is Immediate Switching upon receiving RTS as shown in previous slides
Immediately switching to maximum streams on Link A may result in losing out on channel access on Link B (higher BW, better quality, etc.)
In the above example, Link B cannot be used although idle. Instead, if non-AP MLD did not switch immediately to 2x2 on Link A and AP MLD also obtained Link B access during ongoing transmission on Link A, then throughput can be further improved by the simultaneous transmission on both links if Link B can provide better performance compared to Link A.
Link A
Link B
RTS
CTS
AP A
STA A
AP B
STA B
DATA (2x2)
BA
BUSY

## Slide 9: Non-Immediate Switching Operation Proposal
To facilitate desired operation in previous slide, non-AP MLD should not immediately switch to maximum spatial streams on the less preferred link
Non-AP MLD indicates to AP MLD the link(s) on which it wants to enable non-Immediate switching mode
  By default, immediate switching enabled on all links of receive chain sharing link set
Accordingly, AP MLD uses RTS-type Trigger instead of regular RTS to initiate TXOP on the non-Immediate Switching enabled links. Trigger may include info such as:
  Spatial streams to use for this TXOP from the beginning of data reception in TXOP
  Countdown wait time/ PPDU limit before switching to maximum spatial streams
    0 indicates immediate Switch
      Should be used if only one data PPDU in TXOP

## Slide 10: Non-Immediate Switching Example
  Link A on 6 GHz 160 MHz (default mode: immediate switching)
  Link B on 5 GHz 40 MHz (non-AP MLD indicates non-immediate switching)
  RTS Trigger sent on Link B to initiate TXOP
  RTS sent on Link A to initiate TXOP
Link A
Link B
AP A
STA A
AP B
STA B
DATA (1x1)
DATA (2x2)
BA
RTS
…
BA
CTS
DATA (1x1)
…
BA
BUSY
CTS
RTS
Trigger
Informs non-AP MLD to use 1x1

## Slide 11: MIMO Sounding in Multi-link Operation
Independent of receive chain sharing between links, in certain implementations, beamformee block may be shared among a subset of STAs of a non-AP MLD
CBR/CQI report processing can be performed for one link at a time
Consequently, sounding procedure needs to be conducted only on one link at a time
Sending no response may be detrimental to non-AP MLD’s performance
Link A
Link B
AP A
STA A
AP B
STA B
NDP
Announcement
NDP
CBR/CQI Report
No Response
NDP
NDP
Announcement

## Slide 12: MIMO Sounding in Multi-link Operation Proposal
In case of receive chain sharing at non-AP MLD, AP MLD will not perform simultaneous sounding on multiple links that are sharing the receive chains. We propose to extend this behavior non-AP MLDs in general.
Option 1 (Preferred)
  AP MLD shall not initiate sounding sequence with a non-AP MLD on a link if this sounding sequence would potentially overlap in time domain with an ongoing sounding sequence on another link with the same non-AP MLD.
Option 2
  Capability indication from non-AP MLD if it can participate in sounding concurrently on a set of links
Option 3
  If AP MLD sends NDP-A and NDP to same non-AP MLD simultaneously on multiple links, a mechanism for non-AP MLD to request re-initiating sounding at least on one of the links. Accordingly, AP needs to re-perform sounding procedures on requested links.

## Slide 13: Summary
MLD Spatial Multiplexing capability indication
  Maximum number of spatial streams on each link
  Receive chain sharing among links
Immediate switching to maximum spatial streams on a link should be default receive chain switching operation
Additional non-immediate switching operation may be used on specific links in asymmetric links scenarios
Avoid simultaneous sounding of a non-AP MLD on multiple links

## Slide 14: Straw Poll #1
Do you agree to have following text added to TGbe SFD R1?
  A non-AP MLD shall indicate sharing of receive chain(s) among a set of setup links if operating with maximum spatial streams for transmission/reception on one link of the set results in non-AP MLD being unable to operate concurrently on other links of the set.

## Slide 15: Straw Poll #2
Do you agree to have following text added to TGbe SFD R1?
  AP MLD shall not initiate sounding sequence with a non-AP MLD on a link if this sounding sequence would potentially overlap in time domain with an ongoing sounding sequence on another link with the same non-AP MLD.

## Slide 16: Straw Poll #3
Do you agree to have following mechanism defined in TGbe SFD R1?
  Non-AP MLD to indicate if it can participate in sounding concurrently on a set of links. If Non-AP MLD indicates it cannot participate in concurrent sounding on a set of links, AP MLD shall not initiate sounding sequence with a non-AP MLD on a link of this set if this sounding sequence would potentially overlap in time domain with an ongoing sounding sequence on another link of this set with the same non-AP MLD.

## Slide 17: Straw Poll #4
Do you agree to have following mechanism defined in TGbe SFD R1?
  Non-AP MLD requests AP MLD to re-initiate sounding on a link. Consequently, AP initiates sounding for the non-AP MLD on this link.

## Slide 18: References
[1] 11-20/562, Enhanced Multi-link Single Radio Operation
[2] 11-20/659, TDM Multi-link Operation
[3] 11-20/883, Multi-link Spatial Multiplexing Considerations
[4] 11-20/900, NSTR MLD Operation
[6] 11-20/226, MLO Constraint Indication and Operating Mode
[5] 11-20/760, Multi Link SM Power Save Mode