## Slide 1: RU Allocation Subfield Design in EHT-SIG Follow up
Date: 2020-07-01
Authors:

## Slide 2: Introduction
Many motions and SPs on large-size MRUs have been passed [1].
  For OFDMA, MRUs allowed in 80 MHz PPDU shall be allowed in each 80 MHz segment of 160 MHz/80 MHz + 80 MHz, 240 MHz/160 MHz + 80 MHz and 320 MHz/160 MHz + 160 MHz PPDU.
  For OFDMA, MRUs (996+484) are allowed in the following cases:
    Contiguous 160 MHz in 240 MHz/160 MHz + 80 MHz, primary 160 MHz and secondary 160 MHz in 320 MHz/160 MHz + 160 MHz
  Mandatory large-size MRU combinations (e.g., 2x996+484 in BW 240MHz, 3x996+484 in BW 320MHz, etc.).
  But, whether 2x996+484 is supported in 320MHz is not clear in the SFD
Also, during the TGbe PHY conference calls, the many SPs on RU Allocation subfield table were passed.
  E.g., many entries in RU Allocation subfield table for the mapping from the TBD-bit RU Allocation subfield to the RU assignment were determined.
  But, there are concerns on overhead of RU Allocation subfield table for 11be.
In this contribution, we discuss how to reduce the entries overhead in RU Allocation subfield table by considering the supported large-size MRU combinations and address the required entries to indicate the zero users.

## Slide 3: Large-size MRU Combinations in 240MHz and 320MHz
In 11be SFD [1], there are the following passed motions and SPs.
  For OFDMA, MRUs allowed in 80 MHz PPDU shall be allowed in each 80 MHz segment of 160 MHz/80 MHz + 80 MHz, 240 MHz/160 MHz + 80 MHz and 320 MHz/160 MHz + 160 MHz PPDU.
  For OFDMA, MRUs (996+484) are allowed in the following cases:
    Contiguous 160 MHz in 240 MHz/160 MHz + 80 MHz
    Primary 160 MHz and secondary 160 MHz in 320 MHz/160 MHz + 160 MHz
  For the OFDMA transmission in 320/160+160 MHz, for one STA large-size RU aggregation is allowed only within primary 160 MHz or secondary 160 MHz, respectively
    Note that primary 160 MHz is composed of primary 80 MHz and secondary 80 MHz and secondary 160 MHz is 160 MHz channel other than the primary 160 MHz in 320/160+160 MHz.
  802.11be supports the following mandatory RU combinations for large-size RUs.
BW | RU | Mandatory in OFDMA for:
80 MHz | 484+242 | Non-AP STA only
160 MHz | 996+484 | Non-AP STA only
240 MHz | 2×996+484 | Non-AP STA only
320 MHz | 3×996+484, 3×996 (any 3) | Non-AP STA only

## Slide 4: Large-size MRU Combinations in 240MHz and 320MHz (cont’d)
It is definitely defined in the SFD that 484+242, 996+484, 3x996+484, 3x996 , 2x996 combinations are supported in 320MHz. But, it is not clear whether 2x996+484 is supported for OFDMA transmission in 320MHz.
For the OFDMA transmission in 320 MHz, large-size MRU of 2x996+484 may be allowed within 240 MHz which is composed of three adjacent 80 MHz segments.
But, we don’t know whether the inclusion of 2x996+484 in 320MHz is really valuable to increase the size of RU Allocation subfield table.
Therefore, we think that MRU combinations of 2×996+484 can be supported only in 240MHz PPDU while MRU combinations of 3×996+484 and 3×996 can be supported only in 320MHz PPDU.

## Slide 5: Unified RU Allocation Subfield Values
If the above-mentioned aspect is agreed, we propose to merge the values for MRU combinations of 2×996+484 in RU Allocation subfield table with the values for MRU combinations of 3×996+484 and 3×996 in RU Allocation subfield table for a decrease in the number of entries for RU Allocation subfield table, which may reduce the bit-width of RU Allocation subfield.
The following table shows an example of RU Allocation subfield table for large-size MRU combinations in 240/320MHz PPDU.
  48 entries can be saved compared to the case that merging the values of RU Allocation subfield is not considered.
RU Allocation subfield (B7 B6 B5 B4 B3 B2 B1 B0) | #1 | #2 | #3 | #4 | #5 | #6 | #7 | #8 | #9 | BW | Number of entries
152-159(10011y2y1y0) | 2×RU996+RU484; MRU 1 - [empty-RU484 RU484 RU996 RU996] when BW=240MHz |  |  |  |  |  |  |  |  | 240MHz | 8
160-167(10100y2y1y0) | 2×RU996+RU484; MRU 2 - [RU484 empty-RU484 RU996 RU996] when BW=240MHz |  |  |  |  |  |  |  |  |  | 8
168-175(10101y2y1y0) | 2×RU996+RU484; MRU 3 - [RU996 RU996 empty-RU484 RU484] when BW=240MHz |  |  |  |  |  |  |  |  |  | 8
176-183(10110y2y1y0) | 2×RU996+RU484; MRU 4 - [RU996 RU996 RU484 empty-RU484] when BW=240MHz |  |  |  |  |  |  |  |  |  | 8
184-191(10111y2y1y0) | 2×RU996+RU484; MRU 5 - [RU996 empty-RU484 RU484 RU996] when BW=240MHz |  |  |  |  |  |  |  |  |  | 8
192-199(11000y2y1y0) | 2×RU996+RU484; MRU 6 - [RU996 RU484 empty-RU484 RU996] when BW=240MHz |  |  |  |  |  |  |  |  |  | 8
200-255 | Reserved |  |  |  |  |  |  |  |  |  | 56
152-159(10011y2y1y0) | 3×RU996+RU484; MRU 1 - [empty-RU484 RU484 RU996 RU996 RU996] when BW=320MHz |  |  |  |  |  |  |  |  | 320MHz | 8
160-167(10100y2y1y0) | 3×RU996+RU484; MRU 2 - [RU484 empty-RU484 RU996 RU996 RU996] when BW=320MHz |  |  |  |  |  |  |  |  |  | 8
168-175(10101y2y1y0) | 3×RU996+RU484; MRU 3 - [RU996 empty-RU484 RU484 RU996 RU996] when BW=320MHz |  |  |  |  |  |  |  |  |  | 8
176-183(10110y2y1y0) | 3×RU996+RU484; MRU 4 - [RU996 RU484 empty-RU484 RU996 RU996] when BW=320MHz |  |  |  |  |  |  |  |  |  | 8
184-191(10111y2y1y0) | 3×RU996+RU484; MRU 5 - [RU996 RU996 empty-RU484 RU484 RU996] when BW=320MHz |  |  |  |  |  |  |  |  |  | 8
192-199(11000y2y1y0) | 3×RU996+RU484; MRU 6 - [RU996 RU996 RU484 empty-RU484 RU996] when BW=320MHz |  |  |  |  |  |  |  |  |  | 8
200-207(11001y2y1y0) | 3×RU996+RU484; MRU 7 - [RU996 RU996 RU996 empty-RU484 RU484] when BW=320MHz |  |  |  |  |  |  |  |  |  | 8
208-215(11010y2y1y0) | 3×RU996+RU484; MRU 8 - [RU996 RU996 RU996 RU484 empty-RU484] when BW=320MHz |  |  |  |  |  |  |  |  |  | 8
216-223(11011y2y1y0) | 3×RU996 (any 3); MRU 1 - [empty-RU996 RU996 RU996 RU996] when BW=320MHz |  |  |  |  |  |  |  |  |  | 8
224-231(11100y2y1y0) | 3×RU996 (any 3); MRU 2 - [RU996 empty-RU996 RU996 RU996] when BW=320MHz |  |  |  |  |  |  |  |  |  | 8
232-239(11101y2y1y0) | 3×RU996 (any 3); MRU 3 - [RU996 RU996 empty-RU996 RU996] when BW=320MHz |  |  |  |  |  |  |  |  |  | 8
240-247(11110y2y1y0) | 3×RU996 (any 3); MRU 4 - [RU996 RU996 RU996 empty-RU996] when BW=320MHz |  |  |  |  |  |  |  |  |  | 8
248-255 | Reserved |  |  |  |  |  |  |  |  |  | 8

## Slide 6: Zero User Indication
An RU that is not allocated to a user should be also indicated in EHT.
For both small-size and large-size RU or MRU
  As in 11ax, the STA-ID related information may be set to a determined value to indicate the zero users in 11be. (e.g., The STA-ID subfield in the HE-SIG-B User field is set to 2046 in 11ax.)
For small-size RU or MRU
  As in 11ax, the RU Allocation subfield is set to a value corresponding to the entry including the punctured small-size RU or MRU to indicate the zero users in 11be.
  E.g., if the RU Allocation subfield is set to a value indicating the following entry, it means that there is no user in the middle 26-tone RU.
RU Allocation subfield | #1 | #2 | #3 | #4 | #5 | #6 | #7 | #8 | #9 | Number of entries
TBD | 52 |  | 52 |  | _ | 52 |  | 52 |  | 1

## Slide 7: Zero User Indication (cont’d)
For large-size RU or MRU
  In 11ax, the following three entries can be used to indicate the zero users for large-size RU.
  For 11be, one more entry of ‘242-tone RU; contributes zero User fields to the User Specific field’ to indicate the zero users for MRU combinations of 484+242 is required. But, we don’t need to differentiate this new entry from the entry of ‘484-tone RU; contributes zero User fields to the User Specific field’ because 242-tone RU and 484-tone RU have the same indices of data and pilot tones in 11be [1].
  Therefore, we propose to use the following only three entries in order to indicate the zero users for large-size RU or MRU in 11be.
RU Allocation subfield (B7 B6 B5 B4 B3 B2 B1 B0) | #1 | #2 | #3 | #4 | #5 | #6 | #7 | #8 | #9 | Number of entries
113 (01110001) | 242-tone RU empty (with zero users) |  |  |  |  |  |  |  |  | 1
114 (01110010) | 484-tone RU; contributes zero User fields to the User Specific field |  |  |  |  |  |  |  |  | 1
115 (01110011) | 996-tone RU; contributes zero User fields to the User Specific field |  |  |  |  |  |  |  |  | 1
RU Allocation subfield | #1 | #2 | #3 | #4 | #5 | #6 | #7 | #8 | #9 | Number of entries
TBD | 242-tone RU empty (with zero users) |  |  |  |  |  |  |  |  | 1
TBD | 242-tone RU or 484-tone RU; contributes zero User fields to the User Specific field in the same EHT-SIG content channel as this RU Allocation subfield and is not punctured |  |  |  |  |  |  |  |  | 1
TBD | 996-tone RU; contributes zero User fields to the User Specific field in the same EHT-SIG content channel as this RU Allocation subfield and is not punctured |  |  |  |  |  |  |  |  | 1

## Slide 8: Details for Zero User Indication in Large-size MRUs
For the entry of ‘242-tone RU or 484-tone RU; contributes zero User fields to the User Specific field in the same EHT-SIG content channel as this RU Allocation subfield and is not punctured’, the RU Allocation subfield corresponding to RU484 or RU242 in large-size MRU combinations of 484+242, 996+484, 2×996+484, and 3×996+484 can be set to a value of this entry in RU Allocation subfield table to indicate the zero users.
For the entry of ‘996-tone RU; contributes zero User fields to the User Specific field in the same EHT-SIG content channel as this RU Allocation subfield and is not punctured’, the RU Allocation subfield corresponding to RU996 in large-size MRU combinations of 996+484, 2×996+484, 3×996+484, 3×996, and 2×996 can be set to a value of this entry in RU Allocation subfield table to indicate the zero users.
Example (based on the RU Allocation subfield table in Appendix)
    One user is assigned in MRU of 996+484.
RU Allocation subfield ( B7 B6 B5 B4 B3 B2 B1 B0) | #1 | #2 | #3 | #4 | #5 | #6 | #7 | #8 | #9 | Number of entries
51 | 242-tone RU or 484-tone RU; contributes zero User fields to the User Specific field ---- |  |  |  |  |  |  |  |  | 1
52 | 996-tone RU; contributes zero User fields to the User Specific field ----- |  |  |  |  |  |  |  |  | 1
120-127(01111y2y1y0) | RU996+RU484; MRU 1 - [empty-RU484 RU484 RU996] |  |  |  |  |  |  |  |  | 8
996
484
484
Value of RU Allocation subfield
-
-
120
51
52
52
52
52

## Slide 9: Updated Content (Rev2)
In updated slide, we further address the necessity of the proposed zero user indication method for large-size MRUs by introducing an applicable and useful scenario in EHT.

## Slide 10: Applicable and Useful Scenario
In 11be, considering multi-segment EHT-SIG or A-PPDU structure, the following case can be considered [2].
  BW field in U-SIG can be different across different segments and the content channels per each 80MHz carries the information of its BW.
  In this case, CCs in 1st 80MHz don’t contain the information of 996+484 RU Allocation subfield. Therefore, RU Allocation subfields in 1st 80MHz corresponding to RU484 portion of MRU of 996+484 should be RU484 zero users (for both RU Allocation subfields) in order to indicate the exact information of indices of data and pilot tones in lower 40MHz of 1st 80MHz.
L-preamble+U-SIG1
L-preamble+U-SIG1
L-preamble+U-SIG1
L-preamble+U-SIG1
EHT-SIG CC11
EHT-SIG CC12
EHT-SIG CC11
EHT-SIG CC12
L-preamble+U-SIG2
L-preamble+U-SIG2
L-preamble+U-SIG2
L-preamble+U-SIG2
EHT-SIG CC21
EHT-SIG CC22
EHT-SIG CC21
EHT-SIG CC22
2 RU Allocation subfields per CC
BW=80MHz
BW=160MHz
4 RU Allocation subfields per CC
Data STA1
Data STA2
Data STA3
Data STA4
STA1-4 parking in 1st 80MHz
STA5 parking in 2nd 80MHz
484RU
996RU
Data STA5

## Slide 11: Summary
In this contribution,
  We introduced the way to reduce the entries overhead in RU Allocation subfield table by merging the values for MRU combinations in RU Allocation subfield table.
  Also, we discussed the required entries to indicate the zero users.
Then, we can design 8-bit RU Allocation subfield table which is included in Appendix.

## Slide 12: SP #1 Explain
Propose to have following
  Unassigned RU 242
  Punctured RU 242
  RU xxx with zero user fields, but not unallocated
  STA ID 2046 is indicating unallocated RU for 106-tone or smaller RU.
  Note1: For equal or larger than 242-tone RU, STA ID 2046 shall not be used to indicated unallocated RU instead unassigned RU 242 shall be used.
  Note2: Punctured RU 242 shall be used when the preamble portion of corresponding 20MHz is punctured.
Need to cover following three cases for 242
  242 zero user: assigned to large size MRU including 242 tone RU, e.g. 242+484
  242 unassigned: data not assigned, zero energy, but preamble is not punctured
  242 punctured: data not assigned, zero energy, and preamble is also punctured

## Slide 13: Straw Poll #1
Do you agree to:
  Add two entries in the RU Allocation subfield table to indicate that
    Punctured 242-tone RU
    Unassigned 242-tone RU
  Modify the existing entry “242-tone RU empty (with zero users)” to “242-tone RU; contributes zero User fields to the User Specific field in the same EHT-SIG content channel as this RU Allocation subfield and is not unallocated”
  Modify the existing entry “484-tone RU; contributes zero User fields to the User Specific field in the same EHT-SIG content channel as this RU Allocation subfield” to “484-tone RU; contributes zero User fields to the User Specific field in the same EHT-SIG content channel as this RU Allocation subfield and is not unallocated”
  Modify the existing entry “996-tone RU; contributes zero User fields to the User Specific field in the same EHT-SIG content channel as this RU Allocation subfield and is not punctured” to “996-tone RU; contributes zero User fields to the User Specific field in the same EHT-SIG content channel as this RU Allocation subfield and is not unallocated”
  Add following
    STA ID 2046 is indicating unallocated RU for 106-tone or smaller RU.
    Note1: For equal or larger than 242-tone RU, STA ID 2046 shall not be used to indicated unallocated RU instead unassigned RU 242 shall be used.
    Note2: Punctured RU 242 shall be used when the preamble portion of corresponding 20MHz is punctured.

## Slide 14: Straw Poll #2
Do you agree to add the following text to the TGbe SFD?
  The RU Allocation subfield corresponding to RU242 in large-size MRU combinations of 484+242 is set to x (TBD) to indicate the zero users.
    x is a value corresponding to the entry of ‘242-tone RU; contributes zero User fields to the User Specific field in the same EHT-SIG content channel as this RU Allocation subfield and is not punctured’ in RU Allocation subfield table.
  The RU Allocation subfield corresponding to RU484 in large-size MRU combinations of 484+242, 996+484, 2×996+484, and 3×996+484 is set to y (TBD) to indicate the zero users.
    y is a value corresponding to the entry of ‘484-tone RU; contributes zero User fields to the User Specific field in the same EHT-SIG content channel as this RU Allocation subfield and is not punctured’ in RU Allocation subfield table.
  The RU Allocation subfield corresponding to RU996 in large-size MRU combinations of 996+484, 2×996+484, 3×996+484, 3×996, and 2×996 is set to z to indicate the zero users.
    z is a value corresponding to the entry of ‘996-tone RU; contributes zero User fields to the User Specific field in the same EHT-SIG content channel as this RU Allocation subfield and is not punctured’ in RU Allocation subfield table.

## Slide 15: Reference
[1] 802.11-20/0566r34, Specification Framework for TGbe.
[2] 802.11-20/0964r3, Bandwidth Indication for EHT PPDU.

## Slide 16: Appendix

## Slide 17: Example of RU Allocation Subfield Table
RU Allocation subfield (B7 B6 B5 B4 B3 B2 B1 B0) | #1 | #2 | #3 | #4 | #5 | #6 | #7 | #8 | #9 | BW | Number of entries
0 | 26 | 26 | 26 | 26 | 26 | 26 | 26 | 26 | 26 | - | 1
1 | 26 | 26 | 26 | 26 | 26 | 26 | 26 | 52 |  | - | 1
2 | 26 | 26 | 26 | 26 | 26 | 52 |  | 26 | 26 | - | 1
3 | 26 | 26 | 26 | 26 | 26 | 52 |  | 52 |  | - | 1
4 | 26 | 26 | 52 |  | 26 | 26 | 26 | 26 | 26 | - | 1
5 | 26 | 26 | 52 |  | 26 | 26 | 26 | 52 |  | - | 1
6 | 26 | 26 | 52 |  | 26 | 52 |  | 26 | 26 | - | 1
7 | 26 | 26 | 52 |  | 26 | 52 |  | 52 |  | - | 1
8 | 52 |  | 26 | 26 | 26 | 26 | 26 | 26 | 26 | - | 1
9 | 52 |  | 26 | 26 | 26 | 26 | 26 | 52 |  | - | 1
10 | 52 |  | 26 | 26 | 26 | 52 |  | 26 | 26 | - | 1
11 | 52 |  | 26 | 26 | 26 | 52 |  | 52 |  | - | 1
12 | 52 |  | 52 |  | 26 | 26 | 26 | 26 | 26 | - | 1
13 | 52 |  | 52 |  | 26 | 26 | 26 | 52 |  | - | 1
14 | 52 |  | 52 |  | 26 | 52 |  | 26 | 26 | - | 1
15 | 52 |  | 52 |  | 26 | 52 |  | 52 |  | - | 1
16 | 26 | 26 | 26 | 26 | 26 | 106 |  |  |  | - | 1
17 | 26 | 26 | 52 |  | 26 | 106 |  |  |  | - | 1
18 | 52 |  | 26 | 26 | 26 | 106 |  |  |  | - | 1
19 | 52 |  | 52 |  | 26 | 106 |  |  |  | - | 1
20 | 106 |  |  |  | 26 | 26 | 26 | 26 | 26 | - | 1
21 | 106 |  |  |  | 26 | 26 | 26 | 52 |  | - | 1
22 | 106 |  |  |  | 26 | 52 |  | 26 | 26 | - | 1
23 | 106 |  |  |  | 26 | 52 |  | 52 |  | - | 1
24 | 52 |  | 52 |  | _ | 52 |  | 52 |  | - | 1
25 | 106 |  |  |  | 26 | 106 |  |  |  | - | 1
26 | 26 | 26+52 multi-RU |  |  | 26 | 26 | 26 | 26 | 26 | - | 1
27 | 26 | 26+52 multi-RU |  |  | 26 | 26 | 26 | 52 |  | - | 1
28 | 26 | 26+52 multi-RU |  |  | 26 | 52 |  | 26 | 26 | - | 1
29 | 26 | 26+52 multi-RU |  |  | 26 | 52 |  | 52 |  | - | 1
30 | 26 | 26 | 26 | 26 | 26 | 52+26 multi-RU |  |  | 26 | - | 1
31 | 26 | 26 | 52 |  | 26 | 52+26 multi-RU |  |  | 26 | - | 1
32 | 52 |  | 26 | 26 | 26 | 52+26 multi-RU |  |  | 26 | - | 1
33 | 52 |  | 52 |  | 26 | 52+26 multi-RU |  |  | 26 | - | 1
34 | 26 | 26+52 multi-RU |  |  | 26 | 106 |  |  |  | - | 1
35 | 106 |  |  |  | 26 | 52+26 multi-RU |  |  | 26 | - | 1
36 | 106+26 multi-RU |  |  |  |  | 26 | 26 | 26 | 26 | - | 1
37 | 106+26 multi-RU |  |  |  |  | 26 | 26 | 52 |  | - | 1
38 | 106+26 multi-RU |  |  |  |  | 52 |  | 26 | 26 | - | 1
39 | 106+26 multi-RU |  |  |  |  | 52 |  | 52 |  | - | 1
40 | 106+26 multi-RU |  |  |  |  | 106 |  |  |  | - | 1
41 | 26 | 26 | 26 | 26 | 26+106 multi-RU |  |  |  |  | - | 1

## Slide 18: Example of RU Allocation Subfield Table (Cont’d)
RU Allocation subfield (B7 B6 B5 B4 B3 B2 B1 B0) | #1 | #2 | #3 | #4 | #5 | #6 | #7 | #8 | #9 | BW | Number of entries
42 | 26 | 26 | 52 |  | 26+106 multi-RU |  |  |  |  | - | 1
43 | 52 |  | 26 | 26 | 26+106 multi-RU |  |  |  |  | - | 1
44 | 52 |  | 52 |  | 26+106 multi-RU |  |  |  |  | - | 1
45 | 106 |  |  |  | 26+106 multi-RU |  |  |  |  | - | 1
46 | 26 | 26+52 multi-RU |  |  | 26+106 multi-RU |  |  |  |  | - | 1
47 | 106+26 multi-RU |  |  |  |  | 52+26 multi-RU |  |  | 26 | - | 1
48 | 26 | 26+52 multi-RU |  |  | 26 | 52+26 multi-RU |  |  | 26 | - | 1
49 | 52 |  | 52+26 multi-RU |  |  | 52 |  | 52 |  | - | 1
50 | 242-tone RU empty (with zero users) |  |  |  |  |  |  |  |  | - | 1
51 | 242-tone RU or 484-tone RU; contributes zero User fields to the User Specific field in the same EHT-SIG content channel as this RU Allocation subfield and is not punctured |  |  |  |  |  |  |  |  | - | 1
52 | 996-tone RU; contributes zero User fields to the User Specific field in the same EHT-SIG content channel as this RU Allocation subfield and is not punctured |  |  |  |  |  |  |  |  | - | 1
53-55 | Reserved |  |  |  |  |  |  |  |  | - | 3
56-63(00111y2y1y0) | 242 |  |  |  |  |  |  |  |  | - | 8
64-71(01000y2y1y0) | 484 |  |  |  |  |  |  |  |  | - | 8
72-79(01001y2y1y0) | 996 |  |  |  |  |  |  |  |  | - | 8
80-87(01010y2y1y0) | 2xRU996 |  |  |  |  |  |  |  |  | - | 8
88-95(01011y2y1y0) | RU484+RU242; MRU 1 - [empty-RU242 RU242 RU484] |  |  |  |  |  |  |  |  | - | 8
96-103(01100y2y1y0) | RU484+RU242; MRU 2 - [RU242 empty-RU242 RU484] |  |  |  |  |  |  |  |  | - | 8
104-111(01101y2y1y0) | RU484+RU242; MRU 3 - [RU484 empty-RU242 RU242] |  |  |  |  |  |  |  |  | - | 8
112-119(01110y2y1y0) | RU484+RU242; MRU 4 - [RU484 RU242 empty-RU242] |  |  |  |  |  |  |  |  | - | 8
120-127(01111y2y1y0) | RU996+RU484; MRU 1 - [empty-RU484 RU484 RU996] |  |  |  |  |  |  |  |  | - | 8
128-135(10000y2y1y0) | RU996+RU484; MRU 2 - [RU484 empty-RU484 RU996] |  |  |  |  |  |  |  |  | - | 8
136-143(10001y2y1y0) | RU996+RU484; MRU 3 - [RU996 empty-RU484 RU484] |  |  |  |  |  |  |  |  | - | 8
144-151(10010y2y1y0) | RU996+RU484; MRU 4 - [RU996 RU484 empty-RU484] |  |  |  |  |  |  |  |  | - | 8
152-159(10011y2y1y0) | 2×RU996+RU484; MRU 1 - [empty-RU484 RU484 RU996 RU996] when BW=240MHz |  |  |  |  |  |  |  |  | 240MHz | 8
160-167(10100y2y1y0) | 2×RU996+RU484; MRU 2 - [RU484 empty-RU484 RU996 RU996] when BW=240MHz |  |  |  |  |  |  |  |  |  | 8
168-175(10101y2y1y0) | 2×RU996+RU484; MRU 3 - [RU996 RU996 empty-RU484 RU484] when BW=240MHz |  |  |  |  |  |  |  |  |  | 8
176-183(10110y2y1y0) | 2×RU996+RU484; MRU 4 - [RU996 RU996 RU484 empty-RU484] when BW=240MHz |  |  |  |  |  |  |  |  |  | 8
184-191(10111y2y1y0) | 2×RU996+RU484; MRU 5 - [RU996 empty-RU484 RU484 RU996] when BW=240MHz |  |  |  |  |  |  |  |  |  | 8
192-199(11000y2y1y0) | 2×RU996+RU484; MRU 6 - [RU996 RU484 empty-RU484 RU996] when BW=240MHz |  |  |  |  |  |  |  |  |  | 8
200-255 | Reserved |  |  |  |  |  |  |  |  |  | 56
152-159(10011y2y1y0) | 3×RU996+RU484; MRU 1 - [empty-RU484 RU484 RU996 RU996 RU996] when BW=320MHz |  |  |  |  |  |  |  |  | 320MHz | 8
160-167(10100y2y1y0) | 3×RU996+RU484; MRU 2 - [RU484 empty-RU484 RU996 RU996 RU996] when BW=320MHz |  |  |  |  |  |  |  |  |  | 8
168-175(10101y2y1y0) | 3×RU996+RU484; MRU 3 - [RU996 empty-RU484 RU484 RU996 RU996] when BW=320MHz |  |  |  |  |  |  |  |  |  | 8
176-183(10110y2y1y0) | 3×RU996+RU484; MRU 4 - [RU996 RU484 empty-RU484 RU996 RU996] when BW=320MHz |  |  |  |  |  |  |  |  |  | 8
184-191(10111y2y1y0) | 3×RU996+RU484; MRU 5 - [RU996 RU996 empty-RU484 RU484 RU996] when BW=320MHz |  |  |  |  |  |  |  |  |  | 8
192-199(11000y2y1y0) | 3×RU996+RU484; MRU 6 - [RU996 RU996 RU484 empty-RU484 RU996] when BW=320MHz |  |  |  |  |  |  |  |  |  | 8
200-207(11001y2y1y0) | 3×RU996+RU484; MRU 7 - [RU996 RU996 RU996 empty-RU484 RU484] when BW=320MHz |  |  |  |  |  |  |  |  |  | 8
208-215(11010y2y1y0) | 3×RU996+RU484; MRU 8 - [RU996 RU996 RU996 RU484 empty-RU484] when BW=320MHz |  |  |  |  |  |  |  |  |  | 8
216-223(11011y2y1y0) | 3×RU996 (any 3); MRU 1 - [empty-RU996 RU996 RU996 RU996] when BW=320MHz |  |  |  |  |  |  |  |  |  | 8
224-231(11100y2y1y0) | 3×RU996 (any 3); MRU 2 - [RU996 empty-RU996 RU996 RU996] when BW=320MHz |  |  |  |  |  |  |  |  |  | 8
232-239(11101y2y1y0) | 3×RU996 (any 3); MRU 3 - [RU996 RU996 empty-RU996 RU996] when BW=320MHz |  |  |  |  |  |  |  |  |  | 8
240-247(11110y2y1y0) | 3×RU996 (any 3); MRU 4 - [RU996 RU996 RU996 empty-RU996] when BW=320MHz |  |  |  |  |  |  |  |  |  | 8
248-255 | Reserved |  |  |  |  |  |  |  |  |  | 8

## Slide 19: Straw Poll #1
Do you support that for the OFDMA transmission, large-size MRU of 2x996+484 is not supported in 320MHz?

## Slide 20: Straw Poll #2
Do you support that the values of RU Allocation subfield for MRU combinations of 2×996+484 are unified with the some of values of RU Allocation subfield for MRU combinations of 3×996+484 and 3×996 in RU Allocation subfield table?

## Slide 21: Straw Poll #3
Do you agree to:
  Add two entries in the RU Allocation subfield table to indicate that
    Punctured 242-tone RU
    Unassigned 242-tone RU
  Modify the existing entry “242-tone RU empty (with zero users)” to “242-tone RU; contributes zero User fields to the User Specific field in the same EHT-SIG content channel as this RU Allocation subfield and is not unallocated”
  Modify the existing entry “484-tone RU; contributes zero User fields to the User Specific field in the same EHT-SIG content channel as this RU Allocation subfield” to “484-tone RU; contributes zero User fields to the User Specific field in the same EHT-SIG content channel as this RU Allocation subfield and is not unallocated”
  Modify the existing entry “996-tone RU; contributes zero User fields to the User Specific field in the same EHT-SIG content channel as this RU Allocation subfield and is not punctured” to “996-tone RU; contributes zero User fields to the User Specific field in the same EHT-SIG content channel as this RU Allocation subfield and is not unallocated”
  Add following notes
    Note1: For equal or larger than 242-tone RU, STA ID 2046 shall not be used to indicated unallocated RU instead unassigned RU 242 shall be used.
    Note2: Punctured RU 242 shall be used when the preamble portion of corresponding 20MHz is punctured.

## Slide 22: Straw Poll #4
Do you support to use one entry of “242-tone RU or 484-tone RU; contributes zero User fields to the User Specific field in the same EHT-SIG content channel as this RU Allocation subfield and is not punctured” by merging two entries of “242-tone RU; contributes zero User fields to the User Specific field in the same EHT-SIG content channel as this RU Allocation subfield and is not punctured” and “484-tone RU; contributes zero User fields to the User Specific field in the same EHT-SIG content channel as this RU Allocation subfield and is not punctured” in the RU Allocation subfield table?
Order | #1 | #2 | #3 | #4 | #5 | #6 | #7 | #8 | #9 | Number of entries
TBD | 242-tone RU; contributes zero User fields to the User Specific field in the same EHT-SIG content channel as this RU Allocation subfield and is not punctured |  |  |  |  |  |  |  |  | 1
TBD | 484-tone RU; contributes zero User fields to the User Specific field in the same EHT-SIG content channel as this RU Allocation subfield and is not punctured |  |  |  |  |  |  |  |  | 1
Order | #1 | #2 | #3 | #4 | #5 | #6 | #7 | #8 | #9 | Number of entries
TBD | 242-tone RU or 484-tone RU; contributes zero User fields to the User Specific field in the same EHT-SIG content channel as this RU Allocation subfield and is not punctured |  |  |  |  |  |  |  |  | 1

## Slide 23: Straw Poll #5
Do you agree to add the following text to the TGbe SFD?
  The RU Allocation subfield corresponding to RU484 or RU242 in large-size MRU combinations of 484+242, 996+484, 2×996+484, and 3×996+484 is set to x (TBD) to indicate the zero users.
    x is a value corresponding to the entry of ‘242-tone RU or 484-tone RU; contributes zero User fields to the User Specific field in the same EHT-SIG content channel as this RU Allocation subfield and is not punctured’ in RU Allocation subfield table.
  The RU Allocation subfield corresponding to RU996 in large-size MRU combinations of 996+484, 2×996+484, 3×996+484, 3×996, and 2×996 is set to y to indicate the zero users.
    y is a value corresponding to the entry of ‘996-tone RU; contributes zero User fields to the User Specific field in the same EHT-SIG content channel as this RU Allocation subfield and is not punctured’ in RU Allocation subfield table.

## Slide 24: Straw Poll #6
Do you agree to add the following text to the TGbe SFD?
  The RU Allocation subfield corresponding to RU242 in large-size MRU combinations of 484+242 is set to x (TBD) to indicate the zero users.
    x is a value corresponding to the entry of ‘242-tone RU; contributes zero User fields to the User Specific field in the same EHT-SIG content channel as this RU Allocation subfield and is not punctured’ in RU Allocation subfield table.
  The RU Allocation subfield corresponding to RU484 in large-size MRU combinations of 484+242, 996+484, 2×996+484, and 3×996+484 is set to y (TBD) to indicate the zero users.
    y is a value corresponding to the entry of ‘484-tone RU; contributes zero User fields to the User Specific field in the same EHT-SIG content channel as this RU Allocation subfield and is not punctured’ in RU Allocation subfield table.
  The RU Allocation subfield corresponding to RU996 in large-size MRU combinations of 996+484, 2×996+484, 3×996+484, 3×996, and 2×996 is set to z to indicate the zero users.
    z is a value corresponding to the entry of ‘996-tone RU; contributes zero User fields to the User Specific field in the same EHT-SIG content channel as this RU Allocation subfield and is not punctured’ in RU Allocation subfield table.