## Slide 1: Agenda for IEEE 802.11 Coexistence SC virtual meeting in July 2020
14 July 2020
Authors:
Name | Company | Phone | email
Andrew Myles | Cisco | +61 418 656587 | amyles@cisco.com

## Slide 2: Welcome to the 1st virtual plenary meeting of the Coex SC in July 2020
  The IEEE 802.11 PDED ad hoc was formed in September 2016 at the Warsaw interim meeting
  The IEEE 802.11 PDED ad hoc met in San Antonio (Nov 2016), Atlanta (Jan 2017), Vancouver (Mar 2017) and Daejeon (May 2017)
  In Daejeon in May 2017 it was decided to convert the IEEE 802.11 PDED ad hoc into the IEEE 802.11 Coexistence SC
  The IEEE 802.11 Coexistence SC met in Berlin (July 2017), Hawaii (Sept 2017), Orlando (Nov 2017), Irvine (Jan 2018), Chicago (Mar 2018), Warsaw (May 2018), San Diego (July 2018), Hawaii (Sept 2018), Bangkok (Nov 2018), St Louis (Jan 2019), Vancouver (Mar 2019), Atlanta (May 2019), Vienna (Jul 2019), Hanoi (Sep 2019), Hawaii (Nov 2019) & Irvine (Jan 2020)
  It has not met since then ...

## Slide 3: Coex SC minutes today will be kept by our permanent SC secretary
  It is important to keep proper minutes of all Coexistence SC meetings
  Fortunately, Guido Hiertz (Ericsson) agreed in Berlin (in July 2017) to be appointed the IEEE 802.11 Coexistence SC’s permanent Secretary …

## Slide 4: Meetings shall be conducted in compliance with all applicable laws, including antitrust & competition laws
  Don’t discuss the interpretation, validity, or essentiality of patents/patent claims
  Don’t discuss specific license rates, terms, or conditions
    Relative costs of different technical approaches that include relative costs of patent licensing terms may be discussed in standards development meetings
      Technical considerations remain the primary focus
  Don’t discuss or engage in the fixing of product prices, allocation of customers, or division of sales markets
  Don’t discuss the status or substance of ongoing or threatened litigation
  Don’t be silent if inappropriate topics are discussed … do formally object
  For more details, see IEEE-SA Standards Board Ops Man, 5.3.10 and Antitrust and Competition Policy: What You Need to Know available here
  If you have questions, contact the IEEE-SA Standards Board Patent Committee Administrator at patcom@ieee.org
Approved slide

## Slide 5: Participant behavior in IEEE-SA activities is guided by the IEEE Codes of Ethics & Conduct
  All participants in IEEE-SA activities are expected to adhere to the core principles underlying the:
    IEEE Code of Ethics
    IEEE Code of Conduct
  The core principles of the IEEE Codes of Ethics & Conduct are to:
    Uphold the highest standards of integrity, responsible behavior, and ethical and professional conduct
    Treat people fairly and with respect, to not engage in harassment, discrimination, or retaliation, and to protect people's privacy.
    Avoid injuring others, their property, reputation, or employment by false or malicious action
  The most recent versions of these Codes are available at
    http://www.ieee.org/about/corporate/governance
Approved slide

## Slide 6: Participants in the IEEE-SA “individual process” shall act independently of others, including employers
  The IEEE-SA Standards Board Bylaws require that “participants in the IEEE standards development individual process shall act based on their qualifications and experience”
  This means participants:
    Shall act & vote based on their personal & independent opinions derived from their expertise, knowledge, and qualifications
    Shall not act or vote based on any obligation to or any direction from any other person or organization, including an employer or client, regardless of any external commitments, agreements, contracts, or orders
    Shall not direct the actions or votes of other participants or retaliate against other participants for fulfilling their responsibility to act & vote based on their personal & independently developed opinions
  By participating in standards activities using the “individual process”, you are deemed to accept these requirements; if you are unable to satisfy these requirements then you shall immediately cease any participation
Approved slide

## Slide 7: IEEE-SA standards activities shall allow the fair & equitable consideration of all viewpoints
  The IEEE-SA Standards Board Bylaws (clause 5.2.1.3) specifies that “the standards development process shall not be dominated by any single interest category, individual, or organization”
    This means no participant may exercise “authority, leadership, or influence by reason of superior leverage, strength, or representation to the exclusion of fair and equitable consideration of other viewpoints” or “to hinder the progress of the standards development activity”
  This rule applies equally to those participating in a standards development project and to that project’s leadership group
  Any person who reasonably suspects that dominance is occurring in a standards development project is encouraged to bring the issue to the attention of the Standards Committee or the project’s IEEE-SA Program Manager
Approved slide

## Slide 8: IEEE SA Copyright Policy
  By participating in this activity, you agree to comply with the IEEE Code of Ethics, all applicable laws, and all IEEE policies and procedures including, but not limited to, the IEEE SA Copyright Policy.
    Previously Published material (copyright assertion indicated) shall not be presented/submitted to the Working Group nor incorporated into a Working Group draft unless permission is granted.
    Prior to presentation or submission, you shall notify the Working Group Chair of previously Published material and should assist the Chair in obtaining copyright permission acceptable to IEEE SA.
    For material that is not previously Published, IEEE is automatically granted a license to use any material that is presented or submitted.
Approved slide

## Slide 9: IEEE SA Copyright Policy
  The IEEE SA Copyright Policy is described in the IEEE SA Standards Board Bylaws and IEEE SA Standards Board Operations Manual
    IEEE SA Copyright Policy, see:
      Clause 7 of the IEEE SA Standards Board Bylaws
      Clause 6.1 of the IEEE SA Standards Board Operations Manual
  IEEE SA Copyright Permission
  IEEE SA Copyright FAQs
  IEEE SA Best Practices for IEEE Standards Development
  Distribution of Draft Standards (see Clause 6.1.3 of the SASB Operations Manual)
Approved slide

## Slide 10: The Coex SC will meet one during the virtual IEEE 802 plenary meeting in July 2020
IEEE 802.11 Coex teleconference
  Tuesday, 14 July 2020 @ 5-7 pm ET
  Webex details:
    ieeesa.webex.com/ieeesa/j.php?MTID=m81a00724b8e394780f88ffa6c16ebb5f
    Meeting number: 129 750 9828
    Meeting password: wireless (94735377 from phones and video systems)

## Slide 11: The Coex SC will consider a proposed agenda for its virtual meeting in July 2020
Proposed Agenda
  Bureaucratic stuff
    Scope of IEEE 802.11 Coexistence SC (a reminder)
    Approve minutes
  What is happening this week? (in no particular order)
    LS to/from ERM TG11
    Review of recent ETSI BRAN activities
      EN 301 893 issues (5 GHz)
      EN 303 687 issues (6 GHz)
    Discussion of extension of Coex SC charter
    Plans for next meeting
    Other business

## Slide 12
  Scope of IEEE 802.11 Coexistence SC

## Slide 13: The agreed Coex SC scope focuses on ensuring 802.11ax has fair access to global unlicensed spectrum
Discuss the use of PD, ED or other 802.11 coexistence mechanisms with the goal of promoting “fair” use of unlicensed spectrum
Promote an environment that allow IEEE 802.11ax “fair access” to global unlicensed spectrum
Will initially focus on liaising with 3GPP RAN/RAN1/RAN4 but may also lead to interactions with regulators and other stakeholders
Will probably not conclude at least until RAN4’s 802.11/LAA coexistence testing is defined and successfully executed
May require the SC to consider other simulations and results of tests of potential LAA/802.11 coexistence mechanisms
Will initially focus on encouraging a “technology neutral” solution in the next revision of EN 301 893 that allows IEEE 802.11ax fair access to unlicensed spectrum in Europe (noting the European approach is likely to have global impact)
The effort will also focus on allowing 802.11ax to use innovative mechanisms for frequency reuse without compromising the goal of fair access

## Slide 14: Coex SC will close when determined by the 802.11 WG or 802.11ax is ratified
IEEE 802.11 Coexistence SC close down criteria
  The SC is closed by the IEEE 802.11 WG
    … after it is determined that the SC is unlikely to make further progress towards its goals
  IEEE 802.11ax completes Sponsor Ballot
    … noting that the Coexistence SC ad hoc is unlikely to be relevant at that point anyway

## Slide 15
  Minutes

## Slide 16: The Coex SC will consider approval of its meeting minutes from Irvine in Jan 2020
  The minutes for the Coex SC at the Irvine meeting in Jan 2020 are available on Mentor:
    See 11-20-0334-01
    R1 corrects voting result (from 3/4/10 to 5/4/10) and minor editorials
  Motion:
    The IEEE 802 Coex SC approves 11-20-0334-01 as minutes of its meeting in Irvine in Jan 2020
    Moved:
    Seconded:
    Result:

## Slide 17
LS to/from ERM TG11

## Slide 18: Coex SC held a teleconference to discuss a LS received from ETSI ERM TG11
  On the 4 June 2020, the Coex SC held a teleconference (as requested by WG Chair) to discuss a LS received from ETSI ERM TG11
    The LS asked the WG to review clause 8.1 of draft TR 103 665, which describes IEEE 802.11 operation in the 2.4 GHz band
    The LS particularly asked for feedback on a proposal for a new clause 8.1.4 in draft TR 103 665 related to “current challenges” for 802.11 operation
  The teleconference documents are available on Mentor
    Agenda: 11-20-0860-01
    Draft minutes: 11-20-0878-02

## Slide 19: The Coex SC will consider approval of its teleconference minutes from 4 June 2020
  The minutes for the Coex SC at the teleconference related the LS from ETSI ERM TG11 on 4 June 2020 are available on Mentor:
    See 11-20-0878-02
  Motion:
    The IEEE 802 Coex SC approves 11-20-0878-02 as minutes of its teleconference related the LS from ETSI ERM TG11 to on 4 June 2020
    Moved:
    Seconded:
    Result:

## Slide 20: Coex SC held a teleconference to discuss a LS received from ETSI ERM TG11
  The teleconference focused on the second task, resulting in consensus on the a draft LS response as documented in 11-20-0861-01
    The draft LS response notes that the WG does not recognise the asserted challenges and recommends the proposed text be rejected.
    The draft LS response also objects to assertions elsewhere in draft TR 103 665 that the existing Power Density limit of 10 dBm/MHz is too restrictive
  A request was made during the teleconference and afterwards for further review of clause 8.1 in relation to the first task

## Slide 21: Only a small number of comments have been received on clause 8.1
  Since the teleconference, a small number of comments have been received in relation to clause 8.1 in Draft 17 of TR 103 665
    From Stephen McCann (Blackberry), Carol Ansley (Commscope) & Dick Roy – thank you!
    Most of Stephen’s, Carol’s & Dick’s comments have been included in a revised draft LS
  These comments do not represent a full review of clause 8.1 in Draft 17 of TR 103 665
  It appears the main problems resulting in the lack of response is:
    A lack of interest
    Too busy doing working on other activities
    A lack of understanding why it is important

## Slide 22: The proposed response provides some review from individuals rather than the WG as a whole
  The revised draft LS in 11-20-0861-04 essentially punts on clause 8.1
    Various WG participants have reviewed clause 8.1 in the TR 103 665 draft.
    A few issues with the draft text have been discussed, although for many participants it was difficult to make an informed judgement on the suitability of the current text in clause 8.1 as input into the preparation for the 8th update of the European Commission Decision on SRDs because they are not sufficiently familiar with the purpose and required scope of the material.
    A few comments and suggestions from WG participants are recorded in an appendix to this Liaison Statement.
    In addition, we have highlighted to WG participants the possibility of providing more details input to ETSI ERM TG11 on clause 8.1 in the future to ensure it provides an appropriately detailed description of IEEE 802.11 operation in the 2.4 GHz band.

## Slide 23: The Coex SC may consider approving a LS response to ETSI ERM TG11
  Motion:
    The IEEE 802 Coex SC approves 11-20-0861-04 as the response to the LS from ETSI ERM TG11 in 11-20-0706-00
    Moved:
    Seconded:
    Result:
  Note: if there is not time to consider a completed draft LS in the Coex SC meeting, it will be taken to the WG plenary as a personal motion

## Slide 24
  Agenda items
  Unlicensed LTE deployment

## Slide 25: Latest stats confirm that there is some interest in LAA, suggesting good coexistence may be important
Tech-nology | Stage | GSMA1 (July ‘18) | GSA2 (Oct ‘18) | GSA3 (Jan ‘19) | GSA4 (Jul ‘19) | GSA5 (Nov ‘19) | GSA6 (Dec ‘19) | GSA7 (Mar ‘20)
LAA | Planned | 23 | 22 | 26 | 29 | 30 | 29 | 29
 | Deployed | 4 | 6 | 6 | 8 | 8 | 8 | 9
eLAA | Planned | ? | 1 | 1 | 1 | 1 | ? | 0
 | Deployed | ? | 0 | 0 | 0 | 0 | ? | 1
LWA | Planned | ? | 2 | 2 | 2 | 2 | 2 | 2
 | Deployed | ? | 1 | 1 | 1 | 1 | 1 | 1
LTE-U | Planned | ? | 8 | 8 | 8 | 8 | 9 | 9
 | Deployed | ? | 3 | 3 | 3 | 3 | 3 | 3
1 GSMA (July 2018)
2 GSA: Evolution from LTE to 5G: Global Market Status (Nov 2018)
3 GSA: LTE in unlicensed and shared spectrum (Jan 2019)
4 GSA: Evolution from LTE to 5G: Global Market Status (Aug 2019)
5 GSA: LTE Unlicensed - LTE in Unlicensed and Shared Spectrum (Nov 2019)
GSA: LTE and 5G Market Statistics (Dec 2019)
GSA: LTE in Unlicensed Spectrum and Shared Spectrum (Mar 2020)

## Slide 26: The number planned/testing and deployed LAA networks is slowly increasing (mostly!)
Chart: Globally planned/testing & deployed LAA networks
| 43282 | 43374 | 43466 | 43647 | 43770 | 43800
Planned, testing | 23 | 22 | 26 | 29 | 30 | 29
Deployed | 4 | 6 | 6 | 8 | 8 | 8

## Slide 27: Does anyone have some NR-U data or forecasts?
  The GSA does not currently provide NR-U data or forecasts
  … and so it near term relevance is currently unclear
  Does anyone have a good source?
  The latest news is that it is likely that NR-U in 6 GHz could be delayed to 3GPP Rel 17 …
  … which would give 802.11ax in 6 GHz (Wi-Fi 6E) a great opportunity to prove its value

## Slide 28
  Agenda items
  ETSI BRAN 6 GHz issues

## Slide 29: BRAN#106 made very significant progress towards completing EN 303 687 (6 GHz)
6 GHz issues discussed at BRAN#106
  There is reasonable hope that a compromise for 6 GHz operation will allow fast completion of EN 303 687
  The 6 GHz compromise could result in future refinements to 802.11 and the ETSI HS’s
  Synchronous access is being discussed in ETSI BRAN and may be interesting for 802.11be

## Slide 30
6 GHz compromise

## Slide 31: There is reasonable hope that a compromise for 6 GHz operation will allow fast completion of EN 303 687
Executive summary
  There had been a long standing disagreement on the best LBT detection mechanism in 5 GHz
  The lack of legacy equipment in the 6 GHz band provided an opportunity for a compromise
  ETSI BRAN have now agreed that 6 GHz will use ED-only at -72 dBm for LBT detection
  EN 303 687 should now complete very soon, although there is still some uncertainty

## Slide 32: There had been a long standing disagreement on the best LBT detection mechanism in 5 GHz
  A key issue for the Coex SC over its lifetime has been the question of how to undertake LBT detection of other systems in the 5 GHz band
    IEEE 802.11 has traditionally used PD/ED at -82/-62 dBm
    LAA/NR-U chose (eventually) to use ED-only at -72 dBm (scaled)
    ETSI BRAN chose to allow both in 5 GHz band
  There have been many contradictory assertions on the “best” LBT detection approach
    Simulation have been produced to “prove” just about every approach, but mainly proving that simulations should be treated with caution
    It seems likely that PD/ED at -82 dBm is generally the “best” approach … as long as all systems use it symmetrically
    However, many 3GPP stakeholders reasonably objected to using PD based on the 802.11a preamble, meaning there was not symmetry
    This probably leaves PD/ED+ED-only as a non-optimum compromise in the 5 GHz band

## Slide 33: The lack of legacy equipment in the 6 GHz band provided an opportunity for a compromise
  The discussion about LBT detection in the 5 GHz band recently shifted into a 6GHz band context …
  … with the same old arguments! 
  However, a significant difference for operation in the 6 GHz band is that there is no legacy 802.11 gear using PD/ED (at least not yet) …
    And less contention given the expected increased use of OFDMA
  … which provided an opportunity for a compromise in the 6 GHz band that is different from the PD/ED+ED-only compromise in the 5 GHz band
  The new compromise can focus on LBT detection symmetry in the 6 GHz rather than needing to enable PD for legacy support

## Slide 34: ETSI BRAN have now agreed that 6 GHz will use ED-only at -72 dBm for LBT detection
  A significant number of 3GPP & Wi-Fi stakeholders worked together before BRAN#106 to develop a 6 GHz compromise
    Including Ericsson, HPE, Broadcom, CableLabs, Cisco, Huawei, Intel, Nokia, Ruckus
    Stuart Strickland (HPE) deserves plaudits for driving the compromise
  The compromise is documented in BRAN(20)106004r2, and proposes that LBT detection in 6 GHz be based on ED-only at -72 dBm
    The -72 dBm threshold is defined as a function of the maximum configured transmit power
      This needs to be clarified but it is believed to be the maximum tx power that a device can be operated in a particular configuration
  The inclusion of this compromise in a stable draft of EN 303 687 will allow access to 6 GHz in Europe as soon as it is made available

## Slide 35: ETSI BRAN has formally notified IEEE 802.11 WG of the agreement for compromise in the 6 GHz band
  ETSI BRAN agreed on this compromise and also agreed to notify various organisations about the agreement
    EEE 802.11 WG, 3GPP RAN, 3GPP RAN1, WFA, WBA, GSMA & 5G ACIA
  The LS have been received and is contained in 11-20-1034-00
  It does not appear that any LS reply is needed

## Slide 36: EN 303 687 should now complete very soon, although there is still some uncertainty
  It was believed by many that the compromise would allow EN 303 687 to be completed very quickly …
  … by simply copying all the LBT related clauses from EN 301 893
  Unfortunately, life is never simple …
  … with at least one 3GPP stakeholder wanting to “carefully consider” and possibly modify each LBT related clause
  It is hoped (and now believed) that this situation will change soon …
  … otherwise there is a risk that EN 303 687 (6 GHz) will become as controversial and slow as EN 301 893 (5 GHz) despite the efforts by most parties to find a compromise in good faith

## Slide 37
Future refinements

## Slide 38: The 6 GHz compromise could result in future refinements
Executive summary
  A refinement to 802.11ax in 6 GHz might be considered as a result of the compromise
  EN 301 893 & EN 303 687 may need future refinements to enable 802.11be related innovations
  The different rules in different bands & locations will enable refinements based on deployment experience

## Slide 39: A refinement to 802.11ax in 6 GHz might be considered as a result of the compromise
  The ETSI BRAN compromise does not have any direct impact on the IEEE 802.11 standard, but it will restrict how Wi-Fi device can operate in 6 GHz in Europe & other parts of the world that follow European rules
  It means that 802.11 devices in 6 GHz in Europe will always have to defer at an EDT of -72 dBm before transmission
    Effectively they will be using PD/ED at -82/-72 dBm
  This is likely to provide reasonable coexistence between 802.11 devices, but may give LAA/NR-U devices operating using ED-only at -72 dBm an advantage
  The WG might consider refining 802.11ax operation in 6 GHz to allow the use of ED-only at -72 dBm in some circumstances, particularly when operating in the same channel as another system using ED-only

## Slide 40: EN 301 893 & EN 303 687 may need future refinements to enable 802.11be related innovations
  The requirements in EN 301 893 (5GHz) and EN 303 687 (6 GHz) mean that 802.11be is restricted to using the traditional LBT mechanisms rather than any new access mechanism
    eg, it is unclear that some of the proposed multi-AP mechanisms would be allowed in EN 303 687
  This represents a tradeoff because it restricts innovation in 802.11be …
  … but it protects 802.11ax/be from unilateral “innovations” from NR-U or other technologies, eg like LTE-U
  If 802.11be defines the use of any other type of access …
  … its use in Europe will need to be negotiated in ETSI BRAN for future incorporation into EN 303 687 (and EN 301 893)

## Slide 41: The different rules in different bands & locations will enable refinements based on deployment experience
  The current situations for LBT detection is
    Europe will use ED-only at -72 dBm for 6 GHz
    Europe will use ED-only at -72 dBm or PD/ED at -82/-62 dBm for 5 GHz
    US does not really have any equivalent rules
  This sets up the possibility of using deployment experience to determine the best type of LBT detection for sharing & efficient spectrum use
  If it turns out that ED-only+PD/ED is better than ED-only then EN 303 687 requirements could be expanded to allow PD/ED too
  Similarly, if it turns out the risk of fewer LBT detection rules is acceptable based on US experience then EN 303 687 requirements could be loosed, maybe to allow ED-only at -62 dBm
  In the meantime, ED-only at -72 dBm for 6 GHz is a reasonable starting point (and the starting point we are stuck with)

## Slide 42
Synchronous access

## Slide 43: Synchronous access is being discussed in ETSI BRAN and may be useful for 802.11be
Executive summary
  Qualcomm has been advocating a new synchronous access scheme since BRAN#104
  There were a variety of submissions related to synchronous access before BRAN#106
  There was significant discussion related to the synchronous access proposal at BRAN#106
  The next steps for synchronous access are unclear but it may useful to consider for 802.11be operation

## Slide 44: Qualcomm has been advocating a new synchronous access scheme since BRAN#104
Sync access submission
  In BRAN#104 (Dec 2019), Qualcomm proposed a new synchronous access method
    See BRAN(19)104018: Technology neutral synchronous access (Qualcomm)
Sync access summary
  The new synchronous access method for EN 303 687 (and EN 301 893?) builds on the LBT based LBE mechanism already in EN 301 893
    Uses existing LBT to access the channel
    Always completes a COT on a 6 ms boundary established by a global clock
    Extends the COT length compared to normal async access
      Normal COT is < 6 ms
      Adjusted COT is < 6 ms if COT is not busy at start of 6 ms slot in which COT starts
      Adjusted COT is < 12 ms if COT is busy at start of 6 ms slot in which COT starts

## Slide 45: Example of synchronous operation …

## Slide 46: Qualcomm has been advocating a new synchronous access scheme since BRAN#104
Sync access claimed benefits
  It is claimed that this adjustment to the COT length will allow both sync & async devices about the same access to the medium (on average) …
  … but with the benefit of synchronising devices being able to use advanced features like CoMP (Coordinated Multi-Point) more usefully
    The completion of COTs on the 6 ms boundary by sync devices is claimed to tend to cause all devices to often transmit within the 6 ms globally defined slots (even async devices)

## Slide 47: There were a variety of submissions related to synchronous access before BRAN#106
  Further documents related to sync access were submitted to the BRAN#104e teleconference, but not discussed
    BRAN(20)104e004 (Qualcomm) proposed draft text related to Qualcomm’s synchronous access proposal
    BRAN(20)104e007 (Mediatek) argued that BRAN should focus on FBE rather than Qualcomm’s synchronous access proposal
  There was discussion about sync access were submitted for the BRAN#105e teleconference
    BRAN(20)105027 (Qualcomm) asserted that sync access requires COT extension to ensure fair access with async traffic
    BRAN(20)105028 (Qualcomm) proposed draft text related to Qualcomm’s synchronous access proposal
    BRAN(20)105044 (HPE) argued against acceptance of the proposal at this time
    BRAN(20)105048 (Qualcomm) documented some simulations related to the sync access proposal

## Slide 48: There was significant discussion related to the synchronous access proposal at BRAN#106
  In BRAN#106 there was further discussion of sync access
    BRAN(20)105044r1 (HPE) argued against acceptance of the sync access proposal at this time
    BRAN(20)106011 (Mediatek) argued that the proposed COT extension to 12 ms was too much as tradeoff with normal 6 ms COT
    BRAN(20)106012 (Intel) asserted that there was no clear benefit from sync and improvement came as expense of async
    BRAN(20)106014 (Qualcomm) provided further simulation results and asserted testing would be relatively easy
  The discussion during and after the presentations of the various submissions suggests interest and concern
    There is certainly interest from many stakeholders …
    … but there are also concerns about its immaturity and lack of extensive peer review

## Slide 49: The next steps for synchronous access are unclear but it may interesting to consider for 802.11be operation
  It is not yet clear if synchronous access will be incorporated into EN 303 687 (6 GHz) or EN 301 893 (5 GHz) any time soon
  However, it is probably fair to say that there is interest in the synchronous access proposal, with most concerns based on the lack of proper review of the proposal and its potential impact
  That said, synchronous access may be interesting for 802.11be operation and so it is suggested that 802.11be stakeholders have a look
    If it is useful to NR-U it could easily be useful to 802.11be

## Slide 50
  Agenda items
  ETSI BRAN 5 GHz issues

## Slide 51: Progress in EN 301 893 (5 GHz) is still being held back by arguments about the same old issues
Executive summary
  The PD/ED vs ED-only issue in 5 GHz remains unresolved for 802.11be devices
    Without an agreement to force 802.11be to use ED-only at -72 dBm, testing could be used as a weapon
  There is a new disagreement on LBT detection during multi-channel operation in 5 GHz
  There is ongoing disagreement PD & ED testing with background noise
  It is likely FBE access in EN 301 893 will be refined to make it more useable
  [Spectral mask]
This may lead to deadlock …
… but deadlock is not necessarily a problem as Wi-Fi product continues to have access to the market based on the stable draft of EN 301 893

## Slide 52
PD/ED vs ED-only in 5 GHz

## Slide 53: The PD/ED vs ED-only issue in 5 GHz remains unresolved for 802.11be devices
Executive summary
  The issue of PD/ED vs ED-only as LBT detection mechanisms has been the key coexistence issue for years …
  In BRAN(20)106023, Ericsson proposed that PD/ED only be available to 802.11a/n/ac/ax (D6.0) devices in the 5 GHz band
    ie not available to 802.11ax beyond D6.0, 802.11be or other technologies
  In BRAN(20)106031, Cisco asserted that almost every one of Ericsson’s justifications for this position are incorrect
  However, Cisco also observed the two positions suggest a compromise if agreement can be found on the treatment of 802.11be
  Unfortunately, there was no agreement during BRAN#106 on a proposed compromise to allow 802.11be to use PD/ED

## Slide 54: In BRAN(202)106023, Ericsson proposed that PD/ED only be available to 802.11a/n/ac/ax devices
Ericsson recommendation for EN 301 893
Status quo in EN 3901 893
Option 1 defines requirements for 802.11/n/ac/ax independently from those for other systems
802.11a/n/ac/ax use the adaptivity mechanisms, including the PDTs & EDTs defined in the 802.11a/n/ac standards and 802.11ax D6.0
Other systems (including 802.11be) use ED-only adaptivity using an EDT of -72 dBm (scaled by max tx power)
Option 2 defines requirements in a technology neutral manner so that all systems can use either:
PD/ED adaptivity using a preamble definition based on IEEE 802.11-2016 clause 17.3.6; OR
ED-only adaptivity using an EDT of -72 dBm (scaled by max tx power)
Ericsson asserts can be achieved with limited/simplified testing

## Slide 55: Cisco observed the two positions suggest a compromise if agreement can be found on the treatment of 802.11be
Ericsson appear to accept simplified testing if PD/ED is restricted to 802.11a/n/ac/ax
The Wi-Fi industry are content with simplified testing and a Wi-Fi-only (inc. 802.11be) scope for PD/ED
The key issue in finding a compromise is the treatment of 802.11be
There is a possible compromise if the various parties can agree to allow 802.11be to use PD/ED
Ericsson position
Wi-Fi industry position
Key difference
Possible compromise

## Slide 56: The key issue in finding a compromise between two positions is the treatment of 802.11be
  The key difference in opinion is really the treatment of 802.11be
    It appears Ericsson (and some others) want to draw a line at 802.11ax D6.0 using PD/ED because:
      They do not like the way PD/ED & ED-only devices coexist, and would like to start the transition in 5GHz to ED-only as soon as possible, starting with 802.11be
      They believe there is a risk allowing 802.11be (or 802.11ax beyond draft 6.0) without it being fully defined
    Whereas the Wi-Fi community (at least most of those who have expressed an opinion) want to allow 802.11be to use PD/ED because:
      They believe PD/ED is a well proven coexistence mechanism in 5 GHz
      There is no reason to stop an 802.11be device using exactly the same PD/ED mechanism as a legacy 802.11a/n/ac/ax device
  If this issue can be resolved then a solution for EN 301 893 with reasonable testing becomes possible …

## Slide 57: There is a possible compromise if the various parties can agree to allow 802.11be to use PD/ED
Option 3 (the “compromise”) proposed by Cisco
  Use the definitions for EDT currently in EN 301 893 v2.1.37+
    They allow 802.11be to use PD/ED+ED-only
  Restrict the PD/ED option to Wi-Fi devices,
    Thus stop the use of PD/ED by other technologies, eg LAA/NR-U, etc
    Apply the restriction by defining a Wi-Fi device at a very high level as one that connects to another Wi-Fi device (so very easy testing)
  Define a simple test with the limited scope envisaged by Ericsson for Option 1 to provide reasonable confidence of correct PD/ED operation

## Slide 58: There was no agreement during BRAN#106 on a proposed compromise to allow 802.11be to use PD/ED
  The proposed compromise solution was discussed a little in BRAN#106 but there was no agreement
  The threatened alternative from Ericsson is that they will insist on detailed testing of every aspect of PD/ED
  Hopefully, agreement can be reached before BRAN#107 …
Question to think about:
  Would the Wi-Fi community be happy to restrict 802.11be to ED-only at -72 dBm in the 5 GHz band?
    ED-only at-72 dBm is likely to be the status quo in the 6 GHz band
    802.11be will not hit the market for several years anyway
  Note: there is no compelling need to agree to limit 802.11be to ED-only at -72 dBm in the 5 GHz band because the current stable draft allows 802.11be to use PD/ED

## Slide 59
Testing

## Slide 60: Without an agreement to force 802.11be to use ED-only at -72 dBm, testing could be used as a weapon
  The threat if the proposal to force 802.11be to use ED-only at -72 dBm is not accepted is that there will need to be detailed testing on every last element of every requirement
  Examples of related debates include:
    PD testing
      See BRAN(20)106006 (Ericsson), BRAN(20)106045 (Intel), … and many more
    PD/ED to ED-only mode switch testing
      See BRAN(20)106013 (Ericsson), BRAN(20)106027r1 (Cisco)
    Threshold testing with background noise
      See later in this deck
  In BRAN(20)106027r1, Cisco suggested that ETSI BRAN needs to adopt a more pragmatic approach to testing, rather than testing everything
  After limited discussion in BRAN#106, there was no resolution of the question of pragmatic vs detailed testing

## Slide 61: A pragmatic regime provides a good balance between technical requirements & testing
No testing regime
The status quo: test very little or nothing
Provides guidance, but never tests any technical requirements
Full testing regime
Test every last detail of every technical requirement
Takes too long, and results in complex & expensive tests
Simple testing regime
Include only technical requirements that can be tested easily
Doesn’t promote or test the efficient use of the spectrum
Pragmatic regime
Test as many of technical requirements as useful and practical
A pragmatic regime for EN 301 893 promotes the efficient use of the spectrum in a timely and practical manner, with expansion of testing based on real issues
Three options below are all unsatisfactory in various ways
Option above pragmatically satisfies the essential requirements in RED

## Slide 62
Multi-channel operation

## Slide 63: There is a new disagreement on LBT detection during multi-channel operation in 5 GHz
  In BRAN(20)106013, Ericsson proposed that all sensing on secondary channels occur using ED-only at -72 dBm
    It is asserted that it is unfair to NR-U that that Wi-Fi PD is not possible in secondary channel
  In BRAN(20)106026r1, Cisco notes the case for changing the status quo for multi-channel access is not well justified
    Contrary to Ericsson’s assertion, PD is possible in a secondary channel, albeit not likely
    Wi-Fi also either uses ED at -72 dBm or mid packet detection at -72 dBm (with ED at -62 dBm as a backup), which is more conservative that current requirements in the EN 301 893 draft
    It is unreasonable to change the multi-channel rules that have been in place for at least 4 years
  There was no agreement on this issue

## Slide 64
Floating thresholds

## Slide 65: There is ongoing disagreement PD & ED testing with background noise
  EN 301 893 expresses the PDT (and EDT) as an absolute level
  For some time, Ericsson has expressed a concern that some Wi-Fi devices implement thresholds relative to the noise floor
    See BRAN(20)106005 for details
  Previously, Ericsson had previously proposed that the PD & ED tests be run both with/without background noise of -90 dBm as a way of catching these devices
  Broadcom & Qualcomm undertook testing of a variety of typical Wi-Fi devices & determined that they would all pass with background noise level of -90 dBm
  In BRAN#106, Ericsson changed their proposal to require testing with background noise at -88 dBm, without any justification
  It seems likely that disagreement on this topic will continue

## Slide 66
FBE

## Slide 67: It is likely FBE access in EN 301 893 will be refined to make it more useable
  In BRAN(20)106010, Mediatek proposed refinements to the current FBE (Frame Based) mechanism that would allow independent FBE systems access to a channel
    Currently, two FBE systems would collide with no resolution
    The new scheme would allow collision resolution between FBE systems
  During BRAN#106 there were some objections, but that mainly reflected a lack of understanding on what Mediatek were proposing and why
  It is likely that Mediatek will make further proposals …
  It is believed this refinement to FBE will not have adverse affect on Wi-Fi

## Slide 68
  Relationship topics
  ETSI BRAN activities
  Next meetings

## Slide 69: ETSI BRAN will next meet virtually at BRAN#107 in September 2020
ETSI BRAN meeting schedule
  BRAN#107
    24 September 2020 – 2 October 2020
    Virtual
  BRAN#108
    7 December 2020 – 11 December 2020
    Virtual
  #BRAN109
    22 February 2021 – 26 February 2021
    Sophia-Antipolis, FR?
  #BRAN110
    7 June 2021 – 11 June 2021
    Sophia-Antipolis, FR?

## Slide 70
  Coex SC
  Extension of SC charter

## Slide 71: The Coex SC may discuss and consider a new scope to extend its life beyond 802.11ax (again)
  The question of coexistence between Wi-Fi and various LTE based technologies has been “hot” for the last 4+ years
  The Coex SC is scheduled to close when 802.11ax completes SA Ballot in 2020
  However, here is no reason to think that coexistence will not remain a vitally important issue beyond the completion of IEEE 802.11ax as:
    IEEE 802.11be is developed
    ETSI BRAN develops a Harmonised standard for 6 GHz operation
  As the ratification of IEEE 802.11ax get closer the Coex SC may want to consider a scope extension
  There was discussion in relation to expanding the scope of the Coex SC in Irvine in Jan 2020, but at the time … it appeared that many in the SC wanted to wait until they had a chance to consider the issues

## Slide 72: The agreed Coex SC scope focuses on ensuring 802.11ax has fair access to global unlicensed spectrum
Discuss the use of PD, ED or other 802.11 coexistence mechanisms with the goal of promoting “fair” use of unlicensed spectrum
Promote an environment that allow IEEE 802.11ax “fair access” to global unlicensed spectrum
Will initially focus on liaising with 3GPP RAN/RAN1/RAN4 but may also lead to interactions with regulators and other stakeholders
Will probably not conclude at least until RAN4’s 802.11/LAA coexistence testing is defined and successfully executed
May require the SC to consider other simulations and results of tests of potential LAA/802.11 coexistence mechanisms
Will initially focus on encouraging a “technology neutral” solution in the next revision of EN 301 893 that allows IEEE 802.11ax fair access to unlicensed spectrum in Europe (noting the European approach is likely to have global impact)
The effort will also focus on allowing 802.11ax to use innovative mechanisms for frequency reuse without compromising the goal of fair access

## Slide 73: The Coex SC has potential coexistence work related to 802.11be & 6 GHz
Why should the Coex SC charter be extended?
  The existing Coex SC charter is mostly constrained to 802.11ax & 5 GHz coexistence, despite potential coexistence issues with 802.11be & 6 GHz
    It does not cover coexistence with 802.11be (the next big thing )
    It did not explicitly cover coexistence in 6 GHz (the other next big thing )
      It could be argued that is does implicitly cover 6 GHz with the 802.11ax PAR extension covering 6 GHz
  There is likely to be relevant material to review from other organisations related to coexistence
    3GPP RAN1 will probably not provide as much to review as in the past because the NR-U spec is completed (although they are talking about revisions in Rel 17, particularly wrt 6 GHz)
    ETSI BRAN will continue providing material as the 5 GHz HS (EN 301 893) is completed and the 6 GHz HS (EN 303 687) is developed

## Slide 74: The SC may discuss a possible new scope for a rechartered Coex SC
Possible new scope for Coexistence SC charter extension
  The Coex SC shall promote the establishment of an environment and the use of mechanisms that enable IEEE 802.11 technologies to have “fair access” to global unlicensed spectrum
  The Coex SC should focus particularly on coexistence, for example of 802.11ax & 802.11be with LAA & NR-U in the 5 GHz and 6 GHz bands
  The Coex SC may consider coexistence with other technologies and in other bands as directed by the Chair of the 802.11 WG
Possible close down criteria for Coexistence SC
  The Coex SC will close when it is determined by the 802.11 WG that the SC is unlikely to make further progress towards its goals

## Slide 75: The Coex SC may consider approving the extension of its charter
Possible motion
  The IEEE 802.11 Coex SC recommends to the IEEE 802.11 WG that the Coex SC charter is revised as shown in <see previous slide>
  Moved:
  Seconded:
  Result:

## Slide 76
  Coex SC
  Plans for next meeting

## Slide 77: The Coex SC will continue its normal business in Sept 2020 virtually
Possible agenda items
  Review ETSI BRAN coex activities
    EN 301 893 (5 GHz)
    EN 303 687 (6 GHz)
  Rechartering of the Coex SC
  …

## Slide 78: The IEEE 802.11 Coexistence SC virtual meeting in Jul 2020 is adjourned!