## Slide 1: EHT NDPA Frame Design Discussion
Date: 2020-07-07
Authors:
Name | Affiliation | Address | Phone | Email
Chenchen Liu | Huawei Technologies Co., Ltd Huawei Technologies Co., Ltd | Huawei Base, Bantian, Shenzhen |  | liuchenchen1@huawei.com
Ross Jian Yu |  |  |  | ross.Yujian@huawei.com
Dandan Liang |  |  |  | 
Ming Gan |  |  |  | 
Genadiy Tsodik |  |  |  | 
Shimi Shilo |  |  |  | 
Oded Redlich |  |  |  | 

## Slide 2: Abstract
In this contribution, we will discuss the possible NDPA frame designs with respect to the EHT new features

## Slide 3: Outline
Recap of NDPA frame
Motivations
EHT NDPA indication method
Summary
References

## Slide 4: Recap of NDPA frame
In 802.11, three NDPA frame variants have been defined:
  VHT NDPA frame
  HE NDPA frame
  Ranging NDPA frame
In this contribution, we try to define a new variant for EHT NDPA frame.

## Slide 5: Recap of NDPA frame
The Sounding Dialog Token field indicates the token number and NDPA type
Each NDPA contains one or multiple STA info fields, each with 4 bytes for HE and Ranging, 2 bytes for VHT

## Slide 6: Sounding Dialog Token field
For the VHT, the first two bits in the Sounding Dialog Token field are reserved[1]
For the HE, the first bit is reserved and the second bit is used to distinguish the HE or VHT NDPA frame[2]
In 11az, the Ranging subfield and HE subfield are set to 1 and 0 respectively to identify the frame as Ranging NDPA frame [3]
The legacy VHT STA will regard all the NDPA as VHT NDPA, the legacy HE STA may regard it as HE NDPA as long as the HE subfield is set to 1
The remaining 6 bits are used to record the dialog token number
Ranging | HE | Description
0 | 0 | VHT NDPA
0 | 1 | HE NDPA
1 | 0 | Ranging NDPA
1 | 1 | Reserved

## Slide 7: STA info field
For HE NDPA, AID11 subfield indicate the AID of STA if between 1 and 2007; indicates the Disallowed Subchannel Bitmap if equals 2047；other values are reserved
Partial BW Info subfield indicates the start and end index of the 26-tone RU for which the feedback is requested.
Nc subfield indicates the number of columns (corresponding to Nss of BFee)
Feedback Type And Ng subfield and Codebook Size subfield indicate the Ng, quantization resolution and feedback type.
Disambiguation subfield is set to 1 to prevent a non-HE VHT STA from wrongly determining its AID
HE NDPA
VHT NDPA
Ranging NDPA

## Slide 8: Motivations
802.11be shall supports that
  Wideband band up to 320M and noncontiguous spectrum utilization
  Up to 16 spatial stream
  Aggregated PPDU which consists of multiple sub-PPDUs of the same or different PPDU format
The following modifications maybe need to support the new features:
  Indication of EHT NDPA(add the new variant)
  Partial BW Info(RU Start index and RU end index for HE, the maximum index could be 143 for 320M BW in EHT)
  Number of columns( 4 bits is need in order to support 16 spatial stream)
  Multi-format STA info(for A-PPDU, it is better to finish HE and EHT sounding simultaneously)
  Feedback type, Ng and codebook

## Slide 9: EHT NDPA Indication
One straightforward solution would be that using the reserved state in the Dialog Token field to indicate the EHT NDPA frame and extending the length of the STA Info field
For example, let the EHT STA Info field contains three part each with 2 bytes. Then in order to prevent a HE STA from wrongly determining its AID, the EHT STA Info field must have AID subfield in every two byte. The additional overhead is larger than the extended length, so it does not work.
Ranging | HE/VHT | Description
0 | 0 | VHT NDPA
0 | 1 | HE NDPA
1 | 0 | Ranging NDPA
1 | 1 | EHT NDPA

## Slide 10: EHT NDPA Indication
Two options are proposed for EHT NDPA Indication:
  Option 1: Extend the length of STA Info subfield
  Option 2: Compress the Partial BW Info subfield

## Slide 11: EHT NDPA Indication
Option 1: Extend the length of STA Info field
  Sounding Dialog Token field is set as follows
  STA Info field:
    Length of EHT STA Info can be extended to 2*n byte(e.g. n=3)
    HE STA will regards the EHT NDP as VHT NDP
    Thus only disambiguation subfield positioned at B(16*k+11)(B(i) start with i=0) for k=1, 2, …, n-1 shall be set to 1, so as to prevent a VHT STA from wrongly identifying its AID in the EHT NDPA
Ranging | HE/VHT | Description
0 | 0 | VHT or EHT NDPA
0 | 1 | HE NDPA
1 | 0 | Ranging NDPA
1 | 1 | Reserved

## Slide 12: EHT NDPA Indication
There are many reserved state for the Partial BW Info subfield(for HE STA Info field, the RU Start index and the RU End index each occupies 7 bits, but their valid value rang is 0~73, since the maximum bandwidth is 160M)
Thus, instead of extending the length of STA Info field, the Partial BW Info subfield can be compressed for EHT
Therefore, the option 2 is proposed

## Slide 13: EHT NDPA Indication
Option 2: Compress the Partial BW Info subfield
  Sounding Dialog Token field – Opt A:
  STA Info field:
    Opt2a: the 9-bit RU Allocation subfield[4] is used to replace the Partial BW Info subfield (6/7 bits with 242-tone RU granularity)
    Opt2b: compress the RU start and RU end index with larger granularity,
    Opt2c: RU size subfield and RU Position Index subfield with compressed bitwidth.
    The saved bits can be used for Nc and other subfields
Ranging | HE | Description
0 | 0 | VHT NDPA
0 | 1 | HE NDPA
1 | 0 | Ranging NDPA
1 | 1 | EHT NDPA

## Slide 14: EHT NDPA Indication
Option 2: Compress the Partial BW Info subfield
  Sounding Dialog Token field – Opt B:
  STA Info field:
    For HE STA Info field, the RU Start index and the RU End index each occupies 7 bits, but their valid value rang is 073, since the maximum bandwidth is 160M
    Besides, a valid RU Start index must be smaller than or equal to the RU End index
    Those features can be used to distinguish EHT STA Info field from HE STA Info field
Ranging | HE/VHT | Description
0 | 0 | VHT NDPA
0 | 1 | HE or EHT NDPA
1 | 0 | Ranging NDPA
1 | 1 | Reserved

## Slide 15: EHT NDPA Indication
Option 2: Compress the Partial BW Info subfield
  STA Info field:
    E.g., the two MSB corresponding to the RU End index of HE STA Info field are set to 1 to indicate this STA Info field is EHT STA Info field, Otherwise, it is a HE STA Info field
    The same compression method for Partial BW indication can be used as option2a/2b/2c.
    The save bits can be used for Nc subfield and Codebook Size subfield
    Unified HE/EHT NDPA frame may also support A-PPDU NDP.

## Slide 16: Summary
In this contribution, two EHT NDPA frame design methods are proposed, their comparisons are summarized as following:
 | Pros. | Cons.
Option 1 | Sufficient bits for EHT new features; Similar structure with HE | Large overhead due to extended length; Not supporting aggregated sounding of EHT and HE
Option 2 | The same length of STA Info subfield as HE | Need to compress the partial BW Info subfield

## Slide 17: References
[1] IEEE P802.11-REVmd™/D3.0
[2] IEEE P802.11ax™/D6.0
[3] IEEE P802.11az™/D2.1
[4] Specification Framework for TGbe , doc.: IEEE 802.11-20/0566r23
[5] RU Allocation Subfield Design for EHT Trigger Frame, doc.: IEEE 802.11-20/0828r0

## Slide 18: SP1
Do you support to reuse the VHT/HE NDPA frame for EHT NDPA frame
  Y/N/Abs

## Slide 19: SP2
Which NDPA frame design proposed in the contribution do you prefer
  Option 1: Extend the length of STA Info field(>4 bytes)
  Option 2: Compress the Partial BW Info subfield (4 bytes STA Info field)
  Abstain

## Slide 20: SP3
Do you support to extend the length of the STA Info field in the NDPA frame for EHT, and set the Ranging subfield and HE subfield of Sounding Dialog Token subfield to 0 and 0 respectively for EHT NDPA frame
  Y/N/Abs
Ranging | HE/VHT | Description
0 | 0 | VHT or EHT NDPA
0 | 1 | HE NDPA
1 | 0 | HE Ranging NDPA
1 | 1 | Reserved

## Slide 21: SP4
Do you support to set the Ranging subfield and HE subfield of Sounding Dialog Token subfield to 1 and 1 respectively to identify the frame as EHT NDPA frame, and keep the length of STA Info field for EHT to be 4 bytes
  Y/N/Abs
Ranging | HE | Description
0 | 0 | VHT NDPA
0 | 1 | HE NDPA
1 | 0 | HE Ranging NDPA
1 | 1 | EHT NDPA

## Slide 22: SP5
Do you support to set the Ranging subfield and HE subfield of Sounding Dialog Token subfield to 0 and 1 respectively, and keep the length of STA Info field for EHT to be 4 bytes
  the variant of EHT or HE can be identified from the indication in the STA Info field
    Y/N/Abs
Ranging | HE/VHT | Description
0 | 0 | VHT NDPA
0 | 1 | HE or EHT NDPA
1 | 0 | HE Ranging NDPA
1 | 1 | Reserved

## Slide 23: Appendix1 – RU allocation indication assuming 242-tone RU granularity
RUA Indication (6 bits) | Indicated Partial BW/RU | Number of Options
000000-001111 | 242-tone RUs (20MHz) | 16 Options
010000 - 010011 | 242+484 in 1st 80MHz Segment | 4 Options
010100 - 010111 | 242+484 in 2nd 80MHz Segment | 4 Options
011000 - 011011 | 242+484 in 3rd 80MHz Segment | 4 Options
011100 - 011111 | 242+484 in 4th 80MHz Segment | 4 Options
100000-100111 | 484-tone RUs (40MHz) | 8 Options
101000-101011 | 484+996 in 1st 160MHz | 4 Options
101100-101111 | 484+996 in 2nd 160MHz | 4 Options
110000 | Reserved | 1 Option
110001-111111 | Nx996RU | 15 options - last 4 LSB indicate each 80MHz segment, '1' means segment is requested

## Slide 24: Appendix2 – RU allocation indication assuming 242-tone RU granularity
RUA Indication (7 bits) | Indicated Partial BW/RU | Number of Options
0000000-0001111 | 242-tone RUs (20MHz) | 16 Options
0010000 -0010011 | 242+484 in 1st 80MHz Segment | 4 Options
0010100 - 0010111 | 242+484 in 2nd 80MHz Segment | 4 Options
0011000 - 0011011 | 242+484 in 3rd 80MHz Segment | 4 Options
0011100 - 0011111 | 242+484 in 4th 80MHz Segment | 4 Options
0100000-0100111 | 484-tone RUs (40MHz) | 8 Options
0101000-0101011 | 484+996 in 1st 160MHz | 4 Options
0101100-0101111 | 484+996 in 2nd 160MHz | 4 Options
0110000 - 0110011 | 996RU | 4 Options
0110100 - 0111001 | 2X996RU | 6 Options
0111010 – 1001101 | 2X996+484-tone RU | 12 Options
1001110-1010001 | 3X996RU | 4 Options
1010010- 1011001 | 3X996+484-tone RU | 8 Options
1011010-1111110 | Reserved | 45 Option
1111111 | 4*996-tone RU | 1 Option