## Slide 1: Backup Link for Low Latency Communication
Date: 2020-07-08
Authors:
Name | Affiliations | Address | Phone | Email
Qi Wang Yong Liu Jinjing Jiang Lochan Verma Jarkko Kneckt Tianyu Wu Sk Yong Guoqing Li | Apple Inc. |  |  | qi_wang2@apple.com

## Slide 2: Overview
To achieve low latency (LL), when a link quality deteriorates, it’s critical to switch the LL communication to a new and better link quickly.
  The deteriorated link is no longer suitable for continued data transmission or link quality change notification.
In some devices, there is an extra radio that is not used by ongoing LL communication:
  An extra tx/rx-capable radio
  An extra rx-only radio (e.g., scan radio)
Such an extra radio can be used to establish a Backup Link to reduce latency.

## Slide 3: Assumptions
AP-MLD maintains the same or higher number of simultaneous links than STA-MLD. Ex:
  AP-MLD supports 3 independent links, each in 2.4GHz, 5GHz, and 6GHz
  STA-MLD supports:
    Independent 2.4GHz and 5GHz links, or independent 2.4GHz and 6GHz links
    5GHz and 6GHz links cannot operate independently
  STA-MLD may have an extra rx-only radio (e.g. scan radio).
2.4 GHz
5 GHz
6 GHz
2.4 GHz
5 or 6 GHz
Optionally, rx-only dedicated scan radio
AP-MLD
STA-MLD
Link 3
(Virtual Link)
Link 1
Link 2
Ex: primary LL link
LL communication is conducted over a Primary Low Latency Link (e.g., the 5GHz link) as a result of either explicit or implicit agreement.

## Slide 4: Backup Link Establishment and Update (1/2)
AP-MLD elects a Backup Link that operates independently from the Primary Low Latency Link
  Ex: 5GHz link as the primary link and 2.4GHz link as the backup link
STA-MLD informs AP-MLD:
  Whether it supports Backup Link
  Whether its Backup Link is rx-only or tx/rx-capable and other capability information (e.g., supported BWs, PPDU types)

## Slide 5: Backup Link Establishment and Update (2/2)
A backup link agreement may be applicable only to LL traffic
  Ex: traffic that is associated with certain access categories (e.g, AC_VO) and certain TIDs.
After Backup Link establishment, both AP-MLD and STA-MLD commit to be available on Backup Link during the LL communication on Primary LL link.
AP-MLD may update the Backup Link due to various reasons, for examples:
  Current Backup Link becomes unavailable
    Ex: Backup Link becomes the new LL communication link
  STA’s change in Backup Link preference
  Other considerations.

## Slide 6: Backup Link Enabling Radio
Case 1: Backup link enabling radio is tx/rx-capable:
Example: a regular tx/rx-capable radio that is not used by the Primary LL Link, e.g., the 2.4GHz link where the 5GHz link is the Primary LL Link.
Case 2: Backup link enabling radio that is rx-only (e.g., a scan radio)
A Scan Radio typically is a rx-only simple radio which scans through each channel, listens for “per channel dwell time”, and obtains statistics indicating the corresponding channel quality, and repeats such operation every Scan Interval.

## Slide 7: Operation of Backup Link Enabled by Tx/Rx-capable Radio (1/2)
When AP-MLD detects link quality deterioration on Primary LL Link:
    AP-MDL sends a notification frame to STA-MLD on Backup Link,
    LL communication is switched from Primary LL Link to Backup Link or another link informed by the Notification.
STA-MLD’s power save schedule on Backup Link ensures it’s available to receive DL packet from AP-MLD during the LL packet exchange on Primary LL link
  Two options of STA-MLD’s Backup Link PS schedule are described in the next slide.

## Slide 8: Operation of Backup Link Enabled by Tx/Rx-capable Radio (2/2)
Option 1:
STA-MLD’s Backup Link PS schedule aligns with the LL traffic schedule on Primary LL Link
Option 2:
STA-MLD’s Backup Link PS schedule aligns with the PS schedule on Primary LL Link

## Slide 9: Operation of Backup Link Enabled by Rx-only Radio (1/2)
When AP-MLD detects link quality deterioration on Primary LL Link:
    AP-MDL sends a notification frame to STA-MLD on Backup Link,
    LL communication is switched from Primary LL Link to the Link informed by the Notification.
STA-MLD is available to receive DL packet from AP-MLD on Backup Link during the LL packet exchange on Primary LL link.
  For example, for a scan radio enabled backup link:
    Two options of Scan radio’s scanning schedule are described in the next slide.

## Slide 10: Operation of Backup Link Enabled by Rx-only Radio (Ex: scan radio) (2/2)
Option 1:
Scan radio’s non-scanning phase (i.e., dwell phase) aligns with the schedule of LL traffic on Primary LL Link
Option 2:
Scan radio’s non-scanning phase (i.e., dwell phase) aligns with the PS schedule on Primary LL Link

## Slide 11: Summary
We have proposed the establishment and operation of a Backup Link to assist low latency communication.
The usage of Backup Link reduces the latency of communication.

## Slide 12: Straw Poll
Do you support to define a backup link to assist the low latency communication ?
Result: Y/N/Abs