## Slide 1: Follow up on Feedback Enhancement
Date: 2020-07-09
Authors:

## Slide 2: Introduction
Close loop feedback at the BA has been studied in previous contributions [1] [2]
In [1], receiver prepare feedback containing suggested MCS and NSS.
In this contribution, we evaluated the performance with the feedback provided, and compare with transmitter side link adaptation algorithms

## Slide 3: Non Beamformed cases
For Nrx =1 case, the maximum Nss = 1, and suggested MCS is provided at each BA. In the next transmission, suggested MCS will be applied by transmitter
Compared with AARF or Minstrel link adaptation at the transmitter, the performance is obviously better

## Slide 4: Non Beamformed cases
For Nrx =2 case, maximum Nss = 2. When 1 Nss PPDU was transmitted, only one EHT-LTF is available
In simulation, transmitter will increase Nss and decrease MCS if feedback is suggesting Nss=1 and high MCS for a certain duration
Compared with AARF or Minstrel throughput gain can be up to 40% ~ 50%

## Slide 5: Summary
Present simulation result for close loop feedback.
Suggest that the feedback shall be included in 11 be standard.

## Slide 6: SP 1
Do you agree to support a link adaptation report in the block ack?
  Y:
  N:
  A:

## Slide 7: SP 2
Do you agree to use the BA control field to indicate the appearance of the LA field?
  Y:
  N:
  A:

## Slide 8: Reference
[1] 11-20-0047-01-00be-feedback-enhancement
[2] 11-20-1005-00-00be-Yet-Another-Fast-Link –Adaptation-Attempt