## Slide 1: Terminology for Soft AP MLD
Date: 2020-07-08
Authors:

## Slide 2: Abstract
In this contribution, we propose several definitions to facilitate the future discussion for the use case that a Non-STR Non-AP MLD plays the role as a Soft AP [1]

## Slide 3: AP, Non-AP STA, AP MLD and Non-AP MLD [2][3]
AP: An entity that contains one station (STA) and provides access to the distribution services, via the wireless medium (WM) for associated STAs. An AP comprises a STA and a distribution system access function (DSAF).
STA: A logical entity that is a singly addressable instance of MAC and PHY interface to the wireless medium (WM)
Non-AP STA: A STA that is not contained within an AP
AP MLD: An MLD, where each STA affiliated with the MLD is an AP
Non-AP MLD: An MLD, where each STA affiliated with the MLD is a non-AP STA

## Slide 4: Definition of Soft AP MLD
A non-AP MLD that can operate a subset of its affiliated STAs as APs
Limit the scope such that only a Non-AP MLD can act as a Soft AP
The Soft AP MLD operates the STAs, rather than these Non-AP STAs are APs (which is a conflicting statement based on current specification)

## Slide 5: When Non-STR Non-AP MLD operates as a Soft AP MLD
Basic Link Set: every pair of links in this set on which the Soft AP MLD can simultaneously transmit and receive frames with another MLD(s)
Conditional Link: the link on which and some links in the Basic Link Set, the Soft AP MLD can NOT simultaneously transmit and receive frames with another MLD(s)
  These links in the Basic Link Set are called the corresponding basic links for this conditional link.

## Slide 6: Straw Poll 1
Do you agree to define Soft AP MLD as the following:
Soft AP MLD: A Non-AP MLD that can operate a subset of its affiliated STAs as APs
Y
N
A

## Slide 7: Straw Poll 2
Do you agree to define the Basic Link Set for a Soft AP MLD as the following:
Basic Link Set: every pair of links in this set on which the Soft AP MLD can simultaneously transmit and receive frames with another MLD(s)
Y
N
A

## Slide 8: Straw Poll 3
Do you agree to define the conditional link for a Soft AP MLD as the following:
Conditional Link: the link on which and some links in the Basic Link Set, the Soft AP MLD can NOT simultaneously transmit and receive frames with another MLD(s)
Y
N
A

## Slide 9: Reference
[1] Non-STR AP Operation, 11-20-0755-01-00be-non-str-ap-operation.pptx
[2] IEEE 802.11-2016
[3] tgbe-spec-framework