## Slide 1: Coordinated Spatial Reuse: Extension to Uplink
Date: 2020-07-10
Authors:

## Slide 2: Recap: Coordinated SR (C-SR)
C-SR is a simple Multi-AP coordination scheme that can increase spectrum efficiency by reusing the same time/frequency resources among multiple BSSs
Several contributions propose C-SR procedure and investigate performance gain [1-5]
In our previous contribution, we propose C-SR procedure for downlink transmissions [6]
In this contribution, we extend C-SR procedure to uplink and investigate potential issues caused by the uplink extension

## Slide 3: Introduction
Objective of C-SR
  Enabling simultaneous data transfer of sharing/shared BSS* in the shared TXOP
  Protection of data transfer of sharing AP while enabling the transmissions of shared BSS
C-SR procedure
  Measurement phase
    Collect information for sharing TXOP
      To decide shared APs and calculate Tx power limits for entities of shared BSS
  Announcement phase
    Inform the Tx power limits to shared AP
    Non-overlapping allocation for BA frequency-domain separation of sharing/shared BSS
  Transmission phase
    Data transmission with adjusted power at shared BSS side
    Non-overlapping simultaneous BA transmissions
* Sharing BSS: BSS that sharing AP belongs to * Shared BSS: BSS that shared AP belongs to

## Slide 4: Recap: C-SR Example of 2-BSS DL/DL [6]
AP1
AP2
STA1-1
STA2-1
Preparation Phase
C-SR-A
DL-SAP
BA
Announcement Phase
Transmission Phase
AP1 obtains TXOP  sharing AP
AP2 obtains the shared TXOP  shared AP
STA1-2
STA2-2
BA
DL
BA
BA
* C-SR-A: C-SR announcement frame *DL-SAP: Downlink transmission of shared AP
Collecting
Capability/RSSI
Collecting
Measurement
Report

## Slide 5: UL Transmission Support in C-SR
Scenarios with UL transmission
  Assumed a single shared AP for simplicity
Changes to be caused by introducing UL compared to DL/DL case
  Transmitters and receivers of data frame
    Interferer or/and victim change(s)
      Interferer: (shared AP)  (STAs in shared BSS)
      Victim: (STAs in sharing BSS)  (sharing AP)
  Transmitters and receivers of block acknowledgment (BA) frame
  Additional signaling to support UL
    Trigger frame transmission
 | Sharing BSS: DL | Sharing BSS: UL
Shared BSS: DL | [CASE1] DL/DL | [CASE2] UL/DL
Shared BSS: UL | [CASE3] DL/UL | [CASE4] UL/UL
* Sharing/Shared

## Slide 6: UL Transmission Support in C-SR
Fundamental rule
  Since sharing AP is the owner of TXOP, C-SR procedure shall not limit the shared TXOP utilization of the sharing AP
How to limit the transmission power of transmitting entity of shared BSS when shared AP decides to utilize the sharing TXOP as UL transmission?
  Sharing AP is not able to estimate potential interference from shared BSS since it does not know the transmitter(s) in advance.
Do we need to limit shared AP’s TXOP utilization in the shared TXOP?

## Slide 7: Issue 1: Utilization of Shared TXOP at Shared BSS
Objective
  To protect transmission at sharing BSS from potential interference from shared BSS
Option 1: DL and UL allowed
  Shared AP is free to select UL/DL
  Sharing AP does not know the transmitter of shared TXOP
  Sharing AP may limit the tx power of shared BSS conservatively
Option 2: DL allowed, UL access selectively granted
  Sharing AP indicates whether the shared TXOP is able to utilized as UL transmission or not by shared AP
Option 3: DL allowed, UL prohibited
  Shared TXOP is only utilized for DL
  Sharing AP will estimate the interference to STA of sharing AP from shared AP
Shared AP
STA of shared AP
Sharing AP
STA of
sharing AP
Sharing BSS
Shared BSS
< DL/UL case >
Shared AP
STA of shared AP
Sharing AP
STA of
sharing AP
Sharing BSS
Shared BSS
< DL/DL case >
Notes: Needs scenario for each option

## Slide 8: Issue 1: Utilization of Shared TXOP at Shared BSS
Required changes compared to option3
  Option 2 requires “UL allow” indication per shared AP in C-SR-A frame
  In option 1 and 2, sharing AP carefully calculates appropriate tx power limit for shared BSS
AP1
AP2
STA1-1
STA2-1
Preparation Phase
C-SR-A
BA
Announcement Phase
Transmission Phase
STA1-2
STA2-2
BA
Trigger
UL
BA
UL
DL
Collecting
Capability/RSSI
Collecting
Measurement
Report
Notes: Option2를 통해 AP에게 flexibility를 줄 수 있다.

## Slide 9: Issue 2: Announcement/Trigger Frame Integration
If sharing AP schedules UL transmission in shared TXOP, then C-SR announcement frame can integrate with Trigger frame of the sharing AP
This will reduce signaling overhead of trigger frame transmission
AP1
AP2
STA1-1
STA2-1
Preparation Phase
C-SR-A
DL
BA
Announcement Phase
Transmission Phase
STA1-2
STA2-2
UL
BA
Announcement
Trigger
UL
Collecting
Capability/RSSI
Collecting
Measurement
Report

## Slide 10: Summary
We investigate UL support in C-SR operation
  Concerns
    Sharing AP is difficult to limit tx power of sharing BSS side
We propose three options of TXOP utilization at shared BSS side
We investigate Announcement/Trigger frame integration issue
Notes: Inter-AP signaling for C-SR info is the issue in Preparation phase

## Slide 11: Straw Poll #1
Do you agree that in 11be sharing AP may limit the shared AP’s uplink TXOP utilization during the shared TXOP for C-SR operation?
  The way of limiting TXOP utilization of shared AP is TBD

## Slide 12: Reference
[1] 802.11-20/0410r4
[2] 802.11-20/0576r0
[3] 802.11-20/0457r1
[4] 802.11-20/0107r1
[5] 802.11-20/0073r0
[6] 802.11-20/0590r0

## Slide 13: Appendix

## Slide 14: C-SR Example of 2-BSS UL/UL
Announcement/trigger frame integrated into C-SR-A
AP1
AP2
STA1-1
STA2-1
Preparation Phase
C-SR-A
BA
Announcement Phase
Transmission Phase
STA1-2
STA2-2
Trigger
UL
BA
UL
UL
Collecting
Capability/RSSI
Trigger
UL
Collecting
Measurement
Report
Trigger