## Slide 1: Coordinated Spatial Reuse: Extension to Uplink
Date: 2020-07-10
Authors:

## Slide 2: Introduction
C-SR is a simple Multi-AP coordination scheme that can increase spectrum efficiency by reusing the same time/frequency resources among multiple BSSs
Several contributions propose C-SR procedure and investigate performance gain [1-5]
In our previous contribution, we investigated several issues regarding C-SR downlink transmissions [6]
In this contribution, we investigate the potential issues when extending C-SR procedure to cover uplink transmissions

## Slide 3: Recap: Coordinated SR (C-SR)
Objective of C-SR
  Enabling simultaneous data transfer of entities of the both sharing BSS and shared BSS in the shared TXOP
Requirement of C-SR
  Protecting data transfer of the sharing BSS entities in the shared TXOP
DL C-SR procedure
  Measurement phase
    STA estimates path loss based on the beacon signal and reports to associated AP
    AP collects path loss information to calculate Tx power limit of shared AP
  Announcement phase
    AP transmits announcement frame including Tx power limit of shared AP and the BA resource allocation of sharing/shared BSS to shared AP
  Transmission phase
    Data transmission of shared AP with adjusted power
    Simultaneous BA transmissions
Sharing BSS: BSS that sharing AP belongs to
Shared BSS: BSS that shared AP belongs to

## Slide 4: Recap: C-SR Example of 2-BSS DL/DL [6]
AP1
AP2
STA1-1
STA2-1
Preparation Phase
C-SR-A
DL MU
BA
Announcement Phase
Transmission Phase
AP1 obtains TXOP  sharing AP
AP2 obtains the shared TXOP  shared AP
STA1-2
STA2-2
BA
DL MU
BA
BA
* C-SR-A: C-SR announcement frame
Collecting
Capability/Path loss
Measuring and
Collecting
Path loss
Report
Measurement
Report

## Slide 5: C-SR Scenarios
Four C-SR scenarios
  Assumption: a single shared AP for simplicity
Case 1: DL/DL
  Protection of SIR of “AP1 to STA1”
  AP1 requires
    ,
Case 2: UL/DL
  Protection of SIR of “STA1 to AP1”
  AP1 requires
    ,
Case 1 and 2 can be covered by the path loss estimation from AP2 and the path loss report from STA1
 | Sharing BSS: DL | Sharing BSS: UL
Shared BSS: DL | [Case1] DL/DL | [Case2] UL/DL
Shared BSS: UL | [Case3] DL/UL | [Case4] UL/UL
* Sharing BSS/Shared BSS
AP2
2
AP1
1
[Case 1 and Case 2]

## Slide 6: C-SR Scenarios
Case3: DL/UL
  Protection of SIR of “AP1 to STA1”
  Sharing AP doesn’t know which STA associated with shared AP transmits
Case4: UL/UL
  Protection of SIR of “STA1 to AP1”
  Sharing AP doesn’t know which STA associated with shared AP transmits
Case3 and case4 cannot be covered by the path loss measurement/report procedure proposed for DL C-SR operation
AP2
2
AP1
1
AP2
2
AP1
1
3
3
[Case 3]
[Case 4]

## Slide 7: UL Issues and Proposal
Two issues for supporting UL transmission at shared BSS
  Some PL values are difficult to collect
    OBSS STA-to-AP: ,
    STA-to-STA PL: ,
  Sharing AP cannot calculate Tx power limit (TPL) of UL STA(s) of shared AP in advance
    Shared AP needs to manage the transmission power of UL STA(s)
Proposal
  Tolerable Interference Limit (TIL) for UL transmission at shared BSS
    TIL is a maximum allowed interference power to guarantee a certain level of SIR at sharing AP side transmission
    Sharing AP indicates TIL to shared AP
    Shared AP mandates the TIL requirement for UL scheduled STAs
  Limiting utilization of shared TXOP at shared BSS
    Case 3 cannot be covered even with the proposed path loss signaling
    Sharing AP may not have enough information to calculate TPL
    Sharing AP may believe it’s risky to allow UL at shared AP

## Slide 8: Proposal 1: TPL and TIL Signaling
Different signaling for DL and UL transmission at shared BSS
  Transmission Power Limit for DL at shared BSS
    Sharing AP indicates TPL for shared AP
    Sharing AP requires the following path loss values to calculate TPL
      Path loss report from associated STA(s)
      Path loss measurement from neighboring C-SR capable AP
  Tolerable Interference Limit for UL at shared BSS
    Sharing AP indicates TIL for potential UL STA(s) at shared AP
    Shared AP requires the following path loss values to meet TIL requirement
      Path loss report from associated STA(s)
      Path loss measurement from neighboring C-SR capable AP
To cover the case3, shared AP may require additional operation
  ex. limiting UL STA’s power conservatively with the assumption of the worst case topology

## Slide 9: Proposal 2: Limiting Utilization of Shared TXOP at Shared BSS
Objective
  Sharing AP can limit the shared TXOP utilization at shared BSS
Option 1: DL and UL selectively granted (preferred)
  Sharing AP indicates whether the shared TXOP is able to be utilized DL or/and UL by shared AP
  The information can be included in the announcement frame
  TPL and TIL information can be selectively included
Option 2: DL allowed, UL prohibited
  Shared AP is allowed to use DL transmissions in the shared TXOP
  This option makes the C-SR procedure simpler, but less flexible
DL | UL | Utilization of shared TXOP at shared BSS
0 | 0 | Reserved
0 | 1 | Only UL allowed
1 | 0 | Only DL allowed
1 | 1 | Both DL and UL allowed
Notes: Needs scenario for each option

## Slide 10: Proposal 3: Announcement/Trigger Frame Integration
If sharing AP schedules UL transmission in shared TXOP, then C-SR announcement frame can integrate with Trigger frame of the sharing AP
This will reduce signaling overhead of trigger frame transmission
AP1
AP2
STA1-1
STA2-1
Preparation Phase
C-SR-A
DL
BA
Announcement Phase
Transmission Phase
STA1-2
STA2-2
UL
BA
Announcement
Trigger
UL
Collecting
Capability/Path loss
Measuring and
Collecting
Path loss
Report

## Slide 11: Summary
We investigate all C-SR scenarios according to the shared TXOP utilization of sharing/shared AP
We propose sharing AP indicates Tolerable Interference Limit to shared AP and shared AP needs to meet the requirement when shared AP schedules UL transmission in the shared TXOP
We propose options of limiting TXOP utilization at shared BSS
We investigate Announcement/Trigger frame integration
Notes: Inter-AP signaling for C-SR info is the issue in Preparation phase

## Slide 12: Straw Poll #1
Do you agree that in 11be sharing AP indicates Tolerable Interference Limit to shared AP in the announcement frame?
  The format of indicating Tolerable Interference Limit is TBD
  Tolerable Interference Limit is indicated when sharing AP allows UL transmission at shared AP

## Slide 13: Straw Poll #2
Do you agree that in 11be sharing AP limits the shared AP’s uplink TXOP utilization during the shared TXOP for C-SR operation?
  The way of limiting TXOP utilization of shared AP is TBD

## Slide 14: Reference
[1] 802.11-20/0410r4
[2] 802.11-20/0576r0
[3] 802.11-20/0457r1
[4] 802.11-20/0107r1
[5] 802.11-20/0073r0
[6] 802.11-20/0590r4

## Slide 15: Appendix

## Slide 16: C-SR Example of 2-BSS UL/UL
Announcement/trigger frame integrated into C-SR-A
AP1
AP2
STA1-1
STA2-1
Preparation Phase
C-SR-A
BA
Announcement Phase
Transmission Phase
STA1-2
STA2-2
Trigger
UL
BA
UL
UL
UL
Trigger
Collecting
Capability/Path loss
Measuring and
Collecting
Path loss
Report