## Slide 1: MLO: Protocol for TID-to-link negotiation
Name | Affiliation | Address | Phone | Email
Abhishek Patil | Qualcomm Inc. |  |  | appatil@qti.qualcomm.com
Duncan Ho | Qualcomm Inc. |  |  | 
George Cherian | Qualcomm Inc. |  |  | 
Alfred Asterjadhi | Qualcomm Inc. |  |  | 
Date: 2020-02-26

## Slide 2: Background
TID-to-link feature maps a TID to one or more links
  The frames belonging to the TID are sent on the mapped link(s)
Such traffic separate can aid latency sensitive traffic flow
  Assign a high-volume, latency tolerant traffic flow to a subset of link while mapping latency sensitive flows to all links
  Increases channel access opportunities for a latency sensitive flow
  At a system level, reduces contention between latency sensitive and latency tolerant flows
Other use cases include load balancing, co-ex conditions, separating UL/DL flows etc
STAa 1
…
Link 1
Link 2
STAa 2
TIDvo
…
STAb 1
STAb 2
Link 3
STAa 3
STAb 3
…
TIDbe
MLDa
MLDb
…

## Slide 3: Problem Statement
In MLO, MLDs negotiate TID to link mapping.
  Either MLD can initiate a change to the default or existing mapping
However, the receiving MLD may not agree to the proposed mapping
  What is the outcome of the negotiation?
MLO framework needs to provide a protocol for determining the result of a TID-to-link negotiation
Map TID-4 to 5 GHz
Map TID-4 to 2.4 & 5 GHz
Non-AP MLD
AP MLD
?
Time
TID-4 maps to 5 GHz

## Slide 4: Result of TID to link negotiation
We propose simple rules to decide the outcome of TID mapping negotiation.
We follow existing baseline rules for any negotiation – for example, BA setup
  ADDBA Req [BA size of 128] + ADDBA Resp [BA size of 128] = [BA negotiated for 128]
  ADDBA Req [BA size of 256] + ADDBA Resp [BA size of 64] = [BA negotiated for 64]
If the responding MLD replies with the same set of links as the ones proposed by the initiating MLD, the resulting mapping is the link set proposed by the initiator
  Negotiation is considered success
Else, if the responding MLD proposes an alternative set of links that consists of a subset of requested links, the resulting mapping consists of the subset of links
  Negotiation is considered success
When the responding MLD replies with an empty set, the original mapping is maintained
  Negotiation is considered failed
  The initiating MLD could make another attempt at a later point

## Slide 5: TID mapping negotiation
By default, all TIDs are mapped to all links
  Either MLD can initiate a change to the existing mapping
During the negotiations
  An initiating MLD can:
    request expanding the link set for a TID
    request contracting the link set for a TID
    request switching the link set for a TID
  A responding MLD provides the links (from the proposed set) that it can operate on
    When the proposed link set includes link(s) that are already part of the existing mapping, the responding MLD includes at least one link from that set.
      If the responder was not happy with the current set, it would have initiated a change to the mapping

## Slide 6: Rational for converging on a subset
An MLD (initiator or responder) that has constraints may propose a smaller set of links
  For example, a non-AP MLD may have co-ex or power-save constraints due to which it can’t operate on a certain link (or accept a request to expand to multiple links)
  An AP MLD may want to keep high volume (latency tolerant) flows out of certain links to reduce contention with latency sensitive flows
    Latency sensitive flows are expected to be mapped on to multiple links to benefit from multiple access opportunities.
Further a responding MLD may reject a proposed switching of links if it is unable to operate on the suggested link set
Therefore, by selecting a subset, the convergence protocol can satisfy both parties.
  Once the constraints no longer apply, an MLD can always initiate an expansion of the link set for that TID

## Slide 7: TID Negotiation
Success
Map TID-4 to 2.4 & 5 GHz
Map TID-4 to 2.4 & 5 GHz
MLD 1
MLD 2
Time
After: TID-4 maps to 2.4 & 5 GHz
Success
Map TID-4 to 5 GHz
Map TID-4 to 2.4 & 5 GHz
MLD 1
MLD 2
Time
After: TID-4 maps to 5 GHz
Before: TID-4 maps to 5 GHz
Before: TID-4 maps to 5 GHz
Responding MLD agrees with the proposed set of links. TID mapping for TID 4 expanded to include 2.4.
Link Expansion
Expansion attempt unsuccessful. Responding MLD unable to add to 2.4 to the link set for TID 4
Original TID mapping is maintained
Success
Map TID-4 to 5 GHz
Map TID-4 to 5 GHz
MLD 1
MLD 2
Time
After: TID-4 maps to 5 GHz
Before: TID-4 maps to 2.4 & 5 GHz
Link set for TID-4 reduced to 5 GHz as proposed by the initiating MLD
Link set contraction

## Slide 8: TID Negotiation
Failure
Map TID-4 to 6 GHz
MLD 1
MLD 2
Time
After: TID-4 maps to 5 GHz
Before: TID-4 maps to 5 GHz
Switching attempt unsuccessful. Responding MLD unable to switch to 6 GHz
Original TID mapping is maintained
Success
Map TID-4 to 6 GHz
Map TID-4 to 6 GHz
MLD 1
MLD 2
Time
After: TID-4 maps to 6 GHZ
Before: TID-4 maps to 5 GHz
Responding MLD agrees with the proposed switching. TID mapping for TID 4 switched to 6 GHz.
Link switched to 6 GHz
Success
Map TID-4 to 6 GHz
Map TID-4 to 2.4 & 6 GHz
MLD 1
MLD 2
Time
After: TID-4 maps to 6 GHz
Before: TID-4 maps to 5 GHz
TID switches to subset of proposed link(s). Responding MLD unable to switch to 2.4
Link set switched to subset of proposed

## Slide 9: Conflicting constraints
The table shows the conflicting requirements that need to be satisfied:
  low-lat and power-save are opposing requirements
  Similarly AP/client have opposing view of system performance
    avoid overlap of latency tolerant flow from one client and a latency sensitive flow from another client
Factors | Non-AP MLD | AP MLD
Power-save | Yes prefer to have min RF’s ON | No
Low latency | Yes more links increase access opportunities | Yes more links increase access opportunities
System performance | No has local view and selfish motives | Yes has global view and goal to serve all STAs
Others (coex etc) | Co-ex: Yes Traffic separation: not so much | Co-ex: Yes for soft AP Traffic separation: Yes

## Slide 10: Satisfying conflicting requirements
A non-AP MLD (client device) prefers to:
  have minimal links enabled for power-save reasons (i.e., prefer not to have disjoint mapping)
  use all links for low latency flows
  use any link for UL
An AP MLD serves the needs of many and therefore:
  can receive UL on any link
  strives to reduce the contention between best effort and latency sensitive flows
These conflicting interests can be met by a couple of simple rules:
  Rule #1: A low-lat TID is mapped on to multiple links (multi-primary benefit)
  Rule #2: For a non-AP MLD, AP MLD provides at least one link where all TIDs are mapped (aids power-save)
To reduce contention between best effort and latency sensitive flows:
  AP can attempt to have the set of link(s) where all TIDs are mapping to be common for all non-AP MLDs (link can be on a lower band channel to satisfy range/reachability)
    Goal is to reduce the contention between latency sensitive and latency tolerant flows across all clients

## Slide 11: Summary
This contribution provides simple rules for determining the result of a TID-to-link negotiation
  The negotiation is considered a success when there is at least one link common in the set proposed by the initiating and responding MLD
    The resulting mapping is the subset (consisting of common) links
  In case of no overlap, the negotiation is deemed as failed and there is no change to the TID mapping
The contribution further provides rules for addressing the conflicting requirements from each side.
  An AP MLD must provide at least one link where all TIDs map to
  Map latency tolerant TIDs to a subset of links while latency sensitive flows are mapped to all or most of the setup links

## Slide 12: SP #1
Do you agree that an AP MLD shall ensure that for each non-AP MLD with which it has performed ML setup, there is at least one link to which all TIDs map to?
  Y:
  N:
  A:

## Slide 13: SP #2
Do you agree that the TID-to-link mapping negotiation shall result in a TID being mapped to a set of links that are common between the links proposed by the initiating MLD and the ones proposed by the responding MLD?
  When the proposed link set includes link(s) that are already part of the current mapping, the responding MLD shall include at least one link from that set.
    NOTE: a responding MLD is expected to be OK to operate on the link set where the TID is currently mapped on to
  When there are no common links between the ones proposed by the initiator and responder, the negotiation is deemed as failed and there is no change to the TID mapping
  Y:
  N:
  A:

## Slide 14: SP #3
Do you agree that an AP MLD should have the same set of link(s) to which all TIDs map for all the non-AP MLDs with which it has performed ML setup?
  Y:
  N:
  A:

## Slide 15: SP #4
Do you agree that, when there is an active latency sensitive flow, an AP MLD should negotiate to map a latency tolerant flow belonging to a non-AP MLD to a subset of links and negotiate mapping of the latency sensitive flow to all links?
  Y:
  N:
  A: