## Slide 1: Discussion on Multi-link with Multiple AP MLDs
Authors:
Name | Affiliations | Address | Phone | Email
Yoshihisa Kondo | ATR |  |  | kondo@atr.jp
Hiroyuki Yokoyama |  |  |  | 
Michio Miyamoto |  |  |  | 
Ayano Onishi |  |  |  | 
Toru Osuga | NICT |  |  | 
Taketoshi Nakajima |  |  |  | 
Fumiko Ohori |  |  |  | 
Satoko Itaya |  |  |  | 
Fumihide Kojima |  |  |  | 
Date: 2020-10-21

## Slide 2: Motivations
In multi-link framework discussions [1], it is assumed that a non-AP MLD has links with an AP MLD
However, in many usage cases like enterprise use or industry use, overlapped BSSs are deployed using multiple AP devices to cover a broad area seamlessly
There are many cases where the total available link capacity is expected to be larger if a non-AP MLD has multiple links with different AP-MLDs
In this contribution, following topics are to be discussed:
  Situations where multi-link with multiple AP-MLDs is beneficial
  Multi-link operation with multiple AP-MLDs
AP MLD
Non-AP MLD
AP MLD
AP MLD
Non-AP MLD
Link
Link
Link
Link
Current ML framework
ML framework to be discussed

## Slide 3: Examples where multi-link with multiple AP MLDs is beneficial
Low signal strength
  Signal strength of each link can be very low due to various reasons such as multipath fading
  There are cases where signal strength of an other link with a different AP MLD is much higher
Co-channel interference
  If a frequency channel of one of links is very busy, available link capacity of an alternative link with a different AP MLD may be larger
Load balancing
  If there are non-AP STAs which share the AP with the Non-AP MLD and they have large amount of traffic, available link capacity of an alternative link with a different AP MLD may be larger
AP MLD
Non-AP MLD
a
AP
AP MLD
AP
b
c
d
Ch.a
AP MLD
AP MLD
Non-AP MLD
Co-channel interference
Low signal strength
AP MLD
Non-AP MLD
Non-AP STA
AP MLD
Load balancing
Fading
Non-AP STA
Non-AP STA
Non-AP STA

## Slide 4: Examples where multi-link with multiple AP MLDs is beneficial (Cont.)
Mobility
  A non-AP MLD changes its connections from AP MLD1 to AP MLD2 according to its mobility
  Performance of intermediate state (T2) where available link capacity tends to become small can be improved thanks to multi-link with multiple AP MLDs
AP MLD 1
AP MLD 2
Non-AP MLD
Non-AP MLD
T1
T2
Non-AP MLD
T3
Mobility

## Slide 5: Framework discussion for multi-link with multi AP MLDs
Distribution System
Non-AP MLD logical entity
Non-AP STA1
AP MLD logical entity
AP2
Non-AP STA2
AP1
Link 1
Link 2
Distribution System
Non-AP MLD logical entity
Non-AP STA1
External service
Portal
AP MLD logical entity
Multi-link with multiple AP MLDs
External function is needed to coordinate AP MLDs
Tx frame allocation to AP MLDs
Rx frame reordering and duplication check
Coordination of multi-link setup
AP2
Non-AP STA2
External network
AP1
AP MLD logical entity
AP4
AP3
802.11
Link 1
Link 2
Current framework [1]

## Slide 6: Overview of downlink transmission
An external device allocates transmission frames instead of an AP MLD
For Rx, scoreboarding of each MAC is coordinated by an MLD level features
For Tx, Tx buffer control of each MAC works independently
  If the external device can coordinate Tx buffer control, operation becomes more efficient
PHY
MAC
PHY
MAC
PHY
MAC
PHY
MAC
AP MLD
Non-AP MLD
Tx Buf control
Block Ack
Soreboarding
Scoreboading support
Reordering
(ML operation)
External device
PHY
MAC
PHY
MAC
PHY
MAC
PHY
MAC
AP MLD
Non-AP MLD
PHY
MAC
PHY
MAC
AP MLD
Tx Buf control
Block Ack Scoreboarding
ML setup support
ML setup support
ML setup support
ML setup support
(ML coordination)
(ML operation)
(ML operation)
(ML operation)
(ML operation)
Tx Frame allocation
(Tx Buf Ctl support)
Tx Buf control
Block Ack
Soreboarding
Block Ack
Soreboarding
Scoreboading support
Reordering
Tx Buf. control
Tx Frame allocation
Tx Buf Ctl support

## Slide 7: Overview of uplink transmission
AP MLDs send all received frames to an external device and the external device reorder them
For Tx, Tx buffer control of each MAC is coordinated by an MLD level feature
For Rx, socoreboarding of each MAC works independently
  If the external device can coordinate scorebording, operation becomes more efficient
PHY
MAC
PHY
MAC
PHY
MAC
PHY
MAC
AP MLD
Non-AP MLD
(External device)
PHY
MAC
PHY
MAC
PHY
MAC
PHY
MAC
AP MLD
Non-AP MLD
PHY
MAC
PHY
MAC
AP MLD
(ML operation)
(ML operation)
(ML operation)
(ML operation)
(ML operation)
(ML coordination)
ML setup support
ML setup support
Tx Buf. control
Tx Buf. control
Block Ack Scoreboarding
Scoreboading support
Reordering
Block Ack Scoreboarding
Tx Frame allocation
Tx Bud. cotorol support
ML setup support
ML setup support
Block Ack Scoreboarding
Block Ack Scoreboarding
(Scoreboading support)
Reordering
Tx Buf. control
Tx Buf. control
Tx Frame allocation
Tx Buf. control support

## Slide 8: Conclusions
In this contribution, following topics were discussed:
  Situations where multi-link with multiple AP-MLDs is beneficial
  Multi-link operation with multiple AP-MLDs

## Slide 9: References
[1] 802.11-19/0773r8 Multi-link Operation Framework

## Slide 10: Straw poll
Do you support that the multi-link operation with multiple AP MLDs should be discussed in TGbe?
  Not R1 feature

## Slide 11: Appendix 1: Example of downlink transmission (Scoreboarding coordination)
Non-AP MLD
AP MLD 1
PHY
PHY
PHY
MAC
MAC
MAC
External device
1
3
2
4
BA 1,3,5
BA 1,2,3,4,5
4
3
2
1
1
2
3
4
1
2
3
4
Frame replication
Tx frame selection
AP MLD 2
PHY
MAC
Sync. of Rx status
(Scoreboard)
1
3
2
4
1
2
3
4
7
8
To Non-AP MLD
5
6
9
BA 2,4,7,8,9
6
10
6
8
10
BA 6,10
BA 6,7,8,9,10
6
8
10
6
8
10
AP MLD 1
Non-AP MLD
STA1
STA2
AP MLD 2
1
2
3
4
5
6
7
8
9
10
1
2
3
4
5
6
7
8
9
10
1
2
3
4
5
6
7
8
9
10
2
4
6
7
8
9
10
6
10
Sync of Rx status
1
2
3
4
5
6
7
8
9
10
6
7
8
9
10
Tx buffer
Tx buffer
AP MLD1 (AP MLD2) transmits frames with odd (even) sequence number first
BA includes Rx status of both links and each AP MLD can remove Tx frames delivered by another link
AP MLD1 (AP MLD2) transmits frames with even (odd) sequence number if they are not delivered via another link
Tx buffer：MAC level or MLD level (TBD)

## Slide 12: Appendix 2: Example of uplink transmission (Tx buffer control coordination)
Non-AP MLD
AP MLD 1
PHY
PHY
PHY
MAC
MAC
MAC
External device
1
3
2
4
BA 1,3,5
BA 2,4
4
3
2
1
1
3
2
4
Redundancy check
Reordering
AP MLD 2
PHY
MAC
1
2
3
4
7
8
From Non-AP MLD
5
6
9
BA 7,8,9
6
10
6
8
10
BA 6,10
BA 6,8
6
8
10
6
8
10
AP MLD1
Non-AP MLD
STA1
STA2
AP MLD2
STA1 (STA2) of non-AP MLD transmits frames with odd (even) sequence number first
Rx status of each link is synchronized between MACs in the non-AP MLD
STA1 (STA2) transmits frames with even (odd) sequence number if they are not delivered via another link
Scoreboard of each AP may be updated (slided) without receiving all frames
1
3
2
4
Allocation
Sync. of Rx status
1
2
3
4
5
6
7
8
9
10
1
2
3
4
5
6
7
8
9
10
2
4
6
7
8
9
10
6
10
Tx buffer
6
7
8
9
10
All Rx frames are sent to the external device
Tx buffer：MAC level or MLD level (TBD)