## Slide 1: Error Recovery for Non-STR MLD
Date: 2020-11-03
Authors:
Name | Affiliations | Address | Phone | Email
Yunbo Li | Huawei | Shenzhen, China |  | liyunbo@Huawei.com
Yuchen Guo |  |  |  | 
Yifan Zhou |  |  |  | 
Guogang Huang |  |  |  | 
Yiqing Li |  |  |  | 
Ming Gan |  |  |  | 
Meihong Zhang |  |  |  | 
Arik Klein | Huawei | TLV Research Center, Israel |  | 
Notes: September 2012

## Slide 2: Background
In downlink transmission, PPDU Ending time alignment can be used by AP MLD to avoid simultaneous transmit and receive on two different links for non-STR non-AP MLD;
When transmission failure happens, how AP MLD aligns the following PPDUs in different links is discussed in presentation [1];
But only part of scenarios are discussed, here we want to have more further discussion to give people a more complete picture of how AP MLD to do error recovery when target to a non-STR non-AP MLD.

## Slide 3: Error Recovery with Instant Cross Link Exchange
link1
BA10
PPDU11
BA11
PPDU12
BA12
link2
PPDU20
BA20
PPDU21
BA21
PPDU21’
BA21’
First we assume the AP MLD with instant cross link information exchange capability to make the problem simple;
Below is the case that covered in [1]: success transmission on link 1, and no BA on link 2;
  A delayed PIFS error recovery be used in link 2 to align the following PPDUs
More cases will be discussed in following slides.
  In all the cases, assume the BAs on two links are expected to align both starting and ending times.
PIFS
SIFS
SIFS
SIFS
SIFS
SIFS
SIFS
SIFS
SIFS
SIFS
AP1
AP2
STA1
STA2
PPDU10

## Slide 4: Error Recovery for non-STR AP MLD
Case description: success transmission on link 1, PHY-RXSTART.indication received but decoding failed of BA21 on link2;
When PIFS recovery is used in link2, PPDU21’ will be one SlotTime shorter than PPDU12 in order to align the PPDU ending time；
But this solution can not applied to non-STR AP MLD(soft AP), because PPDU12 is one timeslot earlier than PPDU21’, the PIFS sensing on link2 will be blocked by PPDU12.
link1
PPDU11
BA11
PPDU12
BA12
link2
PPDU21
BA21
PPDU21’
BA21’
SIFS
SIFS
SIFS
SIFS
SIFS
SIFS
SIFS
SIFS
SIFS
PIFS
AP1
AP2
STA1
STA2
PPDU20
BA10
BA20
PPDU10

## Slide 5: Error Recovery for non-STR AP MLD
In order to solve the non-STR AP problem, PIFS before PPDU12 is needed in link1 even when BA11 is correctly decoded;
A following question is should STR AP MLD and non-STR AP MLD use different rule in link1, or define a unified solution which is PIFS after correctly decoded BA;
It is also possible to allow STR AP MLD choose either option it prefers in implementation.
link1
CTS
PPDU11
BA11
PPDU12
BA12
link2
CTS
PPDU21
BA21
PPDU21’
BA21’
SIFS
SIFS
SIFS
PIFS
SIFS
SIFS
SIFS
SIFS
SIFS
PIFS
AP1
AP2
STA1
STA2
PPDU20
BA10
BA20
PPDU10

## Slide 6: Error Recovery with Delayed Cross Link Exchange
When both BA11 and BA21 are correctly received, it looks natural to use SIFS before next PPDUs transmission in both links;
But it has problem for non-STR AP that transmits on both links if the cross link information exchange delay is longer than SIFS;
AP1 doesn’t know receive status of BA21 at the SIFS time boundary after BA11. It means transmit PPDU12 at SIFS time after BA11 may blocked the PIFS sensing on link2 if BA21 is failed.
link1
CTS
PPDU11
BA11
PPDU12
BA12
link2
CTS
PPDU21
BA21
PPDU22
BA22
SIFS
SIFS
SIFS
SIFS
SIFS
SIFS
SIFS
SIFS
SIFS
SIFS
AP1
AP2
STA1
STA2
PPDU20
BA10
BA20
PPDU10

## Slide 7: Error Recovery with Delayed Cross Link Exchange
As a result, PIFS will still be needed for non-STR AP when both BA are correctly received
link1
CTS
PPDU11
BA11
PPDU12
BA12
link2
CTS
PPDU21
BA21
PPDU22
BA22
SIFS
SIFS
SIFS
PIFS
SIFS
SIFS
SIFS
SIFS
SIFS
PIFS
AP1
AP2
STA1
STA2
PPDU20
BA10
BA20
PPDU10

## Slide 8: Error Recovery with Delayed Cross Link Exchange
link1
CTS
PPDU11
BA11
PPDU12
BA12
link2
CTS
PPDU21
BA21
PPDU21’
BA21’
Let’s go back to the figure in slide 3, we can see that it is designed to align the starting time of PPDU21’ and PPDU12;
It can realizes when assume instant cross link exchange, but it may be hard to align the starting time of two PPDUs with delayed cross link information exchange, because AP2 doesn’t know the receive status of BA11 when it starts to transmit PPDU21’.
PIFS
SIFS
SIFS
SIFS
SIFS
SIFS
SIFS
SIFS
SIFS
SIFS
This figure is same as the one in slide 3.
AP1
AP2
STA1
STA2
PPDU20
BA10
BA20
PPDU10

## Slide 9: Error Recovery with Delayed Cross Link Exchange
link1
CTS
PPDU11
BA11
PPDU11’
BA12
link2
CTS
PPDU21
BA21
PPDU21
BA21
When BA11 is failed, there will be a PIFS time before the transmission of PPDU11’. But AP2 can not know the information due to the delay of cross link exchange;
So the starting times of PPDU11’ and PPDU21 are not aligned.
PIFS
PIFS
SIFS
SIFS
SIFS
SIFS
SIFS
SIFS
SIFS
SIFS
AP1
AP2
STA1
STA2
PPDU20
BA10
BA20
PPDU10

## Slide 10: Error Recovery with Delayed Cross Link Exchange
link1
CTS
PPDU11
BA11
PPDU11’
BA12
link2
CTS
PPDU21
BA21
PPDU21
BA21
Since the starting times of PPDUs are hard to be aligned, do we still need to defer the starting time of PPDU21 to SIFS time after BA11?
Maybe we should allow AP2 to transmit PPDU21 right after the ending time of BA11
  Note: This rule only applied to STR AP
  It will also benefit for the case that without delayed cross link exchange
There are two benefits
  Reduce the probability that the third part STAs do channel contention on link 2
  Slightly increase the throughput
PIFS
SIFS
SIFS
SIFS
SIFS
SIFS
SIFS
SIFS
SIFS
SIFS
AP1
AP2
STA1
STA2
PPDU20
BA10
BA20
PPDU10

## Slide 11: Error Recovery with Delayed Cross Link Exchange
If the delay of cross link information exchange is longer than BA + SIFS, when no PHY-RXSTART.indication of BA21 is received in link2, AP2 can not know the receive status of BA11 at BA+ SIFS time;
Same situation happens in link1;
So when none of RXSTART indication of BA21 and BA11 is received, AP1 and AP2 will transmit PPDU11’ and PPDU21’ after expected BA time (or BA+ SIFS)
link1
CTS
PPDU11
BA11
PPDU11’
BA11’
link2
CTS
PPDU21
BA21
PPDU21’
BA21’
SIFS
SIFS
SIFS
PIFS
SIFS
SIFS
SIFS
SIFS
SIFS
PIFS
AP1
AP2
STA1
STA2
PPDU20
BA10
BA20
PPDU10

## Slide 12: Error Recovery with Delayed Cross Link Exchange
When the delay of cross link information exchange is shorter than BA, each AP may get the receive status of BA on another link before the expected BA ending time;
Then this AP can transmit following PPDU immediately after it received the cross link failure notification.
link1
CTS
PPDU11
BA11
PPDU11
BA11
link2
CTS
PPDU21
BA21
PPDU21
BA21
SIFS
SIFS
SIFS
PIFS
SIFS
SIFS
SIFS
SIFS
SIFS
PIFS
Cross link failure notification
AP1
AP2
STA1
STA2
PPDU10
PPDU20
BA10
BA20

## Slide 13: Summary
Potential error recovery scenarios for response non-STR MLD are listed, and possible solutions are introduced;
Several factors are considered during the design
  Avoid simultaneous transmit and receive for non-STR non-AP MLD
  Initiating AP MLD may also be non-STR MLD (soft AP)
  Delay of cross link information exchange

## Slide 14: Reference
[1] 11-20-0427-00-00be-synchronous-multi-link-operation

## Slide 15: Straw Poll 1
Do you agree to allow PIFS time interval between the ending of successful response frame and following PPDU for non-STR AP MLD in R1?
Y/N/A =
Covers slides 5 and 7

## Slide 16: Straw Poll 2
Do you support the inclusion of the following in the SFD for 802.11be R1:
After an AP that affiliates with a STR AP MLD to transmit a frame to a STA that affiliates with a NSTR STA MLD on one link of a NSTR link pair, if no PHY-RXSTART.indication of the response frame is received, this AP can transmit next PPDU as long as it not cause the simultaneous transmit and receive of NSTR STA MLD on this NSTR link pair.
  It required channel be idle base on PIFS sensing before transmit the next PPDU.
Y/N/A =
Covers slide 10

## Slide 17: Straw Poll 3
Do you support the inclusion of the following in the SFD for 802.11be R1:
An AP that affiliate with AP MLD can transmit next PPDU within a TXOP right after cross link failure information is received when no PHY-RXSTART.indication of response frame is received?
  It required channel be idle base on PIFS sensing before transmit the PPDU.
Y/N/A =
Covers slide 12