## Slide 1: Traffic indication of latency sensitive applications
Date: 2020-09-01
Authors:

## Slide 2: Motivations
For UL latency sensitive traffic, such as gaming control and industrial automation, some applications require periodic traffic transmission [1, 2]
  Traffic properties: Data rate < 1 Mbp or bursty fixed amount of data
  Requirements: small jitter and lossless
Since 11ax, AP triggered UL transmission plays a more important role for UL traffic
  Current BSRP/BSR provides a protocol for AP to acquire buffer status of each ACs on the non-AP side, so that AP can send trigger frames to trigger UL traffic
  For latency sensitive and periodic UL traffic, waiting for BSRP is not sufficient to satisfy jitter requirement and latency is not guaranteed
  If characteristics of the period traffic are known to AP, AP can allocate proper resources in advance and can trigger UL transmission in time

## Slide 3: Ideas
Using A-control subfield to carry periodic traffic indication to AP
  Instead of using TSPEC or other negotiation protocols, STA uses A-control to carry informative indication
  Unsolicited or solicited response to BSRP (buffer status report poll) or other TBD polls from AP
  Simple, proactive and more dynamic way on the non-AP side

## Slide 4: Periodic traffic indication (PTI) from non-AP STA to AP
Use A-control subfield (defined in the HE variant HT Control )
Limited access categories (AC) for latency sensitive traffic (VO and VI)
Parameters to carry
  Time period in ms
  delta time from the frame carrying the A-control to next instant the periodic traffic is coming in ms
  Access categories of the periodic traffic
  Periodic traffic size in octet
  Scaling factors of traffic size and period
Transmission
  Unsolicited transmission to AP
  Feedback to BSRP or other poll
    can be reported in parallel with BSR (buffer status report)
Extension of the BSR capability to decode PTI or adding new capability to indicate PTI decoding

## Slide 5: A-control Design Example of PTI
Periodic traffic indication
  Type: activate/deactivate the traffic corresponding to periodic traffic ID
  Periodic Traffic ID: 4 maximum in parallel
  AC: traffic corresponding AC (maybe limited to VI and VO)
  Period: period of the traffic in ms
  Delta period: delta time from the frame carrying the A-control to the next instant the period traffic is coming in ms
  Traffic size in octet
  Period scaling factor
  Traffic size scaling factor
Field | Type | Periodic Traffic ID | AC | Period (ms) | Delta period (ms) | Traffic size (octet) | Period scaling factor | Traffic size scaling factor
bits | 1 | 2 | 1 | 6 | 6 | 6 | 2 | 2

## Slide 6: Summary
Propose to use a new variant of the A-control subfield to carry UL periodic traffic indication
PTI can be solicited or unsolicited

## Slide 7: Straw Poll
Do you support that a non-AP STA can use a variant of the A-control subfield to carry UL periodic traffic indication to AP?
  NOTE: Detailed variant design is TBD

## Slide 8: References
20-0418 QoS Management framework in 802.11be
19-0065 RTA TIG summary and recommendations