## Slide 1: Traffic indication of latency sensitive applications
Date: 2020-09-01
Authors:

## Slide 2: Motivations
For UL latency sensitive traffic, such as gaming control and industrial automation, some applications have different modes of periodic traffic transmission [1, 2]
  Example: In a FPS game, a typical scene requires 40 packets/sec but changing to a busy scene may suddenly require transmitting 200 packets/sec with latency requirements.
  Signaling Requirements: Need to quickly indicate shifting from one periodic mode to another.
For some latency sensitive applications, UL burst traffic may require aperiodic allocation of bandwidth [3, 4]
  Example: In factory automation, an exception event occurred and a large burst of monitoring data needs to be reported within 100ms.
  Signaling Requirements: STA needs AP’s trigger to transmit a burst of traffic in time
Non-AP STA needs to provide timely latency sensitive traffic parameters to the AP so that the AP can better schedule triggered UL traffic
We propose to use a new A-ctrl so that a non-AP STA can provide UL periodic traffic and burst traffic parameters of latency sensitive applications.

## Slide 3: Discussion
Burst traffic indication is required for latency sensitive applications and a-ctrl is a simple and dynamic container fitting burst traffic indication
Difference from TSPEC based traffic indication [5, 6]
  Traffic indication latency is shorter with A-Ctrl based mechanism than TSPEC based mechanism using management frames.
  TSPEC based mechanism indicates information to AP only, with no commitment required on the AP side.
    A-Ctrl based mechanism allows faster acknowledgement from AP.
  TSPEC based mechanism does not cover burst traffic.

## Slide 4: Summary
Propose to design a new A-ctrl based mechanism so that non-AP STA can provide AP UL periodic traffic and burst traffic parameters of latency sensitive applications

## Slide 5: Straw Poll 1
Do you support defining a new A-control based QoS traffic indication mechanism in R2 so that a non-AP STA can provide AP TBD parameters of UL burst traffic and short term UL periodic traffic of latency sensitive applications?

## Slide 6: References
20-0418 QoS Management framework in 802.11be
19-0065 RTA TIG summary and recommendations
20-1006 New Methods To Meet Low Latency Requirement
18-1499 Real-time Console Game Network Profile
20-1693 TSPEC-lite
20-1350 Enhancements for QoS and low latency in 802.11be R1

## Slide 7: backup

## Slide 8: Proposal (1/2)
Use 1 bit to indicate the traffic parameter is burst or periodic
Parameters in periodic traffic indication (PTI)
  Enable: activate/deactivate the traffic corresponding to the TID
  Traffic ID
  Period: period of the traffic in ms
  Delta period: delta time referred to a time reference until the next periodic traffic is coming in ms
    Which time reference is TBD
  Traffic size in octet
  Period scaling factor
  Traffic size scaling factor

## Slide 9: Proposal (2/2)
Parameters in burst traffic indication (BTI)
  Traffic ID
  Period left to transmit: delta time referred to a time reference to transmit the burst traffic
    Which time reference is TBD
  Burst traffic size in octet
  Optional UL burst traffic size scaling factor
  Optional period of periodic UL burst traffic
  Optional repetitions of periodic UL burst traffic

## Slide 10: A-control Design Example of PTI
Periodic traffic indication
  Type: Burst or periodic traffic indication
  Enable: activate/deactivate the traffic corresponding to the traffic ID
  Traffic ID: mapping to one VO TID
  Period: period of the traffic in ms
  Delta period: delta time from the frame carrying the A-control to the next instant the period traffic is coming in ms
  Traffic size in octet
  Period scaling factor
  Traffic size scaling factor
Field | Type | Enable | TID | Period (ms) | Delta period (ms) | Traffic size (octet) | Period scaling factor | Traffic size scaling factor | Reserved
bits | 1 | 1 | 1 | 6 | 6 | 6 | 2 | 2 | 1