## Slide 1: STR capability signalling
Date: 2020-07-22
Authors:

## Slide 2: Abstract
Discusses how the STR capability can be signalled.

## Slide 3: Background (ML channel access)
Following relevant agreements have been reached about MLO channel access capability signaling:
  Simultaneous frame exchange capability: “A MLD can indicate capability to support exchanging frames simultaneously on a set of affiliated STAs to another MLD.”
  Simultaneous Tx/Rx capability: “A MLD that supports multiple links can announce whether it can support transmission on one link concurrent with reception on the other link for each pair of links.
    NOTE 1 – The 2 links are on different channels.
    NOTE 2 – Whether to define a capability of announcing the support transmission on one link concurrent with transmission on the other link is TBD.”
Following agreements on allowed MLO channel access modes itself:
  802.11be shall allow the following asynchronous multi-link channel access:
    Each of STAs belonging to a MLD performs a channel access over their links independently in order to transmit frames.
    Downlink and uplink frames can be transmitted simultaneously over the multiple links.
  802.11be shall allow a MLD that has constraints to simultaneously transmit and receive on a pair of links to operate over this pair of links
    Signaling of these constraints is TBD.
Notes: 1. Check MTk contrib.. :

## Slide 4: Background (ML capability signaling)
Current agreement on MLD-level information sharing:
  New “ML element”: A new element will be defined as a container to advertise and exchange capability information for multi-link setup.
  Common and per STA info in ML element: Do you support that an STA of an MLD can provide MLD-level information that is common to all STAs affiliated with the MLD and per-link information that is specific to the STA on each link in management frames during multi-link setup?
    The specific information is TBD [#SP65]
  Do you agree to define mechanism(s) to include MLO information that a STA of an MLD provides in its mgmt. frames, during discovery and ML setup, as described below?
    MLD (common) Information
      Information common to all the STAs of the MLD
    Per-link information
      Capabilities and Operational parameter of other STAs of the MLD other than the advertising STA [#SP91]

## Slide 5: Definition of constrained MLO
The existing SFD text identifies simultaneous transmit/receive issue over a pair of links but not a clear definition of the constraints.
In this presentation (similar to that proposed in 081r3) we assume that a pair of links at an MLD is considered non-STR if transmission by the MLD in one link impairs its Receiver minimum input level sensitivity or CCA sensitivity on the other link; otherwise that pair is considered STR .
  The transmission may be assumed at max transmit power capability.
Note that this definition still allows potential STR operation by a non-STR pair of links depending on RSSI, MCS level etc.
  For example, Rx at MCS-4 may be possible but not Rx at MCS-13 during Tx on the other link.
Note: the signaling in this presentation is largely independent of this definition.
Notes: Instead of Receiver minimum input level should it be CCA sensitivity for primary 20 MHz channel ? The latter seems to be less conservative.

## Slide 6: Other related submissions
STR capability related submissions:
  Submission 0921r0 proposes an option to signal STR capability + cross-link interference estimate.
  Submission 0809r0 also proposes that a STA signals its leakage estimates to AP.
  Submission 1550r1 lists bit-wise signaling of pairwise STR capability as an option.
We believe that the default mechanism for R1 signaling STR/NSTR capability to be the bit-map signaling. Additional information should be optional.

## Slide 7: Other assumptions
Assumptions:
  Discusses STR Capability exchanged during MLO setup.
  ML element common information contains signaling about the number of setup links/ number of STA profiles (N).
    For example, a single non-AP radio STA that sets up ML with a tri-band AP, N =3.
For STR/non-STR capability signaling we need to signal:
  Maximum number of links in which the MLD can operate simultaneously (M).
    For example, for Single Radio MLDs, M = 1, for dual radio, M = 2.
    Note: there could be configurations where there are restrictions on which links can use which radios.
  For a pair of links whether it is STR or non-STR.
Notes: 2.4 and 5/6.. ?

## Slide 8: Signaling of STR capability
Option 1: signal as an MLD-level capability information within common part of the ML element that is only present if a MR MLD.
  Signal max # of supportable links (M) can be used simultaneously (in STR/NSTR mode).
  Bit-map for each pair of links ( 1=> STR pair; 0 otherwise) when M > 1.
Element ID | Length | Element ID extension | MLD common Info | Information about STA-1 | … | Information about STA N
Other params | SR/MR | # of Supportable links (N) | # of max simultaneous links (M) | STR capability bitmap
STR/Non-STR (links 1 &2)
STR capability bitmap when N =M = 2
Bits: 1
STR/NSTR (links 1&2) | STR/NSTR (links 1&3) | STR/NSTR(links 2&3)
STR capability bitmap when N =3 and M > 1
Bits: 1 1 1
Notes: We can also consider a STR Capability Info element which could be scalable to more than 3 links but has a bit higher overhead.

## Slide 9: Signaling of STR capability (contd.)
Option 2: signal as an MLD-level capability information the max # of supportable links but STA level information for individual pairs.
Element ID | Length | Element ID extension | MLD common Info | Information about STA-1 | … | Information about STA N
Other params | SR/MR | # of Supportable links (N) | # of max simultaneous links (M)
Other params | STR/NSTR (links 1&2) | STR/NSTR (links 1&3)
Information about STA-1 when N =3 & M > 1 (similarly for STA-2,3).
Bits: x 1 1
MLD common Info
Bits: x 1 2 2
Other params | STR/NSTR (links 1&2)
Information about STA-1 when N = M = 2 (similarly for STA-2).
Bits: x 1
Notes: Add an example clarifying linked/ other way to identify STA profile

## Slide 10: Signaling of STR capability (contd.)
Option 3: mixed mode between Option 1 & 2 where the bitmap signaling is inside STA-profile without duplication.
Element ID | Length | Element ID extension | MLD common Info | Information about STA-1 | … | Information about STA N
Other params | SR/MR | # of Supportable links (N) | # of max simultaneous links (M)
Other params | STR/NSTR (links 1&2) | STR/NSTR (links 1&3)
N =3 & M > 1 case
Bits: x 1 1
MLD common Info
Bits: x 1 2 2
Information about STA-1.
Other params | STR/NSTR (links 2&3)
x 1 x
Information about STA-2.
Other params
Information about
STA-3.
Notes: Add an example clarifying linked/ other way to identify STA profile

## Slide 11: Comparison and Usage
Option 2 or 3 is preferable because even though it has slightly higher overhead, the parsing may be easier.
At non-AP STA side,
  Probe Request does not contain STR Capability Info.
  Association Request contains complete STR Cap Info.
At AP side,
  MLD level Probe Response and Association Response contains all the STR Capability Info at the AP side.
  Note: only soft-AP MLD can be non-STR.

## Slide 12: Summary
Proposed bitmap to signal pairwise STR/NSTR capability of an MLD.
Signaling to be carried in the ML element during MLO Setup.

## Slide 13: Sp1
Do you agree to add the following to SFD:
a non-AP MLD that supports STR or NSTR operations includes in the STA specific profiles of an ML element, a bitmap where each bit represents STR/NSTR capability for a pair of links containing this STA ?

## Slide 14: SP2
Do you agree to add the following to SFD:
the common part of ML element transmitted by a non-AP MLD signals the maximum number of affiliated STAs in the MLD that can operate simultaneously ?

## Slide 15: SP3
Do you agree to add the following to SFD:
the ML element transmitted by an MLD contains signaling to identify the set of links that can be used simultaneously ?

## Slide 16: Straw Poll 2
Do you agree to add the following to SFD: a pair of links at an MLD is considered non-STR if transmission by the MLD in one link causes it not to meet its Receiver minimum input level sensitivity or CCA sensitivity requirements on the other link; otherwise that pair is considered STR ?

## Slide 17: 20/0226r5 (MLO Constraint Indication and Operating Mode, Sharan Naribole, Samsung)
Do you support the addition of the following text to TGbe SFD?
A non-AP MLD may update its ability to perform simultaneous transmission and reception on a pair of setup links after multi-link setup.
  This update for any pair of setup links can be announced by non-AP MLD on any enabled link.
NOTE – Specific signaling for update indication is TBD
NOTE - Limitations on dynamic updating is TBD
Y/N/A/No answer: 43/7/29/19