## Slide 1: Multi-link for Battery Powered AP MLD
Date: 2020-12-07
Authors:

## Slide 2: Introduction
802.11be is on its way to define multi-link operations as one way to meet the criteria set in the PAR
Multi-link operations may be used both in access point multi-link devices (AP MLD) and in non-AP multi-link devices (non-AP MLD)
  Each station affiliated with the AP MLD is an AP
  Each station affiliated with the non-AP MLD is a non-AP STA
This implies that whenever the AP MLD has a link in operation, it has the corresponding AP active
  Active AP is always available on its channel and the current specification doesn’t provide any means for it to be periodically unavailable e.g. for power saving purposes
In this presentation, we discuss the case of battery powered AP MLDs which would benefit from ability to use the multi-link operations without the burden of “always-on APs”

## Slide 3: Current AP MLD design and its challenges in use with battery powered AP MLD
An AP MLD has an AP for each link it operates and per the basic rules set for an AP, whenever the AP MLD has a link in operation, it has the corresponding AP active
This implies also that MLME-START and MLME-STOP are the mechanisms of an AP MLD to drive its links up and down
These restrict use of multi-link operations in battery powered APs which would benefit from means to more dynamically drive its links up and down based on e.g. service needs
AP_1
AP_2
AP_3
AP MLD
Non-AP STA
Non-AP STA
Non-AP STA
Non-AP MLD

## Slide 4: Alternative approach for battery powered AP MLD
Battery powered AP MLD would benefit from a design with more relaxed requirements on STAs that such a device needs to have for its links
One possible approach is to allow a battery powered AP MLD to use multi-link operations under control of one AP
  The AP is responsible for one link
    Let’s call this link primary link
  One or more other links may be established as well with one or more non-AP STAs
    Let’s call these links secondary links
The AP is always on in the primary link while the non-AP STAs associated to the secondary links may benefit from different power saving schemes both on the battery powered AP MLD and on the non-AP MLD side
AP
Non-AP STA
Battery powered AP MLD
Non-AP STA
Non-AP STA
Non-AP STA
Non-AP MLD
Non-AP STA

## Slide 5: Summary
We would like to see multi-link operations of 802.11be to be defined in a way that they can be effectively used in battery powered AP MLDs
The current design which requires AP MLD to have an AP for each of its links implies requirements that are heavy for battery powered devices
We wonder if there is interest in the TG to consider a design which would give more freedom for link management in battery powered devices

## Slide 6: SP 1
Do you agree that the 11be shall support the multi-link operations which not requires each station affiliated to AP MLD to be an AP for battery powered devices?
  Yes:
  No:
  Abstain:

## Slide 7: SP 2
Would you be interested in working towards a solution which would allow battery powered AP MLD to operate two or more links with just one AP affiliated with the device?
  Yes:
  No:
  Abstain: