## Slide 1: Follow-ups on Channel Measurement Procedure for WLAN Sensing
Date: 2020-06-13
Authors:
Name | Affiliation | Address | Phone | Email
Chenchen LIU | Huawei |  |  | liuchenchen1@huawei.com
Meihong Zhang |  |  |  | 
Rui Du |  |  |  | 
Yingxiang Sun |  |  |  | 

## Slide 2: Abstract
In this contribution, we discuss the channel measurement procedure for WLAN sensing

## Slide 3: Outline
Background of WLAN sensing
Potential Channel measurement procedure
  Option1: Feedback from the responders
  Option2:No feedback
  Option3: Threshold based NDP feedback
Summary
References

## Slide 4: Background of WLAN sensing
Basic principle
Signal reflected from the target carriers info of the target(e.g. velocity, location, etc.)
Advantages
  Ubiquitous
  Device-free
  Privacy
  High precision
  field of view
intruder detection
Fall detection
Gesture recognition
Gesture recognition

## Slide 5: Background of WLAN sensing
Sensing based on channel sounding
  Explicit
  Implicit
Channel direction not crucial(reciprocal in general)
  Typical use cases only track changes over time
Periodicity
  Some use cases like intruder detection might need a reliable periodicity of CSI feedback
  Most of the feedbacks over a period may be highly correlated
With those principles in mind, let consider the channel measurement procedure for WLAN sensing

## Slide 6: Option1: Feedback from the RSTAs
TX STA and RX STA diversity is very important in the sensing applications [2]
The ISTA broadcast the NDP to all the RSTAs
The RSTAs feedback the sensing measurement report to the ISTA

## Slide 7: Option1: Feedback from the responders
An example of the sensing procedure with feedback from multiple RSTA
Problems:
  If the CSI as feedback, huge amount of data to feedback
  If sensing results as feedback, the RSTAs may have limited ability to resolve angles and perform complex algorithm
  Some coordination is needed

## Slide 8: Option2: No feedback
The ISTA trigger each RSTA to send the NDP to the ISTA[3]
The ISTA receive the NDP from each RSTA and do the sensing measurement within itself

## Slide 9: Option2: No feedback
Examples of the sensing procedure with no feedback from the RSTA
Problems:
  ISTA may need some processing time before processing the next NDP
  Full bandwidth is not utilized for OFDMA
  Complexity at the ISTA

## Slide 10: Option 3: Threshold based feedback
The ISTA set the threshold[4] for each RSTA, and periodically transmit the NDP to all RSTAs
The RSTA measure the CSI and compare it with previous measurement result
If the CSI difference exceeds the threshold, the RSTA sends a NDP to the ISTA(schedule may needed). Otherwise, the RSTA store measurement result and feedback nothing
The ISTA do the sensing measurement within itself based on the NDP send by the RSTA

## Slide 11: Option3: Threshold based feedback
An example of the sensing procedure with threshold based NDP feedback
Problems:
  May cause some delay for certain application(negligible in most case)

## Slide 12: Comparison
Channel measurement procedure | Pros | Cons
Option1:From the responders | Simple measurement | Large overhead, limited processing ability
Option2: No feedback | No feedback needed | Interference or longer airtime
Option3: Threshold based | Small overhead | Latency

## Slide 13: Summary
In this contribution, three channel measurement procedures for WLAN sensing and their corresponding pros and cons are discussed.

## Slide 14: References
[1] CSI-based Wi-Fi Sensing: Results and Standardization Challenges, doc.: IEEE 802.11-19/1769
[2] Wi-Fi Sensing: Cooperation and Standard Support, doc.: IEEE 802.11-19/1416r0
[3] A Channel Measurement Procedure for WLAN Sensing, doc.: IEEE 802.11-20/0842r0
[4] Z. Wu, Y. Han, Y. Chen and K. J. R. Liu, "A Time-Reversal Paradigm for Indoor Positioning System," in IEEE Transactions on Vehicular Technology, vol. 64, no. 4, pp. 1331-1339, April 2015

## Slide 15: Backup
Threshold could be TRRS