## Slide 1: 802.11be Architecture/Association Discussion
Date: 2020-08-24
Authors:

## Slide 2: Abstract
802.11 TGbe has been discussing MLDs for several months, but there has been little discussion of how MLD will fit in the 802 architecture. Top down design concepts may help progress the MLD work. This contribution discusses an MLD architecture that is well aligned with the current 802.11 basic architecture and will hopefully allow many existing 802.11 features to be reused to support MLD operation.

## Slide 3: 802.11 Basic Architecture/Association (review)
Both the AP and non-AP STA are logical entities
An association defines a SAP to SAP connection between an AP MAC SAP to a non-AP MAC SAP (providing a service that allows frames received from the upper layer at a MAC SAP to be passed via the MAC/PHY over the wireless media to another PHY/MAC to its MAC SAP where it is passed to the upper layers)
Reassociation is a means to redefine a SAP to SAP connection to either the same or different AP MAC SAP and a non-AP MAC SAP while maintaining some association status (e.g. security/IP address).
Disassociation is a means of tearing down a SAP to SAP connection.
802.11be should use/align with these existing functions as much as possible.

## Slide 4: 802.11be MLD Architecture Discussion
The introduction of the MLD concept will define an MLD MAC SAP
An MLD MAC SAP of an AP MLD will connect to higher layers via the DS (for non-GLK APs) serving the same purpose as the current MAC SAP
The MLD MAC SAP of an non-AP MLD will connect to higher layers via the LLC sublayer, also serving the same purpose as the current MAC SAP.
The MLD MAC (lower and upper) will manage all aspects of access to the PHY and media (this applies to both the AP MLD and non-AP MLD)
This architecture is an extension of the current 802.11 architecture for all non-GLK STAs (AP and non-AP STA)
This architecture will support a device (e.g. non-AP MLD) being able to choose between MLD associations and 802.11 associations (non-MLD)

## Slide 5: Current Basic 802.11 Architecture (non-GLK)

## Slide 6: Proposed MLD 802.11be Architecture

## Slide 7: Proposed MLD 802.11be Architecture - Alt

## Slide 8: FST Architecture – For Reference

## Slide 9: Possible AP MLD/ Non-AP MLD Associations
Assuming the architecture shown on the “Proposed MLD 802.11be Architecture” slide with an AP MLD that can support 3 links and a non-AP MLD that can support 3 links:
The non-AP MLD can associate with:
  The AP MLD with 3 links
  The AP MLD with 2 links (there are 3 possible 2 link configurations)
  The AP MLD with 1 link (3 possible) – this is “standard” current 802.11 association
Therefore each of configuration needs an identifier (e.g. a MAC address)
  The identifier will be associated with a specific configuration, the configuration will provide the number and parameters of the links.
  The non-AP MLD will associate using the identifier to a specific configuration
  Hence the non-AP MLD only need to use association, reassociation, and disassociation services to manage its link configuration with the AP MLD.

## Slide 10: Conclusion
The proposed MLD architecture:
Is a natural extension to the current 802.11 architecture
Allows the current association, reassociation, and disassociation services to be used to manage MLD connections
Proposes the use of an identifier (MAC address) to define the MLD configuration
Allows for reuse of other defined 802.11 services with only minor updates