## Slide 1: ML element design
Date: 2020-08-10
Authors:

## Slide 2: Background
802.11be defines mechanism(s) to include ML element that a STA of an MLD provides in its mgmt. frames, during discovery and ML setup, as described below[1]:
  MLD Level/Common Info
  Information common to all the STAs of the MLD.
  Per-link information
  Capabilities and Operational parameter of other STAs of the MLD other than the advertising STA.
 | Element ID | Length | Element ID Extension | Common Control | MLD Address | … | … | … | Optional Sub-elements
Octets: | 1 | 1 | 1 | 1 | 0 or 6 | … | … | … | variable
MLD Level/Common Info
Per-Link Info
Multiple Link element
MLD Addr Present

## Slide 3: Recap
During the discovery phase, an AP within an AP MLD should only include the MLD-level/common info field of the ML element in the Beacon or non-ML Probe Response frame
  The MLD-level/common info includes MLD MAC address and other TBD info
  During the multi-link set up phase, a STA in a MLD can provide a complete ML element
  MLD-level information that is common to all STAs in the same MLD
  and per-link information that is specific to the STA on each link in management frames
  Moreover, an AP in an AP MLD can provide a complete or patial ML element in the ML Probe Response frame as per the ML Probe Request frame
  An AP receives the ML Probe Request frame which solicits the specific AP info within the target AP MLD
  An AP receives the ML Probe Request frame which solicits the info of the specific AP MLD

## Slide 4: ML element in discovery phase
To speed up the AP MLD discovery phase, an AP in an AP MLD shall advertise the ML related info for each AP in the same AP MLD and other collocated AP MLD, such as Link ID, ML ID and so on in [2] [3] and[4]
  Link ID is carried in TBTT info of the RNR element for a reported AP, which is used to identify this AP
  ML ID is also carried in the TBTT info of the RNR element for a reported AP , which is used to identify the AP MLD with which this AP is affiliated
However, the ML related info for both transmitting AP and nontransmitted BSSID is missing as mentioned in [2]
  RNR element does not contain the info for both transmitting AP and nontransmitted BSSID
  Moreover, the locations of Change Sequence field for both transmitting AP and nontransmitted BSSID are also TBD now

## Slide 5: ML element in discovery phase
We propose to carry transmitting AP info in the MLD-level/common info field of the ML element
  If the reported AP is nontranmitted BSSID, the MLD-level/common info field of the ML element is carried in non-transmitted BSSID profile
  MLD-level/common info field includes both Link ID and Change sequence
 | Element ID | Length | Element ID Extension | Common Control | MLD Address | Transmitting AP Info | … | … | Optional Sub-elements
Octets: | 1 | 1 | 1 | 1 | 0 or 6 | TBD | … | … | variable
MLD Level/Common Info
Per-Link Info
Multiple Link element
MLD Addr Present
Link ID
Change Sequence

## Slide 6: ML element in ML Probe
As mentioned before, a STA within a non-AP MLD can send the following the following ML Probe Request frames
  The ML Probe Request frame which solicits the specific AP info within the target AP MLD
  The ML Probe Request frame which solicits the info of the specific AP MLD
  The ML Probe Request frame which solicits the info of any AP MLD
  Other cases are TBD
Once an AP in an AP MLD received the above ML Probe Request frame, it will respond with the following info
  One or more specific AP info by using a partial ML element
  One specific AP MLD info by using a complete ML element
  More than one specific AP MLD info by using more than one complete ML element
  Note that non-ML Probe response frame can also provide the info of other AP in the same MLD as per non-ML Probe Request frame

## Slide 7: ML element in ML Probe
For example as shown in the below figure, if AP1x in MLD 1 receives a Probe Request frame which solicits the info of any AP MLD, then AP 1x responds the Probe Response frame with the following info
  The info of MLD 1 since AP 1x is from MLD 1
  The info of MLD 2 since AP 1y on link 1can not respond Probe Response frame
  The info of MLD3 since no AP working on link 1
  To differentiate different ML elements in one Probe Response frame, we propose extra indications carried in ML element for the following two kinds of MLDs, respectively
  The MLD for which there is no affiliated AP working on the same link as the AP which sends the Probe Response
  The MLD for which there is a nontransmitted
  BSSID in the same multiple BSSID as the AP
  which sends the Probe Response

## Slide 8: Summary
In this contribution, we propose to design ML element from aspect of discovery
  Include the info of transmitting AP in the MLD-level/common info field of the ML element, such as link ID and change sequence
  Moreover, the ML Probe Response can carry more than one ML elements as per the STA’s request

## Slide 9: References
[1] 11-20-0566-62-00be-Compendium of straw polls and
potential changes to the Specification Framework Document
[2] 11-20-0615-03-00be-Discovery mechanism for MLD
[3] 11-20-0389-00-00be-Multi-link discovery part 1
[4] 11-20-0390-00-00be-Multi-link discovery part 2