## Slide 1: Restrictions on MLD Probe
Date: 2020-08-26
Authors:
Name | Affiliations | Address | Phone | Email
Cheng Chen | Intel |  |  | 
Po-kai Huang |  |  |  | 
Laurent Cariou |  |  |  | 
Ido Ouzieli |  |  |  | 
Daniel Bravo |  |  |  | 
Notes: September 2012

## Slide 2: Background
We already agreed that for Multi-link discovery
  Basic information of the MLD is carried in RNR in Beacon and probe response
    [Motion 115, #SP93] All APs that are part of the same MLD as a reporting AP and that are collocated with the reporting AP shall be reported in the RNR element that is included in the beacons and the broadcast probe responses transmitted by the reporting AP when the reporting AP is either not part of a multiple BSSID set or corresponds to a transmitted BSSID in a multiple BSSID set.
  Complete information of the MLD can be provided via a ML Probe request
    [Motion 115, #SP97, Motion 119, #SP109] 802.11be agrees to define a mechanism for a STA of a non-AP MLD to send a probe request frame to an AP belonging to an AP MLD, which enables to request a probe response from the AP that includes the complete set of capabilities, parameters and operation elements of other APs affiliated to the same MLD as the AP
    Note: Such a directed probe request requesting complete MLO information for one or more APs of the MLD is referred to as an ML probe request.
    Note: A probe response sent in response to an ML probe request containing complete MLO Information for the requested AP(s) is referred to as an ML probe response.

## Slide 3: Regular probe request vs. ML probe request
We differentiate between regular probe request/response and MLD probe request/response:
  Regular probe request/probe responses:
    Probe request that contains mainly information on the link on which it is transmitted, and generates a regular probe response that contains the RNR (min information – basic discovery)
  MLD probe request/probe responses:
    Probe request that requests complete MLD info on multiple links that the STA supports
    Probe response contains complete information on AP MLD
  These 2 probes are used differently by the STA:
    For basic initial discovery---use regular probe
    For collecting complete info before Multi-link setup---use MLD Probe

## Slide 4: Restrictions on ML probe request
Since ML probe request/response includes complete information of all links supported by the MLD, the associated overhead is likely to be much larger than regular probe request/response.
If we allow a non-AP MLD to arbitrarily use ML probe request, it may cause congestion in the links.
In 6 GHz, we placed several restrictions on the use of probe request. In this contribution we propose to apply similar ideas to limit the use of ML probe request.

## Slide 5: Blind ML probe
We prohibit blind probe request in 6 GHz in 11ax.
  11ax 6 GHz: The non-AP STA shall not transmit a Probe Request frame to the broadcast destination address with the Address 3 field set to the wildcard BSSID, and the SSID set to the wildcard SSID.
For MLD Probing, it should be done after basic discovery. Therefore, we should also prohibit blind MLD Probe Request.
  Proposed rule in 11be: A non-AP STA affiliated with a non-AP MLD shall not transmit a MLD Probe Request to the broadcast destination address with the Address 3 field set to the wildcard BSSID, and the SSID set to the wildcard SSID (Note : 6 GHz is already covered).
  This is consistent with the definition of an ML Probe request:
    Such a directed probe request requesting complete MLO information for one or more APs of the MLD is referred to as an ML probe request

## Slide 6: Frequency of ML probe
We should also limit the frequency of transmitting MLD Probe Request, like what we did in 11ax in terms of limiting Probe Request in 6 GHz.
  11ax 6 GHz: The non-AP STA shall not transmit more than one Probe Request frame to the broadcast destination address with the Address 3 field set to the wildcard BSSID and the SSID field not set to the wildcard SSID during each 20 TU period scanning the channel. The non-AP STA shall not transmit more than three Probe Request frames to the broadcast destination address with Address 3 field set to a non-wildcard BSSID during each 20 TU period scanning the channel.
  Proposed rule in 11be: A non-AP STA affiliated with a non-AP MLD shall not transmit more than one MLD Probe Request frame to the broadcast destination address with the Address 3 field set to the wildcard BSSID and the SSID field not set to the wildcard SSID during each 20 TU period scanning the channel. A non-AP STA affiliated with a non-AP MLD shall not transmit more than three MLD Probe Requests to the broadcast destination address with Address 3 field set to a non-wildcard BSSID during each 20 TU period scanning the channel.

## Slide 7: Additional rules on ML probe
In 11ax 6 GHz, we prohibit the non-AP STA to send a probe if it has already obtained the information from the AP.
  11ax 6GHz: The non-AP STA shall not send a Probe Request frame to the broadcast destination address with the Address 3 field (BSSID) set to the BSSID of an AP from which it has already received a Probe Response or a Beacon frame since the start of its scanning on that channel.
We should apply similar rules in 11be, prohibiting the use of MLD Probe Request if the non-AP MLD has already received complete information from the AP MLD.
  Proposed rule in 11be: None of the non-AP STAs of a non-AP MLD shall send an ML Probe Request frame to the broadcast destination address with the Address 3 field (BSSID) set to the BSSID of the AP of the AP MLD in the corresponding link if any non-AP STA of the same non-AP MLD has already received a ML Probe Response or a Beacon frame including complete information from any of the AP of the AP MLD in any link, since the MLME-SCAN.request primitive with ScanType parameter indicating an Active scan was issued.
  Note: complete information means information of all APs of the AP MLD

## Slide 8: Unsolicited Probe Response
In 11ax 6 GHz, we defined unsolicited probe response.
  If implemented, the AP operating in 6 GHz schedules for transmission unsolicited probe response frames every 20 TUs or less.
Considering the large overhead associated with ML probe response, we think ML probe response should only be sent when requested. In other words, such unsolicited probe response shall not be ML probe response. As a result, we propose the following:
  Proposed rule in 11be : Unsolicited probe responses sent by an AP with dot11UnsolicitedProbeResponseOptionActivated set to true shall not be ML probe response.

## Slide 9: Conclusions
We proposed several rules to restrict the use of MLD Probe in 11be.
  To prevent “probe storm”.
  Most of the rules are adapted from the restriction rules in 11ax 6 GHz and extended to MLD Probe with similar ideas.

## Slide 10: SP 1
Do you agree with the following:
  A non-AP STA affiliated with a non-AP MLD shall not transmit an ML Probe Request to the broadcast destination address with the Address 3 field set to the wildcard BSSID, and the SSID set to the wildcard SSID
  Note: 6 GHz is already covered by existing rules in 11ax.

## Slide 11: SP 2
Do you agree with the following:
  A non-AP STA affiliated with a non-AP MLD shall not transmit more than one ML Probe Request to the broadcast destination address with the Address 3 field set to the wildcard BSSID and the SSID field not set to the wildcard SSID during each 20 TU period scanning the channel. A non-AP STA affiliated with a non-AP MLD shall not transmit more than three ML Probe Requests to the broadcast destination address with Address 3 field set to a non-wildcard BSSID during each 20 TU period scanning the channel.

## Slide 12: SP 3
Do you agree with the following:
  None of the non-AP STAs of a non-AP MLD shall send an ML Probe Request frame to the broadcast destination address with the Address 3 field (BSSID) set to the BSSID of the AP of the AP MLD in the corresponding link if any non-AP STA of the same non-AP MLD has already received a ML Probe Response or a Beacon frame including complete information from any of the AP of the AP MLD in any link, since the MLME-SCAN.request primitive with ScanType parameter indicating an Active scan was issued.
  Note: complete information means information of all APs of the AP MLD.

## Slide 13: SP 4
Do you agree with the following:
  Unsolicited probe responses sent by an AP with dot11UnsolicitedProbeResponseOptionActivated set to true shall not be ML probe response.